## Slide 1: SCEF northbound API Analysis
Group Name: ARC
Source: Bei Xu, Huawei Technologies Co., Ltd. Echo.xubei@huawei.com
Meeting Date: 2016-11-27
Agenda Item: TBD

## Slide 2: Content
Non-IP device Accessing oneM2M platform（MO/MT）
CMDH
  Down Link Data Delivery when UE is unreachable
  UE PSM timer or eDRX Configuration
  Network Monitor：Network Status， Communication Failure
Group Management
  Location
  Network-based location
Others

## Slide 3
Non-IP Data Delivery Configuration
Figure 5.13.2-1: Configuration for NIDD procedure
SCEF API Requirement
  Step1：NIDD Config Req（SCEF->SCS）NIDD Configuration Request (External Identifier or MSISDN, SCS/AS Identifier, SCS/AS Reference ID, NIDD Duration, NIDD Destination Address, SCS/AS Reference ID for Deletion)
  Step6：NIDD Config Rsp（SCS->SCEF）NIDD Configuration Response (SCS/AS Reference ID, Cause)
Stage 2 completeness：
  Y

## Slide 4
non-IP Device MO Service Flow
SCEF API Requirement
  Step3：NIDD MOReq（SCEF->SCS）
  Step4：NIDD MORsp（SCS->SCEF）
Stage 2 completeness
  N

## Slide 5: Non-IP device MT Service Flow
SCEF API Requirement
  Step1：NIDD MTReq（SCS->SCEF）
  NIDD Submit Request (External Identifier or MSISDN, SCS/AS Reference ID, non-IP data)
  Step5/9：NIDD MTRsp（SCEF>SCS）
Stage 2 completeness
  Step1： Y
  Step5/9：N

## Slide 6: Content
Non-IP device Accessing oneM2M platform（MO/MT）
CMDH
  UE PSM timer or eDRX Configuration
  Down Link Data Delivery when UE is unreachable
  Network Monitor：Network Status， Communication Failure
Group Management
Location
  Network-based location
Others

## Slide 7: Downlink Data Delivery when UE is unreachable
3GPP introduction
UE Power Saving Mode（ PSM ）
  That mode is similar to power-off, but the UE remains registered with the network and there is no need to re-attach or re-establish PDN connections.
  A UE in PSM is not immediately reachable for mobile terminating services.
  A UE using PSM is available for mobile terminating services during the time it is in connected mode and for the period of an Active Time that is after the connected mode.
Extended Idle mode Discontinuous Reception （eDRX）
  The UE and the network may negotiate over non-access stratum signaling the use of extended idle mode DRX for reducing its power consumption
  Applications that want to use extended idle mode DRX need to consider specific handling of mobile terminating services or data transfers, and in particular they need to consider the delay tolerance of mobile terminated data.
  oneM2M introduction
  Schedule
  A child <schedule> resource of the <AE> resource shall indicate the time periods when the application of a node can be accessed.

## Slide 8: Monitor Event Configuration
Figure 5.6.1.1-1: Monitoring event configuration and deletion via HSS procedure
SCEF API Requirement
  Step1：Monitoring Request（SCS->SCEF）
  Monitoring Configuration Request of UE reachablity (External Identifier(s) or MSISDN(s), SCS/AS Identifier, SCS/AS Reference ID, Monitoring Type, Maximum Number of Reports, Monitoring Duration, Monitoring Destination Address, SCS/AS Reference ID for Deletion)
    Monitoring Type = UE reachablity (Reachability Type , Maximum Latency ,Maximum Response Time )
    Monitoring Type = Availability after DDN Failure，without Max Number of Reports（one time subscription）
  Step9：Monitoring Response（SCEF->SCS）
  Monitoring Response (SCS/AS Reference ID, Cause)
Interface Supported by 3GPP or not
Y

## Slide 9: UE PSM timer/eDRX Configuration
SCEF API Requirement
  Step1：PSM Timer Set Request（SCS->SCEF）
  Monitoring Request of UE reachablity (External Identifier(s) or MSISDN(s), SCS/AS Identifier, SCS/AS Reference ID, Monitoring Type, Maximum Number of Reports, Monitoring Duration, Monitoring Destination Address, SCS/AS Reference ID for Deletion)
    Monitoring Type = UE reachablity (Reachability Type , Maximum Latency ,Maximum Response Time )
  Step9：PSM Timer Set Response（SCEF->SCS）
  Monitoring Response (SCS/AS Reference ID, Cause)
Stage 2 completeness
Y

## Slide 10: Monitoring Event Report(UE Reachability )
Figure 5.3.2-1 UE Reachability reporting
SCEF API Requirement
  Step2：Monitor Report（SCEF->SCS）
  MonitorReport(SCS/AS Reference ID, External ID or MSISDN, Monitoring Information)
Interface Supported by 3GPP or not
  Partially, Monitoring Information is not clear.

## Slide 11: Monitoring Event(Availability Notification after DDN Failure)
Figure 5.4.4-1: Notification - Availability Notification after DDN Failure
SCEF API Requirement
  Step9：Monitor Report（SCEF->SCS）
  MonitorReport(SCS/AS Reference ID, External ID or MSISDN, Monitoring Information)
Stage 2 completeness
  Partially, Monitoring Information is not clear.

## Slide 12: Network Monitoring
Monitoring Event: Communication failure
This monitoring event allows the SCS/AS to be notified of communication failure events, identified by RAN/NAS Release Cause codes.
Informing about Potential Network Issues
The SCS/AS requests to be informed, one-time/continuously, about the network status by providing a geographical area.

## Slide 13: Monitoring Event: Communication failure
SCEF API Requirement
  Step1：Monitoring Request（SCS->SCEF）
  Monitoring Configuration Request of UE reachablity (External Identifier(s) or MSISDN(s), SCS/AS Identifier, SCS/AS Reference ID, Monitoring Type, Maximum Number of Reports, Monitoring Duration, Monitoring Destination Address, SCS/AS Reference ID for Deletion)
    Monitoring Type Communication Failure
  Step9：Monitoring Response（SCEF->SCS）
  Monitoring Response (SCS/AS Reference ID, Cause)
  Step12：Monitoring Report（SCEF->SCS）
  Monitoring Response(SCS/AS Reference ID, External ID or MSISDN, Monitoring Information)
Stage 2 completeness
  Partially, Monitoring Information is not clear.
Figure 5.8.2-1: Request procedure for one-time or continuous reporting of network status

## Slide 14: Request procedure for one-time or continuous reporting of network status
SCEF API Requirement
  Step1:Network Status Req(SCS->SCEF)
    Network Status Request (Geographical area, SCS/AS Identifier, SCS/AS Reference ID, Duration, Threshold)
    Cancel Network Status Request (SCS/AS Identifier, SCS/AS Reference ID)
  Step6:Network Status Rsp(SCEF->SCS)
    Network Status Report (SCS/AS Reference ID, Congestion level, ECGI/eNodeB-ID/SAI )
    Cancel Network Status Response (SCS/AS Reference ID)
Stage 2 completeness
  Y
Figure 5.8.2-1: Request procedure for one-time or continuous reporting of network status

## Slide 15: Content
Non-IP device Accessing oneM2M platform（MO/MT）
CMDH
  Down Link Data Delivery when UE is unreachable
  UE PSM timer or eDRX Configuration
  Network Monitor：Network Status， Communication Failure
Group Management
Location
  Network-based location
Others

## Slide 16: Group message delivery procedures
SCEF API Requirement
  Step1:Allocate TMGI Request（SCS->SCEF）
  Allocate TMGI Request (External Group ID, SCS Identifier, location/area information)
  Step4:Allocate TMGI Rsp （SCEF->SCS）
  Allocate TMGI Rsp(SCS/AS Reference ID, TMGI and expiration time information)
  Step6:Group Message Request(SCS->SCEF)
  Group Message Request (External Group Identifier, SCS Identifier, location/area information, RAT(s) information, TMGI, start time)
  Step11:Group Message Confirm(SCEF->SCS)
  Group Message Confirm (TMGI (optional), SCEF IP addresses/port)
Stage 2 completeness
  Partial, the interface and parameter is not clear

## Slide 17: Content
Non-IP device Accessing oneM2M platform（MO/MT）
CMDH
  Down Link Data Delivery when UE is unreachable
  UE PSM timer or eDRX Configuration
  Network Monitor：Network Status， Communication Failure
Group Management
Location
  Network-based location
Others

## Slide 18: LocationPolicy
oneM2M introduction
The <locationPolicy> resource represents the method for obtaining and managing geographical location information of an M2M Node.Based on the locationSource attribute, the method for obtaining location information of an M2M Node can be differentiated. The methods for obtaining location information shall be as follows:
  Network-based method: where the CSE on behalf of the AE obtains the target M2M Node's location information from an Underlying Network.
  Device-based method: where the ASN is equipped with any location capable modules or technologies (e.g. GPS) and is able to position itself.
  Sharing-based method: where the ADN has no GPS nor an Underlying Network connectivity. Its location information can be retrieved from either the associated ASN or a MN.

## Slide 19: Monitoring Event: Location Reporting
Figure 5.6.1.1-1: Monitoring event configuration and Report
SCEF API Requirement
  Monitor Event ConfigReq（SCS->SCEF）
  Monitoring Request (External Identifier(s) or MSISDN(s), SCS/AS Identifier, SCS/AS Reference ID, Monitoring Type, Maximum Number of Reports, Monitoring Duration, Monitoring Destination Address, SCS/AS Reference ID for Deletion)
    Monitoring Type = Location Reporting（ Location Type， Accuracy prior ）
    Monitoring Type = Roaming Status (PLMN Information)
  Monitor Event ConfigRsp（SCEF>SCS）
  Monitoring Response (SCS/AS Reference ID, Cause)
  Monitor Report（SCEF>SCS）
    LocationMonitorReport(SCS/AS Reference ID, External ID or MSISDN, geo-location)
    RoamingStatusMonitorReport(SCS/AS Reference ID, External ID or MSISDN, HPLMN PLMN-Id/ Visited PLMN-Id)
Stage 2 completeness
  Y

## Slide 20: Summary（High Priority）
oneM2M comman service function | 3GPP SCEF API Requirement | Prameter of API | 3GPP defined or not | OMA support or not | Remark
Non-IP device Accessing oneM2M platform（MO/MT） | NIDD Configuration Request | External Identifier or MSISDN, SCS/AS Identifier, SCS/AS Reference ID, NIDD Duration, NIDD Destination Address, SCS/AS Reference ID for Deletion | Y | N | 
 | NIDD Configuration Response | SCS/AS Reference ID, Cause | Y | N | 
 | NIDD MOReq |  | N | N | 
 | NIDD MORsp |  | N | N | 
 | NIDD MTReq | External Identifier or MSISDN, SCS/AS Reference ID, non-IP data | Y | Y | OMA-TS-REST_NetAPI_Messaging(NIDD
 | Subscription NIDD Status |  | N | N | OMA-TS-REST_NetAPI_Messaging(NIDD
 | NIDD MTRsp |  | N | N | OMA-TS-REST_NetAPI_Messaging(NIDD
 | Communication failure Monitor Event ConfigReq | External Identifier(s) or MSISDN(s), SCS/AS Identifier, SCS/AS Reference ID, Monitoring Type, Maximum Number of Reports, Monitoring Duration, Monitoring Destination Address, SCS/AS Reference ID for Deletion | Y |  | 
 | Communication failure Monitor Event ConfigRsp | SCS/AS Reference ID, Cause | Y |  | 
 | Communication failure Monitor Report | failure cause code / an abstracted value | N |  | 
CMDH-Down Link Data Delivery when UE is unreachable | Monitor Event ConfigReq-UE reachablity | External Identifier(s) or MSISDN(s), SCS/AS Identifier, SCS/AS Reference ID, Monitoring Type, Maximum Number of Reports, Monitoring Duration, Monitoring Destination Address, SCS/AS Reference ID for Deletion,Reachability Type ， Maximum Latency ， Maximum Response Time ， Suggested number of downlink packets | Y | Y? | OMA-TS-REST_NetAPI_TerminalStatus-V1_0
 | Monitor Event ConfigReq-Availability after DDN Failure | External Identifier(s) or MSISDN(s), SCS/AS Identifier, SCS/AS Reference ID, Monitoring Type, Monitoring Duration, Monitoring Destination Address, SCS/AS Reference ID for Deletion | Y | Y | OMA-TS-REST_NetAPI_Messaging-V1_0
 | Monitor Event ConfigRsp | SCS/AS Reference ID, Cause | Y | Y | OMA-TS-REST_NetAPI_Messaging-V1_1
 | MonitorReport | SCS/AS Reference ID, External ID or MSISDN, Monitoring Information | Y | Y | OMA-TS-REST_NetAPI_Messaging-V1_2 OMA-TS-REST_NetAPI_TerminalStatus-V1_0
UE PSM timer/eDRX Configuration | PSM timer Set Req(Monitor Event ConfigReq-UE reachablity已经支持） | External Identifier(s) or MSISDN(s), SCS/AS Identifier, SCS/AS Reference ID, Monitoring Type, Maximum Number of Reports, Monitoring Duration, Monitoring Destination Address, SCS/AS Reference ID for Deletion,Reachability Type ， Maximum Latency ， Maximum Response Time ， Suggested number of downlink packets | Y | N | 
 | PSM timer Set Rsp（Monitor Event ConfigRsp已经支持） | SCS/AS Reference ID, Cause | Y | N | 
Group Management | Allocate TMGI Request | External Group ID, SCS Identifier, location/area information | Y |  | 
 | Allocate TMGI Rsp | SCS/AS Reference ID, TMGI and expiration time information | Y |  | 
 | Group Message Request | External Group Identifier, SCS Identifier, location/area information, RAT(s) information, TMGI, start time | Y |  | 
 | Group Message Confirm | TMGI (optional), SCEF IP addresses/port | Y |  | 
 | Network Status Req | Geographical area, SCS/AS Identifier, SCS/AS Reference ID, Duration, Threshold | Y |  | 
 | Network Status Report | SCS/AS Reference ID, Congestion level, ECGI/eNodeB-ID/SAI | Y |  | 
 | Cancel Network Status Request | SCS/AS Identifier, SCS/AS Reference ID | Y |  | 
 | Cancel Network Status Response | SCS/AS Reference ID | Y |  | 
Location Network-based location | Monitor Event ConfigReq-= Location Reporting | External Identifier(s) or MSISDN(s), SCS/AS Identifier, SCS/AS Reference ID, Monitoring Type, Maximum Number of Reports, Monitoring Duration, Monitoring Destination Address, SCS/AS Reference ID for Deletion,Location Type， Accuracy prior | Y |  | OMA-TS-REST_NetAPI_TerminalLocation-V1_0_1-20151029-A
 | Monitor Event ConfigReq-= Roaming Status | External Identifier(s) or MSISDN(s), SCS/AS Identifier, SCS/AS Reference ID, Monitoring Type, Maximum Number of Reports, Monitoring Duration, Monitoring Destination Address, SCS/AS Reference ID for Deletion,PLMN Information | Y |  | OMA-TS-REST_NetAPI_TerminalStatus-V1_0
 | Monitoring Event Config Response | SCS/AS Reference ID, Cause | Y |  | OMA-TS-REST_NetAPI_TerminalLocation-V1_0_1-20151031-A
 | LocationMonitorReport | SCS/AS Reference ID, External ID or MSISDN, geo-location | Y |  | OMA-TS-REST_NetAPI_TerminalLocation-V1_0_1-20151032-A
 | RoamingStatusMonitorReport | SCS/AS Reference ID, External ID or MSISDN, HPLMN PLMN-Id/ Visited PLMN-Id | Y |  | OMA-TS-REST_NetAPI_TerminalStatus-V1_0

## Slide 21: Content
Non-IP device Accessing oneM2M platform（MO/MT）
CMDH
  Down Link Data Delivery when UE is unreachable
  UE PSM timer or eDRX Configuration
  Network Monitor：Network Status， Communication Failure
Group Management
Location
  Network-based location
Others

## Slide 22: Monitoring Event: Loss of connectivity
Figure 5.6.1.1-1: Monitoring event configuration and Report
SCEF API Requirement
  Monitor Event ConfigReq（SCS->SCEF）
  Monitoring Request (External Identifier(s) or MSISDN(s), SCS/AS Identifier, SCS/AS Reference ID, Monitoring Type, Maximum Number of Reports, Monitoring Duration, Monitoring Destination Address, SCS/AS Reference ID for Deletion)
    Monitoring Type = Loss of connectivity （ Maximum Detection Time ）
  Monitor Event ConfigRsp（SCEF>SCS）
  Monitoring Response (SCS/AS Reference ID, Cause)
  Monitor Report（SCEF>SCS）
    LossOfConnectivityMonitorReport(SCS/AS Reference ID, External ID or MSISDN, Monitoring Information)
Stage 2 completeness
  Partially, Monitoring Information is not clear.

## Slide 23: Monitoring Event: Change of IMSI-IMEI(SV) association
Figure 5.6.1.1-1: Monitoring event configuration and Report
SCEF API Requirement
  Monitor Event ConfigReq（SCS->SCEF）
  Monitoring Request (External Identifier(s) or MSISDN(s), SCS/AS Identifier, SCS/AS Reference ID, Monitoring Type, Maximum Number of Reports, Monitoring Duration, Monitoring Destination Address, SCS/AS Reference ID for Deletion)
    Monitoring Type = Change of IMSI-IMEI(SV) association （ Association Type ）
  Monitor Event ConfigRsp（SCEF>SCS）
  Monitoring Response (SCS/AS Reference ID, Cause)
  Monitor Report（SCEF>SCS）
    ChangeofAssociationMonitorReport(SCS/AS Reference ID, External ID or MSISDN, Monitoring Information)
Stage 2 completeness
  Partially, Monitoring Information is not clear.

## Slide 24: Procedure for resource management of background data transfer
Figure 5.9-1: Resource management for background data transfer
SCEF API Requirement
  Step1： Background data transfer request （SCS->SCEF）
  Background data transfer request (SCS/AS Identifier, SCS/AS Reference ID, Volume per UE, Number of UEs, Desired time window)
  Step4： Background data transfer response （SCEF->SCS）
  Background data transfer response (SCS/AS Identifier, reference ID, Possible transfer policies)
  Step5：New Background data transfer request （ SCS->SCEF ）
  Background data transfer request (SCS/AS Identifier, SCS/AS Reference ID, Selected transfer policy)
  Step6： NewBackground data transfer response( SCEF->SCS)
  Background data transfer response (SCS/AS Identifier)
Stage 2 completeness
  Y

## Slide 25: Communication Pattern parameters provisioning procedure
SCEF API Requirement
  Step1： Background data transfer request （SCS->SCEF）
  Update Request (External Identifier or MSISDN, SCS/AS Identifier, SCS/AS Reference ID(s), CP parameter set(s), validity time(s), SCS/AS Reference ID(s) for Deletion)
  Step6： Update Response （SCEF->SCS）
Update Response (SCS/AS Reference ID, Cause) Stage 2 completeness
  Y
Figure 5.10.2-1: Signalling sequence for provisioning of CP Parameters

## Slide 26: Setting up an AS session with required QoS procedure
SCEF API Requirement
  Step1： On-demand QoS request （SCS->SCEF）
  On-demand QoS request (UE IP address, SCS/AS Identifier, SCS/AS Reference ID, Description of the application flows reference to a pre-defined QoS)
  Step5： On-demand QoS response （SCEF->SCS）
On-demand QoS response (SCS/AS Identifier, SCS/AS Reference ID, Result)
Stage 2 completeness
  Y
Figure 5.11-1: Setting up an AS session with required QoS

## Slide 27: Others
DeviceTrigger
  Device Triggering is the means by which a SCS sends information to the UE via the 3GPP network to trigger the UE to perform application specific actions that include initiating communication with the SCS for the indirect model or an AS in the network for the hybrid model. Device Triggering is required when an IP address for the UE is not available or reachable by the SCS/AS.
PS-only Service Provision
  PS-only service provision is providing a UE with all subscribed services via PS domain. PS-only service provision implies a subscription that allows only for services exclusively provided by the PS domain, i.e. packet bearer services and SMS services. The support of SMS services via PS domain NAS is a network deployment option and may depend also on roaming agreements. Therefore, a subscription intended for PS-only service provision may allow also for SMS services via CS domain to provide a UE with SMS services in situations when serving node or network don't support SMS via PS domain NAS.
Core Network assisted RAN parameters tuning
  Core Network assisted RAN parameters tuning aids the RAN in optimizing the setting of RAN parameters.
Change the chargeable party at session set-up or during the session
  The SCS/AS may request the SCEF to start or stop sponsoring a data session for a UE that is served by the 3rd party service provider (AS session), i.e. to realize that either the 3rd party service provider is charged for the traffic (start) or not (stop). The SCS/AS may request to be set as the chargeable party, i.e. sponsoring the traffic, either at AS session set-up or to change it during an ongoing AS session.

## Slide 28: Summary（Low Priority）
Others | 3GPP defined or not
DeviceTrigger | Y
PS-only Service Provision | N
Core Network assisted RAN parameters tuning | N
Resource management of background data transfer | Y
E-UTRAN network resource optimizations based on communication patterns provided to the MME | Y
Support of setting up an AS session with required QoS | Y
Change the chargeable party at session set-up or during the session | Y
Monitoring Event: Loss of connectivity | Y
Monitoring Event: Change of IMSI-IMEI(SV) Association | Y

## Slide 29: 3GPP Requirements Summary
  The existing interfaces enhancement for stage2
  NIDD MOReq/Rsp need define the parameters
  NIDD MTRsp need define the parameters
  Monitor Event Report: monitor information need to be specified according to the event type
  Group Management: need more explanation about the parameters of northbound interface and how mapping the parameters between the southbound interface and northbound interface
  PS-only Service Provision need define the service flow, interface and parameter
  Core Network assisted RAN parameters tuning need define the service flow, interface and parameter
  All APIs defining in stage 3
    Support to finish defining the SCEF APIs in Q4 2017
  New Requirement
  Add new parameter in the existing interface or add new service flow after more detail and deeper analysis on the oneM2M other functions interworking with 3GPP

## Slide 30
Questions and comments