| CHANGE REQUEST |
| --- |
| Meeting:* | ARC 26 |
| Source:* | Phil Hawkes, Qualcomm, phawkes@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com |
| Date:* | 2016-11-28 |
| Contact:* | As above |
| Reason for Change/s:* | This CR proposes adding an inlineSimplePrivileges attribute and inlineSimpleSelfPrivileges attribute to those resources which already include the accessControlPolicyIDs attribute. |
| CR against: Release* | 2 |
| CR against: WI* | Active WI-0016 MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0001 and 2.10.1 |
| Clauses/Sub Clauses* | 9.6.1.3.2, 9.6.x for resources including accessControlPolicyIDs attribute |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

The use of accessControlPolicy resources provides great flexibility in defining access control, but have been found to be difficult to use in practice. For example, when a CSE or AE creates a <remoteCSE> or <AE> resource during registration, then it is not clear what value should be assigned to accessControlPolicyIDs attribute for those resources. Anecdotal evidence indicates that implementers are designing work-arounds. Furthermore, correct use of ACPs is difficult without in-depth understanding of how ACPs were intended to use.

This CR proposes adding an optional inlineSimplePrivileges attribute and an optional inlineSimpleSelfPrivileges attribute to those resources which already include the accessControlPolicyIDs attribute.

Corresponding updates to TS-0003 "Security Solutions", TS-0004 "Service Layer Core Protocol" and TS-00011 "Common Terminology", are also being drafted. These CRs currently include:

- SEC-2016-0189 "CR TS-0003 R2 inlineSimplePrivileges".

### ---------------------------Start of Change 1 -------------------------------

##### 9.6.1.3.2	Common attributes

The following attributes are commonly used in multiple, but not all, resource types which are normal, not virtual or announced. Common attributes for announced resource types are independently defined in claused 9.6.26.3.

NOTE:	The list of attributes in table 9.6.1.3.2-1 is not exhaustive.

Table 9.6.1.3.2-1: Common Attributes

| Attribute Name | Description |
| --- | --- |
| accessControlPolicyIDs | The attribute contains a list of identifiers of an <accessControlPolicy> resource. The privileges defined in the <accessControlPolicy> resource that are referenced determine who is allowed to access the resource containing this attribute for a specific purpose (e.g. Retrieve, Update, Delete, etc.). If a resource type does not have an accessControlPolicyIDs attribute definition, then the accessControlPolicyIDs for that resource is governed in a different way, for example, the accessControlPolicy associated with the parent may apply to a child resource that does not have an accessControlPolicyIDs attribute definition, or the privileges for access are fixed by the system. Refer to the corresponding resource type definitions and procedures to see how access control is handled in such cases. If a resource type does have an accessControlPolicyIDs attribute definition, but the (optional) accessControlPolicyIDs attribute is not set, or it is set to a value that does not correspond to valid<accessControlPolicy> resource(s), or it refers to an <accessControlPolicy> resource(s) that is not reachable (e.g. because it is located on a remote CSE that is offline or not reachable), and the inline access control policy (the combination of inlineSimplePrivileges attribute and the inlineSimpleSelfPrivileges attribute) is not set, then the system default access privileges shall apply. All resources are accessible if and only if the access control rules (i.e. stored as privileges or selfPrivileges attribute of <accessControlPolicy> resourcesn or translated inline access control policy) allow it. Therefore all resources shall have at least one of an inline access control policy and an associated accessControlPolicyIDs attribute. The accessControlPolicyIDs attribute is defined either explicitly (setting the attribute in the resource itself) or implicitly (either by using the parent privileges or the system default policies). Which means that the system shall provide a default access privileges in case that the Originator does not provide a specific accessControlPolicyIDs or inline access control policy during the creation of the resource. To update this attribute, a Hosting CSE shall check whether an Originator has Update permission provided by any selfPrivileges of the <accessControlPolicy> resources which this attribute originally indicates, or the inlineSimpleSelfPrivileges attribute in the resource (if present). See clause 7.1.1 of oneM2M TS-0003 [2]. |
| stateTag | An incremental counter of modification on the resource. When a resource is created, this counter is set to 0, and it will be incremented on every modification of the resource (see notes 1 and 2). |
| announceTo | This attribute may be included in a CREATE or UPDATE Request in which case it contains a list of addresses/CSE-IDs where the resource is to be announced. For the case that CSE-IDs are provided, the announced-to CSE shall decide the location of the announced resources based on the rules described in clause 9.6.26. For the original resource, this attribute shall only be present if it has been successfully announced to other CSEs. This attribute maintains the list of the resource addresses to the successfully announced resources. Updates on this attribute will trigger new resource announcement or de-announcement. If announceTo attribute includes resource address(s), the present document does not provide any means for validating these address(s) for announcement purposes. It is the responsibility of the Hosting-CSE referenced by the resource address(s) to validate the access privileges of the originator of the Request that triggers the announcement. |
| announcedAttribute | This attributes shall only be present at the original resource if some Optional Announced (OA) type attributes have been announced to other CSEs. This attribute maintains the list of the announced Optional Attributes (OA type attributes) in the original resource. Updates to this attribute will trigger new attribute announcement if a new attribute is added or de-announcement if the existing attribute is removed. |
| labels | Tokens used to add meta-information to resources. This attribute is optional. The value of the labels attribute is a list of individual labels, each of them being: Either a standalone label-key, used as a simple "tag", that can be used for example for discovery purposes when looking for particular resources that one can "tag" using that label-key Or a composite element made of a label-key and a label-value, separated by a special character defined in [3]. A label-key itself can consist of several sub-elements, separated by a special character also defined in [3]. The list of allowed characters in a label (and in label-keys and label-values) and separator characters is defined in [3], clause 6.3.3. |
| e2eSecInfo | Present in a resource representing an AE or CSE. Indicates the end-to-end security capabilities supported by the AE or CSE. May indicate supported end-to-end security frameworks. May also contains a certificate or credential identifier used by the AE or CSE. May include random values for use in end-to-end security protocols. The details of this attributes are described in oneM2M TS-0003 [2]. This attribute is optional and if not present it means that the represented entity does not support oneM2M end-to-end security procedures. |
| dynamicAuthorizationConsultationIDs | This attribute contains a list of identifiers of <dynamicAuthorizationConsultation> resources. The information defined in a <dynamicAuthorizationConsultation> resource is used by a CSE for initiating consultation-based dynamic authorization requests. Consultation-based dynamic authorization is only performed for a targeted resource if and only if it is linked to an enabled <dynamicAuthorizationConsultation> resource. If the attribute is not set or has a value that does not correspond to a valid <dynamicAuthorizationConsultation> resource(s), or it refers to an <dynamicAuthorizationConsultation> resource(s) that is not reachable, then the dynamicAuthorizationConsultationIDs associated with the parent may apply to the child resource if present, or a system default <dynamicAuthorizationConsultation> may apply if present. To Update this attribute, a Hosting CSE shall check whether an Originator has Update permission provided by any selfPrivileges of the <accessControlPolicy> resources identified by the applicable accessControlPolicyIDs, or the inlineSimpleSelfPrivileges attribute in the resource (if present). See clause 7.1.1 of oneM2M TS-0003 [2]. |
| creator | The AE-ID or CSE-ID of the entity which created the resource containing this attribute. |
| inlineSimplePrivileges | This attribute contains lists providing simple equivalent to the privileges attribute of an <accessControlPolicy> resource for use in Access Decisions as described in oneM2M TS-0003 [2]. The internal structure of this attribute is described in oneM2M TS-0003 [2]. This attribute shall be present in a resource if and only if the inlineSimpleSelfPrivileges attribute is present. To Retrieve this attribute, a Hosting CSE shall check whether an Originator has Retrieve permission provided by the inlineSimpleSelfPrivileges attribute in the resource (if present). See clause 7.1.1 of oneM2M TS-0003 [2]. To Update this attribute when it is already present in a resource, a Hosting CSE shall check whether an Originator has Update permission provided by the inlineSimpleSelfPrivileges attribute in the resource. See clause 7.1.1 of oneM2M TS-0003 [2]. To Update this attribute when it is not already present in a resource, a Hosting CSE shall check whether an Originator has Update permission provided by any selfPrivileges of the <accessControlPolicy> resources identified by the applicable accessControlPolicyIDs. See clause 7.1.1 of oneM2M TS-0003 [2]. |
| inlineSimpleSelfPrivileges | This attribute contains lists providing simple equivalent to the selfPrivileges attribute of an <accessControlPolicy> resource for use in Access Decisions as described in oneM2M TS-0003 [2]. The internal structure of this attribute is described in oneM2M TS-0003 [2]. This attribute shall be present in a resource if and only if the inlineSimplePrivileges attribute is present. To Retrieve this attribute, a Hosting CSE shall check whether an Originator has Retrieve permission provided by the inlineSimpleSelfPrivileges attribute itself in the resource (if present). See clause 7.1.1 of oneM2M TS-0003 [2]. To Update this attribute when it is already present in a resource, a Hosting CSE shall check whether an Originator has Update permission provided by the inlineSimpleSelfPrivileges attribute itself in the resource. See clause 7.1.1 of oneM2M TS-0003 [2]. To Update this attribute when it is not already present in a resource, a Hosting CSE shall check whether an Originator has Update permission provided by any selfPrivileges of the <accessControlPolicy> resources identified by the applicable accessControlPolicyIDs. See clause 7.1.1 of oneM2M TS-0003 [2]. |
| NOTE 1: In order to enable detection of overflow, the counter needs to be capable of expressing sufficiently long numbers. NOTE 2: This attribute has the scope to allow identifying changes in resources within a time interval that is lower than the one supported by the attribute lastModifiedTime (e.g. less than a second or millisecond). This attribute can also be used to avoid race conditions in case of competing modifications. |

### ----------------------------------- End of Change 1 -----------------------------------

The following row is to be added to each tables in clause 9.6 describe the attributes of resource types, satisfying the condition that the resource already includes an accessControlPolicyIDs attribute

### ---Start of Change 2: Add the following row to tables as described above--

| inlineSimplePrivileges | 0..1 | RW | See clause 9.6.1.3. |
| --- | --- | --- | --- |
| inlineSimpleSelfPrivileges | 0..1 | RW | See clause 9.6.1.3. |

### ----------------------------------- End of Change 2 ------------------------------------