| CHANGE REQUEST |
| --- |
| Meeting ID:* | ARC 27 |
| Source:* | Catalina Mladin, Convida, Mladin.Catalina@convidawireless.com Michael Starsinic, Convida, Starsinic.Michael@convidawireless.com |
| Date:* | 2017-02-03 |
| Reason for Change/s:* | Proposes how the oneM2M system may leverage the Low Access Priority Indicator |
| CR against: Release* | Release 3 |
| CR against: WI* | Active WI-0058 MNT maintenance / < Work Item number(optional)> Is this a companion CR? Yes No Companion CR number: (Note to Rapporteur - use latest agreed revision)Is this a mirror CR? Yes No Mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0024, Version 2.0.1 |
| Clauses * | 8.x |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | N/A |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution provides an overview of the Low Access Priority feature in 3GPP and identifies related Key Issues.

R01 provides updates based on offline agreements

### -----------------------Start of Change 1-------------------------------------------

## 8.x Support for Low Access Priority

### 8.x.1 Description

Starting with Release 10, 3GPP has identified signalling congestion control as one of the key issues to be addressed for MTC communications. The solution adopted introduces the concept of “Low Priority Indications” which allow communications from certain MTC devices or applications to be treated as a low priority. A subscriber may configure UEs for low access priority per an agreement with its operator. The agreement may include a specific pricing, so the low access priority use is reflected in CDRs.

### 8.x.2 Feature Gap Analysis

Support for Low Access Priority is enabled by configuring UEs, per agreement with operators, via a simple flag. On the M2M device, low access priority is used by applications or users that can tolerate being deferred when competing with other devices for network resources. UEs may be configured for low access priority and provide indications when performing a NAS procedure or establishing an RRC connection, as described in TS 23.060 and TS 23.401.

When the UE provides the Low Access Priority indication (e.g. in the attach request) to the MME/SGSN during NAS signaling, it is used by the MME/SGSN to help determine if the request should be accepted.

The core network considers the device as ‘low access priority’ for the lifetime of the connection. The CN can choose to terminate the connection and it can reject messages with a backoff time which may be longer under overload/congestion. The network is also allowed to command the UE to move to a state where is does not need to generate further signaling messages and/or does not reselect the PLMN. Consequently, the application needs to be designed to be tolerant to delays when accessing the network.

The UE configuration for Low Access Priority may be provided at the time of production (on UE/USIM) or performed via OMA Device Management procedures or OTA (Over-the-air) interface. This information is not available in the subscription information stored in the HSS/HLR, hence the network cannot identify a ‘low access priority’ device unless the device indicates low access priority in the NAS or RRC procedures.

A subscriber can also, by agreement with its operator, configure the UEs with a permission for overriding Low Access Priority. CDRs show whether the UE activated the PDN connection with or without low access priority.

The existing Low access Priority mechanism depends on the UE providing the indication. However in many scenarios the SCS/AS may be in a better position to determine the importance of the communication with the device than device itself. Mobile Network Operators in particular may be interested in having more dynamic control of this feature without Device Management operations at the UE.

Communication with an M2M device may be critical under specific circumstances meaningful only at Service Layer level. For example, consider the case where sensors are used for monitoring of backup equipment of a power plant. Normally the sensor readings are infrequent and can safely use Low Access Priority. However, when the main power plant has an emergency, the sensors associated with the backup equipment should not be treated as low priority. The Application Server used for management and monitoring is best suited to make this determination based on the status of the platform, sensor locations, etc. This information may be used to override the Low Access Priority indication in the network for selected devices.

### 8.x.3 Key Issues and Requirements

#### 8.x.3.1 Key SCEF NorthBound API Requirements

| Number | Description | Notes |
| --- | --- | --- |
| REQ-8.x-01 | Configure UE connection for Low Access Priority | See clause 8.x.2 |
| REQ-8.x-02 | Configure override of Low Access Priority for a UE connection | See clause 8.x.2 |

#### 8.x.3.2 Possible Impacts on the SCEF Southbound Interface

N/A

#### 8.x.3.3. Further 3GPP Requirements and Clarifications

N/A

### -----------------------End of Change 1 ---------------------------------------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?