| CHANGE REQUEST |
| --- |
| Meeting ID:* | ARC 27 |
| Source:* | Catalina Mladin, Convida Wireless, Mladin.Catalina@ConvidaWireless.com Hongkun Li, Convida Wireless, Li.Hongkun@ConvidaWireless.com Mike Starsinic, Convida Wireless, Starsinic.Micahel@ConvidaWireless.com |
| Date:* | 2017-02-03 |
| Reason for Change/s:* | Proposal for using 3GPP’s Group Communication Pattern and Group Monitoring features. |
| CR against: Release* | Release 3 |
| CR against: WI* | Active WI-0058 MNT maintenance / < Work Item number(optional)> Is this a companion CR? Yes No Companion CR number: (Note to Rapporteur - use latest agreed revision)Is this a mirror CR? Yes No Mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0024, Version 3.0.0 |
| Clauses * |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | N/A |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution provides an overview of the use of External Group Identifiers for configuring monitoring events and configuring communication patterns for groups of devices. The goal is to identify key issues in enabling oneM2M to utilize this 3GPP functionality.

R01 provides some additional use case information and section restructuring based on offline agreements.

R02 reflects ARC 27 agreements

### -----------------------Start of Change 1--------------------.-----------------------

## 8.x Support for Group Communication Patterns and Group Monitoring

### 8.x.1 Description

In 3GPP TS 23.682, 3GPP has defined an External Group Identifier. Section 4.6.3 says “A subscription used for MTC may have one or several IMSI-Group Identifier(s) (see TS 23.003 [4]) that are stored in the HSS.” The External Group Identifier is used on the interface between the SCS/AS and SCEF.

The Monitoring and Communication Pattern provisioning procedures in TS 23.682 allow the SCS/AS to use the External Group Identifier to configuring monitoring events for groups of devices and configure communication patterns for groups of devices.  TS 23.682 says “When the External Group Identifier is used in the communication pattern provisioning or monitoring event configuration and deletion procedures, the HSS is able to resolve the External Group Identifier to an IMSI-Group Identifier.”

### 8.x.2 Feature Gap Anaysis

#### 8.x.2.1 Group Monitoring

The procedure for Monitoring Event configuration from TS 23.682 is shown in Figure 8.x.2.1-1. It is defined for monitoring specific events in 3GPP system and making such monitoring events information available via the SCEF to SCS/AS.  Events such as changes in association of the UE and UICC and/or new IMSI-IMEI-SV association, UE reachability, location change, loss of connectivity, communication failure, roaming status, and availability after DDN failure may be monitored.

As stated in TS 23.682, “If the SCS/AS wants to configure Monitoring Event for the group of UEs, the SCS/AS can send Monitoring Request message including External Group Identifier and Group Reporting Guard Time.” (step 1)

Figure 8.x.2.1-1. Monitoring event configuration and deletion via HSS procedure

#### 8.x.2.2 Communication Patterns for a Group of UEs

The SCEF allows the SCS/AS to provide the network with predictable communication patterns of a UE in order to enable network resource optimizations for such UE(s).  The procedure for configuring communication patterns from TS 23.682 is shown in Figure 8.x.2.2-1.

As stated in TS 23.682, “The SCS/AS sends an Update Request (External Identifier or MSISDN or External Group Identifier, SCS/AS Identifier, SCS/AS Reference ID(s), CP parameter set(s), validity time(s), SCS/AS Reference ID(s) for Deletion) message to the SCEF.” (step 1)

Figure 8.x.2.2-1. Signalling sequence for provisioning of CP Parameters

### 8.x.2.3 Analysis

The group monitoring and group communication pattern provisioning procedures are not very flexible in the sense that the group members are fixed. This limits the cases where they can be leveraged by the Service Layer, since it does not allow for operations using grouping based on service logic

For example, consider a use case where a vending machine company distributes and maintains many vending machines in a shopping mall. The company wants all of the machines to use the same communications patterns so that they can be easily managed. For example, new pricing information can be distributed to all devices at 6:00 am. However, when machines are moved in and out of the mall the vending company may no longer want them to be part of the group.  For example, some machines may be moved to a school; thus healthier food options have been added or different prices should be used.

Moreover, the vending company might expose its machines to advertising companies who can provide content that gets updated regularly. The advertising companies are not allowed to change the pre-provisioned information, but they should be able to use service logic for grouping: e.g. machines used for products from a brand name vs. another.

To enable use cases using grouping based on service logic, e.g. for monitoring and group communication pattern provisioning procedures, addition functionality must be provided SCEF.

Procedures for group management via SCEF, for example, create a group, and modify group membership

### 8.x.3 Key Issues and Requirements

#### 8.x.3.1 Key SCEF NorthBound API Requirements

| Number | Description | Notes |
| --- | --- | --- |
| REQ-8.x-01 | Group management procedures e.g. create, delete, modify group membership, i.e. association between External Group Identifier and External Identifiers. | See clause 8.x.2.3 |

#### 8.x.3.2 Possible impacts on the SCEF Southbound Interface

N/A

#### 8.x.3.3. Further 3GPP requirements and clarifications

N/A

### -----------------------End of Change 1 ---------------------------------------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?