| CHANGE REQUEST |
| --- |
| Meeting ID:* | ARC 27 |
| Source:* | Yulan Lu, China Telecom,luyl@sttri.com.cn Xubei(Echo), Huawei, echo.xubei@huawei.com |
| Date:* | 2017-02-03 |
| Reason for Change/s:* | The 3GPP R13&R14 exposes network capabilities to external entities via SCEF. In oneM2M 3GPP interworking architecture, the IN-CSE may leverage the network capabilities via SCEF APIs to provide E2E CIoT services. In order to support and expedite the standardization of SCEF APIs by other SDOs (e.g. 3GPP), this contribution analyzes the requirements for UE location Reporting event APIs from oneM2M perspective (mapped to Mcn). |
| CR against: Release* | Release 3 |
| CR against: WI* | Active WI-0058 - 3GPP & Cellular Interworking |
| CR against: TS/TR* | TR-0024-3GPP_Rel13_IWK-V2_0_1 |
| Clauses * | 8.* |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | NA |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The Location (LOC) CSF allows AEs to obtain geographical location information of Nodes (e.g. ASN, MN) for location-based services in Mca reference point.The LOC CSF obtains and manages geographical location information based on requests from AEs residing on either a local Node or a remote Node.

This contribution analyzes the requirements for location reporting APIs of SCEF from oneM2M perspective (mapped to Mcn).

### -----------------------Start of change 1-------------------------------------------

## 8.*	Monitoring event(Monitoring Type: Location Reporting)

### 8.*.1 Description

The Location (LOC) CSF allows AEs to obtain geographical location information of Nodes (e.g. ASN, MN) for location-based services in Mca reference point.The LOC CSF obtains and manages geographical location information based on requests from AEs residing on either a local Node or a remote Node. The LOC CSF interacts with any of the following:

a location server in the Underlying Network;

a GPS module in an M2M device; or

information for inferring location stored in other Nodes.

The functions supported by the LOC CSF are as follows:

Requests other Nodes to share and report their own or other Nodes' geographical location information with the requesting AEs.

Provides means for protecting the confidentiality of geographical location information.

The Monitoring Events feature is intended for monitoring of specific events in 3GPP system and making such monitoring events information available via the SCEF.

This monitoring event Location Reporting allows the SCS/AS to request either the Current Location or the Last Known Location of a UE. The supported location accuracy is at either cell level (CGI/ECGI), eNodeB, TA/RA level. Only One-time Reporting is supported for the Last Known Location. One-time and Continuous Location Reporting are supported for the Current Location. For Continuous Location Reporting the serving node(s) sends a notification every time it becomes aware of a location change, with the granularity depending on the requested accuracy.

The Location (LOC) CSF is able to utilize this service to get the node( which is ASN,MN,ADN hosting on the UE) location information from 3GPP network.

The LOC CSF relies 3GPP  SCEF to provide the  functions such as Configure Location Reporting event,Detect the Location Reporting event and Report the Location information

### 8.*.2 Feature Gap Analysis

The 3GPP defined term ‘SCS’ in the flows corresponds to oneM2M IN-CSE.

The service flows defined in 3GPP TS23.682 are used in the following section as informative information only. oneM2M focus is on the northbound APIs of SCEF.

#### 8.*.2.1 Monitoring event configuration and deletion procedure(Location Reporting)

Figure 8.*.2.1-1: Monitoring event configuration and deletion via HSS procedure

The Figure 8.*.2.1-1 illustrates the procedure of configuring monitoring at the HSS or the MME/SGSN. The involved SCEF northbound APIs are as below:

Step1  SCS(IN-CSE) sends Monitoring Request (External Identifier(s) or MSISDN(s) or External Group ID, SCS/AS Identifier, SCS/AS Reference ID, Monitoring Type, Maximum Number of Reports, Monitoring Duration, Monitoring Destination Address, SCS/AS Reference ID for Deletion, Group Reporting Guard Time, Location Type, Accuracy) to SCEF.

Step 4b SCEF sends Monitoring Response() to SCS(IN-CSE).

Step 9 SCEF sends Monitoring Response (SCS/AS Reference ID, Cause) or Indication() to SCS(IN-CSE).

There are some gaps for the SCEF northbound APIs.

- Step 1 The Accuracy parameter indicates desired level of accuracy of the requested location information.In the [2]TS23.682 Notes “ illustrates the format of parameter Accuracy should refer OMA Presence API “.When 3GPP define this API, the format of parameter Accuracy should be specified..

- Step 4b This step is used to indicate that Group processing is in progress from SCEF to SCS. But there is no parameter defined.

- Step 9 For group based processing, SCEF may send the Monitor Indication to the SCS. But there is no parameter defined. At the same time, this step could report of the current or last known location depending on what was requested, the SCEF would map eNodeB-ID/cell-ID/RAI/TAI to geo-location before reporting to the SCS/AS. But there is no parameter indicating geo-location information.

Figure 8.*.2.1-2: Requesting monitoring via PCRF

Figure 8.*.2.1-2 illustrates the procedure to request monitoring events reporting via PCRF. The only one time report is supported by PCRF The involved SCEF northbound APIs are as below:

Step1: SCS sends Monitoring Request(External Identifier(s) or MSISDN(s), SCS/AS Identifier, Monitoring Type("Location Reporting" for a single UE), Priority, Monitoring Duration, Monitoring Destination Address, UE IP address and service information, Location Type) to SCEF

Step4: SCEF sends Monitoring Response(SCS/AS Reference ID, Cause) to SCS(IN-CSE)

# Figure 8.*.2.1-3: Requesting monitoring via PCRF for a group of UEs

Figure 8.*.2.1-3 illustrates the procedure to request monitoring events reporting via PCRF for a group of UEs.For monitoring for a group of UEs, the SPR is configured with the External Group Identifier the UE belongs to.

The involved SCEF northbound APIs are as below:

Step1 SCS(IN-CSE) sends Monitoring Request(External Identifier(s) or MSISDN(s) or External Group ID, SCS/AS Identifier, SCS/AS Reference ID, Monitoring Type, Maximum Number of Reports, Monitoring Duration, Monitoring Destination Address, SCS/AS Reference ID for Deletion, Group Reporting Guard Time, Location Type) to SCEF.

Step5 SCEF sends Monitoring Response(SCS/AS Reference ID) to SCS(IN-CSE)

Step8 SCEF sends Monitoring Indication including multiple instances of the 4-tuple (SCS/AS Reference ID,UE IP address , External Group Identifier, Cause) to SCS(IN-CSE)

There are some gaps for the SCEF northbound APIs.

- Step1 It is the same API interface for Monitoring Request for the sigle UE and group of UE, but whether PCRF support group of UE or not is not definite. The new API should be needed to disguish it.

- Step1 There is no Accuracy parameter to indicate desired level of accuracy of the requested location information comparing with the parameters in Step1 Figure 8.*.3.1-1

#### 8.*.2.2 Monitoring event reporting procedure

Figure 8.*.2.2-1: Monitoring event reporting procedure via HSS or MME

Figure 8.*.2.2-1 illustrates the common procedure flow of reporting Monitoring Events that are detected by the MME/SGSN or HSS. The Monitoring destination node should be IN-CSE in oneM2M perspective. The involved SCEF northbound APIs are as below:

Step 3 SCEF sends Monitoring Indication (SCS/AS Reference ID, External ID or MSISDN, Monitoring Information) for single UE to the Monitoring destination node (IN-CSE.).

SCEF sends Monitoring Indication (SCS/AS Reference ID, External Group Identifier, External ID(s) or MSISDN(s), Monitoring Information) for group of UEs to the Monitoring destination node (IN-CSE.).

There is one gap for the SCEF northbound APIs.

- Step 3, The SCEF maps the reported 3GPP system specific location information to a geo-location and reports it. At last the parameter Monitoring Information of geo-location is not specified.

Figure 8.*.2.2-2: Reporting event procedure

The Figure  8.*.2.2-2  illustrates the procedure to report Monitoring Events via PCRF. The involved SCEF northbound APIs are as below:

Step 2: SCEF sends Monitoring Indication(SCS/AS Reference ID, UE Identity, and Monitoring Information) to SCS(IN-CSE).

There is one gaps for the SCEF northbound APIs.

- Step 2 The SCEF maps the reported 3GPP system specific location information to a geo-location and reports it. At last the parameter Monitoring Information of geo-location is not specified.

### 8.*.3 Key Issues and Requirements

#### 8.*.3.1 Key SCEF Norhtbound API Requicements

Table 8.*.3.1-1 Requirements on SCEF NorthBound interface

| Number | SCEF API Requirements | Note |
| --- | --- | --- |
| REQ-8.*.01 | Support UE Location Reporting Monitoring Configuration | Step1: Monitoring Request（SCS->SCEF）in clause 5.6.1&5.6.4 TS23.682 [i.5] Step 4b Monitoring Response in clause 5.6.1 &5.6.4 TS23.682 [i.5] |
| REQ-8.*.02 | Support UE Location Reporting | Monitoring Indication clause 5.6.3 & 5.6.5 TS23.682 [i.5] |

#### 8.*.3.2 Potential impact on SCEF SouthBound Interface

Table 8.*.3.2-1 Potential impacts on the SCEF Sounthbound Interface

| Number | Description | Note |
| --- | --- | --- |
| IMPAC-8.*.01 | How SCEF choose HSS or PCEF to support UE location Reporting monitor event should be clarified (SCEF-HSS/PCRF). |  |

#### 8.*.3.3 Further 3GPP requirements and clarifications

Table 8.*.3.3-1 Issues to be clarified by 3GPP (Stage 2)

| Number | Description | Note |
| --- | --- | --- |
| ISSUE-8.*.01 | The format of parameter Accuracy should be sepecified | Step 1 Monitoring Request（SCS->SCEF）in clause 5.6.1 TS23.682 [i.5] |
| ISSUE-8.*.02 | The parameter should be defined to indicate that Group processing is in progress from SCEF to SCS. | Step 4b Monitoring Response（SCEF->SCS）i in clause 5.6.1 TS23.682 [i.5] |
| ISSUE-8.*.03 | The parameter should be defined for group based processing. | Step 9 Monitoring Indication（SCEF->SCS）in clause 5.6.3 TS23.682 [i.5] |
| ISSUE-8.*.04 | The new API should be needed to indicate whether 3GPP support group of UEs or not. | Step1: Monitoring Request（SCS->SCEF）in clause 5.6.4 TS23.682 [i.5] |
| ISSUE-8.*.05 | The parameter Accuracy may be missing | Step1: Monitoring Request（SCS->SCEF）in clause 5.6.4 TS23.682 [i.5] |
| ISSUE-8.*.06 | The parameter Monitoring Information of UE geo-location should be specified | Monitoring Indication（SCEF->SCS）in 5.6.3 & 5.6.5 TS23.682 [i.5] |

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?