## Slide 1: CSE Retargeting to AE, IPE, and NoDN Hosted Resources
Group Name: ARC WG
Source: Dale Seed, Convida Wireless (Seed.Dale@ConvidaWireless.com)
Meeting Date: 2017-03-16 (ARC27.2)
Notes: Other suggested titles:
“Benefits of oneM2M Standardization”

## Slide 2: Currently in oneM2M …
A CSE can only send two types of requests to AEs and IPEs
 Notifications and IPE Discovery requests
An AE or IPE cannot host local resources. It must mirror locally hosted resources into the CSE
A CSE cannot send / retarget CRUD requests to an AE or IPE
AE / IPE
CSE
Notification
IPE Discovery
CRUD
x
Local
Resources

## Slide 3: So why do we care?
  oneM2M developers want more end-to-end transparency in the oneM2M system
      E.g. They want to be able to host their own resources on their IoT devices just like other RESTful technologies allow them to do
  Provide more flexibility and optimization for some oneM2M deployments.
      E.g. For interworking oneM2M with other RESTful technologies that allow devices to host their own resources.
      E.g. Deployments requiring lower end-to-end latency request handling
  Examples of some other RESTful technologies that allow device apps to host their own resources include OCF, LWM2M, many CoAP based IoT deployments

## Slide 4: So why not just use a ASN-CSE?
ASN-AE
+
ASN-CSE
AE
MN-CSE
 An ASN-CSE can host its own resources and can receive CRUD requests from other CSEs. So why not just use an ASN-CSE + ASN-AE in a device instead of adding support to oneM2M for retargeting CRUD requests to AEs and IPEs?

## Slide 5: Comparison
ADN-AE
AE
MN-CSE
IPE
NoDN
MN-CSE
AE
Pros:
Allows devices to host their own resources without mirroring and without having to support CSE functionality
  Allows devices to reap the benefits of oneM2M services without the added overhead
  Devices can host a minimal set of oneM2M resources (e.g. container, contentInstance, or flexContainer)
  Provides end-to-end transparency and reduced latency
Still allows an MN-CSE to provide value-add oneM2M services to devices such as the following
  Credential management and authentication of Originators accessing resources hosted on device
  Authorization of access to resources hosted on device
  Discovery of resources hosted on device
  Store and forwarding of requests targeting resources hosted on device based on device’s reachability
  Fanout of a request targeting a group of resources hosted on a device
  Sub/Not management of resources hosted on a device
  Caching of resources hosted on a device
  Non-blocking request handling for resources on device
Cons:
Requires some changes to existing oneM2M architecture
  Changes can be minimal however
- MN-CSE Retargeting to AE / IPE / NoDN
ASN-AE
+
ASN-CSE
AE
MN-CSE
Pros:
No changes to oneM2M architecture
Allows devices to host their own resources
Cons:
Increased complexity / impact to a device – A device must support at least a minimal set of CSE features
  Must support CSE-ID, AE-ID and App-ID
  Must support oneM2M Mcc Security
  Must support CSE Registration
  Must support an increased number of oneM2M resource types and logic (CSEBase, remoteCSE, AE, container, contentInstance, flexContainer, …)
    Must support an increased number of oneM2M primitives types and procedures
For any resources that ASN-CSE hosts its responsible for
  Providing its own ACPs to secure access
  Providing its own oneM2M resource discovery
  Providing its own group management
  Providing its own non-blocking request handling
  Providing its own sub/not management
- MN-CSE Retargeting to ASN-CSE

## Slide 6: Example Use Case
ADN-AE
AE
MN-CSE

## Slide 7: Mirroring Example
ADN-AE
AE
MN-CSE
CREATE Door <AE>
CREATE Door Lock <container>
NOTIFY with Door Lock Command <contentInstance>
CREATE <subscription> on Door Lock Status <container>
Response
Response
Response
Response
Create <contentInstance> with Lock Door Command
Response
CREATE <subscription> on Door Lock Command <container>
Response
Discover Door <AE> and <container> resources
Response
CREATE Door Lock Status <container>
Response
NOTIFY with Door Lock Status <contentInstance>
Response
CREATE <contentInstance> for Door Lock status
Response
Without support for re-targeting requests to AEs, oneM2M can be “chatty” and require increased messaging. This makes oneM2M more complex and less efficient.
12 messages required for initialization
8 messages required to lock door
Mirroring of ADN-AE resources into CSE has an overhead associated with it (Complexity & Latency)
Not an ideal fit for all use cases
Lack of transparency requires separate containers for command and status

## Slide 8: Other Mirroring Concerns
oneM2M notification
elements
Another concern with oneM2M and its ability to scale down for use with lightweight IoT Devices is the message size overhead of oneM2M.
  Many IoT devices have very small message payload requirements. Adding even a small number of bytes can translate into a significant overhead on the device.
Mirroring resources of an IoT device into oneM2M resources typically results in a level of encapsulation and overhead
  IoT device resource is encapsulated into oneM2M resource (e.g. container, contentInstance, flexContainer, mgmtObj, etc)
  The use of notifications for relaying updates of mirrored resources back to IoT devices results in yet another layer of encapsulation and added overhead introduced by the elements of the notification.
Retargeting of requests to AE / IPE can help minimize encapsulation overhead
oneM2M contentInstance
attributes
Content (IoT resource data)

## Slide 9: Retargeting to an ADN-AE
ADN-AE
AE
MN-CSE
CREATE Door <AE> [ADN-AE’s Door Lock flexContainer Info]
Retargeted UPDATE Request to ADN-AE’s flexContainer to lock door
Response
Response [ADN-AE’s Door Lock flexContainer Representation]
UPDATE Request to ADN-AE’s flexContainer to lock door
Retargeted Response
[ADN-AE’s Door Lock flexContainer Representation]
DISCOVER Door <AE>
Response [ADN-AE’s Door Lock flexContainer Resource Info]
Only 4 messages required for initialization
Only 4 messages required for locking the door
 Retargeting can reduce the messaging overhead (no notifications needed) and latency in the system
 Reducing messaging overhead can make system less complex and provide better performance
Retargeting
Transparency allows command and status in one request/ response exchange
Retargeting can also involve value-add services such as ACP checks, store-and-forwarding, scheduling, group fanout, caching, sub/not handling, etc.

## Slide 10: Interworking Example
IPE
AE
MN-CSE
Non-oneM2M Device Node (NoDN)
Retargeting of requests to IPEs can also reduce complexity of IPEs and optimize interworking of oneM2M with other technologies

## Slide 11: Retargeting to an IPE
NoDN
AE
IPE
MN-CSE
CREATE Door <AE> [ADN-AE’s Door Lock flexContainer Info]
Retargeted Response:
[ADN-AE’s Door Lock flexContainer Representation]
DISCOVER Door <AE>
Response
[OCF Compliant Door Lock Resource Representation]
Response
Response
Publish Door Lock Resource Discovery Info
Response [ADN-AE’s Door Lock flexContainer Resource Info]
Retargeted UPDATE
Of Door Lock Resource
[OCF Compliant Door Lock Resource
Representation to unlock door]
UPDATE Request to ADN-AE’s flexContainer to lock door
Response:
[ADN-AE’s Door Lock flexContainer Representation]
Retargeted UPDATE Request to ADN-AE’s flexContainer to lock door
Retargeting
The CSE can re-target CRUD requests to an IPE and in turn a NoDN
Retargeting

## Slide 12: Link Descriptions (FFS)
For RESTful technologies like OCF, LWM2M, CoAP, etc. they are making use of standardized link descriptions coming out of the IETF.
Link descriptions describe each resource hosted by a device.
E.g. Its URI, its interface (i.e. read only, read/write, etc), it access control policies, its supported protocols
Its conceivable that oneM2M could support interworking to this standardized link description format defined by IETF and support retargeting CRUD requests to resources hosted by ADN-AEs, IPEs, NoDN

## Slide 13: Retargeting to a NoDN (FFS)
AE
Non-oneM2M Device Node
 Given that many emerging IoT technologies (e.g., OCF, LWM2M, CoAP-based deployments, etc) are aligning themselves with RESTful design principles, it may even be possible for oneM2M to define a generic enough framework within the CSE to allow re-targeting of requests to these types of RESTful NoDN without the need for a technology specific IPEs!!! [Requires further study and analysis]
MN-CSE
NoDN
AE Retargeting
In addition to the IPE based approach of interworking, oneM2M could even consider defining functionality native to a CSE to interwork with NoDN IETF Link Descriptions

## Slide 14: Retargeting to a NoDN (FFS)
NoDN
(E.g. OCF)
AE
MN-CSE
Retargeted Response
[OCF Compliant Door Lock Resource Representation]
DISCOVER Door <AE>
Response
[OCF Compliant Door Lock Resource Representation]
Response
Publish Door Lock Resource Discovery Info that includes interface definitions
Response
[Door Lock Link Description]
Retargeted UPDATE Request of Door Lock Resource
[OCF Compliant Door Lock Resource Representation to unlock door]
UPDATE AE Door Lock Resource
[Door Lock Resource
Representation compliant with format specified in Link Description (e.g. OCF format)]
Retargeting
For RESTful technologies like OCF, LWM2M, CoAP, etc. it may even be possible for a CSE to re-target CRUD requests directly to NoDN without an IPE
NoDN
AE Retargeting

## Slide 15: Next Steps?
Reach consensus on a way forward regarding lightweight oneM2M entity
  Option 1 – Define support to allow AE’s & IPE’s to host oneM2M resources
    Allow a small subset of existing oneM2M resource types well suited for interaction with telemetry (sensors) and control (actuators) kinds of devices to be hosted by AEs/IPEs.
      E.g. container, contentInstance, flexContainer
    Define a minimal set of enhancements to CSEs to support AE hosted resources
      E.g. Directory of resources hosted by an AE / IPE
    Possibly define some new lightweight resource types well-suited for AEs/IPEs?
      E.g. Lightweight subscription, ACP
  Option 2 – Define a lightweight CSE (Call it ASN-CSE or something else possibly)
    Profile existing oneM2M CSE functionality and identify minimal subset of features
      Minimal set of resource types
      Minimal set of attributes in these resources
    Possibly define some new lighter alternatives for existing resource types well-suited for?
      E.g. Lighter weight subscription or ACP