| CHANGE REQUEST |
| --- |
| Meeting ID:* | ARC 28 |
| Source:* | Catalina Mladin, Convida, Mladin.Catalina@convidawireless.com |
| Date:* | 2017-03-23 |
| Reason for Change/s:* | Moves 3GPP-related text from TS-0001 to TS-0026 (Removes Annex B) |
| CR against: Release* | Release 3 |
| CR against: WI* | Active WI-0058 MNT maintenance / < Work Item number(optional)> Is this a companion CR? Yes No Companion CR number: (Note to Rapporteur - use latest agreed revision)Is this a mirror CR? Yes No Mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0001V3.3.0 |
| Clauses * | Annex B |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | TS-0026 |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

A proposal to move TS-0001 text pertaining to 3GPP interworking to TS-0026 has been made in a TS-0026 CR. The table below shows the proposed text mapping. This CR proposes the corresponding Annex B deletion in TS-0001.

| TS-0001 Section | TS-0001 Section Title | TS-0026 Section | TS-0026 Section Title | Comments |
| --- | --- | --- | --- | --- |
| B | oneM2M System and 3GPP MTC Underlying Network Interworking | N/A | N/A | No content |
| B.1 | 3GPP MTC Underlying Network Introduction | N/A (5) | oneM2M Architecture for 3GPP cellular IoT interworking with oneM2M | Proposed to be removed, content covered by TS-0026 clause 5 Alternatively, a merge with TS-0026 clause 5.1 may be considered |
| B.2 | 3GPP MTC Functionality | N/A | N/A | No content |
| B.2.1 | 3GPP Release-11 MTC Functionality | N/A (5) | oneM2M Architecture for 3GPP cellular IoT interworking with oneM2M | Proposed to be removed. Rel-13 content is covered in TS-0026 clause 5. Alternatively, figure B.2.1-2 and referring text to be merged to TR-0024 clause 5.3 |
| B.2.2 | 3GPP Release-13 MTC Interworking | N/A | N/A | No content |
| B.2.2.1 | General overview of 3GPP Release-13 MTC Interworking | N/A (5.3) | Cellular IoT Features and Services | Propose to delete B.2.2.1. Content is covered by TS-0026 sec 5.3 (except figure B2.2.1-1) |
| B.2.2.2 | 3GPP Release-13 MTC feature for Configuration of Device Communication Patterns | 7.6 (former 6.6) | 3GPP Release-13 MTC Procedure | Propose to include in TS-0026 Traffic Pattern section: former 6.6 (now 7.6) |
| B.3 | ASN/MN-CSE initiated connectivity establishment | New 6 | Connectivity Establishment | New title | Proposing a new section 6 in TS-0026 called “Connectivity Establishment”, as detailed in the body of this document Includes B3-B6 |
| B.3.0 | Overview | New 6.1 | Overview | Merge B3.0, B4 and B5 text into 7.1 |  |
| B.3.1 | Use of DHCP and DNS | New 6.2 | Use of DHCP and DNS | Maintain as 7.2 |  |
| B.3.2 | Pre-configuration | New 6.3 | Pre-configuration | Maintain as 7.3 |  |
| B.4 | Serving IN-CSE initiated connectivity establishment | New 6.1 | Overview | Merge B3.0, B4 and B5 text into 7.1 |  |
| B.5 | Connectivity between oneM2M Service Layer and 3GPP Underlying Network | New 6.1 | Overview | Merge B3.0, B4 and B5 text into 7.1 |  |
| B.6 | Connectivity Establishment Procedures | N/A | N/A | No content |  |
| B.6.1 | General | N/A | N/A | No content |  |
| B.6.1.0 | Overview | N/A | N/A | Propose to delete, only intro to B 6.1.1 and B 6.1.2 |  |
| B.6.1.1 | ASN/MN-CSE Initiated Connectivity Establishment Procedure | New 6.4 | ASN/MN-CSE Initiated Connectivity Establishment Procedure | Maintain as 7.4 |  |
| B.6.1.2 | IN-CSE initiated connectivity establishment procedure over Tsp | New 6.5 and 7.5 | SMS Based Device Triggering | Maintain heading as 6.5. and move to the Device triggering section 7.5 |  |

### -----------------------Start of Change 1 -------------------------------------------

Annex B (informative):
Void.

### -----------------------End of Change 1 ---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause?

# Comments

must not allowed in ETSI documents (except in citations). Consider replacing occurrences

# Text boxes

Application

Server

Application

Server

Application

Server

Operator

Network

Operator Network

UE

UE

UE

SCS

SCS

Operator

Boundary

A

.

Direct Model

B

.

Indirect Model

(MTC Service Provider

Controlled)

C

.

Indirect Model

(Mobile Network Operator

Controlled)

Operator

Network

Control plane

User plane

IN

-

CSE

IN

-

CSE

AE

AE

ASN/MN-CSE  or ADN-AE

ASN/MN-CSE  or ADN-AE