| CHANGE REQUEST |
| --- |
| Meeting ID:* | ARC 28 |
| Source:* | Catalina Mladin, Convida, Mladin.Catalina@convidawireless.com Joerg Swetina, NEC, (joerg.swetina@neclab.eu) |
| Date:* | 2017-03-23 |
| Reason for Change/s:* | The CR corrects the outdated text in section 8.3.2 by replacing it with current text from Annex B2.2.2 of TS-0001 |
| CR against: Release* | Release 3 |
| CR against: WI* | Active WI-0058 MNT maintenance / < Work Item number(optional)> Is this a companion CR? Yes No Companion CR number: (Note to Rapporteur - use latest agreed revision)Is this a mirror CR? Yes No Mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0024, Version 2.0.3 |
| Clauses * | 8.3 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | N/A |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution provides corrections to the outdated text in section 8.3.2 by replacing it with current text from Annex B2.2.2 of TS-0001 and additional editorials. Note that the baseline text is from the newly agreed ARC-2017-0090R01.

### -----------------------Start of Change 1 -------------------------------------------

## 8.3	Configuration of Traffic Patterns

### 8.3.1	Description

M2M devices that have predicable communication behaviour - e.g. in the form of repeating Traffic Patterns - mayprofit in terms of reduction of signalling, energy saving, fewer sleep/awake transitions, etc., when their Traffic Patterns are communicated to the underlying network.

EXAMPLE 1:	3GPP devices could use new 3GPP power savings features such as eDRX (extended discontinuous reception) and PSM (Power Saving Mode) on LTE devices.

Also the underlying network may benefit from being informed about a device's Traffic Patterns by the oneM2M System.

EXAMPLE 2:	If the IN-CSE knows the device's Traffic Patterns and transmits them to an underlying 3GPP network, then this information maybe used by a 3GPP network to set the device's "Maximum Response Time" (3GPP Term) to tune the UE's DRX and PSM parameters.

Thus the network benefits because the UE has fewer sleep/wake transitions and unnecessary signalling in the network isavoided.  Also, if the IN-CSE knows when the device is awake then data maybe sent to the device exactly at the time when the device is listening, thus requiring the network to buffer less data for unavailable devices.

The purpose of the Configuration of Traffic Patterns feature is to provide a means to the oneM2M System  to inform the Underlying Network on parameters tobe used for optimizing the processing at the Underlying Network for a specific Field Domain Node. The feature includes the following functionalities:

- An Application Entity (AE) or a Common Service Entity (CSE) shall be able to provide information on the communication behavior of a Field Domain Node (ASN or MN) to the underlying network.

- To that purpose the AE or CSE shall be able to set Traffic Patterns of a particular Field Domain Node via the Mca or Mcc reference point of a IN-CSE:

- The Field Domain Node is addressed using the (NodeID, AE-IDs) of the Node.

- The IN-CSE shall in turn use the Mcn interface towards the Underlying Network to provide information on Traffic Patterns of a the Field Domain Node:

- The IN-CSE uses the M2M-Ext-ID to identify the Node towards the Underlying Network.

### 8.3.2	Feature Analysis

#### 8.3.2.1	Introduction

oneM2M uses the 3GPP Release-13 MTC feature for Configuration of Device Communication Patterns to configure Node Traffic Patterns in the Underlying Network (see section 8.3.5 Configuration of Node Traffic Patterns). 
To that purpose the IN-CSE translates the oneM2M Node Traffic Pattern (TP) into a 3GPP Device Communication Pattern.

#### 8.3.2.2	3GPP  specific features

A signalling sequence for provisioning of CP parameters is described in the sub-clause 5.10.2 of 3GPP TS 23.682 [i.14]. Following figure 7.6-1 provides the signalling sequence derived from the 3GPP specification. Figure B.2.2.2-2 illustrates the terminology mapping between 3GPP and oneM2M, where the SCS is mapped to IN-CSE and the SCEF is mapped to NSE. In case the SCS is 3GPP network operator controlled, the SCEF maybe deployed co-located with the SCS.

Figure 7.6-1: Signalling sequence for provisioning of CP Parameters

Figure B.7.6 -2: 3GPP and oneM2M mapping

3GPP TS 23.682 [i.14] defines the request message of step 1 as below:

- The SCS/AS sends an Update Request (External Identifier or MSISDN, SCS/AS Identifier, SCS/AS Reference ID(s), CP parameter set(s), validity time(s), SCS/AS Reference ID(s) for Deletion) message to the SCEF.

NOTE 1:	The SCS/AS uses this procedure to add, change or delete some or all of the CP parameter sets of the UE, e.g. if the AS is aware that the UE has started or stopped moving for a significant time period, especially if the AS is instructing the UE to do so, then the SCS/AS provides the corresponding CP parameter set(s) and its validity time to the SCEF.

3GPP TS 23.682 [i.14] defines the request message of step 3 as below:

- The SCEF sends Update CP Parameter Request (External Identifier or MSISDN, SCEF Reference ID(s), SCEF Address, CP parameter set(s), validity time(s), SCEF Reference ID(s) for Deletion) messages to the HSS for delivering the selected CP parameter set(s) per UE. There may be multiple CP parameter sets included in this message where each CP parameter set for addition or modification has been determined to be non-overlapping with other CP parameter sets either included in the message or already provisioned for a given UE. The SCEF derives the SCEF Reference (IDs) for CP parameter sets to be sent to the HSS based on the SCS/AS Reference ID(s) from the SCS/AS.

NOTE 2:	A request for deletion of a CP parameter set from the SCS/AS may result in a request for modification of the non-overlapping CP parameter set by the SCEF.

EXAMPLE 1:	In the case that the selected server NSE is a 3GPP HSS, the protocol of the S6t reference point defined by 3GPP is used for the request. The S6t uses one of Diameter Application protocols defined by 3GPP. The request on the S6t reference point for the configuration of the CP parameter sets (a CIR command) includes a User-Identifier AVP (either an External Identifeir or a MSISDN of the UE), may include one or more AESE-Communication-Pattern AVP. An AESE-Communication-Pattern AVP includes a SCEF-ID AVP (represent the ID of the IN-CSE or M2M-SP-ID), may include a SCEF-Reference-ID AVP (assigned by the IN-CSE or M2M-SP to identify the configuration of CP parameter sets uniquely) , may include one or more Communication-Pattern-Set AVP. A Communication-Pattern-Set AVP may include AVPs for Periodic-Communication-Indicator, Communication-Duration-Time, Periodic-Time, one or more Scheduled-Communication-Time, Stationary-Indication, and Validity-Time. Refer to the 3GPP TS 29.336 [i.31] for the detailed protocol description.

3GPP TS 23.682 [i.14] defines the response message of step 5 as below:

- The HSS sends Update CP Parameter Response (SCEF Reference ID, Cause) message to the SCEF. The cause value indicates successful subscription update or the reason of failed subscription update.

- The actual parameters for the request and response messages in above steps 3 and 5 are defined by 3GPP TS 29.336 [i.31], clauses 7 and 8 for S6t reference point.

EXAMPLE 2:	In the case that the selected server NSE is a 3GPP HSS, the protocol of the S6t reference point defined by 3GPP is used for the response. The response on the S6t reference point for the configuration of the CP parameter sets (a CIA command) includes either Result-Code AVP or Experimental-Result AVP, may include a User-Identifier AVP if successful case, may include one or more AESE-Communication-Pattern-Config-Status AVP. An AESE-Communication-Pattern-Config-Status AVP includes the SCEF-Reference-ID AVP (same value in the request), may include the SCEF-ID (same value in the request) and an AESE-Error-Report AVP. Refer to the 3GPP TS29.336 for the detailed protocol description.

3GPP TS 23.682 [i.14] defines the response message of step 6 as below:

- The SCEF sends the Update Response (SCS/AS Reference ID, Cause) message to inform the SCS/AS whether the provision of the CP parameter set(s) was successful.

### 8.3.2.3	oneM2M specific features

Note: in order to distinguish 3GPP terms from oneM2M terms the 3GPP “Communucation Patterns” are called “Traffic Patterns” in oneM2M

A set of Traffic pattern (TP) parameters isassociated with a Traffic Pattern of one or multiple field domain nodes and are defined in table 8.3.3-1.

A Field Domain Node maybe associated with one or multiple Traffic Patterns. At any time only a single Traffic Pattern maybe associated with a Field Domain Node.

The IN-CSE shall assure that different Traffic Patterns for a Node are not overlapping at any point in time.

A combination of the following TP parameters maybe set for a Traffic Pattern.

Table 8.3.3-1: Traffic Pattern parameters

| TP parameter | Description |
| --- | --- |
| TP Periodic communication indicator | Identifies whether the Node communicates periodically or not, e.g. only on demand. |
| TP Communication duration time | Duration interval time of periodic communication [may be used together with TP periodic communication indicator]. EXAMPLE: 5 minutes. |
| TP Time period | Interval Time of periodic communication [may be used together with TP periodic communication indicator]. Example: every hour. |
| TP Scheduled communication time | Time zone and Day of the week when the Node is available for communication. EXAMPLE: Time: 13:00-20:00, Day: Monday. |
| TP Stationary indication | Identifies whether the Node is stationary or mobile. |
| TP Data size indication | indicates the expected data size for the pattern. |
| TP Validity time | The time after which a TP becomes invalid once it had been set. |

### 8.3.3 Key Issues and Requirements

#### 8.3.3.1 Key SCEF NorthBound API Requirements

| Number | Description | Notes |
| --- | --- | --- |
| REQ-8.3-01 | Create Traffic Patterns |  |
| REQ-8.3-02 | Update Traffic Patterns |  |
| REQ-8.3-03 | Delete Traffic Patterns |  |

#### 8.3.3.2 Possible Impacts on the SCEF Southbound Interface

N/A

#### 8.3.3.3. Further 3GPP Requirements and Clarifications

N/A

#### 8.6.3.4. oneM2M Key Issues

Provide support for the configurations of Traffic Patterns.

Note: Solution 1 proposed in clause 8.3.4.1 implemented in Release 2.

### 8.3.4	Solution(s)

#### 8.3.4.1	Solution1

##### 8.3.4.1.1	Proposed resource types and attributes

This clause provides information of new resource types and new attributes including relationship with existing resource types and attributes.

Proposed new resource types are as below:

- Resource Type <trafficCharacteristics>:

- Note: It is child resource of existing Resource Type <AE> or <node>.

- Resource Type <trafficPattern>.

NOTE:	It is child resource of new Resource Type <trafficCharacteristics>.

Detailed information of new resource types are described in subclauses below.

8.3.4.1.1.1	Resource Type <trafficCharacteristics>

The <trafficCharacteristics> resource represents the characteristic information (e.g. communication pattern, mobility pattern, etc.) of a field domain node. This information may be detected or scheduled by application level processing. This resource type is used to share information with other entities such as the underlying network entity (server NSE) of the field domain node which may optimize the processing of the underlying network for the specific field domain node.

Figure 8.3.4.1.1.1-1: Structure of <trafficCharacteristics> resource

The <trafficCharacteristics> resource shall contain the child resources specified in table 8.3.4.1.1.1-1.

Table 8.3.4.1.1.1-1: Child resources of <trafficCharacteristics> resource

| Child Resources of <trafficCharacteristics> | Child Resource Type | Multiplicity | Description | <trafficCharacteristicsAnnc> Child Resource Types |
| --- | --- | --- | --- | --- |
| [variable] | <subscription> | 0..n |  | <subscription> |
| [variable] | <trafficPattern> | 0..n | See clause 8.3.4.1.1.2. A source AE maycreate multiple number of <trafficPattern> resources for a single target AE of field domain node. In this case the source AE assures that different communication patterns are not overlapping at any point in time. | <trafficPatternAnnc> |

The <trafficCharacteristics> resource shall contain the attributes specified in table8.3.4.1.1.1-2.

Table 8.3.4.1.1.1-2: Attributes of <trafficCharacteristics> resource

| Attributes of <deviceCharacteristics> | Multiplicity | RW/ RO/ WO | Description | <trafficCharacteristicsAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 of oneM2M TS-0001 [i.9]. | NA |
| resourceID | 1 | RO | See clause 9.6.1.3 of oneM2M TS-0001 [i.9]. | NA |
| resourceName | 1 | WO | See clause 9.6.1.3 of oneM2M TS-0001 [i.9]. | NA |
| parentID | 1 | RO | See clause 9.6.1.3 of oneM2M TS-0001 [i.9]. | NA |
| creationTime | 1 | RO | See clause 9.6.1.3 of oneM2M TS-0001 [i.9]. | NA |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 of oneM2M TS-0001 [i.9]. | NA |
| expirationTime | 1 | RW | See clause 9.6.1.3 of oneM2M TS-0001 [i.9]. | MA |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3 of oneM2M TS-0001 [i.9]. | MA |
| Labels | 0..1 (L) | RW | See clause 9.6.1.3 of oneM2M TS-0001 [i.9]. | MA |
| announceTo | 0..1(L) | RW | See clause 9.6.1.3 of oneM2M TS-0001 [i.9]. | NA |
| announcedAttribute | 0..1(L) | RW | See clause 9.6.1.3 of oneM2M TS-0001 [i.9]. | NA |
| Creator | 1 | WO | The AE-ID of the entity which created the resource. | OA |

8.3.4.1.1.2	Resource Type <trafficPattern>

The <trafficPattern> resource represents the communication pattern and the mobility pattern of a field domain node to be shared with other entities such as the underlying network entity (NSE) of the field domain node which may optimize the processing of the underlying network for the specific field domain node by using this information.

Figure 8.3.4.1.1.2-1: Structure of <trafficPattern> resource

The <trafficPattern> resource shall contain the child resources specified in table 8.3.4.1.1.2-1.

Table 8.3.4.1.1.2-1: Child resources of <trafficPattern> resource

| Child Resources of <trafficPattern> | Child Resource Type | Multiplicity | Description | <trafficPatternAnnc> Child Resource Types |
| --- | --- | --- | --- | --- |
| [variable] | <subscription> | 0..n |  | <subscription> |
| [variable] | <schedule> | 0..1 | It provides the mask for the day of week, the starting time and end time for communication. If it is not provided this shall be interpreted as ‘anytime' at the NSE. | <scheduleAnnc> |

The <trafficPattern> resource shall contain the attributes specified in table 8.3.4.1.1.2-2.

Table 8.3.4.1.1.2-2: Attributes of <trafficPattern> resource

| Attributes of <trafficPattern> | Multiplicity | RW/ RO/ WO | Description | <trafficPatternAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 of oneM2M TS-0001 [i.9]. | NA |
| resourceID | 1 | RO | See clause 9.6.1.3 of oneM2M TS-0001 [i.9]. | NA |
| resourceName | 1 | WO | See clause 9.6.1.3 of oneM2M TS-0001 [i.9]. | NA |
| parentID | 1 | RO | See clause 9.6.1.3 of oneM2M TS-0001 [i.9]. | NA |
| creationTime | 1 | RO | See clause 9.6.1.3 of oneM2M TS-0001 [i.9]. | NA |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 of oneM2M TS-0001 [i.9]. | NA |
| expirationTime | 1 | RW | See clause 9.6.1.3 of oneM2M TS-0001 [i.9]. | MA |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3 of oneM2M TS-0001 [i.9]. | MA |
| Labels | 0..1 (L) | RW | See clause 9.6.1.3 of oneM2M TS-0001 [i.9]. | MA |
| announceTo | 0..1(L) | RW | See clause 9.6.1.3 of oneM2M TS-0001 [i.9]. | NA |
| announcedAttribute | 0..1(L) | RW | See clause 9.6.1.3 of oneM2M TS-0001 [i.9]. | NA |
| provideToNSE | 0..1 | RW | It indicates as ‘TRUE' or ‘FALSE' whether the traffic pattern shall be provided to a NSE | OA |
| periodicIndicator | 0..1 | RW | It indicates as ‘Periodical' or ‘On demand'. | OA |
| periodicDurationTime | 0..1 | RW | It provides the time in seconds of the duration of the periodic communication. | OA |
| periodicIntervalTime | 0..1 | RW | It provides the time in seconds of the interval for periodic communication. | OA |
| stationaryIndication | 0..1 | RW | It indicates as ‘Stationary (Stopping)' or ‘Mobile (Moving)'. | OA |
| dataSizeIndicator | 0..1 | RW | It indicates the expected data size for the pattern | OA |
| validityTime | 0..1 | RW | It contains the point of time when the informed <trafficPattern> information to the NSE becoming invalid and shall be deleted at the NSE. | OA |

##### 8.3.4.1.2	Proposed Flow

This clause describes the procedure for resource management of Traffic Patterns to a set of field nodes. Figure 8.3.4.1.2-1 depicts a general procedure for configuration of Traffic Patterns.

The procedure needs to be harmonized with the figure 8.3.2-1.

Figure 8.3.4.1.2-1: General procedure for configuration of Traffic Patterns

Step-1: Provide information on the behavior of a field domain AE or field domain Node

An AE (IN-AE or an AE of the Field Domain Node that reports its communication behaviour) provides the hosting CSE (i.e. ASN/MN-CSE) of the field domain AE/Node with information on the communication behavior of the AE/Node (i.e. TP parameter sets) by creating, updating or deleting its Traffic Patterns (TP).

The AE may provide TP parameter sets for a group of field domain nodes .

The request shall include:

- the originator AE-ID of the requesting AE;

- a target identifier: i.e. the <trafficCharacteristics> child resource of a <node> resource or an <AE> resource of the field domain node or a group identifier of multiple field domain AEs/nodes for which the Traffic Patterns is provided; and

- a set of TP parameters  as indicated in table 8.3.3-1.

The request may include multiple of TP parameter set(s) and validity time(s).

If the hosting CSE has received a request from an AE to create, update or delete Traffic Patterns it shall check if the request from the AE is valid (see note 1).

NOTE 1:	Apart from checking access rights of the AE the validation of the request from the AE could include:

- Consistency with  <schedule> resources supported by an M2M SP in various M2M entities (MN-CSE, ASN) hosting this AE/Node.

- If there are several TP parameter sets active for one Field Domain Node, then the original resource hosting CSE assures that the different TP parameter sets are not overlapping.

Step-2: Announce the Traffic Patterns to the IN-CSE that has an interface to the NSE

If the hosting CSE recognizes an announcement procedure is needed, it shall announce the Traffic Patterns received from the AE to the IN-CSE that has an interface to the NSE contained in the "AnnounceTo" attribute of the Traffic Patterns resources based on the existing announcement procedures.

Step-3: Select the server NSE to request for the configuration of the TP parameter sets

If the IN-CSE receives an announced Traffic Patterns and the IN-CSE recognizes the configuration of the Traffic Patterns  at the NSE is needed by checking "provideToNSE" attribute, the IN-CSE shall perform subsequent steps.

For the configuration of the TP parameter sets for a specific field domain node, the IN-CSE selects the NSE by using the identifier of the Field Domain Node (i.e. the M2M-Ext-ID) by which the Node is identified in the NSE.

NOTE 2:	The correct server NSE may be found by following of a chain of links of multiple resources in the IN-CSE, e.g. the nodeLink in the AEAnnc resource of a target AE of field domain node linking to the nodeAnnc resource having the hostedCSELink linking to the remoteCSE resource having  the M2M-Ext-ID linking to the UNetwork-ID of the server NSE. (See clauses 7.1.8 and 7.1.9 in oneM2M TS-0001 [i.9].)

Step-4: Request for the configuration of the TP parameter sets

For each field domain node received in the AE request the IN-CSE sends a request to provide TP parameter sets for the field domain node to the NSE, using the appropriate Mcn protocol. The request includes an identifier of the filed domain node and one or more TP parameter set(s) as defined at clause 8.3.3.

NOTE 3:	If the Underlying Network is 3GPP-compliant, see clause 8.3.2 for more details.

Step-5: Response for the configuration of the TP parameter sets

The IN-CSE receives the response for the configuration of the TP parameter sets from the NSE. The response includes the result of the request.

NOTE 4:	If the Underlying Network is 3GPP-compliant, see clause 8.3.2 for more details.

### ----------------------- End of Change 1 -------------------------------------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?

# Text boxes

Mca

Infrastructure Domain

Field Domain

1. provide information on the behavior of a field domain AE or field domain Node

2. Announce the Traffic Patterns to the IN-CSE that has an interface to the NSE

- Request for providing 
the TP parameter sets

- Response

3. Select the server NSE to request for the configuration of the TP parameter sets

Mca

Mcn

IN-CSE

Mcc

NSE

ASN/MN-CSE

AE

Any Domain