mei

| CHANGE REQUEST |
| --- |
| Meeting:* | ARC TP28 |
| Source:* | BeiXu，Huawei，Echo.xubei@huawei.com |
| Date:* | 2017-03-02 |
| Contact:* | BeiXu，Huawei，Echo.xubei@huawei.com |
| Reason for Change/s:* | Add new section about UE power saving mode feature |
| CR against: Release* | <Release> Only ONE Release shall be indicated |
| CR against: WI* | Active <WI-0058 - 3GPP & Cellular IoT Interworking> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0024 - 3GPP Rel-13 InterworkingV2_0_3 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

To solve the Issue 3 in clause 8.8.2.4, this contribution provide the solution to synchronize the <schedule> of ASN/MN-CSE,ADN/AE with 3GPP network. This solution include three scenarios:

- Set the PSM timer of the CSE/AE from IN-CSE

- Synchronize <schedule> from 3GPP network

### Delivery Downlink Data When CSE/AE in PSM-----------------------Start of change 1-------------------------------------------

## 8.8 Monitoring event (Monitoring Type: UE reachability)

### 8.8.4 3GPP Parameters

A set of UE reachablity parameters can be associated with a UE reachablity report request, as defined in table 8.8.4.3-1.

# Table 8.8.4.3-1: UE reachablity report parameters

| Parameter | Description |
| --- | --- |
| Monitoring Information | Not be specified. |

### Notes: oneM2M have the requirements of  this function for 3GPP, so the 3GPP parameter may change. This section could be complete when this function in 3GPP have been finished.

### 8.8.5 oneM2M solution

#### 8.8.5.1 Resource Structure

Figure 8.8.5.1-1: Structure of <schedule> resource

Table 8.8.5.1-1: Attributes of <schedule> resource

| Attributes of <schedule> | Multiplicity | RW/ RO/ WO | Description | <scheduleAnnc> Attributes |
| --- | --- | --- | --- | --- |
| settingResource | 1 | RW | • Network; • Device; Application. | NA |

#### 8.8.5.1 Set the PSM timer of the CSE/AE from IN-CSE and Monitoring Request

##### 8.8.5.1.1 ServiceFlow

Step 001: The IN-CSE(SCS) sends a Monitoring Request (External Identifier(s) or MSISDN(s), SCS Identifier, SCS Reference ID, Monitoring Type, Maximum Number of Reports, Monitoring Duration, Monitoring Destination Address,IdleTimeIndication), and  sets Monitoring Type to "UE Reachability".

Step 002-Step 004: 3GPP interworking handling the MonitorRequest  Information，more detail can reference 3GPP TS23.682[i.5]

Notes: There is new requirement  for monitoring  type “UE Reachability” for 3GPP from oneM2M in clause 8.8.3.1, refere the detail in clause 8.8.2.4. The parameters in Step 001 will refer the 3GPP new version TS 23.682[i.5].

Step 005: The SCEF(NSE) sends a Monitoring Response (SCS Reference ID, Cause) message to the IN-CSE(SCS)  to acknowledge acceptance of the Monitoring Request of the identified monitoring event configuration.

Step 006: IN-CSE(SCS) sends PSM setting Request(External Identifier(s) or MSISDN(s), SCS Identifier, SCS Reference ID, Maximum Latency(optional),Maximum Response Time(optional)).

-	Optionally, Maximum Latency indicating maximum delay acceptable for downlink data transfers. Maximum Latency is used for setting the periodic TAU/RAU timer for the UE as it sets the maximum period after which a UE has to connect to the network again and thereby becomes reachable. Determined by the operator, low values for Maximum Latency may deactivate PSM.

-	Maximum Response Time indicating the time for which the UE stays idle status to allow the SCS/AS to reliably deliver the required downlink data. Maximum Response Time is used for setting the Active Time for the UE.

Step 007-Step 009: 3GPP interworking handling the MonitorRequest  Information, more detail can reference 3GPP TS23.682[i.5]

Notes: The PSM setting Request is new requirement for 3GPP from oneM2M in clause 8.8.3.1, refere the detail in clause 8.8.2.4.The parameters of the new separate API will refer the 3GPP new version TS23.682[i.5]

Step 010:SCEF(NSE) returns the PSM setting response(SCS Reference ID, Cause) message to the IN-CSE(SCS) to acknowledge acceptance.

Step 011: CSE/AE (UE) performs Initial Attach procedure of 3GPP  to negoation the active time value for PSM parameter with network.

Step 012: The network return the Initial Attach with the active time value for PSM parameter which is set by the IN-CSE(SCS) in step001.

Step 013: CSE/AE(UE) peforms the oneM2M registration procedure with mobile original message to IN-CSE(SCS), which includes the <schedule>, settingResource of < schedule > is Device. The period of <schedule> may be the Maximum Response Time and Maximum Latency.

Step 014: The IN-CSE(SCS) send the registration response with mobile original response message to the UE.

#### 8.8.5.2 Synchronize <schedule> from 3GPP network

##### 8.8.5.2.1 ServiceFlow

Step 001: The MME sends a Monitoring Report (Idle Timestamp, Subscribed Periodic RAT/TAU timer, Active Timer)  to SCEF when detecting the UE status change to Idle.

Step 002: The SCEF sends a Monitoring Report (Idle Timestamp, Subscribed Periodic RAT/TAU timer(optional), Active Time(optional))  to the IN-CSE(SCS) when receiving the Monitoring Report from MME.

Notes1: There is new requirement  for monitoring  type “UE Reachability” for 3GPP R14 from oneM2M in clause 8.8.3.1, refere the detail in clause 8.8.2.4. The parameters in Step 001 will refer the 3GPP new version TS 23.682[i.5].

Notes2: The sending of Active Time, and Periodic TAU/RAU time is required for cases where:

- The Maximum Response Time is absent when SCS/AS sends PSM setting Request

- SCS/AS does not send PSM setting Request to SCEF

- MME does not set the Maximum Response Time equal to the UE’s Active Time and set the UE’s Active Time based on local policy.

Step 003: The IN-CSE synchronize the <schedule> of the CSE/AE(UE) with the network: set the start time of <schedule> to the time the UE changes to idle state, and the period of <schedule> may be the Active time value and TAU timer. IN-CSE updates the settingResource of < schedule >  to Network.

For example, the Active time value of the UE is 30 minutes, and the TAU timer of UE is 6 hours. The Start time of UE change to idle status is 8:00 am. So the schedule could be set to: * 0-30 2,8,14,20 ****.

In case of the ASN-CSE hosted on UE, the ASN-CSE will establish connection on 2:00-2:30, 8:00-8:30, 14:00-14:30, 20:00-20:30

Step 004: The IN-CSE sends update request to the CSE/AE(UE) to update the <schedule>.

Step 005: The CSE/AE(UE) sends the response message to IN-CSE.

#### 8.8.5.3 Delivery Downlink Data When CSE/AE in PSM

##### 8.8.5.3.1 ServiceFlow

Step 001: AS(IN-AE) sends the data to the CSE/AS(UE)  message request, the target address is the resource ID of CSE/AE hosted on the UE;

Step 002: IN-CSE(SCS) checks the local < schedule> of target CSE/AE(UE) which indicates the  pre-defined  reachable schedule information of  targed CSE/AE(UE). If the settingResource of < schedule >  is Network,  it means the start time of the  < schedule>  is the same with Idle timestamp of  target CSE/AE(UE) . IN-CSE(SCS) check the reachable status of target CSE/AE(UE) in current time

CaseA: if the target CSE/AE(UE) current status is reachable

- Step 003a: IN-CSE(SCS) sends the downlink data to UE (CSE/AE) directly;

- Step 004a: the UE (CSE/AE) sends the response message to the IN-CSE(SCS);

- Step 005a: IN-CSE(SCS) sends response message to the AS(IN-AE);

CaseB:if the target CSE/AE(UE) curren status is unreachable, IN-CSE would calculate the next reachable time based on the <schedule>,  and check the Operation Execution Time  or Request Expiration Timestamp in the AS request message is whether ealier than the next reachable time or not, if yes, or  the Operation Execution Time  or Request Expiration Timestamp absent in the request, then go to Step 003b,

- Step 003b: IN-CSE(SCS) sends error response message to the AS(IN-AE) which indicates the message can not be deliveryed to the target CSE/AE(UE);

CaseC:if the device curren status is unreachable and the Operation Execution Time  and Request Expiration Timestamp in the AS(IN-AE) request message are both later than the next reachable time,  then got Step 003c:

- Step 003c: IN-CSE(SCS) buffers the message until the UE (CSE/AE)  is reachable again;

- Step 004c: IN-CSE(SCS) sends the downlink data  request message to the target UE (CSE/AE) before the Operation Execution Time  and Request Expiration Timestamp expire;

- Step 005c: the UE (CSE/AE) sends the response message to the IN-CSE(SCS);

- Step 006c: IN-CSE(SCS) sends response message to the AS(IN-AE);

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?

# Comments

如果<schedule>是设备或者应用，应该怎么处理？