## Slide 1: Handling for unreachable memberIDs of CREATE <group>
Group Name: ARC WG
Source: F. Sang-Eon Kim, KT (TTA), kim.sangeon@kt.com
Meeting Date: 2017-04-27 (ARC28.2)
Notes: Other suggested titles:
“Benefits of oneM2M Standardization”

## Slide 2: Introduction
This is rationale for ARC-2017-0115 which is CR about resource type group Rel-3.
The ARC-2017-0115 had been presented three times during ARC 28 at ETSI

## Slide 3: CREATE <group>
rqp: Request Primitive
rsp: Response Primitive
to: To
fr: From
op: Operation
rqi: Request Identifier
pc: Primitive Content
rsc: Response Status Code
ty: ResourceType
ri: ResourceID
rn: Resource Name
pi: Parent ID
et: Expiration Time
ct: Creation Time
lt: Last Modified Time
mt: Member Type
cnm: Current Number of Members
mnm: Max Number of Members
mid: Member IDs
csy: Consistency Strategy
fopt:: <fanOutPoint>
Clause 8.2
in TS-0004-V3.0.0
Clause 8.1.2
in TS-0001-V3.4.0
Clause 8.1.3
in TS-0001-V3.4.0
Clause 9.6.13
in TS-0001-V3.4.0
Clause 10.2.7
in TS-0001-V3.4.0
ans clause 7.4.13 in TS-0004-V3.0.0

## Slide 4: Case 1: single resource type
AE
Hosting CSE
CSE1/container
CSE2/container
CSE3/container
CSE4/container
CSE5/container
Originator
Receiver
{"to": "//Hosting CSE/2345", "fr": "//AE/99", "op": 1, "rqi": "A1234", "ty": 9,
"pc": { "m2m:grp": { "ri": "/CSE987776/group001",
"rn": "containergroup", "pi": "CSE987776",
"et": "20170408T004648",
"ct": "20170404T132648", "lt": "20170404T132648", "mt": 3,
"cnm": 5,
"mnm": 6,
"mid": ["CSE1/contaner","CSE2/contaner", "CSE3/contaner", "CSE4/contaner", "CSE5/contaner"],
"csy": 1
}
}
}
Request message
Reachable member
Unreachable member

## Slide 5: Case 1A: single resource type
AE
Hosting CSE
CSE1/container
CSE2/container
CSE3/container
CSE4/container
CSE5/container
Originator
Receiver
{"to": "//Hosting CSE/2345", "fr": "//AE/99", "op": 1, "rqi": "A1234", "ty": 9,
"pc": { "m2m:grp": { "ri": "/CSE987776/group001",
"rn": "containergroup", "pi": "CSE987776",
"et": "20170408T004648",
"ct": "20170404T132648", "lt": "20170404T132648", "mt": 3,
"cnm": 5,
"mnm": 6,
"mid": ["CSE1/contaner","CSE2/contaner", "CSE3/contaner", "CSE4/contaner", "CSE5/contaner"],
"csy": 1
}
}
}
Result of CREATE operation
and RSC=2000
How does Originator discriminates members of fanout for Group Request Target Members (ARC-2016-0484R02) parameter from memberIDs?
How does Hosting CSE know temporarily or permanent unreachable (e.g, CSE4/container, CSE5/container)?
This indicates ABANDON_MEMBER specified at clause 6.3.4.2.12 in TS-0004
This indicates all members are container which is specified at clause 6.3.4.2.11 in TS-0004

## Slide 6: Case 1A: solution, operation of CREATE
AE
Hosting CSE
CSE1/container
CSE2/container
CSE3/container
CSE4/container
CSE5/container
Originator
Receiver
{"to": "//Hosting CSE/2345", "fr": "//AE/99", "op": 1, "rqi": "A1234", "ty": 9,
"pc": { "m2m:grp": { "ri": "/CSE987776/group001",
"rn": "containergroup", "pi": "CSE987776",
"et": "20170408T004648",
"ct": "20170404T132648", "lt": "20170404T132648", "mt": 3,
"cnm": 3,
"mnm": 6,
"mid": ["CSE1/contaner","CSE2/contaner", "CSE3/contaner" ],
"unreachableMemberIDs": ["CSE4/contaner","CSE5/contaner"],
"csy": 1
}
}
}
Result of CREATE operation
and RSC=new code (2XXX) which is proposed by PRO-2017-0060
CSE1/container
CSE2/container
CSE3/container
CSE4/container
CSE5/container

## Slide 7: Case 1A: STE
AE
Hosting CSE
CSE1/container
CSE2/container
CSE3/container
CSE4/container
CSE5/container
Originator
Receiver
ARC-2016-0484R02, ARC-2016-0550R01
Group Request Target Members: optional group request target members: Indicates subset of members of a group for which fanout is to be executed. Example usage of Group Request Target Members: if fanout operation failed for some of the members then the Originator may use this parameter to execute fanout for failed members of a previous fanout operation.
{"to": "//Hosting CSE/2345", "fr": "//AE/99", "op": 1, "rqi": "A1234", "ty": 9,
"pc": { "m2m:grp": { "ri": "/CSE987776/group001", "rn": "containergroup", "pi": "CSE987776",
"et": "20170408T004648", "ct": "20170404T132648", "lt": "20170404T132648",
"GroupRequestTargerMembers": ?, "mt": 3, "cnm": 5, "mnm": 6,
"mid": ["CSE1/contaner","CSE2/contaner", "CSE3/contaner", "CSE4/contaner", "CSE5/contaner"],
"csy": 1 } } }
fanout

## Slide 8: Case 1A: STE has still problem
AE
Hosting CSE
CSE1/container
CSE2/container
CSE3/container
CSE4/container
CSE5/container
Originator
Receiver
fanout
Q1: How does Originator knows or maintains fanout for Group Request Target Members parameter ?
In case of Hosting CSE does not have unreachable memberIDs list.
Q2: Does the <fanoutpoint> provide resource for Group Request Target Members parameter ?
Comments: ARC-2016-0484R02 is for Release 2 only. Mirror CR is needed.

## Slide 9: Case 1A: solution for STE
AE
Hosting CSE
CSE1/container
CSE2/container
CSE3/container
CSE4/container
CSE5/container
Originator
Receiver
{"to": "//Hosting CSE/2345", "fr": "//AE/99", "op": 1, "rqi": "A1234", "ty": 9,
"pc": { "m2m:grp": { "ri": "/CSE987776/group001", "rn": "containergroup", "pi": "CSE987776",
"et": "20170408T004648", "ct": "20170404T132648", "lt": "20170404T132648",
"GroupRequestTargerMembers": ? "mt": 3, "cnm": 5, "mnm": 6,
"mid": ["CSE1/contaner","CSE2/contaner", "CSE3/contaner", "CSE4/contaner", "CSE5/contaner"],
"csy": 1 } } }
fanout
When Originator request operation whith GroupRequestTargerMembers parameter, Hosting CSE executes fanout by using unreachableMemberIDs (from slide 5).

## Slide 10: <uFanOutPoint> resource
AE
Hosting CSE
CSE1/container
CSE2/container
CSE3/container
CSE4/container
CSE5/container
Originator
Receiver
The <uFanOutPoint> resource is a virtual resource because it does not have a representation. It is the child resource of a <group> resource. Whenever a request is sent to the <uFanOutPoint> resource, the request is fanned out to each of the members of the <group> resource indicated by the unreachableMemberIDs attribute of the <group> resource. Before an execution of <uFanOutPoint>, triggering action may required. The responses (to the request) from each member are returned to the Originator. A timer should be set for the aggregation.
The <uFanOutPoint> resource does not have a resource representation by itself and consequently it does not have an accessControlPolicyIDs attribute. The <accessControlPolicy> resource used for access control policy validation is indicated by the membersAccessControlPolicyIDs attribute in the parent <group> resource.
uFanOutPoint

## Slide 11: Case 1B: single resource type
AE
Hosting CSE
CSE1/container
CSE2/container
CSE3/container
CSE4/container
CSE5/container
Originator
Receiver
{"to": "//Hosting CSE/2345", "fr": "//AE/99", "op": 1, "rqi": "A1234", "ty": 9,
"pc": { "m2m:grp": { "ri": "/CSE987776/group001",
"rn": "containergroup", "pi": "CSE987776",
"et": "20170408T004648",
"ct": "20170404T132648", "lt": "20170404T132648", "mt": 3 or 0,
"cnm": 3 or 5,
"mnm": 6,
"mid": ["CSE1/contaner","CSE2/contaner", "CSE3/contaner", "CSE4/contaner", "CSE5/contaner"],
"csy": 3
}
}
}
Result of CREATE operation
The results may different between provider A and B due to unclear in TS.
This indicates SET_MIXED specified at clause 6.3.4.2.12 in TS-0004
All members are container which is for 3. it is not consistent with consistencyStrategy which is 3.
Mixed member type is 0 which is specified at clause 6.3.4.2.11 in TS-0004.

## Slide 12: UPDATE <group>
AE
Hosting CSE
CSE1/container
CSE2/container
CSE3/container
CSE6/container
CSE7/container
Originator
Receiver
{"to": "//Hosting CSE/2345", "fr": "//AE/99", "op": 3, "rqi": "A1234", "ty": 9,
"pc": { "m2m:grp": { "ri": "/CSE987776/group001",
"rn": "containergroup", "pi": "CSE987776",
"et": "20170408T004648",
"ct": "20170404T132648", "lt": "20170404T132648", "mt": 3,
"cnm": 3,
"mnm": 10,
"mid":["CSE6/contaner","CSE7/contaner", "CSE8/contaner"],
"csy": 1
}
}
}
Request of UPDATE operation
CSE8/container
Reachable member to be updated
Unreachable member to be updated
Existing member
UPDATE operation has similar to CREATE operation.
This indicates UPDATE specified at clause 6.3.4.2.5 in TS-0004

## Slide 13: E-mail discussion (20 Apr.)
Hi Jason, Yongjing, Echo, Poornima, Suman, Anupama and all
I have been uploaded ARC-2017-0167 which is about unreachable memberIDs of <group> for CREATE operation.
ARC-2016-0484R02 is agreed to use Group Request Target Members parameter.
ARC-2017-0167 is try to align with Group Request Target Members parameter.
The motivation of 2017-0167 is:
How does Originator knows or maintains fanout for Group Request Target Members ?
How to handle unreachable memberIDs at step of validity check at a Receiver for CREATE operation ?
Could you check 2017-0167 for ARC 28.2 CC or any comments ?
Best Regards,
Francisco / KT

## Slide 14: E-mail discussion (20 Apr.)
Hi Francisco, Please find below the answers of your questions: How does Originator knows or maintains fanout for Group Request Target Members ? In TS-0004, fanoutpoint CRUD operations, for the Originator, we have mentioned (in PRO CR: PRO-2016-0378R04) that after receiving the response of fanoutpoint operation, the Originator upon analyzing the individual responses in an aggregated response knows that operation failed for which members. Now the Originator may issue another request with Group Request Target Members parameter set for failed members. How to handle unreachable memberIDs at step of validity check at a Receiver for CREATE operation ? For <group> CREATE request, currently it is the internal handling of CSE to keep the mapping of such unreachable members. Best Regards, Poornima

## Slide 15: Problem in TS-0001 and TS-0004

## Slide 16: Proposal
New attributes of <group>
unreachableMemberIDs | 0..1(L) | RW | List of memberIDs that is not reachable | NA
enforcement | 1 | WO | This is boolean value and default is TRUE. When enforcement is TRUE, operation shall be performed even if unreachableMemberIDs exist. When enforcement is FALSE, it may check reachability for unreachableMemberIDs or check memberTypeValidated. | MA
When Originator request operation whith GroupRequestTargerMembers parameter, Hosting CSE executes fanout by using unreachableMemberIDs
New virtual resource <uFanOutPoint>
Refer to slide 9