| Input Contribution |
| --- |
| Meeting ID* | ARC#29 |
| Title:* | OPC-UA IWK Possible Impacts on oneM2M |
| Source:* | Chengsui Lu, Hitachi, cslu@hitachi.cn Yuanchen Ma, Hitachi, ycma@hitachi.cn |
| Date:* | 2017-05-12 |
| Input related to* | WI-0059 OPC-UA Interworking TR-0018 Industrial Domain Enablement |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) | N/A |
| Decision requested or recommendation:* | To agree on the new content in TR-0018 (Industrial Domain Enablement) to include oneM2M and OPC-UA interworking impacts. |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# 10.4		Possible Impacts on oneM2M TSs

This clause concludes the study of oneM2M and OPC-UA interworking and proposes the possible impacts to oneM2M current specifications based on the consideration of the focus of oneM2M. The possible impacts may be addressed for resource/procedure mapping of OPC-UA interworking and semantic support for the industrial domain.

### -----------------------Start of Change 1-------------------------------------------

Based on the OPC-UA interworking study from this chapter, possible impacts on oneM2M TSs may lead to the corresponding transparent interworking developements, semantic enhancements, and security aspects.

- OPC-UA transparent interworking would be developed as the next phase of TR. Target TS could be TS-0033 Proximal IoT interworking or a new TS.

To support OPC-UA resource model mapping as described in 10.3.3, <flexContainer> needs to be further specified in the TS and summarized within [i.15] 9.6.1.2.2 including opcuaView, opcuaObject, opcuaObjectType, etc. As a conclusion from 10.3.3 and 10.3.4, OPC UA Method and ReferenceType nodes should be mapped to <contentInstance> resource.

Simultaneously, towards OPC-UA procedure mapping in 10.3.4, new messages format of each discovery, simple reading, subscription and notification service procedure would be provided in the TS. Mappings should be defined in details, e.g. OPC UA Views mapped to oneM2M <accessControlPolicy>, OPC UA queue attributes mapped to oneM2M CMDH buffer.

- Moreover, semantic enhancements could be proposed as industrial domain information model. Considering industry equipments include a large number of static devices (boilers, pipes, valves, etc.) and dynamic machines (compressors, pumps, pressure filters, disintegrators, etc.), that would be difficult to list all of them, another option FFS is to adopt B2MML (Business To Manufacturing Markup Language) from ISA-95 on manufacturing systems level, and AutomationML/PLCopen on supervisory and control level, which are utilized by OPC UA for oneM2M ontology, as shown in Figure 10.4-1.

Figure 10.4-1 OPC UA semantic canditates

- Security would be another area FFS. As shown in Figure 10.1.5-2, OPC UA security architecture is composed of secure session and secure channel. Although secure session could be achieved by oneM2M existing AEs and CSEs, it is still necessary to consider from oneM2M side how to support secure channel establishment, e.g. to convert broken OPC UA pieces into understandable security messages (e.g. credentials to be treated as UA Binary payload for oneM2M protocol) possibly on CSE.

### ----------------------- End of Change 1-------------------------------------------