## Slide 1: Service Enabled AE (SAE)
Group Name: ARC WG
Source: Dale Seed, Convida Wireless (Seed.Dale@ConvidaWireless.com)
Josef Blanz, Qualcomm (jblanz@qti.qualcomm.com)
Meeting Date: 2017-05-22 (ARC29)
Notes: Other suggested titles:
“Benefits of oneM2M Standardization”

## Slide 2: Background
At TP28 we had some good discussion (ARC-2017-0066R02) regarding the benefits of allowing an AE (and IPE) to host its own services.
  E.g. Allow an AE on a resource constrained IoT device (door lock) to host its own services (lock / unlock door)
  E.g. Allow an IPE on a IoT GW to host its own services for interworking NoDNs to a oneM2M system
In the end, consensus was reached that doing so would address some shortcomings and limitations in the oneM2M architecture
Two potential options were discussed:
  Allow AEs (and IPEs) to host their own services and corresponding resources
  Define a “minimal” CSE profile such that a CSE can realistically be hosted by a resource constrained IoT device
   The following slides focus on the first option  Service Enabled AE (SAE)

## Slide 3: Proposal
Define some extensions to the Mca interface to allow AEs to host their own services
  Define a subset of existing resource types that can be hosted by an AE/IPE
  Define a simple & lightweight sub/not mechanism for AE/IPE hosted resources
  Define a simple & lightweight ACP mechanism for AE/IPE hosted resources
  Restrict addressing to only structured addressing for AE/IPE hosted resources
  Restrict communication to only blocking mode for AE/IPE hosted resources
Define some extensions to CSE to allow it to re-target CRUD requests to AE/IPE hosted resources

## Slide 4: Allowed AE/IPE Hosted Resource Types
<container>
<contentInstance>
<flexContainer>
<mgmtObj>
<subscription> (Note - See separate slide)

## Slide 5: Subscription / Notification
Attributes of <subscription> | Multiplicity | RW/ RO/ WO
resourceType | 1 | RO
resourceID | 1 | RO
resourceName | 1 | WO
parentID | 1 | RO
expirationTime | 1 | RW
creationTime | 1 | RO
lastModifiedTime | 1 | RO
labels | 0..1 (L) | RW
subscribedAttributes | 0..1 (L) | RW
notificationURI | 1 (L) | RW
subscribedToAttributes enables attribute-level subscription and notification is triggered when any attribute(s) specified in subscribedToAttributes is updated.
  We need a lightweight subscription mechanism for AE/IPE
    Option #1 – Define a new resource type <AESubscription>
      Justification - keep oneM2M specs cleaner and simpler to understand since <subscription> resource and procedures are pretty complex as-is. Also this could allow further streamlining of AE subscriptions without impacting CSE subscription functionality
    Option #2a - Profile / Restrict <subscription> functionality that can be used by AEs
    Option #2b - Define a resource inheritance model in oneM2M ARC
      E.g. Use an inheritance model to define a <subscriptionBase> with minimal functionality that is inherited by <subscription>. Use <subscriptionBase> for AEs and <subscription> by CSEs.
 Proposal is to use Option 1 as defined below
Notification content contains only the modified attributes of the subscribed-to-resource
By default, AESubscription is a resource-level subscription and notification is triggered when any attribute in subscribed-to-resource is updated.

## Slide 6: Access Controls
  Leverage existing oneM2M security association between an AE and its Registrar CSE.
    No changes proposed to security association procedure.
  Once oneM2M security association (e.g. D/TLS session) is established between an AE and Registrar CSE, AE will only allow its Registrar CSE to access its AE hosted resources. All others will be denied access by the AE
    AE will perform “Registrar CSE impersonation check”
    To enable this, Registrar CSE will configure From parameter with its CSE-ID in all requests it re-targets to an AE
    AE will verify the value in the From parameter of all requests it receives is the same CSE-ID as the one established during security association with its Registrar CSE
  In addition, Registrar CSE can host oneM2M ACPs for AE. Registrar CSE can use these ACPs to restrict access to AE hosted resources to only those Originators that have proper privileges assigned.
    AE does not need to be burdened with supporting <accessControlPolicy> resources and checks. Registrar CSE well positioned to do this on AE’s behalf.

## Slide 7: Addressing
  Proposal - support only structured addressing scheme to keep things simple for AE hosted resources (i.e. structured AE-Relative addressing)
      E.g. lock/sub01

## Slide 8: Registration
Enhance existing AE registration procedure to allow an AE to configure its Registrar CSE with a list (i.e. directory) of its AE hosted resources
    Each entry in directory can contain info such as a path to an AE hosted resource, the type of resource, link to an ACP for the resource, whether ACP is applicable to child resources (DEEP) of this AE hosted resource or not (SHALLOW), etc
This will enable Registrar CSE to service requests to discover AE hosted resources and the capability to re-target requests to AE hosted resources
  Registrar CSE can also assist with the authorization to access AE hosted resources
    default is only Registrar CSE has authorization to access AE hosted resources

## Slide 9: Registration
ADN-AE
MN-AE
MN-CSE
CREATE To: MNCSEBase, Content: <AE>
AEHostedResources = {path=/lock, type=doorLock, acp=acp01, acpMode=DEEP}
CREATED

## Slide 10: Retargeting to an ADN-AE
ADN-AE
AE1
MN-CSE
Retargeted Request
CREATED
CREATE To: MNCSEBase/frontDoor/lock,
Content: <AESubscription>
CREATED
Retargeting
CREATE To: /lock, Content: <AESubscription>
UPDATE To: MNCSEBase/frontDoor
AEHostedResources = {path=/lock, type=doorLock, acp=acp01, acpMode=DEEP;
path=/lock/sub01, type=AESubscription}
UPDATED
Alternatively, Registrar CSE can update AEHostedResources and add “lock/sub01” entry

## Slide 11: Retargeting to an ADN-AE
ADN-AE
AE2
MN-CSE
Retargeted Request
UPDATED
UPDATE To: MNCSEBase/frontDoor/lock,
Content: {state = LOCKED}
UPDATED
Retargeting
UPDATE To: /lock, Content: {state = LOCKED}

## Slide 12: Retargeting to an ADN-AE
ADN-AE
AE1
MN-CSE
OK
NOTIFY To: AE1, Content: {state = LOCKED,…}
OK
Retargeting
NOTIFY To: /MN-CSE/AE1, Content: {state = LOCKED,…}

## Slide 13: Communication Modes
  To simplify AE, recommendation is for AE to only support blocking request handling for requests it services for AE hosted resources

## Slide 14: Next Steps?
Reach some consensus on whether this approach of supporting AE hosted resources is acceptable