| Input Contribution |
| --- |
| Meeting ID* | ARC#29 |
| Title:* | Modbus Interworking Solutions |
| Source:* | Qiuting Li, ZTE, li.qiuting@zte.com.cn |
| Date:* | 2017-05-14 |
| Input related to* | WI-0072/ TR-0043 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) |  |
| Decision requested or recommendation:* | New text about Modbus interworking Solution need to be incorporated into TR-0043. |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This contribution is proposal for possible solution for oneM2M and Modbus interworking, including Functional Architecture and Generic Entity Mapping.

## -------------------------------Start of new text-------------------------------------

# 7 Possible Solutions for oneM2M and Modbus Interworking

## 7.1 Introduction

This clause describes possible solutions for oneM2M and Modbus interworking and provides:

- Functional architecture

- Resource Model Mapping and operation translation

- Operational procedures

Firstly functional architecture with main entities is described. Secondly possible resource model mappings  and operation translations are described. Thirdly operational procedure mappings are described, i.e oneM2M entity reads or writes Modbus devices. This functional architecture can address all scenarios from clause 6 where Modbus devices are controlled and monitored by the oneM2M system.

## 7.2 Functional Architecture for Interworking

The Modbus interworking scheme is based on IPE (Interworking Proxy Application Entity) as a specialized AE or a part of CSE whichtranslates different protocol messages and exposes services provided by both system, oneM2M and Modbus.

As depicted in Figure7.2-1, the IPE is characterized by the support of a non-oneM2M reference point (Modbus interface) and by the mapping the non-oneM2M (Modbus) data models to oneM2M resources exposed via the Mca reference point. If IPE is deployed within CSE, the mapping oneM2M resource is directly exposed to remote CSE or AE via Mcc or Mca.The remote CSE or AE operates the oneM2M resource which represents Modbus device in hostingCSE, and triggers Modbus translation in IPE to operate Modbus device via Modbus interface.

The IPE may support two levels of interworking. One is the semantic interworking of full mapping so that an oneM2M application can access non-oneM2M solutions without the need to know the specific protocol encoding. The other is transparent transport of encoded non-oneM2M data and commands that the CSE or AE needs to know the specific protocol encoding rules.

Figure 7.2-1Functional Architecture with IPE

The main entities and their characteristics are as below.

- IPE : A specialized AE or a part of CSE for Modbus interworking.The IPE communicates with Modbus device via a non-oneM2M reference point, and has the capability of remapping the related data model to the oneM2M resources exposed via the oneM2M Mca reference point.The IPE may deploy on Modbus device, oneM2M ASN, MN or IN.

- Modbus Device : NoDN which only plays Modbus Server roles that implementates Modbus application and saves Modbus data. CSE or AE as Modbus Client accesses the Modbus Server to read and write Modbus data by Modbus function codes, i.e. data collection & controlling.

- oneM2M CSE: A Common Service Entity represents an instantiation of a set of “common service function” of the M2M/IoT environments. Such service functions are exposed to other entities through the Mca and Mcc reference points.

The figure 7.2-2 demonstrates a possible deployment model which describes the main entities and their interworking via reference points. According to different interworking scenarios IPE may be deployed in different nodes.

Figure 7.2-2 Deployment Model based on Functional Architecture

## 7.3 Resource model mapping

### 7.3.1 Introduction

In Modbus, a master as client always initiates request to slave (server) and waits for response. A user implements service by accessing data in Modbus device of application memory blocks.This clause firstly describes a possible mapping between oneM2M and Modbus entities at devices, resources and attribute level. Then mapping between Modbus termperature device to oneM2M resource as an example is described.

### 7.3.2	Generic Entity Mapping

The diagram below represents these different levels of model. The tree represents a structure of any Modbus device and how it is mapped into oneM2M entities. Each Modbus device may include four memory blocks for four types of data models. Each data model represents application data, e.g. temperature, status of Modbus device. A user can access and change the value of these data models by simple reading and writing operation. One possible entity mappings are:

  - Modbus Device --- <AE> oneM2M resource

  - Modbus Data model and Modbus Function --- <container>/<flexContainer> oneM2M resource

  - Modbus Data and Modbus function representation --- <contentInstance> oneM2M resource

Modbus devices is represents by Modbus data models that have to be bound to the device application. Modbus data is organized and saved in device application memory based on Modbus data models. In the Modbus data models each element is saved within a memory block. Each Function is mapped to a Modbus Function Code which well defined in Modbus protocol and determine how data is accessed and modified by oneM2M entity.

Though further procedures in this document map Modbus Device to oneM2M <AE> resource, it is also possible that a Modbus Device be mapped to a oneM2M <container> resource.

Figure 7.3.2-1 Generic Entity Mapping

In interworking scenarios, oneM2M entities play originator role to operate Modbus devices by IPE which translates oneM2M operations on mapping resources to Modbus operations on physical Modbus devices. Below table shows a brief translation between Modbus and oneM2M.

Table7.3.2-1 Modbus Function Request Translation

| Modbus Operation | OneM2M Resource and operation |
| --- | --- |
| Write registers or coils | Create <contentInstance> as Instance to corresponding <container> or <flexContainer> which represents Modbus Function, Note: each data model support different Modbus Function which represent by function code in Modbus |
| Read registers or coils |  |
| Diagnostics | Create <container> or <flexContainer> which represent diagnosed object, e.g. device identification. Note: each diagnostic operation mapping to Modbus Function code. |

In the Figure 7.3.2-2, for example a temperature device is mapped to oneM2M <AE> resource which comprises of several <container> or <flexContainer> resources and its child resources which represent temperature values and device information saved in the temperature device. ReadTemperature represents Modbus function which exposes to oneM2M system to access data in TemperatureRegister of Modbus device. Temperature Instance represents temperature value and related description, it may be represented with <timeSeries> if IPE periodically reports Temperature in Modbus Temperature Device to hostingCSE.

Figure 7.3.2-2 Modbus Temperature Device mapping into oneM2M entities

At the originator, oneM2M CREATE operation is translated to Modbus operation to read or write registers or coils, or to diagnose Modbus devices. For example, CREATE a <contentInstace> to ReadTemperature as an operation instance is translated to the Read operation onTemperature Register with corresponding Modbus Function code, e.g.Write single Register, the data field content of Modbus message is represented within content attribute.

## -------------------------------End of new text-------------------------------------