| Input Contribution |
| --- |
| Meeting ID* | ARC#29 |
| Title:* | TR-0044 Potential enhancements |
| Source:* | Yuan Tao, CNICG, taoyuan@cnicg.cn; Ye Tian, CNIC, tianye@cnic.cn; Bo Yuan, CNIC, yuanbo@cnic.cn; Yang Liu, CAICT, liuyang1@ritt.cn. |
| Date:* | 2017-05-22 |
| Input related to* | TR-0044 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) | TR-0044 v0.0.1 |
| Decision requested or recommendation:* | To agree on the new text in TR-0044. |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# 8	Potential enhancements to oneM2M

## 8.1	Scenarios analysis based on oneM2M architecture

## 8.1.1	Creation of mapping information

oneM2M entity captures the tangible identifier from tag attaching on the physical entity and records the related information, with the location information of the entity together constitute the mapping information, which is created and maintained on the corresponding entities. The creation procedures are shown in Figure 8.1.1-1.

Figure 8.1.1-1 Creation procedures

- AEs (AE1, AE2) captures the tangible identifiers attaching on the physical entities.

- AE2 creates the mapping between identifier and the related information on the CSE2.

- CSE2 creates the mapping between the identifiers (e.g. the tangible identifier and the location identifier) on the CSE3.

- CSE3 provides the tangible identifier (or identifier type) and the associated location information to the CSE4. If the CSE4 doesn’t get the information of identifier type (e.g. ‘epc’, ‘handle’, ‘oid’) from the CSE3, it may recognize the identifier type for each tangible identifier and maintain the mapping between the tangible identifier, identifier type and location information.

## 8.1.2	Discovery of identifiers related information

The application wants to discover the tangible identifier related information from the CSE that provides the 		heterogeneous service. There are two cases depicted as follows:

Case 1: the CSE4 maintains the tangible identifier related mapping information, the discovery procedures are shown in 	Figure 8.1.2-1.

Figure 8.1.2-1 discovery procedures for case 1

- The discovery application AE3 initiates a request to discovery the related information, the tangible identifier is 	contained in the request.

- The CSE4 receives the request, if the identifier type is not included in the request, the CSE4 may recognize the 	type of tangible identifier, and then searches the corresponding information by the identifier type or tangible 	identifier. CSE4 sends the discovery request to the CSE3.

- The CSE3 searches the location information of the entities that have the information associated with the tangible 	identifier, and responds the results to CSE4.

- The CSE4 forwards the results (location information of the CSE1 and CSE2) to the AE3.

- The AE3 sends the discovery request to CSE1 and CSE2 to retrieve the tangible identifier related information.

Case 2: the mapping information is not recorded on the queried CSE3, it will request the external identification 	resolution systems to implement the identification resolution. The discovery procedures are shown in figure 8.1.2-2.

Figure 8.1.2-2 discovery procedures for case 2

- The discovery application AE3 initiates a request to discovery the related information, the tangible identifier is 	contained in the request.

- The CSE3 receives the request, if the identifier type is not included in the request, the CSE4 may recognize the 	type of tangible identifier, and converting the tangible identifier to the compatible identifier with the specific format.

- The CSE3 sends the compatible identifier to the corresponding external resolution system (e.g. Handle system), 	and gets and resolution results from the resolution system.

- The CSE3 responds the results (location information of CSE1 and CSE2) to the AE3.

- The AE3 sends the discovery request to CSE1 and CSE2 to retrieve the tangible identifier related information.

## 8.2	Potential solutions

This section includes the changes needed in TS-0001 in existing resources, Figures and Tables to support the above 	scenarios. Imapcted sections in TS-0001 will be shown using the applicable section number.

### 9.6.6	Resource Type container

The <container> resource represents a container for data instances. It is used to share information with other entities and potentially to track the data. A <container> resource has no associated content. It has only attributes and child resources.

Figure 9.6.6-1: Structure of <container> resource

The <container> resource shall contain the child resources specified in table 9.6.6-1.

Table 9.6.6-1: Child resources of <container> resource

| Child Resources of <container> | Child Resource Type | Multiplicity | Description | <containerAnnc> Child Resource Types |
| --- | --- | --- | --- | --- |
| [variable] | <semanticDescriptor> | 0..n | See clause 9.6.30 | <semanticDescriptor>, <semanticDescriptorAnnc> |
| [variable] | <contentInstance> | 0..n | See clause 9.6.7 | <contentInstance>, <contentInstanceAnnc> |
| [variable] | <subscription> | 0..n | See clause 9.6.8 | <subscription> |
| [variable] | <container> | 0..n | See clause 9.6.6 | <container> <containerAnnc> |
| [variable] | <flexContainer> | 0..n | See clause 9.6.35 | <flexContainer> <flexContainerAnnc> |
| la | <latest> | 1 | See clause 9.6.27 | None |
| ol | <oldest> | 1 | See clause 9.6.28 | None |

The <container> resource shall contain the attributes specified in table 9.6.6-2.

Table 9.6.6-2: Attribute of <container> resource

| Attributes of <container> | Multiplicity | RW/ RO/ WO | Description | <containerAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3. | NA |
| resourceID | 1 | RO | See clause 9.6.1.3. | NA |
| resourceName | 1 | WO | See clause 9.6.1.3. | NA |
| parentID | 1 | RO | See clause 9.6.1.3. | NA |
| expirationTime | 1 | RW | See clause 9.6.1.3. | MA |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3. If no accessControlPolicyIDs value is configured, the accessControlPolicyIDs of the parent resource shall be applied for privilege checking. | MA |
| labels | 0..1 (L) | RW | See clause 9.6.1.3. | MA |
| creationTime | 1 | RO | See clause 9.6.1.3. | NA |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3. | NA |
| stateTag | 1 | RO | See clause 9.6.1.3. | OA |
| announceTo | 0..1 (L) | RW | See clause 9.6.1.3. | NA |
| announcedAttribute | 0..1 (L) | RW | See clause 9.6.1.3. | NA |
| dynamicAuthorizationConsultationIDs | 0..1 (L) | RW | See clause 9.6.1.3. | OA |
| creator | 0..1 | RO | See clause 9.6.1.3. | NA |
| maxNrOfInstances | 0..1 | RW | Maximum number of direct child <contentInstance> resources in the <container> resource. | OA |
| maxByteSize | 0..1 | RW | Maximum size in bytes of data (i.e. content attribute of a <contentInstance> resource) that is allocated for the <container> resource for all direct child <contentInstance> resources in the <container> resource. | OA |
| maxInstanceAge | 0..1 | RW | Maximum age of a direct child <contentInstance> resource in the <container> resource. The value is expressed in seconds. | OA |
| currentNrOfInstances | 1 | RO | Current number of direct child <contentInstance> resource in the <container> resource. It is limited by the maxNrOfInstances. The currentNrOfInstances attribute of the <container> resource shall be updated on successful creation or deletion of direct child <contentInstance> resource of <container> resource | OA |
| currentByteSize | 1 | RO | Current size in bytes of data(i.e. content attribute of a <contentInstance> resource) stored in all direct child <contentInstance> resources of a <container> resource. This is the summation of contentSize attribute values of the <contentInstance> resources. It is limited by themaxByteSize. The currentByteSize attribute of the <container> resource shall be updated on successful creation of deletion of direct child <contentInstance> resource of <container> resource | OA |
| locationID | 0..1 | RW | An ID of the resource where the attributes/policies that define how location information are obtained and managed. This attribute is defined only when the <container> resource is used for containing location information. | OA |
| ontologyRef | 0..1 | RW | A reference (URI) of the ontology used to represent the information that is stored in the child <contentInstance> resources of the present <container> resource (see note). | OA |
| disableRetrieval | 0..1 | RW | Boolean value to control RETRIE/UPDATE/DELETE operation on the child <contentInsance> resource. When the value is set to 'TRUE', RETRIEVE/DELETE/UPDATE operations for child <contentInstance> shall be rejected at all times. When the value is updated from 'TRUE' to 'FALSE', all existing <contentInstance> are deleted immediately. When the value is set to 'FALSE', all operations are permitted on the <contentInstance> resource as per existing procedures. | OA |
| tangibleIDInformation | 0..1(L) | RW | This attribute represents a set of tangible identifiers and its related information. The attribute is comprised of 2-tuples (tangibleID, IDType) with parameters shown in table 9.6.4-3. At least one of them shall be contained in this attribute. | OA |
| NOTE: The access to this URI is out of scope of oneM2M. |

The tangibleIDInformation attribute shall contain the parameters specified in table 9.6.4-3.

Table 9.6.4-3: Parameters in tangibleIDInformation attribute

| Parameters in tangibleIDInformation | Multiplicity | Description |
| --- | --- | --- |
| tangibleID | 0..1(L) | It represents the set of tangible identifiers that is associated with the specific physical entities. It is described as a list of tangible identifiers (e.g. 86.1000.11/70140703307739, 1.2.156.20000.2010319). It shall be present in case IDType parameter is null. |
| IDType | 0..1 | It shall be present in case tangibleID parameter is null. If the tangibleID parameter is present, it represents the corresponding type of the tangible identfiers. If the tangibleID parameter is not present,it represents the identifier type that is supported by the creation originator. The identifier type is expressed in string： epc; handle; oid; ucode; mcode; ecode. |