| CHANGE REQUEST |
| --- |
| Meeting ID:* | ARC#29 |
| Source:* | Catalina Mladin, Convida, Mladin.Catalina@convidawireless.com Quiting Li, ZTE, li.qiuting@zte.com.cn Rocco DiGirolamo, Convida, DiGirolamo.Rocco@convidawireless.com, Michael Starsinic, Convida, Starsinic.Michael@convidawireless.com Weixiang Shao, ZTE, shao.weixiang@zte.com.cn Gerald Görmer, Nokia, gerald.goermer@nokia-bell-labs.com |
| Date:* | 2017-05-23 |
| Reason for Change/s:* | Provides resources and flows for Background Data Transfer |
| CR against: Release* | Release 3 |
| CR against: WI* | Active WI-0058 MNT maintenance / < Work Item number(optional)> Is this a companion CR? Yes No Companion CR number: (Note to Rapporteur - use latest agreed revision)Is this a mirror CR? Yes No Mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0026 V0-2-0 |
| Clauses * | 7.10 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | N/A |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The 3GPP “Resource Management of Background Data Transfer” procedure is defined in 3GPP TS 23.682. When the IN-CSE knows that, at a future time, it will need to send a certain amount of data to a number of nodes, it can ask the 3GPP network for a background Data Transfer policy.

The IN-CSE asks for a background data transfer policy by telling the 3GPP network (via the SCEF API) that it wants to send a certain amount of data, in a certain time window, to a number of nodes.  The SCEF will ask the PCRF for a background data transfer policy that meets the request from the IN-CSE (via the Nt Interface).  The SCEF will offer one or more policies (time windows for data transmission) to the IN-CSE for when the transfer can be performed.

After an IN-CSE has received a policy, the IN-CSE will initiate a new procedure with the SCEF to apply the policy to each UE that it wants to apply the policy to.  The SCEF will apply the policy to the PCRF via the Rx Interface.

Note: When the SCEF requests the policy from the PCRF, the IN-CSE does not indicate the specific UE’s for which the policy is to apply; it only indicates how many UEs the policy will apply to.

The advantages of this procedure are:

- By requesting network resources in advance of a data transfer, the network and IN-CSE are less likely to experience a congestion situation.

- The unique policy ReferenceID is provided to the IN-CSE and will be reflected in the 3GPP CDR’s. This identifier identifies the policy that was provided to the IN-CSE and the information can be used for correlating CDR’s between the 3GPP and oneM2M systems.

- The procedure allows the MNO to offer multiple policies, each with a different charging rate to the oneM2M system.  In other words, the MNO can tell the oneM2M system that the transfer will cost X at 5:00pm and Y at 6:00pm.

This contribution proposes that the oneM2M system be able to make use of this feature in two different scenarios:

- When sending similar amount of data to a number of nodes.

- When sending the same data to a group of nodes (via the <group> resource)

R01 introduces the contribution for ARC#29 in tandem with an additional discussion document.

R02 addresses comments received in ARC#29

R03 addresses comments received during ARC#29 on charging data collection and offline agreements. It also provides corrections for clause numbering changes (see newly introduced change 2)

### -----------------------Start of change 1-------------------------------------------

## 7.10 Background Data Transfer

### 7.10.1.	Introduction

For the oneM2M system, Background Data Transfer (BDT) allows the IN-AE/CSE to have some control over its transmissions to field domain nodes that use an underlying network that provides transfer of data in the background. Namely, the IN-AE/CSE is provided with a list of potential transfer policies (time windows, with associated maximum bit rate) and charging condition so that the IN-AE/CSE may use a time window that is more favorable in terms of tariff/cost and/or overall throughput.

For the cellular network, management of the background data traffic for UEs (such as M2M devices) may result in significant gains for the network. For example, it is expected that for some use cases, 3rd party entities will select the more underutilized time windows to take advantage of the more favorable tariff and/or cost for the charging conditions. This effectively allows the cellular operator to spread the network utilization over time.

The purpose of this feature is to provide a means for the oneM2M System to inform the underlying network of parameters that can be used for optimizing the background data traffic over the underlying network for a set of Field Domain Nodes (UEs). Such parameters may include the expected number of UEs in the set and amount of data to be transferred a desired/preferred time window for the data transfer to these UEs, and network area information. In response, the underlying network may inform the oneM2M system about policies that may be used to meet the given background data transfer request.

Background Data Transfer takes place in 3 steps.

Policy Request and Selection:

  - An initiating entity (AE or CSE) will provide information on the requested BDT (e.g. expected data volume per UE) for a set of Field Domain Nodes (ADN/ASN /MN) to the IN-CSE.  The information will include a group or list of Field Domain Nodes that will use the policy, as well as some guidance to the IN-CSE so that it can better select from a set of potential transfer policies offered by the underlying network.

  - The IN-CSE will use the Mcn interface to provide the SCEF of the selected underlying network with the BDT information and to ask for the Policy.

  - The SCEF may provide the IN-CSE with a set of possible transfer policies for BDT and collect for charging. Using the guidance provided by the initiating Application Entity (AE) or Common Service Entity (CSE), the IN-CSE selects the transfer policy based on its own local policies, and notifies the initiating entity about the selected transfer policy.

  - The IN-CSE indicates to the SCEF which policy was selected and the SCEF records the selection for charging.

- Policy Enablement:

  - The IN-CSE contacts the PCRF via SCEF and enables the policy for each UE.

- Background Data Transfer:

  - During the policy time window, the IN-CSE transfers the data to the UE through the cellular network, and based on the chosen policy.

Editor’s note: Charging of the data transfer in the cellular network is F.F.S.

### 7.10.2	oneM2M resources/attributes involved

The <backgroundDataTransfer> resource is a child of <CSEBase>, <AE>, or <remoteCSE> and is used to request that the IN-CSE negotiates a background data transfer for a set of field nodes, with the Underlying Network. The resource attributes provide the characteristics of the background data transfer (volume per node, number of nodes), optionally a preferred time window for the transfer and geographic information, as well as the nodes that will be involved with the data transfer. Additionally, the resource also includes guidance to the IN-CSE so that it may select a transfer policy, if the underlying network provides multiple potential transfer policies (transferSelectionGuidance).

The groupLink(s) or memberIDs attributes are used to identify the target nodes for the background data transfer request.  It is assumed that the memberIDs list only includes field nodes that are UE’s. If the IN-AE wishes to send the same message to a group of field domain nodes, it is assumed that the IN-AE has already created a <group> resource in the IN-CSE, with a memberIDs list that includes all field domain nodes that need to be reached through the background data transfer.  Note that the memberIDs must be known when the <backgroundDataTransfer> resource is created so that the IN-CSE can determine the proper underlying network to contact.

Figure 7.10.2-1: Structure of <backgroundDataTransfer> resource

The <backgroundDataTransfer> resource contains the child resources specified in table 7.10.2-1.

Table 7.10.2-1: Child resources of <backgroundDataTransfer> resource

| Child Resources of <backgroundDataTransfer> | Child Resource Type | Multiplicity | Description | <backgroundDataTransfer> Child Resource Types |
| --- | --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 of oneM2M TS-0001 [1]. | <subscription> |

The <backgroundDataTransfer> resource contains the attributes specified in table 7.10.2-2.

Table 7.10.2-2: Attributes of <backgroundDataTransfer> resource

| Attributes of < backgroundDataTransfer > | Multiplicity | RW/ RO/ WO | Description | <backgroundDataTransferAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 of oneM2M TS-0001 [1]. | NA |
| resourceID | 1 | RO | See clause 9.6.1.3 of oneM2M TS-0001 [1]. | NA |
| resourceName | 1 | WO | See clause 9.6.1.3 of oneM2M TS-0001 [1]. | NA |
| parentID | 1 | RO | See clause 9.6.1.3 of oneM2M TS-0001 [1]. | NA |
| creationTime | 1 | RO | See clause 9.6.1.3 of oneM2M TS-0001 [1]. | NA |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 of oneM2M TS-0001 [1]. | NA |
| expirationTime | 1 | RW | See clause 9.6.1.3 of oneM2M TS-0001 [1]. | MA |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3 of oneM2M TS-0001 [1]. | MA |
| labels | 0..1 (L) | RW | See clause 9.6.1.3 of oneM2M TS-0001 [1]. | MA |
| announceTo | 0..1(L) | RW | See clause 9.6.1.3 of oneM2M TS-0001 [1]. | NA |
| announcedAttribute | 0..1(L) | RW | See clause 9.6.1.3 of oneM2M TS-0001 [1]. | NA |
| creator | 1 | RO | See clause 9.6.1.3 of oneM2M TS-0001 [1]. | OA |
| volumePerNode | 1 | WO | Expected data volume for the background data transfer. | OA |
| numberOfNodes | 1 | WO | Desired number of nodes for the background data transfer. | OA |
| desiredTimeWindow | 0..1 | WO | Desired time window for the background data transfer. | OA |
| transferSelectionGuidance | 0..1(L) | WO | List that includes guidance to IN-CSE in selecting from multiple transfer policies provided by underlying network. Possible values include:” lowest cost”, “highest throughput given maximum cost of X”, etc. If not included, the IN-CSE may independently choose from among multiple transfer policies. | OA |
| geographicInformation | 0..1 | WO | Provides geographic information for the policy request | OA |
| groupLink | 0..1 | RW | The resource identifier of a <group> resource that stores the entities that are part of the group for which the transfer applies. The resource may have either a groupLink attribute or a list of memberIDs | OA |
| memberIDs | 0..1 (L) | RW | List of member resource IDs for which the transfer policy applies. Only valid resource IDs include <remoteCSE> resources and/or <AE> resources. The resource may have either a groupLink attribute or a list of memberIDs | OA |

### 7.10.3	Signaling Flows

#### 7.10.3.1	Requesting and Selecting a Background Data Transfer Policy

Figure 7.10.3.1-1 depicts a general procedure for configuration of traffic policy for BDTinitiated by an IN-AE's request.  The procedure may also be initiated by a request from an MN/ASN-CSE or from the IN-CSE itself.

Figure 7.10.3.1-1: General Procedure for configuration of Background Data Transfer

Step-1 Request background data transfer configuration

An IN-AE requests IN-CSE to negotiate with SCEF in the underlying network, to configure background data transfer, by creating a <backgroundDataTransfer> resource.

The request includes:

the originator AE-ID of the requesting AE,

a target identifier: i.e. the <backgroundDataTransfer> child resource of <AE>, <CSEBase> or <remoteCSE> resource.

a set of Background Data Transfer Parameters as indicated in table 7.10.2-2.

If the IN-CSE has received a request from an IN-AE or another Originator to create <backgroundDataTransfer> resource, it checks if the request is valid.

Step-2 IN-CSE prepares for background data transfer negotiation

IN-CSE selects the SCEF and assumes the responsibility of negotiating with the underlying network for the background data transfer.

Step-3  Request background data transfer

The IN-CSE sends a request, providing Background Data Transfer parameters, to the selected SCEF for negotiating background data transfer. The request includes an identifier of the IN-CSE and the following parameters based on those provided in the < backgroundDataTransfer> resource: the volume of data expected to be transferred per node, the expected number of nodes,  the desired time window and the optional geographic information.  This request maps to the Background-Data-Transfer-Request (BTR) on the Nt reference point as defined in 3GPP TS 29.154 [i.2]. The SCEF enables the collection of charging information based on the charging condition for the parameters in the request.

NOTE:	The IN-CSE selects the SCEF based on the nodes that were identified in the groupLink(s) or memberIDs list of the background data transfer request. The exact selection methods are outside the scope of this specification, however, it is expected that the external identifiers of the group members can be resolved to an SCEF.

Step-4 The Underlying Network provides applicable policies for Background Data Transfer

The Underlying Network determines one or more applicable transfer policies based on requesting Background Data Transfer parameters and the SCEF records the charging information for the provided policies.

Step-5 Response for transfer policies

The SCEF responds to the IN-CSE with one or more applicable transfer policies and a Reference-ID.  This request maps to the Background-Data-Transfer-Answer (BTA) on the Nt reference point as defined in 3GPP TS 29.154 [i.2].

Step-6 Response for transfer policies provided by the underlying network

The IN-CSE manages the SCEF response. If more than one transfer policy was received from the underlying network, the IN-CSE uses the transferSelectionGuidance and its own selection policies to select one of them. If transferSelectionGuidance is not provided, then the IN-CSE uses internal policies to select a policy.

Step-7 Issue response to Entity initiating the background data transfer

IN-CSE responds to the original background data transfer request from the initiating entity. In its response message to the initiating entity, the IN-CSE includes the relevant policy information that it received in the SCEF response, namely the start and end time of the policy time window, the maximum aggregated authorized bandwidth for downlink transmission (in bps), and the maximum aggregated authorized bandwidth for uplink transmission (in bps).

Step-8 Confirm the transfer policy

If more than one transfer policy was offered in step-4, the IN-CSE forwards the selected transfer policy identifier and the Reference-ID to the SCEF as a confirmation.  This request maps to the Background-Data-Transfer-Request (BTR) on the Nt reference point as defined in 3GPP TS 29.154 [i.16].

Step-9 Store the confirmed transfer policy

The transfer policy confirmed by the IN-CSE is used by SCEF to store/update charging information and the Reference-ID.

Step-10 Response to IN-CSE

Once the underlying network has recorded the confirmed transfer policy, it returns a response to IN-CSE.  This request maps to the Background-Data-Transfer-Answer (BTA) on the Nt reference point as defined in 3GPP TS 29.154 [i.2].

#### 7.10.3.2	Enabling a Background Data Transfer Policy

Figure 7.10.4-1 depicts a general procedure for informing the underlying network about the field domain nodes (UEs) that should follow the negotiated policy. This is necessary as the underlying network needs to configure its internal nodes so that these may monitor the traffic for these UEs against the negotiated policy. The procedure starts after the procedure of Section 7.10.3.1.  Note that this procedure may occur immediately after the procedure of Section 7.10.3.1 or during the time window of the selected policy.

Figure 7.10.3.2-1: General Procedure for Policy Enablement

It is assumed that the IN-AE has already requested Background Data Transfer and the IN-CSE has selected the policy. The IN-AE has created the <backgroundDataTransfer> resource either with a list of memberIDs, or with a link to the <group> resource that includes a list of memberIDs.

Step-1 IN-CSE determines the impacted UEs

The IN-CSE uses the member list to determine the UEs that are impacted by the traffic policy. It uses the PoA for the entities on the member list, to obtain the IP address of the field domain nodes.

Step-2 IN-CSE informs SCEF of UE background data transfer

For each UE involved in the Background Data Transfer, the IN-CSE provides the Reference-ID to the SCEF.  The IN-CSE identifies the target UE by the IP address of the UE.

Note: Alternatively, the IN-CSE could provide the M2M External Identifier of the field node, and rely on the underlying network to map the M2M-Ext-ID to the underlying network specific Identifier it allocated to the target M2M Device,

Step-3 SCEF informs PCRF of UE background data transfer

For each UE involved in the Background Data Transfer, the SCEF executes the Initial Provisioning of Session Information Procedure or the Modification of Session Information procedures as described in 3GPP TS 29.214 [i.3].  This message maps to the AA-Request (AAR) command on the Rx reference point as defined in 3GPP TS 29.214[i.3].  The SCEF sets the Reference-ID field of the AAR command to the referenceID attribute.  The SCEF identifies the target UE by setting the Framed-IP-Address AVP or the Framed-Ipv6-Prefix AVP of the AAR Command to the IP address of the UE.

Note: The IP Addresses that are provided by the SCEF must be the non-NAT’d IP address of the nodes.

Step-4 PCRF is configured

The underlying network is configured with traffic policy information.

Note: The MNO will not enforce the maximum aggregated bitrate of a selected transfer policy. However, the operator may apply offline CDRs processing to determine whether the maximum aggregated bitrate was exceeded and charge the excess traffic.

Step-5 PCRF acknowledges UE enablement

The PCRF informs the SCEF that the UE has been enabled for background data transfer. This message maps to the AA-Answer (AAA) command on the Rx reference point as defined in 3GPP TS 29.214[i.3].

Step-6 SCEF acknowledges UE enablement

The SCEF informs the IN-CSE that the UE has been enabled for background data transfer. If there is more than one UEs listed in memberIDs, the IN-CSE then moves onto the next UE to enable, and repeats steps 2-6.

#### 7.10.3.3	Using Background Data Transfer Policy

One the transfer policy has been enabled and the time window has arrived, the initiating entity may:

- Use the fanout and group communication procedure to send the same request to each of the field domain nodes configured for background data transfer, or

- Send individual (and potentially different) requests to each of the field domain nodes configured for background data transfer.

Note: The data transfers corresponding to this step need to use the SGi interface.

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

## 5.3	Cellular IoT Features and Services

The SCEF exposes the following services to the IN-CSE.  This document describes how the IN-CSE may access each service.

  - Configuring Communication Patterns, see clause 7.6.

  - Configuring Session QoS, see clause 7.9.

  - Configuring Session Sponsorship, see clause 7.11.

  - Background Data Transfer, see clause 7.10.

  - Monitoring, see clause 7.4.

  - High Latency Communication – Extended S-GW and SCEF Buffering, see clause 7.3.

  - High Latency Communication – Configuring PSM and eDRX, see clause 7.3.

  - Mobile Core Network Issue Reports, see clause 7.8.

  - SMS Based Device Triggering, see clause 7.5.

  - Group Messaging (via MBMS), see clause 7.7.

  - Non-IP Data Delivery, see clause 7.1.1.

A UE hosted ADN-AE, MN-CSE, or ASN-CSE may access the following features that may be exposed by the 3GPP modem.  This document describes how the UE hosted ADN-AE, MN-CSE, or ASN-CSE may access each service.

- SMS Based Device Triggering, see clause 7.5.

- Group Messaging (via MBMS), see clause 7.7.

- Non-IP Data Delivery, see clause 7.1.1.

- Configuring Low Access Priority Connections, see clause TBD.

- High Latency Communication – Configuring PSM and eDRX, see clause 7.3.

- User Plane CIoT Optimizations (Suspend / Resume), see clause TBD.

Editor’s Note: A full list of 3GPP Release 13 & Release 14 service capabilities exposure functions will be shown and in order to scope down the work in R3, a subset of functions that are considered to be the highest priority and are aimed to be specified in this TS in R3 will also be given in this subclause.

### -----------------------End of change 2 ---------------------------------------------

### --------------------   Start Change to References Section  -------------------------------

## 2.2	Informative references

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

[i.1]     	oneM2M Drafting Rules (http://www.onem2m.org/images/files/oneM2M-Drafting-Rules.pdf).

[i.2]	3GPP TS 29.154: "Service capability exposure functionality over Nt reference point".

[i.3]	3GPP TS 23.214: "Policy and charging control over Rx reference point".

### -----------------------End Change to References Section-------------------------------