| CHANGE REQUEST |
| --- |
| Meeting ID:* | ARC#29.1 |
| Source:* | Joerg Swetina, NEC, joerg.swetina@neclab.eu |
| Date:* | 2017-06-08 |
| Reason for Change/s:* | Introduces a “flexAttribute” with multiplicity 0..n to a flexContainer |
| CR against: Release* | 3 |
| CR against: WI* | Active WI 0063 Release 3 Enhancements on Base Ontology & Generic Interworking) MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0001 v3.5.0 |
| Clauses * | 9.6.35 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | <TS/TR number>, <Version Number>, and <Description on which aspect should be reflected in this TS/TR> |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This CR introduces a new optional “flexAttribute” to the <flexContainer> resource. This attribute will be used in the context of generic interworking, but seems useful for other purposes too, in particular for interworking.

A <flexContainer> resource may include an indefinite number (0..n) of flexAttributes with variable names.

A flexAttribute is an attribute of type typedContent and is a general-purpose attribute that is capable to contain content of type xs:string, xs:boolean, xs:double, list (containing a list of contents) and structure (containing a list of contents together with a names), that are sub-types of typedContent.

Attribute type typedContent for a flexAttribute ensures that the attribute can contain structured content and that along with the content also type information about the content is provided by the attribute.

Change 1 begin

### 9.6.35	Resource Type flexContainer

The <flexContainer> resource type is a customizable container for data instances. It is a template for the definition of flexible specializations of data containers. Like a <container> resource, specializations of this <flexContainer> resource type are used to share information with other entities and potentially to track the data. While the <container> resources includes data to be made accessible to oneM2M entities inside <contentInstance> children, a specialization of the <flexContainer> resource includes associated content directly inside the <flexContainer> by means of one or more [customAttribute] attribute(s). The attribute name and attribute data type of [customAttribute] attributes are defined explicitly for each specialization of <flexContainer>, i.e. the specific set of attribute name and type are defined in a corresponding XSD-file.

A <flexContainer> resource may include an indefinite number (0..n) of flexAttributes with variable names. 
A flexAttribute is an attribute of type typedContent and is a general-purpose attribute that is capable to contain content of type xs:string, xs:boolean, xs:double, list (containing a list of contents) and structure (containing a list of contents together with a name), that are sub-types of typedContent. 
Attribute type typedContent for a flexAttribute ensures that the attribute can contain structured content and that along with the content also type information about the content is provided by the attribute.
The attribute name of any instance of a flexAttribute shall be unique within the instance of the <flexContainer> resource and shall be provided by the creator of the flexAttribute (i.e. in a CREATE or UPDATE operation).

Example usage of <flexContainer>: As a specialization of <flexContainer> that includes two [customAttribute] attributes, named "temperature"(xs:float type) and "humidity"(xs:positiveInteger type) can be specified in some TS. The actual data types of [customAttribute] will be described both in the specification document or XSD file which are referred by the value of containerDefinition attribute.

Figure 9.6.35-1: Structure of <flexContainer> resource

The <flexContainer> resource shall contain the child resource specified in table 9.6.35-1.

Table 9.6.35-1: Child resources of <flexContainer> resource

| Child Resources of <flexContainer> | Child Resource Type | Multiplicity | Description | <flexContainerAnnc> Child Resource Type |
| --- | --- | --- | --- | --- |
| [variable] | <semanticDescriptor> | 0..n | See clause 9.6.30 | <semanticDescriptor>, <semanticDescriptorAnnc> |
| [variable] | <subscription> | 0..n | See clause 9.6.8 | <subscription> |
| [variable] | <container> | 0..n | See clause 9.6.6 | <container> <containerAnnc> |
| [variable] | <flexContainer> | 0..n | <flexContainer> resource can include any of its specializations as child resource | <flexContainer> <flexContainerAnnc> |

The <flexContainer> resource shall contain the attributes specified in table 9.6.35-2.

Table 9.6.35-2: Attributes of <flexContainer> resource

| Attributes of <flexContainer> | Multiplicity | RW/ RO/ WO | Description | <flexContainerAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3. | NA |
| resourceID | 1 | RO | See clause 9.6.1.3. | NA |
| resourceName | 1 | WO | See clause 9.6.1.3. | NA |
| parentID | 1 | RO | See clause 9.6.1.3. | NA |
| expirationTime | 0..1 (note 1) | RW | See clause 9.6.1.3. | MA |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3. | MA |
| labels | 0..1 (L) | RW | See clause 9.6.1.3. | MA |
| creationTime | 0..1 (note 1) | RO | See clause 9.6.1.3. | NA |
| lastModifiedTime | 0..1 (note 1) | RO | See clause 9.6.1.3. | NA |
| stateTag | 1 | RO | See clause 9.6.1.3. This stateTag attribute value shall be incremented when a <container> or [flexContainer] child resource is created or deleted. This works same as the stateTag attribute update on a <container> resource at a <contentInstance> resource creation or deletion. | OA |
| announceTo | 0..1 (L) | RW | See clause 9.6.1.3. | NA |
| announcedAttribute | 0..1 (L) | RW | See clause 9.6.1.3. | NA |
| dynamicAuthorizationConsultationIDs | 0..1 (L) | RW | See clause 9.6.1.3. | OA |
| creator | 0..1 | RO | See clause 9.6.1.3. | NA |
| containerDefinition | 1 | WO | This contains an identifier reference (URI) to the <flexContainer> schema definition which shall be used by the CSE to validate the syntax of the <flexContainer> resource. This URI may refer to one of the oneM2M <flexContainer> defintions specified in the following documents: Generic Interworking [6]] AllJoyn Interworking [7]; Home Domain Information Model [8] A list of oneM2M <flexContainer> defintions is also provided in clause 9.6.1.2.2 [3]. Other URI for other <flexContainer> definitions may be specified. | MA |
| ontologyRef | 0..1 | RW | A reference (URI) of the ontology used to represent the information that is stored in the present <flexContainer> resource. | OA |
| [customAttribute] | 0..n | RW | Specialization-specific attribute(s). Name and data type defined in each specialization of <flexContainer> resource. | OA |
| [variable] | 0..n | RW | A flexAttribute consists of: Name of the flexAttribute The name shall be provided by the creator of the attribute and shall be unique within the <flexcontainer> instance Content of type typedContent The type typedContent of a flexAttribute consists of the pair: Identifier for the type of content of the flexAttribute. The identifier shall take one of the values: NODATA BOOL NUMBER STRING LIST STRUCT Content of the flexAttribute. The content of the flexAttribute needs to be formatted according to the Identifier for the type of content (Note 2) | OA |
| NOTE 1: When an instance of <flexContainer> is a child of a <flexContainer> resource, these attributes can be optional. Their presence is determined by the respective definition referred to by the containerDefinition attribute. |
| NOTE 2: The content for identifier BOOL contains content of type xs:boolean The content for identifier NUMBER contains content of type xs:double The content for identifier STRING contains content of type xs:string The content for identifier LIST contains an indefite number of content items, each formatted as typedContent The content for identifier STRUCT contains an indefite number of content items, each being a pair: (a) name of the structure element (b) content of the structure element, formatted as typedContent The content for identifier NODATE contains no data. It allows to UPDATE the attribute without providing data (which is different to setting its value to NULL in the Content parameter of the UPDATE Request message, as this would delete the attribute) |

Change 1 end