| CHANGE REQUEST |
| --- |
| Meeting ID:* | ARC #29.4 |
| Source:* | Dale Seed, Convida Wireless, Seed.Dale@ConvidaWireless.com Mike Starsinic, Convida Wireless, Starsinic.Michael@ConvidaWireless.com Catalina Mladin, Convida Wireless, Mladin.Catalina@ConvidaWireless.com |
| Date:* | 2017-07-02 |
|  | See Introduction |
| Reason for Change/s:* | Rel-3 |
| CR against: Release* | Active <WI-0058> - 3GPP & Cellular IoT Interworking MNT maintenance / < Work Item number(optional)> Is this a companion CR? Yes No Companion CR number: (Note to Rapporteur - use latest agreed revision)Is this a mirror CR? Yes No Mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: WI* | TS-0026 Version 0.0.2 |
| CR against: TS/TR* | 7.4.1 |
| Clauses * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Type of change: * | <TS/TR number>, <Version Number>, and <Description on which aspect should be reflected in this TS/TR> |
| Impacted other TS/TR(s) | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The SCEF supports an API to allow an IN-CSE to be informed when there are network congestion issues in a particular geographical area in the underlying 3GPP network.

This contribution proposes functionality to enable an IN-CSE to request that the SCEF send it reports whenever the network congestion level in a specified geographical area crosses defined threshold value(s).  Based on these reports, the IN-CSE can start/stop throttling of requests initiated by the ADN-AEs and ASN/MN-CSEs in this geographical area to help manage the congestion levels in the underlying 3GPP network.

### -----------------------Start of change 1-------------------------------------------

## 7.4.2	Throttling of requests based on Network Status Reports

The 3GPP SCEF Network Status Monitoring functionality described in 3GPP TS 23.682 [2] supports an API to allow an IN-CSE to be informed when there are network congestion issues in a particular geographical area in the underlying 3GPP network.

An IN-CSE may request to receive notifications from an underlying 3GPP network when the network congestion level in a specified geographical area crosses defined threshold value(s).  Based on these reports, the IN-CSE can start/stop throttling of requests initiated by or targeted towards its registree AEs and CSEs residing in this geographical area to help manage the congestion levels in the underlying 3GPP network.

Figure 7.4.2-1: Request for Network Status Reports

Pre-conditions:

There is a relationship in place between the IN-CSE and MNO allowing the IN-CSE to request Network Status Reports from the underlying 3GPP network.  The method for establishing this relationship is outside the scope of the present document.

The IN-CSE is configured with system defaults for the following.  The method for configuring these system defaults is outside the scope of the present document.

•	The network congestion levels to receive reports for

•	The severity of each specified congestion level

•	The specified actions to take based on the severity of each congestion level.

An ASN/MN-CSE or ADN-AE registers with the IN-CSE and configures the M2M-Ext-ID attribute of its <remoteCSE> or <AE> resource. The IN-CSE examines the M2M-Ext-ID and recognizes that it is associated with an MNO that it has a relationship with.

The IN-CSE is able to determine the location of its registree ASN/MN-CSEs and/or ADN-AEs.  For example, a <locationPolicy> resource may be used by an IN-CSE to determine the location of each ASN/MN-CSE or ADN-AE.

The ADN-AE’s <AE> resource has a <schedule> resource and the IN-CSE has permissions to update it.  The ADN-AE has a <subscription> to its <schedule> resource and when it receives a notification it updates its communication schedule accordingly.

The ASN/MN-AE’s <remoteCSE> resource has a <schedule> resource and the IN-CSE has permissions to update it. The ASN/MN-CSE has a <subscription> to its <schedule> resource and when it receives a notification it updates its communication schedule accordingly.

Step 1: IN-CSE determines to issue Network Status Request

The IN-CSE determines to issue a Network Status Report request via one or more of the following approaches.

The IN-CSE may periodically check the location of its registree ASN/MN-CSE’s and ADN-AE’s. When the IN-CSE detects that a certain number of ASN/MN-CSE’s and/or ADN-AE’s are in the same geographical area, it may further check if the ASN/MN-CSE’s and ADN-AE’s are connected to the same network.  The IN-CSE can determine if the ASN/MN-CSE’s and ADN-AE’s are connected to the same network by examining their M2M-Ext-ID attributes.  For example, a 3GPP external identifier is composed of a local identifier and a domain identifier.  If the ASN/MN-CSE’s and ADN-AE’s have the same domain identifier they may be connected to the same network. When the IN-CSE detects that a number of ASN/MN-CSE’s and/or ADN-AE’s are in the same geographical area and attached to the same network, it may decide to request a Network Statuss Report in that geographical area.

- The IN-CSE may use [cmdhNwAccessRule] resources for corresponding registree CSEs that support CMDH functionality.  The IN-CSE may check the targetNetwork attribute and use this attribute to identify a SCEF and issue a Network Status Request to this SCEF.  When issuing the request for a Network Status Report, the IN-CSE shall provide a geographic area for which the report will apply.  The IN-CSE may determine the geographic area for which the policy applies by checking the location that is associated for each CSE to which the set of CMDH policies apply.  For example, <locationPolicy> resources may be associated with an registree CSEs for which the CMDH policies apply and used by an IN-CSE to determine location for the CSEs.

How the IN-CSE determines which of the above approach(es) to use is implementation specific and outside the scope of the present document.

Step 2 (Optional): DNS Query/Response

To determine which SCEF to contact, an IN-CSE may determine the IP address(es)/port(s) of the proper SCEF by performing a DNS query using the M2M-Ext-ID (M2M External Identifier) assigned to the targeted ASN/MN-CSE(s) or ADN-AE(s).  Alternatively, an IN-CSE may use a pre-configured SCEF identifier.  The method for pre-configuring a SCEF identifier into the IN-CSE is outside the scope of the present document.

Step 3: Network Status Request

The IN-CSE requests network status reports for a particular geographical area, the fields of the API are populated as follows.

- SCS Identifier shall be set to a value that is prearranged between the Service Provider and MNO.

- T8 Destination Address is set to the IP Address of the IN-CSE.

- TTRI is used to correlate this request with future responses. It shall be assigned based on internal IN-CSE policies.

- TLTRI is used to identify the Network Status Report request.  It shall be assigned based on internal IN-CSE policies.  Later, when reports are received, the value shall be used to reference the original request so that the IN-CSE can know what Network and what geographical area the report pertains to.

- Threshold shall specify what congestion threshold(s) the IN-CSE wants to receive a report.  Whenever the congestion in the geographical area goes above or below an indicated threshold, a report will be sent.  The threshold(s) that are indicated by the IN-CSE are determined based on local IN-CSE policies.

Editor’s Note: 3GPP has not yet defined the stage 3 details of the supported format for the thresholds but abstracted value such as High, Medium, Low have been proposed.

- Duration shall be used to indicate how long reports will be sent.  For example, if duration is set to “1 day”, reports will be sent every time the congestion level falls above or below the indicated threshold(s) for one day.  After the duration expires, the SCEF will stop sending reports.

Note, If no duration is provided, then only one Network Status Report will be provided to the IN-CSE

- Geographical Area shall be configured with geopgraphical information specified by the IN-CSE.

Step 4: Process Network Status Request

The SCEF processes the request

Step 5: Network Status Response

The SCEF responds to the request with a cause value that indicates if the request was accepted and the TTRI that was provided in Network Status Request so that the IN-CSE can correlate the response with the original request

Step 6: Detect Congestion

After receiving the initial Network Status Request or when the congestion level passes one of the indicated threshold(s), the SCEF will create a Network Status Report.

Step 7: Network Status Report

The SCEF sends a Network Status Report to the IN-CSE.  The message includes a TTRI value that is assigned by the SCEF and will be provided back to the SCEF when the IN-CSE responds.  The message also includes the TLTRI value that was provided in the Network Status Request in Step 3 so that the IN-CSE can correlate the report with the original request. The message also includes a list of what congestion threshold(s) were crossed.

Step 8: Network Status Report Acknowledgement

The IN-CSE shall acknowledge the request and the acknowledgement shall include the TTRI that was provided by the SCEF in step 7.

Note, When the IN-CSE provides a duration in step 3, Steps 6-8 are repeated until the duration expires or until step 10 is executed

Step 9: Process Network Status Report

In response to the Network Status Report, the IN-CSE may decide to throttle up/down traffic in the congested network via one or more of the following approaches.

- An IN-CSE may reject requests that target nodes in congested areas of the network.  If an IN-CSE rejects a request due to network congestion it shall return a corresponding response code informing the cause of rejection is due to network congestion.  The IN-CSE may also inform the Originator to retry the request after some specified backoff delay.

- An IN-CSE may delay the processing (i.e. buffer) of requests that target nodes in congested areas of the network.

  - If the request is a blocking request, the IN-CSE should not delay the processing of the request and should instead reject these request with a corresponding response code informing the cause of rejection is due to network congestion.

  - If the request includes an Event Category that is set to immediate the IN-CSE should not delay the processing of the request and should instead reject the request with a corresponding response code informing the cause of rejection is due to network congestion.  In this case, the IN-AE may decide to resubmit the request with the Event Category set to “bestEffort” or “latest” to indicate the IN-CSE may buffer the request.

- An IN-CSE may modify the <schedule> resource of its registree AEs or CSEs that are located in congested area of the network such that they modify the times they send or receive requests.

  - A registree AE or CSE may subscribe to its <schedule> resource such that it receives notifications if the IN-CSE updates the scheduleElement attribute.  Upon receiving a notification with an updated scheduleElement an AE or CSE shall modify the times which it sends requests and makes itself available to receive requests.

- An IN-CSE may modify the [cmdhNwAccessRule] resources for corresponding registree CSEs that support CMDH functionality.

How the IN-CSE determines which of the above approach(es) to use is outside the scope of the current document and may be based on agreements with the network operator.

Step 10: Network Status Request Cancellation

Before the Duration expires, the IN-CSE may request that the SCEF stop sending status reports. The IN-CSE may make this decision, for example, when it detects that a number of devices are no longer in the geographical area applicable to the Network Status Request.

The IN-CSE sends a Network Status Cancellation Request.  The request shall include a TTRI value that is generated by the IN-CSE and is used to correlate this request with the response that will come from the SCEF.  The request shall also include the TLTRI value of the original Network Status Request.

Step 11: Process Network Status Cancellation Request

The SCEF processes the cancelation request.

Step 12: Acknowledge Network Status Cancellation Request

The SCEF acknowledges the request to cancel Network Status Reports for the geographical area.  The acknowledgement will include the TTRI that was provided by the IN-CSE in the Network Status Cancellation Request

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?