| Input Contribution |
| --- |
| Meeting ID* | ARC#29.4 |
| Title:* | Representation of services in oneM2M |
| Source:* | Jiaxin Yin, Huawei Technologies Co., Ltd., yinjiaxin@huawei.com |
| Date:* | 2017-7-2 |
| Input related to* | TS-0033 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) | TS-0033 v0.0.2 |
| Decision requested or recommendation:* | Incorporated the contribution if agreed. |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## 7.2	Representation of device services

## oneM2M defines different types of  resources that may be used to represent services provided by the device. For example, <container> and <contentInstance> resources are used for data management and repository, <subscription> is used for event based notifications, <group> is used for fan out of requests. When representing services from devices, proper resource types shall be used. The mis-usage of resource types for representing services may cause interoperability problems. Resource types defined in TS-0001 shall be used when representing services from the device.

There are two ways of expressing relationship between resources as well as relationships between the services these resources represent: parent-child relationship and linkage relationship. The linkage relationship only applies to specific oneM2M resource types such as accessControlPolicy, announced resources etc.

- The parent child relationship of resources shall be used to represent the hierachical relationship of services.

- The parent-child relationship of resources should be used if the resources have lifecycle dependencies

## If the the lifecycle of a certain service is subject to another existing service, application or common service entity, then the resource representing the service should be hosted as child resource of the resource representing the existing service, e.g. <AE> resource representing the application or <CSEBase> representing the common service entity. If the parent service is deleted, the child services are deleted automatically.

# Comments

感觉跟lifcycle没有本质区别。deployment dependency是形成lifecycle dependency的原因之一。