| CHANGE REQUEST |
| --- |
| Meeting ID:* | ARC #29.4 |
| Source:* | Catalina Mladin, Convida Wireless, Mladin.Catalina@ConvidaWireless.com Dale Seed, Convida Wireless, Seed.Dale@ConvidaWireless.com Mike Starsinic, Convida Wireless, Starsinic.Michael@ConvidaWireless.com James Hu, AT&T, James.Hu@att.com |
| Date:* | 2017-07-02 |
| Reason for Change/s:* | Providing support for Loss of Connectivity monitoring |
| CR against: Release* | Rel-3 |
| CR against: WI* | Active <WI-0058> - 3GPP & Cellular IoT Interworking MNT maintenance / < Work Item number(optional)> Is this a companion CR? Yes No Companion CR number: (Note to Rapporteur - use latest agreed revision)Is this a mirror CR? Yes No Mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0026 v 0.3.0 |
| Clauses * | 7.4 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | None |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution proposes a description of the Loss of Connectivity monitoring flow.

R01 updates cosigners and makes changes based on agreements at ARC 29.4 to reflect the use of schedule in <node>.

Update mcc/mca, resolve UE reachability

### -----------------------Start of change 1-------------------------------------------

## 7.4 Monitoring events

### 7.4.x UE Loss of Connectivity

The IN-CSE communicates with large numbers of devices, many of which are reachable for short periods of time. The IN-CSE wants to be informed when devices are not reachable to the Underlying Network, in order to better manage its communications. For example, IN-AEs which normally communicate with the device might not attempt communications if neither signalling or user plane communication are available.

3GPP TS 23.682 [2] supports Loss of Connectivity monitoring, via SCEF, by the IN-CSE. The Loss of Connectivity Monitoring Event configuration request allows the IN-CSE to provide to the network a Maximum Detection Time, which indicates the maximum period of time without any communication between the UE and Network after which the IN-CSE is to be informed that the device is considered to be unreachable.

The Maximum Detection Time of loss of connectivity is on the order of 1 minute to multiple hours. A timer with the order of magnitude of a few minutes can only apply to a limited number of devices due to the network signalling cost.

Note: In the 3GPP Network, the Maximum Detection Time of loss of connectivity may be used to determine the order of magnitude of the Periodic Update timer.

The UE Loss of Connectivity Monitoring flow is assumed to take place after the UE has attached to the 3GPP Network and registered with the IN-CSE.

Figure 7.4.x -1: Loss of Connectivity monitoring

Step 0: UE Attach and oneM2M Registration Procedures.

The UE attaches to the 3GPP network and the ADN-AE(s) or ASN/MN-CSE hosted on the UE perform the oneM2M registration procedures, as detailed in clause 6.5. The IN-CSE hosts the corresponding <AE> or <remoteCSE> resources for the registree, and an associated <node> resource. During this procedure, a <schedule> resource is created as child of the <node> resource .

If an IN-AE is interested in the reachability status of the UE, it may subscribe to the <schedule> resource (step 0b, optional).

Step 1: IN-CSE (SCS) sends a Monitoring Request to SCEF to monitor the UE Loss of Connectivity.

The monitoring request from the IN-CSE to SCEF contains information as specified in 3GPP TS 23.682 [3]. Such information includes:

- SCS Identifier shall be set to a value that is prearranged between the Service Provider and MNO.

- T8 Destination Address is set to the IP Address of the IN-CSE.

- TTRI is used to correlate this request with future responses. It shall be assigned based on internal IN-CSE policies.

- TLTRI is used to identify the monitoring request.  It shall be assigned based on internal IN-CSE policies.  Later, when reports are received, the value shall be used to associate them to the original request.

- Monitoring type shall be set to “Loss of Connectivity"

- Maximum Number of Reports or Monitoring Duration shall be optionally set according to IN-CSE pre-provisioning if continuous monitoring is supported.

- Chargeable Party identifier shall be optionally set according to IN-CSE pre-provisioning

- External Identifier shall be set to the M2M-Ext-ID of the UE

- Maximum Detection Time shall be set according to IN-CSE pre-provisioning. This value should be set to a value that is longer than the length of time of inactive communications as configured in the <schedule> resource

This information uses the values pre-provisioned at the IN-CSE or is derived from local policies.

Step 002: -Step 003: Monitoring Request Handling in the Underlying Network.

The SCEF handles the Monitoring Request together with the Mobile Core Network, as described in 3GPP TS23.682[3]. The SCEF sends a Monitoring Response (TLTRI, Cause) message to the IN-CSE (SCS) to acknowledge acceptance of the Monitoring Request of the identified monitoring event configuration.

Step 004: Detection of Loss of Connectivity and reporting to SCEF.

Later, when the UE losses connectivity, the MME detects the condition and sends a Monitoring Report to SCEF

Step 005: SCEF sends a Monitoring Report to IN-CSE (SCS) indicating UE Loss of Connectivity.

The SCEF sends a Monitoring Report to the IN-CSE as specified in 3GPP TS 23.682 [3]. Such information includes:

- External Identifier (M2M-Ext-ID of the UE)

- TLTRI (same as in the request)

Step 006: Loss of Connectivity Handling at the IN-CSE (SCS).

The IN-CSE uses the information provided in the Monitoring Report to update the <schedule> child resource of the <node> resource to indicate that no communications are currently available (e.g by using a keyword such as “NULL”).

Note: It is recommended that UE Reachability monitoring is also enabled in conjunction with the Loss of Connectivity monitoring. This enables the IN-CSE to provide updated timing information in the <schedule> resource, once the UE becomes reachable again.

Step 007: (Optional) Notifying subscribers.

Optionally, if IN-AEs have subscribed to changes in the <schedule> resources a notification will be sent to the subscribers.

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?