| CHANGE REQUEST |
| --- |
| Meeting ID:* | ARC #29.4 |
| Source:* | Catalina Mladin, Convida Wireless, Mladin.Catalina@ConvidaWireless.com Dale Seed, Convida Wireless, Seed.Dale@ConvidaWireless.com Mike Starsinic, Convida Wireless, Starsinic.Michael@ConvidaWireless.com James Hu, AT&T, James.Hu@att.com |
| Date:* | 2017-07-02 |
| Reason for Change/s:* | Describes UE Attach |
| CR against: Release* | Rel-3 |
| CR against: WI* | Active <WI-0058> - 3GPP & Cellular IoT Interworking MNT maintenance / < Work Item number(optional)> Is this a companion CR? Yes No Companion CR number: (Note to Rapporteur - use latest agreed revision) Is this a mirror CR? Yes No Mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0026 v0.3.0 |
| Clauses * | 6.5 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | None |
| Post Freeze checking: * | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution updates TS-0026 with a description of the UE Attach procedure as it pertains to oneM2M.

R01 updates cosigners

Addressing notes from ad-hoc:

- Update figure

- Update extGroupID

- Updates regarding the <node> association

R02 reflects discussions on Friday about hostedAElinks

R03 fixes cover page, update for more than one AE for ADN and to show networkCoordinated use

### -----------------------Start of change 1-------------------------------------------

## 6.5	UE Attach with oneM2M Registration Procedure

After a UE attaches to 3GPP network and establishes a data (i.e. PDN/PDP) connection, assuming it has not been registered previously with the oneM2M platform, it will initiate a oneM2M registration procedure. The oneM2M part of the procedure corresponds to the generic one described in clause 10.2.2 of TS-0001[1], where the Registrar CSE is the IN-CSE.

If the UE hosts an ADN, the registration will result in the IN-CSE hosting one or more corresponding <AE> resources for the UE. If the UE hosts an ASN or a MN, the registration of the ASN/MN-CSE will result in the IN-CSE hosting a corresponding <remoteCSE> resource for the ASN/MN-CSE.  The flow is depicted in figure 6.5-1.

Figure 6.5-1 UE Attach Procedure with oneM2M Registration

Steps 1a and 1b: UE Attach Request and Response

The UE determines that it needs to perform the 3GPP Attach procedure.

The 3GPP Network responds to the UE Attach request.

Steps 2a and 2b: oneM2M Registration Request and Response

The UE Hosting an ADN or an ASN/MN determines that it needs oneM2M services and decides to register to the oneM2M infrastructure, so it performs the registration procedure detailed in clause 10.2.2 of TS-0001[1].

- If the UE hosts an ADN, the registration procedure of the ADN-AE(s) will include the creation of corresponding <AE> resource(s) being hosted at the IN-CSE.

- If the UE hosts an ASN or MN, the registration procedure of the ASN/MN-CSE will include the establishment of a security association and the creation of a <remoteCSE> resource, corresponding to the registree CSE, to be hosted at the IN-CSE.

The IN-CSE responds to the UE hosted ADN-AE(s) or ASN/MN-CSE request for registration.

These steps allow the UE hosted ADN-AE(s) or ASN/MN-CSE to provide the IN-CSE with information needed for communication and providing services, e.g. pointOfAccess. In return the IN-CSE provides the UE with oneM2M specific information, e.g. by assigning AE-ID(s) or CSE-ID to the registree(s), respectively

Information provided by the ASN/MN-CSE or ADN-AE(s) to the IN-CSE at this time shall include:

- M2M-Ext-ID, Trigger-Recipient-ID as attributes of <AE> or <remoteCSE>, if available.

- externalGroupID as attribute of <remoteCSE>, if available.

- nodeLink as an attribute of the <AE> or <remoteCSE> resources, providing the resource identifier of a corresponding <node> resource, if pre-provisioned at the UE.

Step 3: Handling of association with a <node> resource

If in Step 2, the IN-CSE receives a valid nodeLink (as an attribute of the <AE> or <remoteCSE> resources) it means that the <node> resource storing the node specific information for this UE exists and has been pre-provisioned at the UE. For a UE hosted ASN/MN, the IN-CSE shall ensure that the hostedCSELink attribute of the corresponding <node> resource contains the resource identifier of the <remoteCSE > resource. For a UE hosted ADN, the IN-CSE shall ensure that the hostedAELinks attribute of the corresponding <node> resource includes the resource identifier of all the corresponding <AE > resources.

If in Step 2, the IN-CSE does not receive a valid nodeLink (as an attribute of the <AE> or <remoteCSE> resources) or the attribute is not present, the IN-CSE shall create a <node> resource for this UE. The IN-CSE shall populate the nodeLink attribute of the <AE> or <remoteCSE> resources with the resource identifier of the newly created <node> resource. For a UE hosted ASN/MN, the IN-CSE shall also populate the hostedCSELink attribute of the <node> resource with the resource identifier of the <remoteCSE > resource. For a UE hosted ADN, the IN-CSE shall ensure that the hostedAELinks attribute of the <node> resource includes the resource identifiers of all the corresponding <AE > resources.

If the following resources do not exist for this Underlying Network, the IN-CSE shall:

- create a <schedule> resource as a child of the <node> representing the UE, which represents the communication schedule for the 3GPP Underlying Network where the Attach procedure was completed. While no specific scheduling information is available, the <schedule> may reflect that communications are available continuously. The IN-CSE may set the networkCoordinated attribute, based on the UE pre-provisioned information or local policies, to indicate if the schedule should be coordinated with the Underlying Network.

- create the [activeCmdhPolicy] resource as a child of the <node> resource representing the UE, providing the active communication policies for the 3GPP Underlying Network where the Attach procedure was completed. The IN-CSE shall populate the mgmtLink of the active [cmdhNwAccessRule] with a link to the <schedule> resource created for the communication schedule with this Underlying Network.

.-----------------------End of change 1-------------------------------------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables? Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?