| CHANGE REQUEST |
| --- |
| Meeting ID:* | ARC #29.4 |
| Source:* | Catalina Mladin, Convida Wireless, Mladin.Catalina@ConvidaWireless.com Dale Seed, Convida Wireless, Seed.Dale@ConvidaWireless.com Mike Starsinic, Convida Wireless, Starsinic.Michael@ConvidaWireless.com James Hu, AT&T, James.Hu@att.com |
| Date:* | 2017-07-02 |
| Reason for Change/s:* | Provide Network Parameter Configuration functionality |
| CR against: Release* | Rel-3 |
| CR against: WI* | Active <Work Item number> <WI-0058> - 3GPP & Cellular IoT Interworking MNT maintenance / < Work Item number(optional)> Is this a companion CR? Yes No Companion CR number: (Note to Rapporteur - use latest agreed revision)Is this a mirror CR? Yes No Mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0026 v.0.0.2 |
| Clauses * | 7.4 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | None |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution proposes a description of the Network Parameter Configuration monitoring flow.

Cellular Devices that are used in IoT applications can make use of new power savings features such as Power Saving Mode (PSM) and extended discontinuous reception (eDRX).  PSM and eDRX allow the device to sleep for long stretches of time. However, when a device is sleeping, it is not available for mobile terminated commination.  If the network application wants to contact the device, it needs to wait until the device is awake.

The oneM2M IN-CSE has a <schedule> resource for its regsitrees.  The information in the <schedule> resource can be used provide the network with information about how to configure a UE’s Power Saving Mode (PSM) and extended discontinuous reception (eDRX) settings. If the IN-CSE does not assist the network in configuring UE’s Power Saving Mode (PSM) and extended discontinuous reception (eDRX) settings, then the UE would be required to negotiate the values with the network and the IN-CSE would have no influence on the UE’s UE’s Power Saving Mode (PSM) and extended discontinuous reception (eDRX) settings.

R01 adds cosigner and addresses the changes to using the <schedule> of the node resource.

Correct mcc/mca line in figure.,language for multiple AEs on ADN.

### -----------------------Start of change 1-------------------------------------------

### 7.x Network Parameter Configuration

The 3GPP SCEF functionality described in 3GPP TS 23.682 [2] supports an API for Network Parameter Configuration which may be used by the IN-CSE to suggest to the 3GPP Mobile Network specific configuration parameters. The procedure may be used by the IN-CSE to influence certain aspects of UE/network behaviour such as the UE's PSM and extended idle mode DRX. For this purpose, parameter values may be suggested for Maximum Latency and Maximum Response Time for a UE. The Mobile Core Network may choose to accept, reject or modify (via the SCEF) the suggested configuration parameter value.

NOTE 1: Once the network provides the SCEF with the configured values, the MME could later change the values.  For example, the UE may be roaming and the visited network might not allow certain values.  In this scenario, the SCEF can request a reachability notification with the Idle Status Indication set to indicate that it wants to be notified of the UE’s active timer and periodic TAU/RAU timer when the UE enters the idle state.

In the 3GPP interworking architecture of oneM2M, the UE can host an ADN-AE or an ASN/MN-CSE. The UE Monitoring flow in Figure 7.x-1 takes place after the UE has attached to the 3GPP Network and the ADN-AE or ASN/MN-CSE is registered with the IN-CSE.

Figure 7.x -1: Network Parameter Configuration flow

Step 0: UE Attach and oneM2M Registration Procedures.

The UE attaches to the 3GPP network and the ADN-AE(s) or ASN/MN-CSE hosted on the UE perform the oneM2M registration procedure, as detailed in clause 6.5. The IN-CSE hosts the corresponding <AE> or <remoteCSE> resources and an associated <node> resource for the registree. During this procedure, a <schedule> resource is created as child of the <node>  resource. The UE hosted ADN-AE(s) or ASN/MN may subscribe to the node <schedule> resource. If an IN-AE is interested in the reachability status of the UE, it may also subscribe to the <schedule> resources

Step 1: IN-CSE (SCS) sends to the SCEF a Network Parameter Configuration request.

This step is triggered by the creation or modification of the node <schedule> resource (step 0b),.

The IN-CSE determines the SCEF based on the M2M-Ext-ID’s of the registree ASN/MN-CSE or ADN-AEs (e.g. either a DNS lookup on the M2M-Ext-ID or the based on the domain portion of the M2M-Ext-ID’s.).  The IN-CSE provides the network pattern to the SCEF, the fields of the API are populated as follows.

  - External Identifier shall be set to M2M-Ext-ID

  - SCS Identifier shall beset to a value that is prearranged between the Service Provider and MNO.

  - TTRI is used to correlate this request with future responses. It shall be assigned based on internal IN-CSE policies.

  - TLTRI is used to identify the Communication Pattern request.  It shall be assigned based on internal IN-CSE policies.  Later, when the IN-CSE decides to change the communication pattern, the value will be used to reference the original request.  The SCEF will use this information to identify what communication pattern should be modified.

  - Maximum Latency – This value tells the network how long the UE is allowed to sleep.  Setting it to 0 will disable PSM, extended idle mode DRX, and S-GW buffering.  The IN-CSE shall extract the periodicity of the active periodicity in the scheduleElement, if it exists. The IN-CSE shall set Maximum Latency to be approximately the periodicity of the active periods in the scheduleElement. If there is no periodicity it is recommended not to utilize this parameter.

  - Maximum Response Time – When the UE uses PSM, Maximum Response Time tells the network how long the UE should stay reachable after a TAU.  When the UE uses eDRX, Maximum Response Time is used by the network to determine when to send a reachability notification before a UE’s paging occasion.  The IN-CSE extract a duration of activity from the scheduleElement. The IN-CSE shall set Maximum Response Time to reflect this duration of activity, indicating how long the UE should stay reachable for downlink communications.

Step 002: -Step 003: Network Parameter Configuration Handling in the Underlying Network.

The SCEF authorizes the request and responds with a cause value that indicates if the request was accepted and with the TTRI that was provided in step 2, so that the IN-CSE can correlate the response with the original request.

The response may also include updated values of Maximum Latency, Maximum Response Time, and Suggested Number of Downlink Packets, if the network chose to use values that were different than the values that were suggested by the IN-CSE.  If the values are updated, then the IN-CSE should adjust the <schedule> accordingly.

If the SCEF discarded any of the parameters that were provided in step 1 it indicates which values were discarded. The IN-CSE does not need to take any actions to account for discarded values.

Step 004: Network Parameter Configuration Handling at the IN-CSE (SCS).

- The IN-CSE information received in the Monitoring response may include updated values of Maximum Latency, Maximum Response Time and Suggested Number of Downlink Packets if the network chose to use values that were different than the values that were suggested by the IN-CSE.  If the values are updated, then the IN-CSE uses the information provided to update the <schedule> child resource of the <node> resource.

The IN-CSE changes the node  <schedule> resource such that the duration of the activity time of the scheduleElement reflects the Maximum Response Time and the periodicity of the active periods reflects the Maximum Latency.

Note: the IN-CSE shall ensure that there are no loops

Step 005: (Optional) If IN-AEs have subscribed to changes in the <schedule> resources, a notification will be sent to the subscribers. Notifications will also be sent to the UE hosted ADN-AE or ASN-CSE/MN-CSE, if subscriptions to their respective <schedule> resources have been created.

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?

# Comments

Add note about the loops

Include example