| CHANGE REQUEST |
| --- |
| Meeting ID:* | ARC#30 & MAS#30 |
| Source:* | Feng Zhang, Huawei, zhangfeng49@huawei.com Yongjing Zhang, Huawei, zhangyongjing@huawei.com Mengxuan Zhao, Easy Global Market, mengxuan.zhao@eglobalmark.com |
| Date:* | 2017-06-30 |
| Reason for Change/s:* | This contribution proposes to add the CRUD operation definition for <ontologyRepository>, <ontology> and <semanticValidation> resources for ontology management based on the concluded study in TR-0033. |
| CR against: Release* | Release 3 |
| CR against: WI* | Active WI-0053 MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0001. v3.5.0, Functional Architecture |
| Clauses * | 10.2.14 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | <TS/TR number>, <Version Number>, and <Description on which aspect should be reflected in this TS/TR> |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

# Introduction

This clause describes CRUD operations for <ontologyRepository>, <ontology> and <ontologyRepository> resources.

This CR is technically identical to MAS-2017-0149 (TS-0034) and can be withdrawn if ARC and MAS agree to MAS-2017-0149.

### -----------------------Start of change 1------------------------------------------

#### 10.2.14.x	Create <ontologyRepository>

This procedure shall be used for creating a <ontologyRepository> resource.

Table 10.2.14.x-1: <ontologyRepository> CREATE

| <ontologyRepository> CREATE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | All parameters defined in table 8.1.2-2 apply with the specific details for: Content: The resource content shall provide the information as defined in clause 9.6.x |
| Processing at Originator before sending Request | According to clause 10.1.2. |
| Processing at Receiver | According to clause 10.1.2. The hosting CSE shall also create the <semanticValidation> virtual child-resource if the addressed <ontologyRepository>resource is successfully created. |
| Information in Response message | According to clause 10.1.2. |
| Processing at Originator after receiving Response | According to clause 10.1.2. |
| Exceptions | According to clause 10.1.2. |

#### 10.2.14.y	Retrieve <ontologyRepository>

This procedure shall be used for retrieving <ontologyRepository> resource.

Table 10.S2.14.y-1: <ontologyRepository> RETRIEVE

| <ontologyRepository> RETRIEVE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc'. |
| Information in Request message | All parameters defined in table 8.1.2-2. |
| Processing at Originator before sending Request | According to clause 10.1.3. |
| Processing at Receiver | According to clause 10.1.3. |
| Information in Response message | All parameters defined in table 8.1.3-1 apply. |
| Processing at Originator after receiving Response | According to clause 10.1.3. |
| Exceptions | According to clause 10.1.3. |

#### 10.2.14.z	Update <ontologyRepository>

This procedure shall be used for updating an existing <ontologyRepository> resource.

Table 10.2.14.z-1: <ontologyRepository> UPDATE

| <ontologyRepository> UPDATE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | All parameters defined in table 8.1.2-2. |
| Processing at Originator before sending Request | According to clause 10.1.4. |
| Processing at Receiver | According to clause 10.1.4. |
| Information in Response message | According to clause 10.1.4. |
| Processing at Originator after receiving Response | According to clause 10.1.4. |
| Exceptions | According to clause 10.1.4. |

#### 10.2.14.a	Delete <ontologyRepository>

This procedure shall be used for deleting an existing <ontologyRepository> resource.

Table 10.2.14.a-1: <ontologyRepository> DELETE

| <ontologyRepository> DELETE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | All parameters defined in table 8.1.2-2 apply. |
| Processing at Originator before sending Request | According to clause 10.1.5. |
| Processing at Receiver | According to clause 10.1.5. The hosting CSE shall also delete the <semanticValidation> virtual child-resource if the addressed <ontologyRepository>resource is successfully created. |
| Information in Response message | According to clause 10.1.5. |
| Processing at Originator after receiving Response | According to clause 10.1.5. |
| Exceptions | According to clause 10.1.5. |

#### 10.2.14.b	Create <ontology>

This procedure shall be used for deleting an existing <ontology> resource.

Table 10.2.14.b-1: <ontology> CREATE

| <ontology> CREATE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | All parameters defined in table 8.1.2-2 apply with the specific details for: Content: The resource content shall provide the information as defined in clause 9.6.x |
| Processing at Originator before sending Request | According to clause 10.1.2. |
| Processing at Receiver | According to clause 10.1.2. |
| Information in Response message | According to clause 10.1.2. |
| Processing at Originator after receiving Response | According to clause 10.1.2. |
| Exceptions | According to clause 10.1.2. |

#### 10.2.14.c	Retrieve <ontology>

This procedure shall be used for deleting an existing <ontology> resource.

Table 10.2.14.c-1: <<ontology> RETRIEVE

| <ontology> RETRIEVE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc'. |
| Information in Request message | All parameters defined in table 8.1.2-2. |
| Processing at Originator before sending Request | According to clause 10.1.3. |
| Processing at Receiver | According to clause 10.1.3. |
| Information in Response message | All parameters defined in table 8.1.3-1 apply. |
| Processing at Originator after receiving Response | According to clause 10.1.3. |
| Exceptions | According to clause 10.1.3. |

#### 10.2.14.d	Update <ontology>

This procedure shall be used for deleting an existing <ontology> resource.

Table 10.2.14.d-1: <ontology> UPDATE

| <ontology> UPDATE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | All parameters defined in table 8.1.2-2. |
| Processing at Originator before sending Request | According to clause 10.1.4. |
| Processing at Receiver | According to clause 10.1.4. |
| Information in Response message | According to clause 10.1.4. |
| Processing at Originator after receiving Response | According to clause 10.1.4. |
| Exceptions | According to clause 10.1.4. |

#### 10.2.14.e	Delete <ontology>

Table 10.2.14.e-1: <ontology> DELETE

| <ontology> DELETE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | All parameters defined in table 8.1.2-2 apply. |
| Processing at Originator before sending Request | According to clause 10.1.5. |
| Processing at Receiver | According to clause 10.1.5. |
| Information in Response message | According to clause 10.1.5. |
| Processing at Originator after receiving Response | According to clause 10.1.5. |
| Exceptions | According to clause 10.1.5. |

#### 10.2.14.f Create <semanticValidation>

The <semanticValidation> resource shall be created when the parent <ontologyRepository> resource is created by the hosting CSE. The Create operation is not applicable via Mca, Mcc or Mcc’.

#### 10.2.14.g Retrieve <semanticValidation>

The Retrieve operation is not applicable for <semanticValidation>

#### 10.2.14.h Update <semanticValidation>

This procedure shall be used for validating a <semanticDescriptor> resource contained in the Update request against its referenced ontology. The semantic validation process shall also take into account linked <semanticDescriptor> resources (if any) of the <semanticDescriptor> resource in the request.

Table 10.2.14.h-1: <semanticValidation> UPDATE

| <semanticValidation> UPDATE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc'. |
| Information in Request message | All parameters defined in table 8.1.2-3. Besides, the resource representation in the Content parameter of the request message shall be set as the <semanticDescriptor> resource to be validated. |
| Processing at Originator before sending Request | According to clause 10.1.4. |
| Processing at Receiver | The originator shall follow the basic procedure according to clause 10.1.4, with the following specific details: retrieve the semantic description (i.e. the triples in descriptor attribute of), the URI to the referenced ontology in ontologyRef attribute and potential links to other linked <semanticDescriptor> resources from the <semanticDescriptor> resource to be validated; retrieve the referenced ontology, any linked <semanticDescriptor> resources and the referenced ontologies of the linked <semanticDescriptor> resources; perform semantic validation according to oneM2M TS-0034 [x]. |
| Information in Response message | According to clause 10.1.4. |
| Processing at Originator after receiving Response | According to clause 10.1.4. In case the Originator is the hosting CSE of the <semanticDescriptor> resource being validated, the Originator shall update the semanticValidated attribute (true or false) of the hosted <semanticDescriptor> resource according to the received response code accordingly. |
| Exceptions | According to clause 10.1.4. |

#### 10.2.14.i Delete <semanticValidation>

The <semanticValidation> resource shall be deleted when the parent <ontologyRepository> resource is deleted by the hosting CSE. The Delete operation is not applicable via Mca, Mcc or Mcc’.

### -----------------------End of change 2------------------------------------------

### -----------------------Start of change 3------------------------------------------

## 2.1	Normative references

[x]	oneM2M TS-0034: "Semantics_Support".

### -----------------------End of change 3------------------------------------------