| CHANGE REQUEST |
| --- |
| Meeting:* | ARC TP30 |
| Source:* | BeiXu，Huawei，Echo.xubei@huawei.com |
| Date:* | 2017-06-02 |
| Contact:* | BeiXu，Huawei，Echo.xubei@huawei.com |
| Reason for Change/s:* | Add new section about UE location reporting |
| CR against: Release* | <Release> Only ONE Release shall be indicated |
| CR against: WI* | Active <WI-0058 - 3GPP & Cellular IoT Interworking> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0026-V-0.3.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution adds procedures to TS-0026 to show how oneM2M interworks with an underlying 3GPP network’s location monitoring and reporting functionality via the SCEF API.  The contribution provides details on how the oneM2M <locationPolicy>, <container> and <contentInstance> resources are used to interwork with the SCEF API and provide location monitoring capability for an ASN/MN-CSE or ADN-AE hosted on a 3GPP UE..

### -----------------------Start of change 1-------------------------------------------

## 7.5	Monitoring event(Location Reporting)

### 7.5.1 Introduction

The 3GPP location monitoring feature supports reporting the current location of a UE as well as the last known location of UE.  This clause provides details on how the IN-CSE oneM2M <locationPolicy>, <container> and <contentInstance> resources are used to interwork with the SCEF API and provide location monitoring capability for an ASN/MN-CSE or ADN-AE hosted on a 3GPP UE. To interwork the 3GPP location reporting functionality with oneM2M, the <locationPolicy>, <container> and <contentInstance> resources and corresponding procedures are used.

### 7.5.2 Resource Structure

Refer to the clause 9.6.10 Resource Type locationPolicy of TS-0001[1]

### 7.5.3 ServiceFlow

#### 7.5.3.1 Location updating triggered by retrieval

Figure 7.5.3.1-1: Service Flow of Location updating triggered by retrieving

Step 001: The IN-AE sends a < locationPolicy> create request to IN-CSE with the following settings:

- locationSource shall be set to Network Based.

- locationUpdatePeriod shall not be present or set to 0.

- locationTargetID shall be set to the M2M-Ext-ID of the targeted UE hosting an ASN/MN-CSE or ADN-AE.

- locationServer shall not be present.

- locationContainerID shall not be present.

- locationInformationType shall be set to position fix.

- retrieveLastKnownLocation shall be configured with either True or False based on the requirements of the IN-AE.

- locationUpdateEventCriteria shall be not present.

Step 002:  IN-CSE shall create the <locationPolicy> resource and corresponding <container> resource for storing location information based on the procedure specified in clause 10.2.9 of oneM2M TS-0001[i.9].

Step 003: The IN-AE sends a RETRIEVE request to the <latest> child resource of the <container> resource created in Step 002.

Step 004: The IN-CSE checks the locationSource attribute of the <locationPolicy> resource that is linked to the <container> targeted by the RETRIEVE request in Step 003.  If the locationSource attribute is set to Network Based and the locationUpdatePeriod attribute is set to zero or NULL, then the IN-CSE shall issue a Location Monitoring Request to the SCEF. The request shall contain the following information as specified in 3GPP TS 23.682 [i.5].

- External Identifier shall be set to the locationTargetID.

- SCS Identifier shall be set to a value that is prearranged between the Service Provider and MNO.

- SCS Reference ID shall be configured by the IN-CSE to refer to a specific transaction initiated by the IN-CSE towards the SCEF; SCS Reference ID is stored by the SCEF

- Monitoring Type shall be set to “Location Reporting”.

- Monitoring Destination Address shall be set to the IP address of the IN-CSE.

- Location Type shall be set to”Current Location”.

- Accuracy shall be set set by the IN-CSE (e.g. based on a pre-provisioned policy setting).

NOTE: The format of Accuracy has not yet been defined in 3GPP TS 23.682 [i.5].

Step 005-006: The Location Monitoring Request is processed by the Underlying 3GPP Network based on the procedure defined in 3GPP TS 23.682 [i.5].

Step 007: The SCEF sends the Monitor Indication to the IN-CSE.

Step 008: The IN-CSE shall create a new <contentInstance> child resource of the <container> targeted by the RETRIEVE request in Step 003.

Step 009b: If the Monitor Indication in Step 007 indicates a failure, then the IN-CSE shall send a Location Monitoring Request to the SCEF to get the last known location if the retrieveLastKnownLocation attribute of the <locationPolicy> is set to TRUE.  The request shall contain the following information as specified in 3GPP TS 23.682 [i.5].

- External Identifier shall be locationTargetID.

- SCS Identifier shall be set to a value that is prearranged between the Service Provider and MNO.

- SCS Reference ID shall be configured by the IN-CSE to refer to a specific transaction initiated by the IN-CSE towards the SCEF; SCS Reference ID is stored by the SCEF

- Monitoring Type shall be set to “Location Reporting”.

- Monitoring Destination Address shall be set to the IP address of the IN-CSE.

- Location Type shall be set to” Last Known Location”.

- Accuracy shall be set set by the IN-CSE (e.g. based on a pre-provisioned policy setting).

NOTE: The format of Accuracy has not yet been defined in 3GPP TS 23.682 [i.5].

Step 010b-011b: The Location Monitoring Request is processed by the Underlying 3GPP Network based on the procedure defined in3GPP TS 23.682 [i.5].

Step 012b: The SCEF sends the Monitor Indication to the IN-CSE.

Step 013b: The IN-CSE shall create a new <contentInstance> child resource of the <container> targeted by the RETRIEVE request in Step 003.

Step 014: The IN-CSE sends the retrieve response to IN-AE. The response shall include the newly created <contentInstance> .

#### 7.5.3.2 Location updating triggered by location change

Figure 7.5.3.2-1: Service Flow of location updating triggered by location change

Step 001: The IN-AE sends <locationPolicy> CREATE request to IN-CSE with the following settings:

- locationSource shall be set to Network Based.

- locationUpdatePeriod shall not be present or set to 0.

- locationTargetID shall be set to the M2M-Ext-ID of the targeted UE hosting an ASN/MN-CSE or ADN-AE.

- locationServer shall not be present.

- locationContainerID shall not be present.

- locationInformationType shall be set to position fix.

- retrieveLastKnownLocation shall be configured with either True or False based on the requirements of the IN-AE .

- locationUpdateEventCriteria shall be set to LocationChange

Step 002:  IN-CSE shall create the <locationPolicy> resource and corresponding <container> resource for storing location information based on the procedure specified in clause 10.2.9 of oneM2M TS-0001[i.9].

Step 003: The IN-CSE sends Monitoring Request to SCEF. The request contains information as specified in 3GPP TS 23.682 [i.5]. Such information includes (but is not limited to):

- External Identifier shall be set to the locationTargetID.

- SCS Identifier shall be set to a value that is prearranged between the Service Provider and MNO.

- SCS Reference ID shall be configured by the IN-CSE to refer to a specific transaction initiated by the IN-CSE towards the SCEF; SCS Reference ID is stored by the SCEF

- Monitoring Type shall be set to “Location Reporting”.

- Monitoring Destination Address shall be set to the IP address of the IN-CSE.

- Location Type shall be set to”Current Location”.

- Accuracy shall be set set by the IN-CSE (e.g. based on a pre-provisioned policy setting).

NOTE: The format of Accuracy has not yet been defined in 3GPP TS 23.682 [i.5].

Step 004-Step 005: The Location Monitoring Request is processed by the Underlying 3GPP Network based on the procedure defined in 3GPP TS 23.682 [i.5].

Step 006: The SCEF sends the Monitor Indication to the IN-CSE to acknowledge acceptance of the Monitoring Request.

Step 007: The IN-AE sends the <subscription> CREATE request of <container> which stores location information to the IN-CSE.

Step 008: The IN-CSE sends the response to the IN-AE.

Step 009: The Underlying 3GPP Network sends a Monitoring Indication to SCEF when detecting a change in location of the UE hosting an ASN/MN-CSE or ADN-AE.

Step 010: The SCEF sends a Monitoring Indication message to the IN-CSE to notify the IN-CSE of a change in location of the UE hosting an ASN/MN-CSE or ADN-AE.

Step 011: IN-CSE creates a new <contentInstance> child resource within the <container> created in Step 002.

Step 012: IN-CSE sends NOTIFY request to the IN-AE about the <container>  change information.

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?