| CHANGE REQUEST |
| --- |
| Meeting ID:* | ARC30 |
| Source:* | Catalina Mladin, Convida, mladin.catalina@convidawireless.com Chonggang Wang, Convida, wang.chonggang@convidawireless.com |
| Date:* | 2017-07-11 |
| Reason for Change/s:* | Implements agreements about division of content for semantics between TS-0001 and TS-0026 |
| CR against: Release* | Release 3 |
| CR against: WI* | Active WI-0053 for Rel-3 Enhancements on Semantic Support MNT maintenance / < Work Item number(optional)> Is this a companion CR? Yes No Companion CR number: (Note to Rapporteur - use latest agreed revision) Is this a mirror CR? Yes No Mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0001, v3.6.0 |
| Clauses * | 10.2.14, 2.1 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | TS-0026 |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Introduction

The discussion around ARC-2017-0265 resulted in the following agreements:

- Specialized resources for semantics should be defined in TS-0001 section 9.6

- CRUD procedures for specialized semantic resources should be defined in TS-0034

- Semantic management in TS-0001 (section 10.2.14) should be kept short and point toward TS-0034 content.

This contribution proposes changes to implement the agreements above.

R01 makes some additions for ontologies and validation

R02 correction to references

### -----------------------Start of change 1-------------------------------------------

#### 10.2.7.12	Retrieve <semanticFanOutPoint>

This procedure shall be used for performing semantic discovery or semantic query procedures using the descriptor content of all member <semanticDescriptor> resources belonging to an existing <group> resource. For detailed descriptions of this procedure see [11] Clause 6.2

### -----------------------End of change 1-------------------------------------------

### -----------------------Start of change 2-------------------------------------------

### 10.2.14	Semantics management

Semantics management is performed for the purpose of leveraging CRUD operations on semantic-related resources to enable semantic functionalities in service layer (e.g. enhancing the meaning of resources and data in the system).

Table 10.2.14-1 summarizes the specialized resource types defined for the purpose of providing semantic enablement, providing references to the resource type definition clause. The table also provides references to the corresponding CRUD procedures.

Table 10.2.14 -1: Specialized resource types for semantic management

| Resource type | Description | Resource Type Reference | CRUD procedures |
| --- | --- | --- | --- |
| <semanticDescriptor> | Resource type used for annotating resources with semantic descriptions, providing the means for resource discovery in a semantically- aware fashion and for semantic queries | 9.6.30 | [11] Clause 6.c1 |
| <semanticFanOutPoint> | Virtual resource type used to form an overall graph based on the content of the semantic descriptors associated with the members of the group, for the purpose of performing semantic resource discovery and semantic query | 9.6.14a | [11] Clause 6.c2 |
| <semanticMashupJobProfile> | Resource type describing the profile and necessary information (e.g. input parameters, member resources, mashup function, output parameters) required for a specific mashup service. | 9.6.x1 | [11] Clause 6.c3 |
| <semanticMashupInstance> | Resource type describing a mashup instance based on mashup request and implementing the semantic mashup function. Each instance corresponds to a semantic mashup job profile . | 9.6.x2 | [11] Clause 6.c4 |
| <mashup> | Virtual resource type used for triggering a calculation and generation of the mashup result based on its parent resource. | 9.6.x3 | [11] Clause 6.c5 |
| <semanticMashupResult> | Resource type storing the result generated when it executes a semantic mashup operation | 9.6.x4 | [11] Clause 6.c6 |
| <ontology> | Resource type storing the representation of an ontology | 9.6.x5 | [11] Clause 6.c7 |
| <ontologyRepository> | Resource type for storage of all ontology representations | 9.6.x6 | [11] Clause 6.c8 |
| <semanticValidation> | Virtua resource type used to trigger validation of semantic content | 9.6.x7 | [11] Clause 6.c9 |

Table 10.2.14-2 summarizes the specialized procedures defined for the purpose of providing semantic enablement, providing references to the TS-0034 [11] clauses where the detail procedural descriptions are provided.

Table 10.2.14-2: Specialized procedures and functions for semantic management

| Procedure | Description | Reference |
| --- | --- | --- |
| Access Control for Semantic Content | Functionality enabling the use of access control information applicable to resources for accessing RDF triple content when executing semantic operations. | [11] Clause 6.c6 |
| Semantics Annotation | Functionality for providing semantic description for resources and content | [11] Clause 6.c6 |
| Semantic Filtering and Discovery | Procedures for the discovery of resources and semantic information, respectively, based on the semantic annotation. | [11] Clause 6.c6 |
| Semantics Mash-up | Procedures enabling the creation, execution and result retrieval of functions based on semantic mashup. | [11] Clause 6.c6 |
| Semantic Query | Procedures for directly retrieving both explicitly and implicitly derived information based on syntactic, semantic and structural information contained in semantic content data (such as RDF triples). The result of a semantic query is the semantic information/knowledge for answering/matching the query. | [11] Clause 6.c6 |
| Semantic Validation | Procedures enabling the validation of semantic content. | [11] Clause 6.c6 |
| Ontology Management | Procedures enabling the use and management of ontologies. | [11] Clause 6.c6 |

### ------------------------End of change 2--------------------------------------------

### ------------------------Start of change to references --------------------------------------------

# 2	References

## 2.1	Normative references

References are either specific (identified by date of publication and/or edition number or version number) or non-specific. For specific references, only the cited version applies. For non-specific references, the latest version of the reference document (including any amendments) applies.

The following referenced documents are necessary for the application of the present document.

[1]	oneM2M TS-0011: "Common Terminology".

[2]	oneM2M TS-0003: " Security Solutions".

[3]	oneM2M TS-0004: "Service Layer Core Protocol Specification".

[4]	W3C RDF 1.1 Concepts and Abstract Syntax.

[5]	W3C SPARQL 1.1 Query Language.

[6]	oneM2M TS-0012: "oneM2M Base Ontology".

[7]	oneM2M TS-0021: "oneM2M and AllJoyn Interworking".

[8]	oneM2M TS-0023: "Home Appliances Information Model and Mapping".

[9]	oneM2M TS-0016: “Secure Environment Abstraction”

[10]	oneM2M TS-0022: "Field Device Configuration".

[11]	oneM2M TS-0034: "Semantic Support".

### ------------------------End of change to references --------------------------------------------