| CHANGE REQUEST |
| --- |
| Meeting ID:* | ARC30 |
| Source:* | Josef Blanz, Qualcomm Inc., jblanz@qti.qualcomm.com |
| Date:* | 2017-07-09 |
| Reason for Change/s:* | Progress Work Item WI0056 on “Evolution of Proximal IoT Interworking” to the point we can freeze stage 2. |
| CR against: Release* | Rel-3 |
| CR against: WI* | Active WI-0056 “Evolution of Proximal IoT Interworking” MNT maintenance / < Work Item number(optional)> Is this a companion CR? Yes No Companion CR number: (Note to Rapporteur - use latest agreed revision)Is this a mirror CR? Yes No Mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0033 v0.0.2 |
| Clauses * | 6 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | N/A |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

In order to progress the work on WI0056, text for resource mapping rules in clause 7 of TS-0033 are proposed. The main goal is to implement the changes already discussed in ARC 29.4 with more consistent headings and some further editorial improvements.

### -----------------------Start of change 1-------------------------------------------

# 7	Representation of non-oneM2M entities in Proximal IoT networks

.

## 7.1	Representation of non-oneM2M Proximal IoT Devices

From a device management perspective in oneM2M, a device is represented using a <node> resource. All management related capabilities of a device are then represented using <mgmtObj> child resources of a <node> resource. This principle shall also be applied for non-oneM2M Proximal IoT devices (which NoDNs), i.e. all aspects of device management of a device subject to device management methods defined in oneM2M should be exposed by using <mgmtObj> child resources of a <node> resource. The <node> resource instances representing device management aspects of non-oneM2M Proximal IoT devices shall be created by the responsible IPE on the IPE’s Registrar CSE.

If the device complies to oneM2M-defined information models – such as the ones defined in TS-0023 [3] – the device should be represented using the respective specializations of  resources specified in oneM2M. For example, a home domain device for a light as defined in TS-0023  is represented using the corresponding specializations of <flexContainer> defined by the [deviceLight] resource type. If the information model of the device is not defined by oneM2M, a <flexContainer> may also be used with its containerDefinition attribute configured with a URI linking to the schema definition for that device type specified by the respective organization. Also if the <flexContainer> resource represents the device, the resourcemay be linked with the corresponding <node> resource that is used to reflect device management aspects of the device, if applicable. The instances of specializations of <flexContainer> resource types representing non-oneM2M Proximal IoT devices shall be created by the responsible IPE on the IPE’s Registrar CSE. The preferred parent resource for such specialization of <flexContainer> resource instances is the IPE’s own <AE> resource instance. The linkage between an instance of a specialization of the <flexContainer> resource type, representing a non-oneM2M Proximal IoT device, and the corresponding <node> resource instance, that is used to reflect device management aspects of the device, shall be established as follows:

- If present, a nodeLink attribute of the <flexContainer> specialization instance, representing the non-oneM2M Proximal IoT device, shall point to the <node> resource instance, that is used to reflect device management aspects of that device.

- Otherwise, a mgmtLink attribute of the <flexContainer> specialization instance, representing the non-oneM2M Proximal IoT device, shall point to a <deviceInfo> resource instance that is a child of the <node> resource instance, that is used to reflect device management aspects of that device.

For devices that don’t follow any standardized information model nor have any management requirements, there is no distinct resource types to be instantiated in the oneM2M system for the representation of the device.

## 7.2	Representation of non-oneM2M Proximal IoT Applications

A general pattern in oneM2M is the use of instances of an <AE> resource to represent applications running on devices/gateways if needed. In addition, all services provided by these applications should be represented as child resources of the respective <AE> resource instance. By browsing the child resources of an <AE> resource instance, it’s easily understood what are all the services provided by the respective application. If an application de-registers (i.e. the <AE> resource instance is deleted) from the system, all the resources representing its services are also deleted since they are child resources of the <AE> instance. For example, if an application is to report temperature data, after registration, an <AE> resource instance representing the application is created on the registrar CSE. The data reporting service is then e.g. represented as a <container> or <flexContainer> child resource of the <AE> resource. If the <AE> resource gets deregistered, the <container> or <flexContainer> resource is deleted at the same time. The same principles should be applied to represent non-oneM2M Proximal IoT Applications on NoDN(s) and the services they provide (see next sub-clause).

According to the specific needs in a service deployment, the service provider may deploy one or multiple application instances on one device. Each NoDN application instance that needs to be exposed to the oneM2M system shall be represented by one <AE> resource instance and be assigned with one unique AE-ID to identify the application instance.

Depending on the type of oneM2M node hosting an application, its <AE> resource instance(s) may be hosted by different types of CSEs in the oneM2M system:

- For applications on ASNs and MNs, the corresponding <AE> resources shall be created under the <CSEBase> of the corresponding ASN-CSE and MN-CSE, accordingly.

- For applications on an ADN, the corresponding <AE> resources shall be created under the <CSEBase> of the Registrar CSE of the ADN (which may be an MN-CSE or IN-CSE).

If there is a need to represent applications on interworked NoDNs – which is the case if the interworked applications need to be identifiable for the purpose of service subscription, charging, access control, authentication, App-ID registry, etc. – then one or more <AE> resource instances shall be created to represent those applications. The IPE is responsible to issue requests to the oneM2M system on behalf of the interworked applications by using the AE-ID of the created <AE> resources. Care should be taken for determining the number of necessary security associations for the created <AE> resources. No matter if there is a need to represent the applications on interworked NoDNs or not, at least one <AE> resource shall be created as the representation of the IPE that is responsible for accessing the NoDN services.

When a non-oneM2M Proximal IoT application running on a NoDN is represented by an <AE> resource instance and at the same time device management aspects of that NoDN are represented by a <node> resource instance, the nodeLink attribute of that <AE> resource instance shall point to the <node> resource instance corresponding to the device management aspects of that NoDN. Also the reverse linkage via the hostedAELinks attribute of the <node> resource shall be established.

Editor’s Note: Determination of how to represent a Device that hosts multiple applications still needs to be specified. Right now the Device resource that is represented as a child of an AE might be incorrect – we might want to expose the Device resource and have the AE resources as their children. It might be necessary to allow creation of <AE> resource instances under resources representing a device, e.g. under an instance of  a specialization of <flexContainer> that represents a device. Another option would be to use some form or linkage. Linkage between <AE> and <node> is already supported… what is missing is linkage between <AE> and <flexContainer>. Such a linkage would probably need to be bi-directional in order to find out which applications are on a device as well as on which device is a specific application. Parent/child would probably be simpler. Need for discussion. If a <node> ressouce is always used when a <flexContainer> is representing a device (true for all in TS-0023), then we got all the linkage we need.

## 7.3	Representation of non-oneM2M Proximal IoT Services

## oneM2M defines different types of  resources that may be used to represent services provided by a device. When representing non-oneM2M Proximal IoT services from interworked NoDN(s), proper resource types shall be chosen since the misusage of resource types for representing services may cause interoperability problems. General guidelines for resource representation of different services are as follows:

## For device management services: Specialized <mgmtObj> resource types as specified in oneM2M TS-0001 [2] and oneM2M TS-0022 [4], and <mgmtCmd>, <execInstance> as specified in oneM2M TS-0001 [2] shall be used. These resources shall be created by the responsible IPE as child resources of the <node> resource which represents the managed device (see clause 7.1).

## Home appliance services: Specialized <flexContainer> resource types for moduleClasses as specified in oneM2M TS-0023 [3] shall be used to represent those services.

- Data management services (not covered by TS-0023 [3]): <container>, <contentInstance>, <timeSeries>, <timeSeriesInstance> as specified in oneM2M TS-0001 shall be used.

## Location services: <locationPolicy>, <container>, <contentInstance>, <latest>, <oldest> as specified in oneM2M TS-0001 [2] shall be used.

## Group services: <group>, <fanOutPoint>, <localMulticastGroup> as specified in oneM2M TS-0001 [2] shall be used

## Event/notification services: <subscription>, <notificationTargetSelfReference>, <notificationTargetMgmtPolicyRef>, <notificationTargetPolicy>, <policyDeletionRules> as specified in oneM2M TS-0001 [2] shall be used.

## Security services: <accessControlPolicy>, <dynamicAuthorizationConsultation>, <role>, <token>, <authorizationDecision>, <authorizationPolicy>, <authorizationInformation> as specified in oneM2M TS-0001 [2] and oneM2M TS-0003 [5] shall be used

- Semantic services: <semanticDescriptor>, <ontologyRepository>, <ontology>, <semanticValidation>, <semanticMashupJobProfile>, <semanticMashupInstance>, <mashup>, <semanticMashupResult>  as specified in oneM2M TS-0001 [2] and oneM2M TS-0034 [6] shall be used.

## Charging services: <statsConfig>, <eventConfig>, <statsCollect> as specified in oneM2M TS-0001 [2] shall be used.

## Editor’s note: the resource types above need to be updated according to latest progress before publication.

There are two ways of expressing relationships between resources as well as relationships between the services these resources represent: Parent-child relationship and linkage relationship. The linkage relationship only applies to specific oneM2M resource types such as <accessControlPolicy>, announced resources, and <mgmtObj> resources, etc.

### The parent-child relationship of resources shall be used when the service represented by the child resource cannot exist independent of the services represented by the parent resource. If the parent service is deleted, the child services shall be deleted automatically.

### -----------------------End of change 1---------------------------------------------

# Comments

All changes in different colours below indicate changes relative to the contributions already discussed and improved during ARC29.4 (300R02, 301R03, 305R02)

check with Andreas to see if moduleClass can exist without deviceModel for e.g. KNX

it doesn’t exist yet.

Do we want to enforce ALLWAYS to use a <node> resource when a <flexContainer> represents a device? So either <node> resource only… or <flexContainer> plus <node> resource.

Allows for the existing <flexContainer> specializations in TS0023 to used the mgmtLink as well as other – maybe new – specializations of <flexContainer> to use a nodeLink.

not to represent at all?

but service could be represented independently

Do we want this <node> resource to exist when a <flexContainer> is used to represent the device?

感觉跟lifcycle没有本质区别。deployment dependency是形成lifecycle dependency的原因之一。