| CHANGE REQUEST |
| --- |
| Meeting ID:* | ARC 30 |
| Source:* | Francisco Sang-Eon Kim, KT, kim.sangeon@kt.com |
| Date:* | 2017-07-11 |
| Reason for Change/s:* | See the introduction. |
| CR against: Release* | Release 2 |
| CR against: WI* | Active <Work Item number> MNT maintenance WI-0049 Is this a mirror CR? Yes No mirror CR number: ARC-2017-0288R03 STE Small Technical Enhancements / WI-0050 |
| CR against: TS/TR* | TS-0001-V2.14.0 |
| Clauses * | 9.6.7 Resource Type contentInstance |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) |  |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The contentInfo attribute is introduced to <contentInstance> resource by ARC-2014-1670R01 since TS-0001-V1.3.0

TS-0001 specifies contentInfo at clause 9.6.7 as follows:

Information on the content that is needed to understand the content.

This attribute is a composite attribute.

It is composed first of an Internet Media Type (as defined in the IETF RFC 6838) describing the type of the data, and second of an encoding information that specifies how to first decode the received content.

Both elements of information are separated by a separator defined in [i.2]

ARC-2014-1670R01 explains at introduction as following.

For example, we would have: “application/json; encoding: plain” or “application/xml; encoding: base64”

On the other hand, data type of contentInfo specifies at clause 6.3.3 in TS-0004.

A string consisting of a media type followed by a m2m:encodingType and optional m2m:contentSecurity, each separated by ':' character.

If the m2m:contentSecurity value is not present, then the preceding ':' shall also be not present. If the m2m:contentSecurity value is not present then this has the same interpretation as a value of 0 for m2m:contentSecurity.

Internet Media Type is defined in the RFC 6838.

A list of media type can be found at https://www.iana.org/assignments/media-types/media-types.xhtml

Encoding Type is defined at clause 6.3.4.2.28 in TS-0004. It is enumerated data type as specified at Table 6.3.4.2.28-1 as following.

| Value | Interpretation | Note |
| --- | --- | --- |
| 0 | Plain - no transfer encoding is applied |  |
| 1 | base64 encoding (see [9]) is applied on string data |  |
| 2 | base64 encoding (see [9]) is applied on binary data |  |

Content Security is defined at clause 6.3.4.2.38 in TS-0004. It is enumerated data type as specified at Table 6.3.4.2.38-1 as following.

| Value | Interpretation | Note |
| --- | --- | --- |
| 0 | ESData has not been applied to the content data. |  |
| 1 | ESData using JWE and/or JWS with Compact Serialization has been applied to the content data with no subsequent transfer encoding. See note 2. | See Note 3 |
| 2 | ESData using JWE and/or JWS with JSON Serialization has been applied to the content data with no subsequent transfer encoding. | See Note 4 |
| 3 | ESData using JWE and/or JWS with JSON Serialization has been applied to the content data and subsequent base64 encoding (see [9]) has been applied. | See Note 4 |
| 4 | ESData using XML encryption and/or XML-Signature has been applied to the content data has been applied with no subsequent transfer encoding. | See Note 5 |
| 5 | ESData using XML encryption and/or XML-Signature has been applied to the content data and subsequent base64 encoding (see [9]) has been applied. | See Note 5 |
| NOTE 1: See oneM2M TS-0003 [7] for details on these security protocols NOTE 2: JWE and/or JWS with Compact Serialization is almost entirely base64URL encoded by default - see m2m:e2eCompactJWS and m2m:e2eCompactJWE in Table 6.3.3. Consequently, there is no option for additional base64 encoding of JWE and/or JWS with Compact Serialization. NOTE 3: The ESData envelope (see oneM2M TS-0003 [7]) in this case has media type application/jose. NOTE 4: The ESData envelope in this case has media type application/jose+json. NOTE 5: The ESData envelope in this case has media type application/xenc+xml or application/xml (the latter is the media type for XML Signature). |

## Problem

The contentInfo attribute is not consistent between TS-0001 and TS-0004.

A description of  contentInfo is:

- TS-0001	Media Type (RFC 6838) encoding information

- TS-0004 	Media Type (RFC 6838): encoding information (encodingType):contentSecurity

An example of  contentInfo is:

- TS-0001	“application/json; encoding: plain”

- TS-0004 	application/xml:1

application/xml:1:0

application/xml:1:5

Example

Figure 1 : A conceptual example of procedures for <contentInstance> to create

The Figure 1 shows a conceptual example of procedure for <contentInstance> to create operation.

An Originator can send a Request message at step 1 in Figure 1 as an example 1 which is an example of  json serialization. It is not clear contentInfo attribute at current specification.

A Receiver processes for Request message at step 2.  After that Receiver responses as an example 2 at step 3.

{

"rqp": {

"to": "//example.net/C190XX7T",

"fr": "C2345",

"op":  1,

"rqi": "A1234",

"rt": 4,

"pc": {

"m2m:cin": {

"rn": "car",

"lbl": "speed",

"dgt": "20170616T112032",

"contentInfo":  "not clear",

"con": {

"thing": "car",

"status": "drive",

"speed":"100"

}

}

}

}

}

Example 1 <code for Request message to create>

{

"rsp": {

"rsc": 2001,

"rqi": "A1234"

}

}

Example 2 <code for Response message to create>

The content information at the example 1 and example 4 has following information implicitly.

Case A:

- Media type is “application/json”

- Encoding type is “Plain”

- contentSecurity is none

{

"thing": "car",

"status": "drive",

"speed": "100"

}

However, there are many ways to respresent content in accordance with Media type, Encoding type and content security.

Case B:

- Media type is “application/json”

- Encoding type is “Base64”

- contentSecurity is none

ew0KCSJ0aGluZyI6ICJjYXIiLA0KCSJzdGF0dXMiOiAiZHJpdmUiLA0KCSJzcGVlZCI6ICIxMDAiDQp9

Case C:

- Media type is “application/xml”

- Encoding type is “Plain”

- contentSecurity is none

<con>

<thing>car</thing>

<status>drive</status>

<speed>100</speed>

</con>

Case D:

- Media type is “application/XML”

- Encoding type is “Base64”

- contentSecurity is none

PGNvbj4NCgk8dGhpbmc+Y2FyPC90aGluZz4NCgk8c3RhdHVzPmRyaXZlPC9zdGF0dXM+DQoJPHNwZWVkPjEwMDwvc3BlZWQ+DQo8L2Nvbj4=

Case E:

- Media type is “text/csv”

- Encoding type is “Plain”

- contentSecurity is none

car, drive, 100

Case D:

- Media type is “test/csv”

- Encoding type is “Base64”

- contentSecurity is none

Y2FyLCBkcml2ZSwgMTAw

If the Receiver provides information to understand value of content attribute, the Originator can use this resource easily.

## Discussion & Proposal

Discussion on delimeter either semi-colon or colon

ARC-2014-1670R01 has not been considered data type at the discussion.

Protocol WG is specified data type with ‘:’ character as of delimeter.

Discussion on multiplicity

It should be mandatory not optional. Because any of elements is not defined by default. If this is optional and absent, content instance may not understand between Originator and Receiver.

If it should be optional, then a default value should be specified.

This CR includes a results of the discussion on ARC-2017-0288 at ARC29.4

A contentInfo attribute at <timeSeries> is more efficient than conteintInfo at every <timeSeriesInstance> in terms of processing and communication bandwidth.

A delimeter is responsible for PRO WG. Therefore, ARC WG describes just reference.

A defult value has discussed and contentInfo attribute is optional (multiplicity is 0..1)

R02 includes comments from discussion at ARC 30.

- It is recommend to use this attributes instead of define dafault for contentInfo,

- Withdraw CR2

### -----------------------Start of change 1-------------------------------------------

### 9.6.7	Resource Type contentInstance

The <contentInstance> resource represents a data instance in the <container> resource. The content of the contentInstance can be encrypted.

Unlike other resources, the <contentInstance> resource shall not be modified once created. An AE shall be able to delete a contentInstance resource explicitly or it may be deleted by the platform based on policies. If the platform has policies for contentInstance retention, these shall be represented by the attributes maxByteSize, maxNrOfInstances and/or maxInstanceAge attributes in the <container> resource. If multiple policies are in effect, the strictest policy shall apply.

The <contentInstance> resource inherits the same access control policies of the parent <container> resource, and does not have its own accessControlPolicyIDs attribute.

Figure 9.6.7-1: Structure of <contentInstance> resource

The <contentInstance> resource shall contain the child resources specified in table 9.6.7-1.

Table 9.6.7-1: Child resources of <container> resource

| Child Resources of <contentInstance> | Child Resource Type | Multiplicity | Description | <contentInstanceAnnc> Child Resource Types |
| --- | --- | --- | --- | --- |
| [variable] | <semanticDescriptor> | 0..n | See clause 9.6.30 | <semanticDescriptor>, <semanticDescriptorAnnc> |

The <contentInstance> resource shall contain the attributes specified in table 9.6.7-2.

Table 9.6.7-2: Attributes of <contentInstance> resource

| Attributes of <contentInstance> | Multiplicity | RW/ RO/ WO | Description | <contentInstanceAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3. | NA |
| resourceID | 1 | RO | See clause 9.6.1.3. | NA |
| resourceName | 1 | WO | See clause 9.6.1.3. | NA |
| parentID | 1 | RO | See clause 9.6.1.3. | NA |
| labels | 0..1 (L) | WO | See clause 9.6.1.3. | MA |
| expirationTime | 1 | WO | See clause 9.6.1.3. | NA |
| creationTime | 1 | RO | See clause 9.6.1.3. | NA |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3. | NA |
| stateTag | 1 | RO | See clause 9.6.1.3. The stateTag attribute of the parent resource should be incremented first and copied into this stateTag attribute when a new instance is added to the parent resource. | OA |
| announceTo | 0..1 (L) | WO | See clause 9.6.1.3. | NA |
| announcedAttribute | 0..1 (L) | WO | See clause 9.6.1.3. | NA |
| dynamicAuthorizationConsultationIDs | 0..1 (L) | RW | See clause 9.6.1.3. | OA |
| creator | 0..1 | RO | See clause 9.6.1.3. | NA |
| contentInfo | 0..1 | WO | This attribute contains information to understand the contents of content attribute. It shall be composed of two mandatory components consisting of Internet Media Type (as defined in the IETF RFC 6838) and an encoding type. In addition, an optional content security component may also be included. The format of this attribute is defined in oneM2M TS-0004 [3]. This attribute should be used so that AEs can understand the content. | OA |
| contentSize | 1 | RO | Size in bytes of the content attribute. | OA |
| contentRef | 0..1 | RW | This attribute contains a list of name-value pairs. Each entry expresses and associative reference to a <contentInstance> resource. The name of the entry indicates the relationship and the value of the entry the indicates reference (URI) to the resource. | OA |
| ontologyRef | 0..1 | WO | A reference (URI) of the ontology used to represent the information that is stored in the contentInstances resources of the <container> resource. If this attribute is not present, the contentInstance resource inherits the ontologyRef from the parent <container> resource if present (see note). | OA |
| content | 1 | WO | Actual content of a contentInstance. This content may be opaque data for understandable with the help of the contentInfo. This may, for example, be an image taken by a security camera, or a temperature measurement taken by a temperature sensor. | OA |
| NOTE: Access to this URI is out of scope of oneM2M. |

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2---------------------------------------------

#### 10.2.4.7	Create <contentInstance>

This procedures shall be used for creating a <contentInstance> resource.

Table 10.2.4.7-1: <contentInstance> CREATE

| <contentInstance> CREATE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc'. |
| Information in Request message | All parameters defined in table 8.1.2-3 apply with the specific details for: Content: The resource content shall provide the information as defined in clause 9.6.7. |
| Processing at Originator before sending Request | According to clause 10.1.2. |
| Processing at Receiver | According to clause 10.1.2. If the newly created <contentInstance> resource violates any of the policies defined in the parent <container> resource (e.g. maxNrOfInstances or maxByteSize), then the oldest <contentInstance> resources shall be removed from the <container> to enable the creation of the new <contentInstance> resource. |
| Information in Response message | All parameters defined in table 8.1.3-1 apply with the specific details for: Content: Address of the created <contentInstance> resource, according to clause 10.1.2. |
| Processing at Originator after receiving Response | According to clause 10.1.2. |
| Exceptions | According to clause 10.1.2. |

### -----------------------End of change 2---------------------------------------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?