| CHANGE REQUEST |
| --- |
| Meeting ID:* | ARC 30.2 |
| Source:* | Catalina Mladin, Convida, mladin.catalina@convidawireless.com Chonggang Wang, Convida, wang.chonggang@convidawireless.com Xu Li, Convida, li.xu@convidawireless.com |
| Date:* | 2017-08-02 |
| Reason for Change/s:* | Introduce the Semantics CSF |
| CR against: Release* | Release 3 |
| CR against: WI* | Active WI-0053 for Rel-3 Enhancements on Semantic Support MNT maintenance / < Work Item number(optional)> Is this a companion CR? Yes No Companion CR number: (Note to Rapporteur - use latest agreed revision)Is this a mirror CR? Yes No Mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0001, v3.7.0 |
| Clauses * | 6.2.x (new) |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | <TS/TR number>, <Version Number>, and <Description on which aspect should be reflected in this TS/TR> |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Introduction

### -----------------------Start of change 1-------------------------------------------

### 6.2.x	Semantics

#### 6.2.x.1	General Concepts

The Semantics (SEM) CSF assists applications in managing semantic information which provides the system with value-add meaning of the data and resources. The SEM CSF functionality is based on semantic descriptions and supports features such as: annotation, resource filtering and discovery, querying, validation, mash-up, reasoning,  analytics, etc. The SEM CSF also provides input for Access Control applied to semantic content and is responsible for the management of ontologies.

#### 6.2.x.2	Detailed Descriptions

The SEM CSF uses semantic descriptions pertaining to resources based on ontologies which annotate the corresponding resources. The SEM CSF handles the processes of discovery of resources and querying of semantic information, respectively, based on syntactic, semantic and structural information contained in semantic content data (such as RDF triples. When executing semantic operations and accessing RDF triple content, the SEM CSF uses access control information applicable to resources.

The SEM CSF enables also the creation, execution and result retrieval of functions based on semantic mashup, the validation of semantic content, and the use and management of ontologies.

### ------------------------End of change 1--------------------------------------------