| CHANGE REQUEST |
| --- |
| Meeting ID:* | ARC 31 |
| Source:* | Bob Flynn, Convida Wireless, Flynn.Bob@Convidawireless.com Dale Seed, Convida Wireless, Seed.Dale@Convidawireless.com |
| Date:* | 2017-09-09 |
| Contact:* |  |
| Reason for Change/s:* | Proposes changes to accessControlObjectDetails |
| CR against: Release* | Release 3 |
| CR against: WI* | Active <Work Item number> MNT maintenance / < Work Item number(optional)> Is this a companion CR? Yes No Companion CR number: (Note to Rapporteur - use latest agreed revision)Is this a mirror CR? Yes No Mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004V3.7 |
| Clauses * | Section 9.6.2.4 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | NA |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

# As per TS0001v2_15_0, section 9.6.2.4 accessControlObjectDetails functionality is limited to create operation only. This contribution extends this functionality for other primitive operation as well. i.e. DISCOVER, RETRIEVE, UPDATE and DELETE.

## ----------------------- Start of change 1 -----------------------

#### 9.6.2.4	accessControlObjectDetails

The accessControlObjectDetails is an optional parameter of an access control rule that may be used to specify the types of resources and/or child resources that the access control rule applies to.  For example, allow deletion of subscription resources but not container resources.  The accessControlObjectDetails parameter shall consist of the elements listed in table 9.6.2.4-1.

For the case when accessControlOperations includes DISCOVER, RETRIEVE, UPDATE or DELETE, accessControlObjectDetails specifies a subset of resource types to which the DISCOVER, RETRIEVE, UPDATE or DELETE access control rule applies.  For this case, the resourceType and specialization elements shall specify the type of resource or specialization for which the DISCOVER, RETRIEVE, UPDATE or DELETE access control rule applies. The childResourceType shall not be verified for these operations.

For the case when accessControlOperations includes CREATE, the accessControlObjectDetails specifies a subset of child resource types of the targeted resource for which the CREATE access control rule applies.  For this case, the childResourceType element shall specify the type of child resources or specializations for which the CREATE access control rule applies.  The resourceType and specialization elements are optional in this case. If either the resourceType or specialization element is present in accessControlObjectDetails, the CSE shall match the type of resource or specialization of the targeted resource with the value specified in the resourceType or specialization element.  Further checking of childResourceType shall be done only if the resourceType or specialization match occurs. However, if the resourceType and specialization elements are not provided, only childResourceType match shall be performed.  Once a child resource is created, the Access Control Policies assigned directly to it shall apply.

Table 9.6.2.4-1: Types of Parameters in accessControlObjectDetails

| Name | Description |
| --- | --- |
| resourceType | List of Identifiers of the resource types to which this access control rule applies |
| specialization | When the resourceType is mgmtObj or flexContainer, list of the identifiers of the specializations as defined by mgmtDefinition or containerDefinition attribute, respectively, shall be specified. |
| childResourceType | List of child resource types and/or the identifiers of the specializations. The identifiers of the specializations shall be specified when the resourceType is mgmtObj or flexContainer. This shall be used only when, one of the accessControlOperations is CREATE. |

## ----------------------- End of change 1 -----------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?