## Slide 1: NIDD Discussion Points
Group Name: ARC WG
Source: Dale Seed, Convida Wireless Seed.Dale@ConvidaWireless.com
Mike Starsinic, Convida Wireless, Starsinic.Michael@ConvidaWireless.com
Catalina Mladin, Convida Wireless, Mladin.Catalina@ConvidaWireless.com
Meeting Date: 2017-09-18 (ARC31)
Notes: Other suggested titles:
“Benefits of oneM2M Standardization”

## Slide 2: 3GPP Defined NIDD Paths
Focus of this discussion is on these two NIDD paths
NIDD can be performed via SCEF or P-GW

## Slide 3: Some Challenges
oneM2M:
  oneM2M currently relies on underlying transports such as TCP and CoAP for the following capabilities:
    Reliable delivery of oneM2M primitives – Retries, acknowledgements, detection and elimination of duplicates
    Ordered segmentation and re-assembly of larger oneM2M primitives exceeding the MTU of underlying transports
3GPP:
  3GPP supports NIDD Reliable Delivery Service (RDS)
    NIDD RDS supports retries, acknowledgements, detection and elimination of duplicate packets
    NIDD RDS does net yet support segmentation and re-assembly
    NIDD RDS supported on SCEF NIDD path but not yet on P-GW NIDD path
  Max NIDD packet size is configured when connection is established (e.g. Can be 1300 bytes or as low as 128 bytes)
    oneM2M primitives can exceed Max NIDD packet size

## Slide 4: Study of some typical oneM2M primitive sizes
Type1 | Create REQ | Create RESP | Retrieve REQ | Retrieve RESP
AE | 662 | 425 | 293 | 562
Container | 633 | 533 | 296 | 585
contentInstance2 | 537 | 573 | 300 | 603
Subscription | 1012 | 534 | 309 | 1029
Notification | 788 | 171 |  | 
Type1 | Create REQ | Create RESP | Retrieve REQ | Retrieve RESP
AE | 490 | 272 | 159 | 442
Container | 435 | 370 | 162 | 439
contentInstance2 | 327 | 421 | 175 | 469
Subscription | 884 | 382 | 170 | 894
Notification | 711 | 83 |  | 
XML
JSON
1Measurements made on IDCC’s oneMPOWER and include mandatory attributes and typical optional attributes
2contentInstance CREATE REQ and RESP can be made smaller (see next slide)

## Slide 5: Example: <contentInstance> CREATE
{"op":"1","fr":"CAE01","to":“CSE01/C1/","rqi":“R001","pc":{"m2m:ci":{“con":“23”}},"ty":4,"rcn":"0"}
JSON <contentInstance> CREATE request = 109 bytes
{“rsc":“2001",“rqi":“R001”}
JSON <contentInstance> CREATE response : 34 bytes
A <contentInstance> CREATE request and response can be reduced down to ~100 bytes by including only the minimal number of required request & response params and small content (e.g. sensor reading)
   oneM2M primitives of this size start to look like a good fit for NIDD 
78637B226F70223A2231222C226672223A224341453031222C22746F223A2243534530312F43312F222C22727169223A2252303031222C227063223A7B226D326D3A6369223A7B22636F6E223A223233227D7D2C22747922 A342C2272636E223A2230227D
CBOR <contentInstance> CREATE request = 101 bytes
781B7B22727363223A2232303031222C22727169223A2252303031227D
CBOR <contentInstance> CREATE response : 29 bytes
oneM2M should consider adding support to make responses optional
oneM2M could also consider adding support to make responses optional altogether

## Slide 6: Some possible way forwards
  Use underlying 3GPP network for NIDD reliable delivery and segmentation and re-assembly support
    Pro – Keeps oneM2M architecture simple and symmetric with its other underlying transport bindings (CoAP, HTTP, MQTT, WebSockets)
    Con – Creates a contingency on 3GPP agreeing to enhance NIDD RDS
  Propose a new NIDD CoAP binding to the IETF for reliable delivery and segmentation and re-assembly support (similar to CoAP over SMS)
    Pro - Keeps oneM2M architecture simple and symmetric
    Con – Adds a layer of encapsulation & overhead between oneM2M and NIDD
    Con – Creates a contingency on IETF agreeing to this
  Propose a new oneM2M adaptation layer for NIDD reliable delivery and segmentation and re-assembly support
    Pro – No dependencies on 3GPP or IETF
    Con – Adds complexity to oneM2M and makes NIDD binding non-symmetric to other underlying transport bindings

## Slide 7: SCEF NIDD Path
As long as oneM2M primitives do not exceed NIDD Max Packet Size, current SCEF + RDS is a viable NIDD option for Rel-3 timeframe
If 3GPP adds segmentation and re-assembly to RDS this enables more applications to use NIDD (i.e. oneM2M primitives > NIDD Max Packet Size)

## Slide 8: Rel-3 Proposed Way Forward
Proposal to finalize NIDD for Rel-3 at TP31 Meeting
  Develop a SCEF NIDD binding for oneM2M that uses RDS and assumes that the operator and SP have a pre-establish SLA that defines a maximum packet size that is compatible with at least oneM2M <contentInstance> primitive sizes (e.g. a 100-200 hundred bytes).
  Specify a guideline that applications sending oneM2M primitives larger than NIDD maximum packet size shall not use NIDD.
    E.g. NIDD used only for smaller oneM2M primitives such as <contentInstance> CREATE
  To reduce overhead, add support to oneM2M to make responses optional for cases where Originator doesn’t require a response
    E.g. <contentInstance> CREATE
   NIDD binding becomes straight forward for Rel-3.

## Slide 9: Rel-3 Proposed Way Forward
3GPP UE
(ASN/MN-CSE or ADN-AE
3GPP Network Entities
3GPP
SCEF
SCS
(IN-CSE)
IN-AE
Non-NIDD based initialization steps performed over Mca / Mcc
(E.g. oneM2M Registration, ACP and container creation, etc)
NIDD Config Request
NIDD Config Response
MO non-IP Request
[contentInstance CREATE Request]
MO NIDD Indication
[contentInstance CREATE Request]
NIDD Submit Request
[contentInstance CREATE Response]
Process contentInstance CREATE Request
Process contentInstance CREATE Response
MO NIDD Acknowledgement
NIDD Submit Request
[contentInstance CREATE Request]
.
.
.
MT NIDD Submit Request
[contentInstance CREATE Response]
MT NIDD Submit Response
MT non-IP Request
[contentInstance CREATE Response]
NIDD Submit Response
MT NIDD Submit Response
oneM2M should consider adding support to make oneM2M responses optional altogether.
Note - RDS acks can still be used in this case.

## Slide 10: Rel-4 Proposed Way Forward
Explore ways to streamline oneM2M primitives to make them lighter weight and better suited for transports like NIDD and lighter weight devices.
  Enable more oneM2M primitives to fit within NIDD Max Packet Size constraints
Ask 3GPP to add support for RDS segmentation and reassembly so that more applications can use NIDD (I.e. applications that want to send oneM2M primitives larger than NIDD Max Packet Size)
  Adding this support will make NIDD a more useable transport and the operators will be able to charge more if they are charging per message.
Assess if NIDD over P-GW path offers any additional value-add vs. NIDD SCEF path and how to support this in oneM2M
  E.g. Whether oneM2M should ask 3GPP (or not) to add RDS support to NIDD P-GW path such that it is symmetric to NIDD SCEF path and supports reliable delivery and fragmentation and re-assembly
Investigate interworking of non-oneM2M NIDD devices to oneM2M
  E.g. definition of NIDD-based IPEs