## Slide 1: Modifying condition tags of Filter Criteria
Group Name: ARC
Source: Kei Harada – harada.kei@lab.ntt.co.jp,
Hiroyuki Maeomichi – maeomichi.hiroyuki@lab.ntt.co.jp Meeting Date: 2018-05-22

## Slide 2: Introduction
There are some limits in Discovery with Filter Criteria parameter.
Attribute operator exists but it is used for only matching (=). For attribute of number type, it needs comparison operators.
  We already have xxBefore/After/Smaller/Bigger condition tags, but they are applied only to specific attributes (creation Time, state Tag and so on)
Complicated queries are not supported.
  Like (A=n1 OR B=n2) AND C<n3

## Slide 3: Current filterCriteria
Condition Tag | Multiplicity | Targeted Resource Attribute | Matching Condition
createdBefore | 0..1 | creationTime | creationTime < createdBefore, see clause 7.3.3.17.1
createdAfter | 0..1 |  | createdAfter ≤ creationTime , see clause 7.3.3.17.1
stateTagSmaller | 0..1 | stateTag | stateTagSmaller < stateTag, see clause 7.3.3.17.3
stateTagBigger | 0..1 |  | stateTag ≤ stateTagBigger, see clause 7.3.3.17.3
expireBefore | 0..1 | expirationTime | expirationTime < expireBefore, see clause 7.3.3.17.4
expireAfter | 0..1 |  | expireAfter ≤ expirationTime , see clause 7.3.3.17.4
sizeBelow | 0..1 | contentSize | contentSize < sizeBelow, see clause 7.3.3.17.7
sizeAbove | 0..1 |  | sizeAbove ≤ contentSize, see clause 7.3.3.17.7
attribute | 0..n | (variable) | name and value of Filter Criteria attribute matches resource attribute, see clause 7.3.3.17.9
TS-0004 7.3.3.17
GOOD POINT
  having comparison operators
  target attribute is general
mix!
Problem1:
comparison operator

## Slide 4: Proposal
Condition Tag | Multiplicity | Targeted Resource Attribute | Matching Condition
createdBefore | 0..1 | creationTime | creationTime < createdBefore, see clause 7.3.3.17.1
createdAfter | 0..1 |  | createdAfter ≤ creationTime , see clause 7.3.3.17.1
stateTagSmaller | 0..1 | stateTag | stateTagSmaller < stateTag, see clause 7.3.3.17.3
stateTagBigger | 0..1 |  | stateTag ≤ stateTagBigger, see clause 7.3.3.17.3
expireBefore | 0..1 | expirationTime | expirationTime < expireBefore, see clause 7.3.3.17.4
expireAfter | 0..1 |  | expireAfter ≤ expirationTime , see clause 7.3.3.17.4
sizeBelow | 0..1 | contentSize | contentSize < sizeBelow, see clause 7.3.3.17.7
sizeAbove | 0..1 |  | sizeAbove ≤ contentSize, see clause 7.3.3.17.7
attribute | 0..n | (variable) | name and value of Filter Criteria attribute matches resource attribute, see clause 7.3.3.17.9
attributeBelow | 0..n | (variable) | resource attribute < name and value of Filter Criteria attribute
attributeAbove | 0..n | (variable) | name and value of Filter Criteria attribute ≤resource attribute
can search <timeSeriesInstance> by dataGenerationTime attribute
can search <flexContainer> by [customAttribute]
  useful for HAIM (Datapoints are mapped with [customAttribute])
Problem1:
comparison operator

## Slide 5: Current filterCriteria
Condition Tag | Multiplicity | Targeted Resource Attribute | Matching Condition
filterOperation | 0..1 | (not applicable) | Indicates the logical operation (AND/OR) to be used for different conditions. The default value is logical AND.
contentFilterSyntax | 0..1 | (not applicable) | Indicates the Identifier for syntax to be applied for content-based discovery.
contentFilterQuery | 0..1 | content | The query string shall be specified when contentFilterSyntax parameter is present. See clause 7.3.3.17.13 for applicable syntax for content-based discovery.
TS-0004 7.3.3.17
EXAMPLE (TS-0004 7.3.3.17.0):
labels=floor1, stateTagSmaller=3, labels=floor2, filterOperation=2 will match if any of these conditions are true resource has [labels with value "floor1" OR "floor2"] OR stateTagSmaller than 3.
PROBLEM:
filterOperation cannot express complex condition, like {(A=n1 OR B=n2) AND C<n3}
1 means AND,
2 means OR
Problem2:
complicated queries

## Slide 6: Current filterCriteria
Condition Tag | Multiplicity | Targeted Resource Attribute | Matching Condition
filterOperation | 0..1 | (not applicable) | Indicates the logical operation (AND/OR) to be used for different conditions. The default value is logical AND.
contentFilterSyntax | 0..1 | (not applicable) | Indicates the Identifier for syntax to be applied for content-based discovery.
contentFilterQuery | 0..1 | content | The query string shall be specified when contentFilterSyntax parameter is present. See clause 7.3.3.17.13 for applicable syntax for content-based discovery.
TS-0004 7.3.3.17
EXAMPLE:
contentFilterSyntax: JSON_PATH_SYNTAX
contentFilterQuery: ‘heart rate’
GOOD POINT:
easily use many query expressions.
Problem2:
complicated queries

## Slide 7: LDAP filter
GOOD POINT:
easily express complex condition.
Problem2:
complicated queries
AND=‘&’
OR=‘|’
NOT=‘!’
including=‘*’
{(A=n1 OR B=n2) AND C<n3} (&(|(A=n1)(B=n2))(C<n3))
including “temperature”, AND NOT including A=n1 (&(temperature=*)(!(A=n1))
Lightweight Directory Access Protocol
LDAP filter is the filter for searching at LDAP directory

## Slide 8: Proposal
Condition Tag | Multiplicity | Targeted Resource Attribute | Matching Condition
filterOperation | 0..1 | (not applicable) | Indicates the logical operation (AND/OR) to be used for different conditions. The default value is logical AND.
contentcustomFilterSyntax | 0..1 | (not applicable) | Indicates the Identifier for syntax to be applied for content-based discovery.
contentcustomFilterQuery | 0..1 | content(variable) | The query string shall be specified when contentFilterSyntax parameter is present. See clause 7.3.3.17.13 for applicable syntax for content-based discovery.
add the LDAP filter as a candidate for the query expression
like customFilterSyntax: LDAP_filter customFilterQuery: (&(|(A=n1)(B=n2))(C<n3))
allow not only content attribute but also any attributes as target attributes
  can search in even [customAttribute] with LDAP filter
Problem2:
complicated queries