## Slide 1: Procedure for UE Reachability monitoring
Group Name: ARC WG, ARC-2018-0121
Source: F. Sang-Eon Kim, KT (TTA), kim.sangeon@kt.com
Meeting Date: 2018-05-14 (ARC35)
Notes: Other suggested titles:
“Benefits of oneM2M Standardization”

## Slide 2: Problem
Reference: TS 0026 V0.7.0 Figure 7.4.1-1

## Slide 3: Review 3GPP TS 29.122
A Monitoring API has three basic APIs.
  MonitoringEventSubscription
    This type represents a subscription to monitoring events. The same structure is used in the subscription request and subscription response.
  MonitoringEventNotification
    This data type represents a monitoring event notification which is sent from the SCEF to the SCS/AS.
  MonitoringEventReport
    This data type represents a monitoring event notification which is sent from the SCEF to the SCS/AS

## Slide 4: MonitoringEventSubscription API
M: Mandatory for UE Reachability monitoring
Attribute name | Data type | Cardinality | Request (step 1) | Response (step 3)
tltrId | TltrId | 0..1 | M | M
self | Link | 0..1 | NA | M
externalId | ExternalId | 0..1 | M | M
msisdn | Msisdn | 0..1 | M | M
externalGroupId | ExternalGroupId | 0..1 | M | M
notificationDestination | Link | 0..1 | M | M
requestTestNotification | boolean | 0..1 |  | 
websockNotifConfig | WebsockNotifConfig | 0..1 |  | 
monitoringType | MonitoringType | 1 | M | M
maximumNumberOfReports | Integer | 0..1 | M | 
monitorExpireTime | dateTime | 0..1 | M | 
groupReporGuardTime | DurationSec | 0..1 |  | 
reachabilityType | ReachabilityType | 0..1 | M | M
maximumLatency | DurationSec | 0..1 | O | O
maximumResponseTime | DurationSec | 0..1 | O | O
suggestedNumberOfDlPackets | integer | 0..1 | O | O
idleStatusIndication | boolean | 0..1 | M | M

## Slide 5: Notification API (step 5)
Attribute name | Data type | Cardinality | Application to oneM2M
subscriptionId | string | 1 | M
subscription | Link | 1 | M
tltrId | TltrId | 0..1 | 
monitoringEventReports | MonitoringEventReport | 1..N | M
Attribute name | Data type | Cardinality | Application to oneM2M
externalId | ExternalId | 0..N | 
idleStatusInfo | IdleStatusInfo | 0..1 | M
maxUEAvailabilityTime | dateTime | 0..1 | M
msisdn | Msisdn | 0..N | M
monitoringType | MonitoringType | 1 | M (UE_REACHABILITY)
reachabilityType | ReachabilityType | 0..1 | M (SMS, DATA, SMS_AND_DATA)
MonitoringEventReport
MonitoringEventNotification

## Slide 6: Notification API (step 5)
Attribute name | Data type | Cardinality | Application to oneM2M
activeTime | DurationSec | 0..1 | M
edrxCycleLength | DurationSec | 0..1 | M
suggestedNumberOfDlPackets | integer | 0..1 | M
idleStatusTimestamp | dateTime | 0..1 | M
periodicAUTimer | DurationSec | 0..1 | M
IdleStatusInfo

## Slide 7: Discussion for consensus