## Slide 1: MN De-Registration
Presented by: Neeta Meshram (neeta@cdot.in) C-DOT

## Slide 2: De-Registration of MN
Consider the scenario
MN1
MN2
<RMN2>(RemoteCSE of MN2)
<RMN1>(RemoteCSE of MN1)
<cont>
announceTo attribute contains RID of <contA> resource hosted on MN2
<contA>
MN1 Registered on MN2
AE
Create <container> with announceTo
attribute set as MN2

## Slide 3: De-Registration of MN cont..
MN1 is registered on MN2 and has created its <remoteCSE> resource RMN1 as a child of <CSEBase> resource of MN2.
AE sends a request to create <container> resource to MN1 with announceTo attribute set as MN2.
According to Announcement procedures, MN1 will send create request for <containerAnnc> resource to MN2 with To parameter set as RMN1(RemoteCSE of MN1).
MN2 will create <containerAnnc> resource as a child of RMN1.
If MN1 Deregisters from MN2.
<remoteCSE> of MN1(RMN1) gets deleted from MN2 and subsequently all the child resources of RMN1 including <containerAnnc> resource gets deleted.

## Slide 4: Problem
MN1
MN2
<RMN2>(RemoteCSE of MN2)
<RMN1>(RemoteCSE of MN1)
<cont>
announceTo attribute contains RID of <contA> resource hosted on MN2
<contA>
MN1 de-registers on MN2
AE
Resource Id of <contA> is present which is non-existing

## Slide 5: Problem
announceTo attribute of <container> resource of MN1 still has RID of <containerAnnc> resource which is now non-existing.

## Slide 6: Proposed Solution
Whenever any announced Resource gets deleted implicitly, a request should be sent to update the announceTo attribute of its corresponding original resource.

## Slide 7: ‘INACTIVE’ link attribute
Consider the second scenario
MN1
MN2
<RMN2>(RemoteCSE of MN2)
<RMN1>(RemoteCSE of MN1)
<AE>
<AEAnnc>
link attribute contains Resource ID of <AE> resource
MN1 Registered on MN2
AE
Create <AE> with ‘S’ type
AE-ID stem.

## Slide 8: ‘INACTIVE’ link attribute Cont..
MN is registered on IN-CSE and created <remoteCSE> resource.
AE sends registration request with ‘S’ type AE-ID stem to MN.
MN sends create request for <AEAnnc> resource to IN-CSE.
<AEAnnc> resource is created with link attribute set to RID of <AE> resource.
AE sends de-registration request to MN.
MN sends request to update <AEAnnc> resource to update link attribute with value ‘INACTIVE’.
AE sends re-registration request to MN.
MN sends request to update <AEAnnc> resource to update link attribute.
Whenever there is some request to modify announced resource, there is a validation that If the value of the from parameter in Request Primitive is identical with the CSE-ID included in the link attribute in the announced resource, the Receiver shall grant the Request after successful validation of the Request.

## Slide 9: Problem
MN1
MN2
<RMN2>(RemoteCSE of MN2)
<RMN1>(RemoteCSE of MN1)
<AE>
<AEAnnc>
link set to ‘INACTIVE’
AE
Delete <AE> request

## Slide 10: Cont..
Attribute Update: UPDATE | 
Associated Reference Point | Mcc.
Information in Request message | Information described for the Originator of the UPDATE Request as in clause 10.1.4. Content: Parameter includes the names of the attributes to be updated with their target values.
Processing at the Originator before sending Request | The Originator shall request to update the announced attributes by using the UPDATE Request as specified in clause 10.1.4. Attributes marked as MA or OA can be updated: Content: Parameter in the UPDATE Request shall provide the names of the attributes to be updated by setting their target values.
Processing at the Receiver | If the value of the From parameter in Request message is identical with the CSE-ID included in the link attribute in the announced resource, the Receiver (CSE hosting announced resource) shall grant the Request after successful validation of the Request. The Receiver shall perform as follows: Update the target attributes identified by the Content parameter in the UPDATE Request as per procedures in clause 10.1.4. Respond to the Originator with the appropriate UPDATE Response as in clause 10.1.4.
Information in Response message | Parameters defined in table 8.1.3-1 that are applicable.
Exceptions | All exceptions described in the basic procedures (clause 10.1.4) are applicable.
10.2.13.11 Procedure for original resource Hosting CSE for Updating Attributes
This clause describes procedure that shall be used by the original resource Hosting CSE to update announced attributes at the remote announced resources. The Originator of this Request shall be the original resource Hosting CSE.

## Slide 11: Problem
When link attribute is ‘INACTIVE’, how to decide who all can update this <AEAnnc> resource?

## Slide 12
THANK-YOU