## Slide 1: Group Schedule solution
Bei（Echo）Xu, Huawei, Nov 2017
Echo.Xubei@huawei.com
oneM2M www.oneM2M.org

## Slide 2: Group fan out message for members in PSM mode
The reachability times of member hosting CSE are different.
When to fanout the group message when Group Hosting CSE receives the request from IN-AE?
How to synchronize wake up for group messages reception by members in a group that are using power saving functions??
Group Hosting CSE
Member Hosting CSE1
Group Hosting CSE2
IN-AE
Wake up during 08:00-14:00
Wake up during 10:00-12:00
Group Hosting CSE4
Wake up during 15:00-18:00
When ?
Send group message at 9:00
Group Hosting CSE3
Always wake up

## Slide 3: Group message delivery using MBMS
In 3GPP TS-23.682
In Step6/13a, when SCS/AS sends Group Message Req to SCEF, there is a parameter Message Delivery Start Time which indicates the time at which the group message is to be sent by the network on the MBMS bearer(s)
In step 5/12, Application level interactions may be applied for the devices of specific group to retrieve the related MBMS service information, e.g. TMGI, start time which is out of the scope of 3GPP.
The problem is how does group Hosting CSE set the start time to 3GPP network and UE both?

## Slide 4: Problems in oneM2M existing solution
If the member Hosting CSE is in PSM when receiving the group fanout message, it can not process the fanout message. The <schedule> of <node> can be used to indicate the time when the member Hosting CSE can be reachable. But this <schedule> cannot indicate the time at which the group message is to be sent by the IN-AE/CSE.
Operation Execution Time or Request Expiration Timestamp in the request from IN-AE/CSE can be used to indicate when the group message is to be sent. But the member Host CSE does not know it before receiving the request. So Operation Execution Time or Request Expiration Timestamp cannot be used to wake up the member Hosting CSE in PSM.
oneM2M needs new mechanism to solve the problems which should be input from IN-AE/CSE and make sure the member Hosting CSE can receive the group message at the same time.

## Slide 5: New Usecase1: Turn on Street Lights of Group
Group Hosting CSE
IN-AE
Member Hosting CSE1
Set schedule
Application Server sets 6:00 PM to turn on the street lights and 7:00 AM to turn off the street lights from Oct to May year+1.
Application Server sets 8:00 PM to turn on the street light and 6:00 AM to turn off the street lights from May to Oct.
The street lights store the schedule to turn on/off at that time
Turn on/off automatically
at the schedule
Turn on/off automatically
at the schedule
Turn on/off automatically
at the schedule
Member Hosting CSE2
Member Hosting CSE3

## Slide 6: New Usecase2: Periodic device management of Group
Group Hosting CSE
IN-AE
Set schedule
During 1:00 AM – 2:00 AM of the 1st day of each month, the application server will maintain the device by different methods, such as battery check, memory check or firmware upgrade.
The device shall store the schedule and wake up to receive the message at that time in case it is in PSM.
Send DM message
Member Hosting CSE2
Member Hosting CSE1
Member Hosting CSE3
Wakes up to ready to receive DM message at the schedule
Wakes up to ready to receive DM message at the schedule
Wakes up to ready to receive DM message at the schedule

## Slide 7: Resource structure
<group>
<schedule>
Group Hosting CSE
Member Hosting CSE1
Member Hosting CSE2
Member Hosting CSE3
Multicast Group
<localMulticastGroup>
<schedule>
<CSEBase>
<schedule>
indicate the time periods when the group fanout requests are sent.
indicate the time periods when the group members are available and listening to receive multicast fanout requests.
indicate the anticipated time periods when the CSE is available for processing.
The Group Hosting CSE add <schedule> child resource of the <group> resource to indicate the time periods when the group fanout requests are sent.
The member Hosting CSE add <schedule> child resource of <localMulticastGroup> resource or <CSEBase> resource to indicate the time periods when the group members are available and listening to receive fanout requests.

## Slide 8: Solution—3GPP Network Coordination
Group Hosting CSE
Member Hosting CSE1
Member Hosting CSE2
MBMS Multicast Group
Member Hosting CSE3
3GPP
1 Allocate TMGI
2 Group Message Delivery(Group Message Payload, Message Delivery Start Time)
3 Activate MBMS Bearer Procedure(Start Time)
and MBMS session start procedure(Start Time)
0 All the member shall wake up and listen to the group message by the <schedule>
4 Group Message Delivery by multicast
0 TAU to fresh the UE status and make sure the reachability of UE
4 Group Message Delivery by Unicast
3GPP supports to activate MBMS bearer from the Group Hosting CSE at the Start Time from the <schedule> resource for multicast.
3GPP does not support to change the UE status from the Group Hosting CSE when UE is in PSM. So the Member Hosting CSE shall send TAU to fresh the UE status and make sure the reachability of UE.
Get from <schedule> of <group>.

## Slide 9: <schedule> of <group> Creation Procedure
Group Hosting CSE
IN-AE/CSE
Member Hosting CSE1
Member Hosting CSE2
Member Hosting CSE3
Multicast Group
1 Create <schedule> of <group> Request
2 Check PoA and Determine How to create <schedule> for member Host CSEs
3 Create <schedule> of <localMulticastGroup> Request
3 Create new element for <schedule> of <CSEBase> Request
3 Create <schedule> of <localMulticastGroup> Request
4 Create Response
4 Create Response
4 Create Response
6 Create Response
2.1 If all the members do not allow to update the schedule info, get the subset of all <schedule> of the <CSEBase> for all members
2.2 Return error or the schedule subset
The Group Hosting CSE shall try it’s best effort to create the schedule information for all the Member Hosting CSEs.
If some Member Hosting CSEs fail to create the schedule and the others succeed, the Group Hosting CSE shall return an result code to IN-AE/CSE to indicate the result.

## Slide 10: Group Fanout Procedure.
Group Hosting CSE
IN-AE/CSE
Member Hosting CSE1
Member Hosting CSE2
Member Hosting CSE3
Multicast Group
1 Request for group members
2 Check <schedule> of <group> and Determine when to fanout the message
3 Request to multicast address by multicast
3 Request to Member Hosting CSE3 by unicast
4 Response
4 Response
6 Response
0 All the member shall wake up and listen to the group message by the <schedule>
4 Response
5 Aggregate response messages

## Slide 11: Proposal
In oneM2M, the <schedule> of <node> indicates the time periods when the node can communicate via the Underlying Network. In TS-0026, oneM2M supports to coordinate with 3GPP network to synchronize the <schedule>.
The child <schedule> resource of the <CSEBase> resource indicates the anticipated time periods when the CSE is available for processing. It’s used in oneM2M layer and underlying network independent.
Propose child <schedule> resource of the <CSEBase> to wake member hosting CSE if there is no multicast group information.

## Slide 12: Thank You