## Slide 1: Local Breakout in oneM2M
Group Name: ARC
Source: Youngjin Na, Min-Byeong Lee, Joon-Young Kim / HYUNDAI Motor (TTA)
JaeSeung Song (KETI)
Meeting Date: 2018-09-17 to 2018-09-21
ARC-2018-0264-Local-Breakout-in-oneM2M

## Slide 2: Issues
IoT applications are limited to get its services from visited CSE
Managing resources should be stayed at the Home CSE
Even IoT applications are located far away from its home CSE, the IoT application should access its home CSE to get required information and services
Why not applying Local Break Out (LBO) concept to oneM2M
“Local Breakout, a mechanism where roaming traffic does not traverse back to the home network and is handled by the local operator, allows for cheaper tariffs and will also bring increased localised revenue.”

## Slide 3: Use Case and High-level Functions
Consider a case where an IoT application is visited other places
  For example, a vehicle having IoT application visits Pyeongchang where it only has an internet access via LTE
  The user of the application wants to access its home or office IoT assets
  The application can’t get any services via its local IoT service provider
IoT applications should be able to discover oneM2M service providers using Service Provider Discovery mechanism (to be standardized via Registry)
IoT application requests LBO procedures
  With it’s home domain service provider
  Home and Visited service provider should have an agreement
Home and Visited providers
  Should exchange required information
  Places copy resources (belongs to the user) to the visited CSE
  Indicate copied resources as LBO
  Configure proper access control
  Enable other available services (open resources) at the local visited CSE

## Slide 4: How LBO works?
A resource for LBO IN-CSE can be modelled
<LBO> should include required information to be discovered by other IN-CSEs or IoT applications
<LBO> could have the following information:
  Contact of Address (IP Address)
  Port number
  Name of IN-CSE
  Status
  Profile of IN-CSE
  Type of IN-CSE
  Supported public services
  Maintenance information (for example, from 01:00 ~ 02:00)
  Access information (or credencial)
IN-CSE having <LBO> should exchange its description with other IN-CSE
  IN-CSEs having Service Level Agreement should exchange their information
  IN-CSEs having open data and services allow other IN-CSEs to discover
  Platform providers could manually add <registryResource>

## Slide 5: Thank you!