| INPUT CONTRIBUTION |
| --- |
| Group Name:* | TP#4 WG MAS |
| Title:* | Considerations on DM reference points |
| Source:* | Huawei Technologies UK (ETSI) Huawei Technologies Co., Ltd (CCSA) |
| Contact: | Jiaxin Yin, yinjiaxin@huawei.com |
| Date:* | 2013-04-18 |
| Abstract:* | The contribution proposes one possible way to enable device management in the oneM2M architecture. The contribution also suggests the rational and the reference point in the architecture to implement device management. |
| Agenda Item:* | TBD |
| Work item(s): | WI0002 |
| Document(s) Impacted* | Technical Report - Study of Management Capability Enablement Technologies for Consideration by oneM2M |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the text in the TR if approved. |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

7.x	OMA DM

7.x.1	DM Architecture and reference points

Figure 2.1: DM Architecture and reference points

Editor’s note: The architecture may be changed according to the progress in ARC WG

As is shown in Figure 2.1 is a proposed architecture for consideration by oneM2M for leveraging OMA DM for device management purpose.

For the M2M Device/Gateway, a DM Client is included in the CSE. For the M2M Service Infrastructure, there could also be a DM Server A in the CSE. A DM Server B can be reside in the Underlying Network.

There are three cases for the device management.

Case 1: Device management through DM Server A in support of reference point Y

Applications performs device management through DM Server A resides in DM-Function in CSE of M2M Service Infrastructure. In this case, the interfaces DM-1 and DM-2[i.1] are a part of the Y reference point.

Case 2: Device management through DM Server B in support of reference point Z

Applications performs device management through DM Server B resides in the Underlying Network. In this case, DM-Function utilizes DM Server B over Z reference point. DM Server B sends management commands to DM Client using interfaces DM-1 and DM-2. The Y reference point between CSE in the Service Infrastructure and CSE in the M2M Device/Gateway is achieved by utilizing Z reference point.

Case 3: Device management through delegation between DM Server A and DM Server B

With both DM Server A in the CSE of M2M Service Infrastructure and DM Server B in the Underlying Network, Application performs device management via the delegation mechanism [OMA-TS-DM_Server_Delegation_Protocol-V1_3-20121009-C] from DM Server A to DM Server B. In this case, DM-Function containing DM Server A utilizes DM-6 interface over Z reference point to perform the delegation procedure, then DM Sever B performs the delegated management procedures using interfaces DM-1 and DM-2. The Y reference point between CSE in the Service Infrastructure and CSE in the M2M Device/Gateway is achieved by utilizing Z reference point.