| INPUT CONTRIBUTION |
| --- |
| Group Name:* | REQ WG / MAS WG |
| Title:* | Preparing consolidated requirements and definitions for Abstraction and Semantics |
| Source:* | NEC (ETSI), Samsung SDS, InterDigital, LG Electronics |
| Contact: | Jaeseung Song (jaeseung.song@neclab.eu) |
| Date:* | 2013-05-06 |
| Abstract:* | This contribution initiates a discussion on preparing consolidated requirements and definitions for Abstraction and Semantics. |
| Agenda Item:* | Tbd |
| Work item(s): | Requirements, Abstraction&Semantics |
| Document(s) Impacted* | The Requirements TS and the Definitions TR |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Discussion and initial agreement for potential inclusion in the Requirement TS and the Definitions TR. |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

- Introduction

In the previous TP #3 meeting, oneM2M-REQ-2013-0162 was proposed to put “Abstraction and Semantics” (ABS) related requirements into the Requirement TS. However, because of time limitation, only two ABS related requirements were agreed (oneM2M-REQ-2013-0162R02).

In this meeting, we have additional two contributions containing potential ABS requirements as follows:

- oneM2M-REQ-2013-0159R4 (InterDigital, Samsung SDS, LGE)

- oneM2M-MAS-2013-0020 (NEC)

This contribution proposes to analyse these two new input contributions together with the agreed and not handled requirements in the last meeting in order to derive a list of consolidated ABS related requirements.

- Available ABS related requirements

  - Agreed Abstraction and Semantics (ABS) related requirements (source: oneM2M-REQ-2013-0162R02)

| REQ-Number | Requirements |
| --- | --- |
| ABS-01 | The M2M System shall provide the capability for M2M Applications to communicate with a device without the need for the M2M Applications to be aware of the technology specific communication protocol of the device. |
| ABS-02 | M2M system shall be able to support translation mechanism of information models (including meta-data) used by applications and devices. |

  - Abstraction and Semantics (ABS) related requirements in the requirement lists. (source: oneM2M-REQ-2013-0162R01)

| REQ-Number | Document ID | Description |
| --- | --- | --- |
| Group 1 |  |  |
| HLR-070 | oneM2M-REQ-2012-0046R03 | The M2M System shall provide the capability for M2M Applications to communicate with a device without the need for the M2M Applications to be aware of the technology specific communication protocol of the device. |
| HLR-103 | oneM2M-REQ-2012-0073R01 | The M2M System shall provide a capability to an Application to allow, via the M2M Service Capability Set, access to its Devices, Virtual Devices and Things to individual other Applications. |
| Group 2 |  |  |
| HLR-128 | oneM2M-REQ-2012-0063R03 | M2M system shall be able to provide translation mechanism of information models (including meta-data) used by applications and devices. |
| Group 4 |  |  |
| HLR-139 | oneM2M-REQ-2012-0046R03 | The M2M System shall provide the capability to map sets of similar device functionalities of devices to specified application objects. |
| HLR-140 | oneM2M-REQ-2012-0046R03 | The M2M System shall provide a capability to associate application objects with the functionalities of a device. |
| HLR-141 | oneM2M-REQ-2012-0046R03 | The M2M System shall provide the capability for M2M Applications to invoke a function of the device through the application objects associated with the functionalities of the device. |
| Group 8 |  |  |
| HLR-099 | oneM2M-REQ-2012-0073R01 | The M2M System shall provide a capability to an Application to create/delete/update/manage Virtual Devices and Things in the M2M Service Capability Set. |
| Group 12 |  |  |
| HLR-081 | oneM2M-REQ-2012-0067R03 | The M2M System shall be capable of providing to authorized Applications a syntactic and sematic description of Diagnostic data of M2M Application, Devices and Gateways |
| HLR-100 | oneM2M-REQ-2012-0073R01 | The M2M System shall provide a capability to an Application to publish to authorized Applications semantic descriptions and meta-data (e.g. location) of its Devices, Virtual Devices and Things in the M2M Service Capability Set. |
| HLR-101 | oneM2M-REQ-2012-0073R01 | The M2M System shall provide a capability to an Application to search for and discover Devices, Virtual Devices and Things in the M2M Service Capability Network based on their semantic descriptions and meta-data. The supported formats of semantic descriptions shall be described in the oneM2M standard. |
| HLR-102 | oneM2M-REQ-2012-0073R01 | The M2M System shall provide a capability to an Application to control, via the M2M Service Capability Network, access to semantic descriptions and meta-data of its Devices, Virtual Devices and Things. |
| HLR-142 | oneM2M-REQ-2012-0046R03 | The M2M system shall provide a semantic/ meta-language model that can map industry-specific information models for end device application functionalities to common and application-agnostic abstract functions that are understood components of the M2M system. |

  - Requirements from InterDigital, Samsung SDS and LGE: (source: oneM2M-REQ-2013-0159R4 )

| REQ-Number | Requirements |
| --- | --- |
| X-01 | The M2M System shall support storing, access, retrieval and updates of the semantics information, at locations local to or remote from the associated resources. |
| X-02 | The M2M System shall provide capabilities to manage semantic information (e.g., creating, retrieving, updating, deleting). |
| X-03 | The M2M System shall support associating/linking of semantic information with local or remote resources. |
| X-04 | The M2M System shall support semantic formats for representing and publishing semantic information of applications (e.g. title, version, related devices). |
| X-05 | The M2M System shall have the capability to provide translation, association and abstraction functionality between the semantic formats (e.g. XML, JSON) supported. |
| X-06 | The M2M System shall support parsing and interpreting of semantic information. |
| X-07 | The M2M System shall support services that perform analytics on content using semantic information. |

  - Requirements from ETSI use cases: (source: oneM2M-MAS-2013-0020)

| REQ-Number | Requirements |
| --- | --- |
| E-01 | The M2M System shall support a common (e.g. per vertical domain) semantic data model (e.g. represented by Ontology) available to M2M application. |
| E-02 | The M2M System shall provide discovery capabilities that enable the discovery of M2M resources based on their semantic information, e.g. semantic categories and relationship among them. (e.g. all heaters and windows in a room; the room in which a window is located…). |
| E-03 | The M2M System shall provide representation and discovery functionality of real-world entities (rooms, windows) that are not necessarily physical devices. |
| E-04 | The M2M system shall be able to map control commands issued towards an abstract device to the concrete commands of a specific device. |
| E-05 | The M2M System shall support a semantic data model that is at least common to the vertical industry in which a Thing is used to describe Things registered in the M2M System. |
| E-06 | The M2M entity shall be able to expose its semantic description to the M2M System. |
| E-07 | If a Thing is capable to expose semantic information to the M2M System the M2M System shall be able to use that information to represent the Thing. |
| E-08 | The M2M System shall be able to describe the semantic relationship between Things. |

- Analysis

The intention of this part is grouping similar requirements into the same group. Requirements in the same group are subject to merge or split to derive consolidated requirements.

- Group-01 (Overall): ABS-01

- Group-02 (Translation): ABS-02, X-05

- Group-03 (Publishing): E-03, E-06, HLR-100

- Group-04 (Discovery): E-02, HLR-101

- Group-05 (Accessing): X-01, HLR-141, HLR-103

- Group-06 (Managing): X-01, X-02, X-06, HLR-102, HLR-081, HLR-099

- Group-07 (Data model): E-01, E-05, E-08, X-04, HLR-142,

- Group-08 (Mapping): E-04, X-03, X-05, HLR-140, HLR-139

- Group-09 (Virtual thing and Services): E-07, X-07, HLR-099

- Consolidated requirements (Proposal)

NOTE:

  - Blue colored cell (Previously approved requirements)

  - Yellow colored cell (Merged and under discussion)

  - Purple colored cell (unclear intention)

| REQ-Number | Category | Requirements | Status |
| --- | --- | --- | --- |
| ABS-01 | abstraction | The M2M System shall provide the capability for M2M Applications to communicate with a device without the need for the M2M Applications to be aware of the technology specific communication protocol of the device. | Approved |
| ABS-02 (X-02) | Semantics | The M2M System shall provide capabilities to manage (e.g., creating, retrieving, updating, deleting) semantic descriptions. | Discussion |
| ABS-03 (E-01) | Semantics | The M2M System shall support a common (e.g. per vertical domain) semantic data model (e.g. contained in the meta-model represented by Ontology) in order to make it available to M2M applications. | Discussion |
| ABS-04 (E-08) | Semantics | The M2M System shall be capable to understand semantic descriptions and semantic relationships between Things. Editor’s note: Things needs to be defined | Discussion |
| ABS-05 (X-04) | Semantics | The M2M System shall support formats for semantic descriptions (e.g. title, version, related devices) of M2M Applications. | Discussion |
| ABS-06 | Semantics | M2M system shall be able to provide the translation mechanisms for the Information Models (including meta-data) used by applications and devices. Editor’s note: It is FFS whether to include parsing and interpreting features in this requirement. | Discussion |
| ABS-07 (out of X-05) | Semantics | The M2M System shall have the capability to exchange semantic descriptions (of Information Models) between entities using different formats (e.g. RDF, XML, JSON). Editor’s note: Entity needs to be defined. | Discussion |
| ABS-08 (E-03) | Abstraction | The M2M System shall provide the capability to represent real-world entities (e.g. rooms, windows) and virtual devices that are not necessarily physical devices. Editor’s note: Virtual Device needs to be defined | Discussion |
| ABS-09 (out of E-06, HLR-100) | Semantics | The M2M System shall be able to understand semantic descriptions exposed by M2M Resources. Editor’s note: M2M Resource needs to be defined | Discussion |
| ABS-10 (out of HLR-101, E-02) | Semantics | The M2M System shall provide capabilities that enable the discovery of M2M Resources based on semantic descriptions. | Discussion |
| ABS-11 (X-01a) | Semantics | The M2M System shall support the capability to store, access and manage semantic descriptions of local or remote M2M resources. | Discussion |
| ABS-12 (X-01b) | Semantics | The M2M System shall support the capability to store and retrieve semantic descriptions that are outside of the M2M System. | Discussion |
| ABS-13 (X-03) | Semantics | The M2M System shall support association/linkage of semantic descriptions with local or remote M2M resources. | Discussion |
| ABS-14 (HLR-103) | Semantics | The M2M System shall support capabilities for M2M Applications to allow other M2M Applications to access and manage its M2M resources by using semantic descriptions of the management operations. | Discussion |
| ABS-15 (E-04) | Abstraction | The M2M System shall be able to map commands issued towards an abstract device to the commands of physical device(s). | Discussion |
| ABS-16 (X-07) | Semantics | The M2M System shall enable capabilities to perform analytics on M2M data using semantic descriptions. | Discussion |
| ABS-17 (HLR-139) |  | The M2M System shall provide the capability to map sets of similar functionalities of devices to specified M2M resources. | Discussion |
| ABS-17 (HLR-140) |  | The M2M System shall provide capabilities to associate M2M resources with the functionalities of a device. | Discussion |
| ABS-18 (HLR-141) |  | The M2M System shall provide the capability for M2M Applications to invoke a function of the device through the M2M resources associated with the functionalities of the device. | Discussion |

- Required Definitions (Proposal)

- Thing: an element of the environment that is individually identifiable in the oneM2M system

- Relation: stating a relationship among Things such as “is-part-of”, “is-subtype-of”

- Information Model:  the information model of an Application, including data and methods.

- Device Information Model: technology (e.g. ZigBee) specific Information Model of the physical device.

- Abstract Information Model: Information Model of common functionalities abstracted from a set of Device Information Models.

- Abstraction: the process of mapping between a set of Device Information Models and an Abstract Information Model according to a specified set of rules.

- Entity: a tangible element that is intrinsic to the environment, and that is not specific to a particular M2M application in this environment.

- Resource: is a uniquely addressable entity in the oneM2M System. A resource has a representation that can be transferred and manipulated.

- Virtual Device: a logical device (implemented as software) that acts similar to physical M2M device and provides derived data such as average temperature of a room, number of vehicles that passed during the last minute.