| INPUT CONTRIBUTION |
| --- |
| Group Name:* | TP#6 WG MAS |
| Title:* | Device management architecture |
| Source:* | Huawei Technologies UK (ETSI) Huawei Technologies Co., Ltd (CCSA) |
| Contact: | Jiaxin Yin, yinjiaxin@huawei.com |
| Date:* | 2013-07-02 |
| Abstract:* |  |
| Agenda Item:* | TBD |
| Work item(s): | WI0004 |
| Document(s) Impacted* | Technical Report - Study of Management Capability Enablement Technologies for Consideration by oneM2M |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the text in the TR if approved. |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

## 7.4	Management Generalized Architectural Framework

Figure 7.1: DM Architecture and reference points

Figure 7.1 is the generalized architecture framework for device management.

DMF is the CSF to perform the functionality on device management. DMF is responsible for exposing the device management capabilities supported by the CSE to other CSEs or M2M Applications. DMF is also responsible for translating the device management related requests from other CSEs or Applications to device management commands corresponding to individual device management technologies.

DMF in the CSE of the Infrastructure Node is used to manage M2M Devices/Gateways as well as devices in the M2M Area Network. The DMF could have embedded Management Server, third party Management Server outside of the CSE or interact with Management Server from the underlying network. The DMF is also embedded with a Management Adapter to translate the requests from the X or Y reference point to trigger the Management Server to send management commands to devices.

DMF in the CSE of the End Node is deployed with a Management Client as well as a Management Adapter. The Management Client interacts with Management Server using individual management protocols. The Management Adapter is to interact with the Management Client to perform managements and acquire information.

DMF in the CSE of the Intermediate Node is the same in function as the DMF in the CSE of the End Node. The only difference is that DMF in the CSE of the Intermediate Node can be used to manage devices in the M2M Area Network. In this case, the DMF is deployed with a Proxier. The Proxier could be in transparent mode, adaption mode or proxy mode. In different modes the interface between the Proxier and the Native Protocol Management Client are different.

# Text boxes

Infrastructure Node

CSE

Management Adapter

Application

X

Proxier

Native Protocol Management Client

CSE

Z(Ms)

DMF

Intermediate/End Node

Z(Mc)

Management Server

Underlying Network

Service Layer

Device in M2M Area Networks

Y(Mc)

Management Server

Management Client

Management Server

Management Adapter

Management Client

DMF