| INPUT CONTRIBUTION |
| --- |
| Group Name:* | TP#6 WG MAS |
| Title:* | Device management architecture |
| Source:* | Huawei Technologies UK (ETSI) Huawei Technologies Co., Ltd (CCSA) |
| Contact: | Jiaxin Yin, yinjiaxin@huawei.com |
| Date:* | 2013-07-02 |
| Abstract:* |  |
| Agenda Item:* | TBD |
| Work item(s): | WI0004 |
| Document(s) Impacted* | Technical Report - Study of Management Capability Enablement Technologies for Consideration by oneM2M |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the text in the TR if approved. |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

## 7.4	Management Generalized Architectural Framework

Figure 7.1: DM Architecture and reference points

Figure 7.1 is the generalized architecture framework for device management.

The Device Management Function (DMF) is the Common Service Function (CSF) functional architectural component that is responsible for management of intermediate and end nodes. The DMF is responsible for exposing the device management capabilities supported by the CSE to other CSEs or M2M Applications. In addition the DMF is responsible for management of the CSE within for intermediate and end nodes. In order to manage the CSE and device capabilities of these nodes, the DMF utilizes existing device management technologies (e.g., TR-069, OMA-DM, and LWM2M). As such, the DMF translates or adapts the management related requests from other CSEs or M2M Applications to device management commands corresponding of the device management technology.

In the oneM2M functional architecture, the DMF in the CSE of the Infrastructure Node is used to manage intermediate and end nodes that are representative of M2M Gateways/Devices as well as devices in the M2M Area Network. The DMF of the Infrastructure node manages the intermediate and end nodes using the device management technologies Management Server. These Management Servers could reside within the CSE (embedded Management Server), outside the CSE as part of the infrastructure node or as separate entity in the Underlying Network.

The DMF has a functional component termed the Management Adapter that translates requests between:

- M2M Applications and Management Servers across the X reference point

- DMF and Management Clients for management and information acquirement.

While the Management Adapter provides a translation function between the DMF and Management Servers and Clients, the communication between the Management Client and Management Server uses the technology specific protocol (e.g., TR-069, OMA-DM, LWM2M).

In the case of the Intermediate and End Nodes, the DMF in the CSE of the Intermediate Node has the same functionality as the DMF in the CSE of the End Node. In addition, the DMF in the Intermediate Node can be used to manage devices in the M2M Area Network. In this case, the Management Client in the DMF is deployed with Proxy functionality. Depending on the technology of the Management Client (e.g., TR-069, OMA-DM, LWM2M), the Proxy functionality (mode) can differ (e.g., transparent, adaptation, proxy). For example TR-069 only supports an adaptation mode, OMA-DM supports transparent, adaptation and proxy modes and LWM2M does not currently support a Proxy function. Depending on the mode the Proxy Management Client may be a Technology Specific (OMA-DM) or Native Protocol (ZigBee) Management Client.

# Text boxes

Infrastructure Node

CSE

Management Adapter

Application

X

Proxy

Proxy Management Client

CSE

Z(ms)

DMF

Intermediate/End Node

Z(mc)

Management Server

Underlying Network

Service Layer

Device in M2M Area Networks

Y(mc)

Management Server

Management Client

Management Server

Management Adapter

Management Client

DMF