| INPUT CONTRIBUTION |
| --- |
| Group Name:* | MAS WG |
| Title:* | Discussion of Management General Architecture |
| Source:* | LG Electronics |
| Contact: | Seongyoon Kim, LG Electronics, seongyoon.kim@lge.com |
| Date:* | 2013-07-29 |
| Abstract:* | The contribution gives suggestion on management general architecture currently we have in TR. |
| Agenda Item:* | TBD |
| Work item(s): | WI0004 |
| Document(s) Impacted* | Technical Report - Study of Management Capability Enablement Technologies for Consideration by oneM2M |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the text in TR0006 if approved. |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

1	Rationale

The discussion point of this contribution is whether Y and Z are proper reference points for device management interface (ms and mc).

The below general architecture is currently we have in TR section 7.4 Management Generalized Architectural Framework.

In the figure, mc interface is included in Y and Z reference point.

- mc Interface

The interface between the management server and the management client. This interface can be realized by the existing device management technologies such as BBF TR-069, OMA DM, etc.

- Y Reference Point

This is the reference point between two CSEs. The Y reference point allows a CSE to use the services of another CSE in order to fulfil needed functionality. Accordingly, the Y reference point between two CSEs shall be supported over different M2M physical entities. The services offered via the Y reference point are dependent on the functionality supported by the CSEs

- Z Reference Point

This is the reference point between a CSE and the Underlying Network. The Z reference point allows a CSE to use the services (other than transport and connectivity services) provided by the Underlying Network in order to fulfil the needed functionality

- Change of mc Interface

Endpoint of Y(CSE-CSE) and mc(Management Server-Client) is different and Management Server can reside outside of CSE, which means that we cannot include mc interface into Y reference point.

| Endpoint | Location (either) |
| --- | --- |
| Management Client | Inside of CSE | Outside of CSE |
| Management Server | Inside of CSE | Outside of CSE |

Also endpoint of Z(Underlying Network-CSE) and mc(Underlying Network-Management Client) is different and Management Client can reside outside of CSE, which means that we cannot include mc interface into Z reference point.

Also mc interface is defined outside of oneM2M, which means oneM2M doesn’t define/modify anything to mc interface. ( Making mc interface dashed line to make clear mc is not scope of oneM2M.

- Change of ms Interface

- ms Interface

The interface that is exposed by the management server in the underlying network domain or in the M2M service domain for use by other systems. Using this interface, systems can perform management operations on devices through the management server.

| Endpoint | Location (either) |
| --- | --- |
| Management Server | Inside of Service Layer Domain | Outside of Service Layer Domain |

Endpoint of Z(Underlying Network-CSE) and ms(Management Server-CSE) is different and Management Server can reside inside of CSE, which means that we cannot include ms interface into Z reference point.

Also oneM2M doesn’t define ms interface. ( Making ms interface dashed line to make clear mc is not scope of oneM2M.

Please note that we don’t need to include out-of-scope interface into in-scope reference point.

====================== 1st Change========================

## 7.4	Management Generalized Architectural Framework

Figure 7.1: DM Architecture and reference points of oneM2M

# Text boxes

Figure 1. Current Architecture

Infrastructure Node

CSE

Application

X

Y(mc)

Device in M2M Area Networks

Management Server

Z(ms)

Service Layer

Underlying Network

DMF

Intermediate/End Node

DMF

CSE

Management Client

Proxy

Z(mc)

Proxy Management Client

Management Server

mp

Management Adapter

Management Adapter

Figure 2. Change of mc Interface

Infrastructure Node

CSE

Application

X

Y(mc)

Device in M2M Area Networks

Management Server

Z(ms)

Service Layer

Underlying Network

DMF

Intermediate/End Node

DMF

CSE

Management Client

Proxy

mc

Proxy Management Client

Management Server

mp

Management Adapter

Management Adapter

mc

Figure 3. Change of ms Interface

Infrastructure Node

CSE

Application

X

Y(mc)

Device in M2M Area Networks

Management Server

ms

Service Layer

Underlying Network

DMF

Intermediate/End Node

DMF

CSE

Management Client

Proxy

Z(mc)

Proxy Management Client

Management Server

mp

Management Adapter

Management Adapter

ms

Infrastructure Node

CSE

Application

X

Y(mc)

Device in M2M Area Networks

Management Server

ms

Service Layer

Underlying Network

DMF

Intermediate/End Node

DMF

CSE

Management Client

Proxy

mc

Proxy Management Client

Management Server

mp

Management Adapter

Management Adapter

mc

ms

Infrastructure Node

CSE

Application

X

Y(mc)

Device in M2M Area Networks

Management Server

Z(ms)

Service Layer

Underlying Network

DMF

Intermediate/End Node

DMF

CSE

Management Client

Proxy

Z(mc)

Proxy Management Client

Management Server

mp

Management Adapter

Management Adapter