| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG5 MAS |
| Title:* | CSE and AE Management CSF Description |
| Source:* | Tim Carey, Alcatel-Lucent, timothy.carey@alcatel-lucent.com |
| Contact: | Tim Carey, Alcatel-Lucent, timothy.carey@alcatel-lucent.com |
| Date:* | 2013-08-20 |
| Abstract:* | General and Detail Descriptions of the Management CSF. |
| Agenda Item:* |  |
| Work item(s): | Architecture TS |
| Document(s) Impacted* | Architecture TS |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree that the MGT CSF could be contributed to the Architecture TS |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

### 6.2.x	Management

#### 6.2.x.1	General Concepts

The Management (MGT) CSF is responsible for providing management of AEs and CSEs on the Application, Device, Middle and Infrastructure nodes. This includes functions to configure, troubleshoot and upgrade the functions of the CSE as well as upgrade the AEs.

#### 6.2.1.2	Detailed Descriptions

The MGT CSF provides management capabilities for functions of a CSE. These management capabilities are aligned to management services provided by the CSE.

Figure1: Management Layers and Services

Note: The MGT CSF capabilities on Device and Middle nodesS should utilize the capabilities provided by the DM CSF for interaction with the Device Management Server.

Editor's Note:  Specific management capabilities for services are FFS.

The management services include:

- Configuration Services (CS): This service includes the configuration of the capabilities and features of the CSE.

- Diagnostics and Monitoring Services (DMS): This service includes the troubleshooting of the CSE through the use of diagnostic tests, alert generation and retrieval of operational status (e.g., local context) and statistics of associated with the CSE capabilities and features.

- Software Management Services (SMS): This service provides the lifecycle management for software components and associated artifacts for different components such as CSE and AE.

The MGT CSF shall provide capabilities to manage the CSE’s configuration capabilities on Infrastructure, Intermediate and Device nodes.

The MGT CSF shall provide capabilities to manage the CSE’s troubleshooting capabilities on Infrastructure, Intermediate and Device nodes.

The MGT CSF shall provide capabilities to manage the lifecycle for software components and associated artifacts that comprise the CSE on Infrastructure, Intermediate and End nodes.

The MGT CSF should provide capabilities to manage the lifecycle for software components and associated artifacts that comprise an AE on Application, Intermediate and End nodes.

Note: Service access is controlled through Role based permissions.

##### 6.2.1.2.1	Configuration Service

The MGT CSF’s configuration service provides the interface(s) to configure the capabilities of the Application Layer provided by the following CSF’s:

- Xxxxx:

- Yyyyy:

The MGT CSF’s configuration service provides the interface(s) to configure the capabilities Common Services Layer provided by the following CSF’s:

- Xxxxx:

- Yyyyy:

The Configuration Service is exposed through a set of resources defined in section 9.4 Resource Structure.

These information exchange of the resources for the Configuration Service is exposed through the X and Y reference points using the procedures defined in section 8.1 General Communication Flow Scheme.

##### 6.2.1.2.2	Diagnostic and Monitoring Service

The MGT CSF’s configuration service provides the interface(s) to:

- Execute requested diagnostics for specified CSE capabilities

- Retrieve logs, statistics and status of resources associated with CSE capabilities.

###### 6.2.1.2.2.1	CSE Diagnostics

CSE Diagnostics are tests or measurements that are performed to troubleshoot and monitor capabilities within the CSE. Depending on the test or measurement, a test shall be performed using a synchronous and/or asynchronous communication scheme.

CSE test and measurements for the synchronous communication scheme are exposed through the X and Y reference points using the procedures defined in section 8.1 General Communication Flow.

CSE  tests and measurements for the asynchronous communication scheme are exposed through the X and Y reference points using the procedures defined in section 8.x YYYYYY.

In addition to the type of communication scheme, CSE test and measurements shall define a recurrence pattern or schedule (e.g., daily, once, every 4 hours). CSE tests shall define a test repetition to be executed within the schedule.

CSE tests and measurements are provided by the following CSF’s for the Application Layer:

- Xxxxx:

- Yyyyy:

CSE tests and measurements are provided by the following CSF’s for the Common Services Layer:

- Xxxxx:

- Yyyyy:

CSE tests and measurements are exposed through a set of resources defined in section 9.4 Resource Structure.

###### 6.2.1.2.2.2	CSE Monitoring

CSE Monitoring provides operating characteristics of the CSE capabilities. These operating characteristics include attributes for operational status, configuration and statistics as well as management of alerts.

CSE Monitoring is provided by the following CSF’s for the Application Layer:

- Xxxxx:

- Yyyyy:

CSE Monitoring is provided by the following CSF’s for the Common Services Layer:

- Xxxxx:

- Yyyyy:

CSE Monitoring is exposed through a set of resources defined in section 9.4 Resource Structure.

A CSE’s operational characteristics information exchange shall be provided to an Application by the CSE as a result of a retrieval request, alert generation or bulk transfer operations.

The information exchange of the resources for the CSE Monitoring using the retrieval operation is exposed through the X and Y reference points using the procedures defined in section 8.1 General Communication Flow Scheme.

The information exchange of the resources for the CSE Monitoring using the bulk transfer request operation is exposed through the X and Y reference points using the procedures defined in section 8.x YYYYYYY.

The information exchange of the resources for the CSE Monitoring using the alert generation operation is exposed through the X and Y reference points using the procedures defined in section 8.x YYYYYYY.

##### 6.2.1.2.3	Software Management Service

The CSE is comprised of software modules and artifacts (e.g., configuration files) that are associated with a deployable release package. The SMS CSF provides the capability to manage the lifecycle of the release package.

Editor's Note:  Details for the software lifecycle and integration in the Services extension enabler are FFS.