| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG5 |
| Title:* | DM Server Interaction |
| Source:* | Tim Carey, Alcatel-Lucent, timothy.carey@alcatel-lucent.com |
| Contact: | Tim Carey, Alcatel-Lucent, timothy.carey@alcatel-lucent.com |
| Date:* | 2013-10-16 |
| Abstract:* | Detail Description of the Device Management CSF for Interactions with the Device Management Server. |
| Agenda Item:* |  |
| Work item(s): | Architecture TS |
| Document(s) Impacted* | Architecture TS |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree to move over to Architecture WG for inclusion in the Functional Architecture TS. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

#### 6.2.4.1.1	Device Management Architecture

In order to manage the CSE and device capabilities of the Middle and Device Nodes, the DMG may utilize existing device management technologies (e.g., TR-069, OMA-DM, and LWM2M) in addition to management of Management Resources across the Y reference point.

When the DMG utilizes existing device management technologies, the DMG translates or adapts the management related requests from other CSEs or M2M Applications to device management commands corresponding of the device management technology.

The DMG of the Infrastructure Node manages the Middle and Device Nodes using the device management technology’s Management Server. These Management Servers could reside within the CSE (embedded Management Server), outside the CSE as part of the Infrastructure Node or as separate entity in the Underlying Network.

The DMG has a functional component termed the Management Adapter that performs the adaptation between the:

- DMG and Management Servers 
After the DMG receives the requests from M2M Applications via the X reference points, the Management Adapter in the DMG translates the requests from the M2M Applications to requests that can be understood by the Management Server. The Management Server then communicates with the Management Client or Proxy.

- DMG and Management Clients 
The Management Adapter in the DMG of Middle or Device Node interacts with the Management Client to exchange information with the Management Client using the interface provided by the Management Client (e.g. DM-7,8,9 in OMA DM). The Management Adapter can then interact with DMG in the Infrastructure Node over the Y reference point using interface defined between CSEs.

While the Management Adapter provides a translation function between the DMG and Management Servers and Clients, the communication between the Management Client and Management Server uses the technology specific protocol (e.g., TR-069, OMA-DM, LWM2M).

The interface between Management Server and Management Client is the mc interface which is subject to the device management technology that is used (e.g. OMA DM, BBF TR069 or OMA LWM2M). The mc interface represented by a gray dashed line is technology dependent and is outside the scope of this specification.

The interface between Management Server and Management Adapter is the ms interface which is provided by the Management Server.

The interface between Management Client and Management Adapter is the la interface which is provided by the Management Client.

In the case of the Middle and Device Nodes, the DMG in the CSE of the Middle Node has the same functionality as the DMG in the CSE of the Device Node. In addition, the DMG in the Middle Node can be used to manage devices in the M2M Area Network. In this case, the DMG is deployed with Proxy functionality that interacts with the Proxy Management Client using the mp interface. The mp interface represented by a gray dashed line is technology dependent and is outside the scope of this specification.

Figure 1 - Device Management Architecture

The Device Management Server and Device Management Client are depicted with dashed lines as these entities may be implemented as an entity external to the node or they may be implemented as an entity embedded within the node.

Editors note: Need to depict the multiplicity of Management Adapters and Management Servers.

Editors note: Extend the CSE to the Device Management Server and Device Management Client to show the ability to have an embedded Device Management Client or Device Management Server.

Editors note: Need to state the ms is not specified by oneM2M inside the figure.

##### 6.2.4.2.1	Device Management Server Interaction

##### 6.2.4.2.1.1	Overview

The DMG CSF has the capability to utilize Device Management Servers from existing device management technologies (e.g. OMA-DM, TR-069) to implement the Device Management Functions.

A Device Management Server may be located in the Underlying Network using the Z reference point as depicted in Figure 2 or the Device Management Server may be located in the M2M Service Layer as depicted in Figure 3.

Figure 2 - Device Management Server in Underlying Network

Figure 3 - Device Management Server in M2M Service Layer

The ms interface is functionally the same interface regardless if the Device Management Server resides in the Underlying Network or the Service Layer. For example in Figure 2, the Device Management Server in the Underlying Network controls access of the exposed resources from the associated Device Management technology while, in the Figure 3, the Device Management Server in the M2M Service Layer controls access to the resources.

Since the M2M Service Layer interacts with multiple instances of Device Management Servers the selection of the Device Management Server is based on which Device Management Server controls access to the resources associated with the Device Management technology. Note that according to the deployment scenarios each Device Management Server may expose different permissions on those resources depending on the access control specified by the Device Management technologies.

##### 6.2.4.2.1.2	Device Management Server – Access Permissions

When an operation on a M2M Service Layer Resource is performed, the access permissions are checked by the security functions described in the Security CSF. The Security CSF uses the information in the Access Rights associated with the Resource to determine if the requested access to the Resource is granted.

If the access to the Resource is granted and the operation for the Resource utilizes Device Management Server external to the service Layer, the DMG CSF selects one or more among the authenticated Device Management Servers necessary to access the requested resources. The procedure for selecting the Device Management Server is FFS.