| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG#5 |
| Title:* | Mapping of cmdhPolicy resources for TS-0006 |
| Source:* | Qualcomm Inc. (TIA) |
| Contact: | Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com |
| Date:* | 2014-05-25 |
| Abstract:* | This contribution provides text for clause 7 of TS-0006 on mapping between cmdhPolicy resources and BBF TR-069 objects. |
| Agenda Item:* | MAS#10.4 |
| Work item(s): | MAS BBF TS |
| Document(s) Impacted* | TS-0006 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Add proposed text to clause 7 of TS-0006v0.2.0 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

Introduction

Following text is proposed to be added to clause 7 of TS-0006v0.2.0:

## ----------------------- start of text addition ---------------

## 7.x	Resource cmdhPolicy

The cmdhPolicy Resource represents a set of rules defining which CMDH parameters will be used by default when a request issued by a local originator contains the ec (event category) parameter but not all other CMDH parameters, see clause D.12 of TS-0001 [1].

The information shall be provisioned to the managed device using the SetParameterValues RPC of TR-069 [4].

| Attribute Name of cmdhPolicy | X_oneM2M Parameter |
| --- | --- |
| name | Device.X_oneM2M_CSE.{i}.CMDH.Policy.{i}.Name |
| mgmtLink to cmdhDefaults | Device.X_oneM2M_CSE.{i}.CMDH.Policy.{i}.DefaultRule |
| mgmtLink(s) to cmdhLimits | Device.X_oneM2M_CSE.{i}.CMDH.Policy.{i}.LimitRules |
| mgmtLink(s) to cmdhNetworkAccessRules | Device.X_oneM2M_CSE.{i}.CMDH.Policy.{i}.NetworkAccessECRules |
| mgmtLink(s) to cmdhBuffer | Device.X_oneM2M_CSE.{i}.CMDH.Policy.{i}.BufferRules |

## 7.x.1	Resource activeCmdhPolicy

The activeCmdhPolicy Resource provides a link to the currently active set of CMDH policies, see clause D.12.1 of TS-0001 [1].

| Attribute Name of activeCmdhPolicy | X_oneM2M Parameter |
| --- | --- |
| mgmtLink to cmdhPolicy | Device.X_oneM2M_CSE.{i}.CMDH.ActivePolicy.Active |

## 7.x.2	Resource cmdhDefaults

The cmdhDefaults Resource defines default CMDH policy values, see clause D.12.2 of TS-0001 [1].

| Attribute Name of cmdhDefaults | X_oneM2M Parameter |
| --- | --- |
| mgmtLink(s) to cmdhDefEcValue | Device.X_oneM2M_CSE.{i}.CMDH.Default.{i}.DefaultECRules |
| mgmtLink(s) to cmdhEcDefParamValues | Device.X_oneM2M_CSE.{i}.CMDH.Default.{i}.DefaultECParamRules |

## 7.x.3	Resource cmdhDefEcValues

The cmdhDefEcValues Resource represents a value for the ec (event category) parameter of an incoming request, see clause D.12.3 of TS-0001 [1].

| Attribute Name of cmdhDefEcValues | X_oneM2M Parameter |
| --- | --- |
| order | Device.X_oneM2M_CSE.{i}.CMDH.DefaultECRule.{i}.Order |
| defEcValue | Device.X_oneM2M_CSE.{i}.CMDH.DefaultECRule.{i}.EventCategory |
| requestOrigin | Device.X_oneM2M_CSE.{i}.CMDH.DefaultECRule.{i}.RequestOrigin |
| requestContext | Device.X_oneM2M_CSE.{i}.CMDH.DefaultECRule.{i}.RequestContext |
| requestContextNotification | Device.X_oneM2M_CSE.{i}.CMDH.DefaultECRule.{i}.RequestContextNotificationEnable |
| requestCharacteristics | Device.X_oneM2M_CSE.{i}.CMDH.DefaultECRule.{i}.RequestCharacteristics |

## 7.x.4	Resource cmdhEcDefParamValues

The cmdhEcDefParamValues Resource represents a specific set of default values for the CMDH related parameters rqet (request expiration timestamp), rset (result expiration timestamp), oet (operational execution time), rp (response persistence) and da (delivery aggregation) that are applicable for a given ec (event category) if these parameters are not specified in the request, see clause D.12.4 of TS-0001 [1].

| Attribute Name of cmdhEcDefParamValues | X_oneM2M Parameter |
| --- | --- |
| applicableEventCategory | Device.X_oneM2M_CSE.{i}.CMDH.DefaultECParamRule.{i}.EventCategory |
| defaultRequestExpTime | Device.X_oneM2M_CSE.{i}.CMDH.DefaultECParamRule.{i}.RequestExpTime |
| defaultResultExpTime | Device.X_oneM2M_CSE.{i}.CMDH.DefaultECParamRule.{i}.ResultExpTime |
| defaultOpExecTime | Device.X_oneM2M_CSE.{i}.CMDH.DefaultECParamRule.{i}.OperationExecTime |
| defaultRespPersistence | Device.X_oneM2M_CSE.{i}.CMDH.DefaultECParamRule.{i}.ResponsePersistence |
| defaultDelAggregation | Device.X_oneM2M_CSE.{i}.CMDH.DefaultECParamRule.{i}.DeleteAggregation |

## 7.x.5	Resource cmdhLimits

The cmdhLimits Resource represents limits for CMDH related parameter values, see clause D.12.5 of TS-0001 [1].

| Attribute Name of cmdhLimits | X_oneM2M Parameter |
| --- | --- |
| order | Device.X_oneM2M_CSE.{i}.CMDH.Limit.{i}.Order |
| requestOrigin | Device.X_oneM2M_CSE.{i}.CMDH.Limit.{i}.RequestOrigin |
| requestContext | Device.X_oneM2M_CSE.{i}.CMDH.Limit.{i}.RequestContext |
| requestContextNotification | Device.X_oneM2M_CSE.{i}.CMDH.Limit.{i}.RequestContextNotificationEnable |
| requestCharacteristics | Device.X_oneM2M_CSE.{i}.CMDH.Limit.{i}.RequestCharacteristics |
| limitsEventCategory | Device.X_oneM2M_CSE.{i}.CMDH.Limit.{i}.EventCategories |
| limitsRequestExpTime | Device.X_oneM2M_CSE.{i}.CMDH.Limit.{i}.RequestExpTime |
| limitsResultExpTime | Device.X_oneM2M_CSE.{i}.CMDH.Limit.{i}.ResultExpTime |
| limitsOpExecTime | Device.X_oneM2M_CSE.{i}.CMDH.Limit.{i}.OperationExecTime |
| limitsRespPersistence | Device.X_oneM2M_CSE.{i}.CMDH.Limit.{i}.ResponsePersistence |
| limitsDelAggregation | Device.X_oneM2M_CSE.{i}.CMDH.Limit.{i}.DeleteAggregation |

## 7.x.6	Resource cmdhNetworkAccessRules

The cmdhNetworkAccessRules Resource defines the usage of underlying networks for forwarding information to other CSEs during processing of CMDH-related requests in a CSE, see clause D.12.6 of TS-0001 [1].

| Attribute Name of cmdhNetworkAccessRules | X_oneM2M Parameter |
| --- | --- |
| applicableEventCategories | Device.X_oneM2M_CSE.{i}.CMDH.NetworkAccessECRule.{i}.EventCategories |
| mgmtLink(s) to cmdhNwAccessRule | Device.X_oneM2M_CSE.{i}.CMDH.NetworkAccessECRule.{i}.NetworkAccessRules |

## 7.x.7	Resource cmdhNwAccessRule

The cmdhNwAccessRule Resource define limits in usage of specific underlying networks for forwarding information to other CSEs during processing of CMDH-related requests, see clause D.12.7 of TS-0001 [1].

| Attribute Name of cmdhNwAccessRule | X_oneM2M Parameter |
| --- | --- |
| targetNetwork | Device.X_oneM2M_CSE.{i}.CMDH.NetworkAccessRule.{i}.TargetNetworks |
| minReqVolume | Device.X_oneM2M_CSE.{i}.CMDH.NetworkAccessRule.{i}.MinimumReqVolume |
| backOffParameters | Device.X_oneM2M_CSE.{i}.CMDH.NetworkAccessRule.{i}.BackoffTime |
|  | Device.X_oneM2M_CSE.{i}.CMDH.NetworkAccessRule.{i}.BackoffTimeIncrement |
|  | Device.X_oneM2M_CSE.{i}.CMDH.NetworkAccessRule.{i}.MaximumBackoffTime |
| otherConditions | Device.X_oneM2M_CSE.{i}.CMDH.NetworkAccessRule.{i}.???? |
| mgmtLink to allowedSchedule | Device.X_oneM2M_CSE.{i}.CMDH.NetworkAccessRule.{i}. AllowedSchedule |

## 7.x.8	Resource cmdhBuffer

The cmdhBuffer Resource represents limits in usage of buffers for temporarily storing information that needs to be forwarded to other CSEs during processing of CMDH-related requests in a CSE, see clause D.12.8 of TS-0001 [1].

| Attribute Name of cmdhBuffer | X_oneM2M Parameter |
| --- | --- |
| applicableEventCategory | Device.X_oneM2M_CSE.{i}.CMDH.Buffer.{i}.EventCategories |
| maxBufferSize | Device.X_oneM2M_CSE.{i}.CMDH.Buffer.{i}.MaximumBufferSize |
| storagePriority | Device.X_oneM2M_CSE.{i}.CMDH.Buffer.{i}.StoragePriority |

## ------------------------ end of text addition ----------------