| Input contribution Use case |
| --- |
| Use Case Title:* | Semantic smart building light control |
| Group Name:* | MAS WG5 |
| Source:* | China Unicom |
| Contact: | Junling Mao (maojl11@chinaunicom.cn) Peng Wang (wangpeng@chinaunicom.cn) Changwei Hu (hucw5@chinaunicom.cn) Xueqing Jia (jiaxq11@chinaunicom.cn) |
| Date:* | <2014-6-4> |
| Abstract:* | This contribution gives a use case named “semantic based smart building light control” to show potential semantic requirements. |
| Agenda Item:* | TBD |
| Work item(s): | oneM2M-WI-0005-Abstraction_&_Semantics_Capability_Enablement |
| Document(s) Impacted* | oneM2M-TR-0007-Study_on_Abstraction_and_Semantics_Enablement V0_9_0 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | For discussions and adoption in the Abstraction and Semantics Technical Report |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Title

### Semantic smart building light control

## Description

## The smart building light control use case has been mentioned in the oneM2M use case collection (see [i.29]. section 6.1) from group management aspects. In this contribution, we describe the smart building light control use case from semantic aspects. The light control for one target room is given as an example.

## In the use case, all the smart building appliances are connected with M2M gateway. M2M gateway and Smart building control center are connected with oneM2M platform.  The light control application sends the semantic query request to the smart building control center to find the desired appliances.

## In the following, we show how the use case could semantically be modelled based on OWL [i.26] ontology. There are two ontologies involved in this use case. One ontology is a basic M2M ontology named ontology A, which is referred by all actors (e.g. oneM2M platform, smart building control centre and light control application).  The other ontology is a specific ontology on light domain named ontology B, which is referred by light control application.

## Note that ontology A and ontology B are compatible ontologies in this use case, which indicates that there exists corresponding relationships between the same concepts (that may corresponding different vocabularies) in ontology A and ontology B. The compatibility can be realized in the ways such  has

## Ontology A/B refers to ontology B/A and use the vocabularies in ontology B/A to describe same concepts.

## There are some triple stores [i.28] to express corresponding relationships (e.g. be equivalent to) between the vocabularies in ontology A and ontology B. These triple stores can be added in ontology A or ontology B or be stored in other referenced ontologies.

## In this use case, the first way is adopted.

## Fig.1 Class Concepts in ontology A

## The class concepts in ontology A for this use case are described in Fig. 1, and the data properties model for class “light” and class “luminosity_sensor” in ontology A are described in Fig. 2. The class concepts in ontology B for this use case are described in Fig. 3. Some basic concepts in ontology B are referred from ontology A. The “brightness_adjustable_light” in ontology B is defined as the “light” which “brightness_adjustable” data property is “true”, i.e. the domain of class “brightness_adjustable_light” is union of the domain of class “light” and the domain of the class where “brightness_adjustable” data property is “true”.  Similarly, the “led_light” and “fluorescent_light” in ontology B are defined as the “light” which “kind” are “led” and “fluorescent” respectively.

## Fig. 2 data properties model in ontology A

## Fig. 3 Class related Concepts in ontology B

## Examples of   instances related to this use case are described in Fig. 4, where “type” means “instance of”.

## Fig. 4 Example of instances

## Source (as applicable)

## China Unicom

## Actors (as applicable)

### Light control application (developed by application provider)

### Smart building Control centre (operated by smart building service provider)

### M2M gateway (operated by M2M service provider)

### oneM2M platform  (operated by M2M service provider)

### Smart building appliances (installed by smart building service provider)

## Pre-conditions (if any)

### The smart building service provider establishes a business relationship with the M2M service provider so that the Smart building Control centre and Smart building appliances can use M2M gateway and oneM2M platform.

### All smart building appliances are registered in oneM2M platform, and smart building control centre can control smart building appliances via oneM2M platform.

## Triggers (if any)

### Light control application intends to control the light to adjust the brightness conditions in target room (perhaps when the motion sensor in that room detects that there are people entering that room).

## Normal Flow (as applicable)

## Since luminosity sensors can sense the brightness conditions of rooms, light control application sends semantic request to smart building control centre to find luminosity sensors in room701.

PREFIX building: <http://example.org /buildingOntology.owl#>

Select ?luminosity_sensor ?brightness

WHERE { building:room701 hasDevice ?luminosity_sensor.

?luminosity_sensor a building: luminosity_sensor.

?luminosity_sensor building:brightness ?brightness}

Given the Search results for the example in Fig. 4

| luminosity_sensor | brightness |
| --- | --- |
| SensorA | 200 |
| SensorB | 250 |

## Smart building Control centre forwards the semantic query requests to oneM2M platform.

## oneM2M platform returns the URI of target luminosity sensor resources and the associated semantic information.

## Light control application send requests to smart building control centre to create the group of the returned resources and to subscribe the brightness data of created group.

## Smart building control centre forwards the group management requests and subscription requests to oneM2M platform.

## The brightness data is notified to light control application.

## Light control application finds that the brightness is a little lower than desired value,  and intends to adjust the brightness of some lights instead of switching on more lights for power saving.  The Led light is preferred, and the brightness level of led light should be lower than the highest level 5. So light control application  sends semantic query request to smart building control centre to find the target brightness_adjustable light.

PREFIX building: <http://example.org/buildingOntology.owl#>

PREFIX light:< http://example.org /lightOntology.owl#>

Select ?light ?brightness_level

WHERE { building:room701 hasDevice ?light.

?light a light: brightness_adjustable_light.

?light a light: led_light.

?light building:brightness_level ?brightness_level.

FILTER(?brightness_level < 5)}

Given the Search results for the example in Fig. 4

| light | brightness_level |
| --- | --- |
| lightA | 2 |
| lightB | 3 |

## Smart building Control centre forwards the semantic query requests to oneM2M platform.

## Although  the instances of “light” (e.g. “lightA” and “lightB”) are semantically annotated based on ontology A which do not explicitly indicate that they are instances of “brightness_adjustable light” and “led_light”, with the help of reasoning, oneM2M platform can still correctly return the URI of target light resources and the associated semantic information.

## Light control application sends requests to smart building control centre to create the group of the returned resources.

## Smart building control centre forwards the group management requests to oneM2M platform.

## The Light control application sends the requests to adjust the brightness level of  created light group.

## Post-conditions (if any)

## High Level Illustration (as applicable)

### Potential requirements (as applicable)

### The oneM2M systems shall support the reasoning capability for deriving implicit knowledge from semantically annotated information according to referenced ontologies.