| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG#5 |
| Title:* | MAS-2014-0403-Overview_of_Modelling_Aspects |
| Source:* | NEC (ETSI, TTC) |
| Contact: | Martin Bauer, NEC, martin.bauer@neclab.eu Joerg Swetina, NEC, joerg.swetina@neclab.eu Ataru Kobayashi, NEC, a-kobayashi@df.jp.nec.com |
| Date:* | 2014-06-09 |
| Abstract:* | Updates to section 8.2, should be inserted before current Section 8.2.1 Device and Device Template Modelling Using Ontologies. Current section 8.2.1 is renumbered 8.2.3 Note that contribution MAS-2014-0404 (Modelling of Devices and Things) introduces a new section 8.2.2 |
| Agenda Item:* | TBD |
| Work item(s): | oneM2M-WI-0005-Abstraction_&_Semantics_Capability_Enablement |
| Document(s) Impacted* | oneM2M-TR-0007-Study_on_Abstraction_and_Semantics_Enablement V0_9_0 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* |  |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

New section 8.2.1

## 8.2	Modeling aspects for abstraction and semantics in oneM2M

Editor’s Note: should contain issues related to semantic modeling.

Editor’s Note: This section has been moved from 7.6 “Approaches for oneM2M”

### 8.2.1	Overview of modelling aspects

In Release 1, the oneM2M System enables applications to interact with each other using opaque, application specific containers, based on the resource concept. In order to enable interaction between applications that use similar data (e.g. temperature) but employ different encoding for these data a common abstraction layer can be built that provides services to convert the data into a abstracted, common format. With such an abstraction layer, regarding communication, application developers do not have to consider the underlying heterogeneity of their communication partners as this is abstracted away. However, applications in most cases still need to know a priori their communication partners as the Rel-1 discovery functionality is very limited and does not allow discovering other applications based on their semantics, e.g. the services they support. Data is treated as a black box without providing information about its structure and semantics. Thus this information needs to be known in advance by the respective applications and cannot be discovered. For a more flexible system that allows the reuse of information and functionality by different applications the structure and semantics of application data exchanged in the oneM2M System can be made explicit. Providing common abstractions not just for the purpose of interaction, but also for sharing information about the provided functionality is one aspect of it.

M2M allows applications to extend their reach into the physical world. Devices enable the sensing of, as well as the actuation on relevant aspects of the physical world. The physical world is populated by Things in a broad sense, including buildings, rooms, windows, roads, bottles etc. Ultimately, the applications interact with these Things, using the Devices for mediating this interaction. Figure 8.1 shows the underlying domain model.

Figure 8.1 Domain Model

Whereas the oneM2M Services are directly involved in the communication between application and Device, they nevertheless should model and provide support for real-world aspects as ultimately M2M is about supporting a mediated interaction between the applications and Things.

In the following subsections we want to further discuss how Devices and Things can be modelled in an appropriate way, how they can be represented and how the respective models can be used in future releases of the oneM2M System.

End of New section 8.2.1

Renumbering current section 8.2.1 to 8.2.3

### 8.2.3	Device and Device Template Modelling Using Ontologies

In this section we show an approach of how device types and device instances can be modelled in a homogeneous way using ontologies. The focus is on explaining the approach, not on completeness of the device types and device instance aspects being modelled. Due to their relevance for creating resource structures for representing devices in the oneM2M platform, the focus is on modelling input-output operations, but also the modeling of some manufacturer-specific aspects like manufacturere name and product identifier is shown.

The modelling follows a two-layer approach. The upper layer is for modelling device types, the lower layer for modelling device instances. The upper layer provides a given device type template that is modelled as classes and properties of an ontology. The device types are then modelled as instances of the classes and properties of this ontology. In the lower layer, the same device types that were modelled as instances of the template classes in the upper layer are now interpreted as the classes of the device ontologies. The actual individual devices can then be modelled by creating instances of these classes. The dual character of instance and class can, for example, be modelled in the OWL Full variant of the Web Ontology Language (OWL) [i.33].In the following we show an example of how a device type can be modelled based on a device type template and an individual device based on a device type.

Figure 7.X: Modelling of device type templates, device types and individual devices

Figure 7.X shows the three parts that make up the upper and lower layer, each consisting of classes and the corresponding instances. There are three and not four parts due to the dual character of the device type, which makes up an instance in the upper layer, but provides the class structure for the lower layer.

The device type template provides the structure that models a type of device, e.g. a manufacturer producing a temperature sensor can "fill out" the template by creating an ontology instance. In the case shown in figure 7.X RD2D_Enterprises manufactures an R2D2_Temperature_Sensor with the Product ID R2D2_4711. It has an operation called R2D2_TempReading, which in turn has a parameter R2D2_Temperature of type double. This information in turn serves as the structure for describing an individual temperature sensor of the type R2D2_Temperature_Sensor. It provides the basis for creating the resource structure representing the individual device in oneM2M, which is depicted on the right side of figure 7.X. The value of the R2D2_Temperature parameter, which refers to the temperature measured, is given as 12.345 represented as a double.

The example has been modelled as a set of OWL Full ontologies, using imports for including required classes and properties.

In the following tables, we describe the ontology classes (Table 7.X) and properties (Table 7.Y) for describing the device template in more detail. Where appropriate, subclasses can be used to model specialisations of common classes. In this case, this is done to distinguish different types of operations.

Table 7.X: Ontology Classes for Device Template

| Class => SubClass | Explanation |
| --- | --- |
| DeviceType | Manufacturer defined name/ID for a class of alike devices (= type) that are e.g. described in a product description |
| Operation | Identifies an operation of the device |
| => OutputOperation | The operation produces only an output message. The device does not expect correlated input/ack |
| => InputOperation | The operation consists of an input message only. The device does not produce correlated input/ack |
| => In-OutOperation | The operation receives an input message and produces a correlated output/ack |
| Parameter | Identifies a parameter of the operation |
| DataType | Identifies the datatype of the parameter (e.g. xsd: double) |
| Manufacturer | Name/ID of the manufacturer |
| Product ID | Manufacturer defined handle/ID to identify the type of the device, e.g. Type/Model-number. |

Table 7.Y: Object and Datatype Properties for Device Template

| Domain | Property | Range |  |
| --- | --- | --- | --- |
| DeviceType | hasOperation | Operation | Object Properties |
| Operation | hasParameter | Parameter |  |
| Parameter | hasParameterType | Datatype |  |
| DeviceType | hasManufacturer | xsd:string | Datatype Properties |
| DeviceType | hasProductID | xsd:string |  |

In the following tables, we describe the ontology classes (Table 7.A) and properties (Table 7.B) for describing individual device instances of the R2D2_Temperature_Sensor. A hierarchy of superclasses may be defined, e.g.Temperature_Sensor and Device superclasses could be introduced, which could be useful for discovering different types of temperature sensors from different manufacturers. Also, an Abstract Temperature Sensor providing a standardized interface to applications could be introduced, either on the same level as the R2D2_Temperature_Sensor, i.e. as a subclass of TemperatureSensor, or in a separate hiereachy. In the latter case the link to the concrete temperature sensors has to be explicitly modelled.

Table 7.A: Ontology Classes for R2D2_Temperature_Sensor

| Class => SubClass | Explanation |
| --- | --- |
| Device => Temperature_Sensor =>R2D2_Temperature_Sensor | User defined name/ID for a specific instance of the R2D2_Temperature_Sensor instance., e.g. My_SensorNo_3 |
| R2D2_TempReading | Specific operation of the instance of R2D2_Temperature_Sensor |
| R2D2_Temperature | Specific parameter of the instance of R2D2_TempReading |
| Metadata | Metadata related to the value of an R2D2_Temperature |

Table 7.B: Object and Datatype Properties for R2D2_Temperature_Sensor

| Domain | Property | Range |  |
| --- | --- | --- | --- |
| R2D2_Temperature_Sensor | hasTemperatureOperation | R2D2_TempReading | Object Properties |
| R2D2_TempReading | hasTemperatureParameter | R2D2_Temperature |  |
| R2D2_Temperature | hasMetadata | Metadata |  |
| R2D2_Temperature | hasValue | xsd:double | Datatype Properties |

The listing below gives an example of how an individual device instance of the R2D2_Temperature_Sensor is modelled in OWL, using the more concise and readable Turtle representation [i.36], instead of the more commonly used RDF/XML notation [i.37].

Device Instance (in OWL/Turtle)

@prefix : <http://InstanceOntology#> .

@prefix owl: <http://www.w3.org/2002/07/owl#> .

@prefix rdf: <http://www.w3.org/1999/02/22-rdf-syntax-ns#> .

@prefix xsd: <http://www.w3.org/2001/XMLSchema#> .

@prefix dev: <http://DeviceOntology#> .

@prefix dev-temp: <http://DeviceTemplateOntology#> .

@base <http://InstanceOntology> .

<http://InstanceOntology> 	rdf:type 	owl:Ontology ;

owl:imports  	<http://DeviceOntology>

:Resource:My_SensorNo_3 	rdf:type 	dev-temp:R2D2_Temperature_Sensor,

owl:NamedIndividual;

dev:hasTemperatureOperation		:R2D2_TempReading .

:R2D2_TempReading	 	rdf:type 	dev-temp:R2D2_TempReading ,

owl:NamedIndividual ;

dev:hasTemperatureParameter		:R2D2_Temperature .

:R2D2_Temperature		rdf:type dev-temp:R2D2_Temperature,
owl:NamedIndividual;
dev:hasValue			  “23.45"^^xsd:double .

End of Renumbering current section 8.2.1 to 8.2.3