| CHANGE REQUEST |
| --- |
| Group Name:* | MAS#11 |
| Source:* | Thierry GARNIER, Gemalto N.V, thierry.garnier@gemalto.com |
| Format:* | Plenary |
| Date:* | 2014-6-09 |
| Contact:* | Thierry GARNIER, Gemalto N.V, thierry.garnier@gemalto.com |
| Reason for Change/s:* | This contribution is to upgrade the resource mappings for OMA LWM2M. |
| CR against: Release* | Release1 |
| CR against: TS/TR* | TS-0005, Management Enablement (OMA) ver 0.1.2 |
| Clauses/Sub Clauses* | 6.2 ~ 6.3 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution is to upgrade  the resource mapping between oneM2M and OMA LWM2M

### -----------------------Start of change 1-------------------------------------------

# 6.	OMA Lightweight M2M 1.0

## 6.1	Mapping of basic data types

## 6.2	Mapping of Identifiers

OMA LWM2M   [6] defines specific identifiers for entities (e.g. End Point Client Name or Device identifier, Server identifier, Objects identifiers ..) To enable the device management using OMA LWM2M  [6], oneM2M identifiers need to be mapped to identifiers specified by OMA LWM2M [6].

6.2.1 Device identifier

A unique identifier is assigned to the Device and referenced as Endpoint Client Name in OMA LWM2M [6].This value is globally unique and is formatted as a URN.

Several URN formats are recommended in OMA LWM2M [6] as UUID URN defined in [RFC4122], OPS URN defined in [TR-069], IMEI URN defined in [3GPP-TS_23.003]….

## This Device identifiers shall map onto the oneM2M Node Identifier (M2M-Node-ID)

6.2.2 Object identifier

In OMA LWM2M [6], each object is characterized by a unique identifier represented by an integer. This identifier is provided  by OMNA (OMA Naming Authority) and is registered as a unique URN :

urn:oma:lwm2m:{oma,ext,x}:objectID (e.g. the LWM2M 1.0  Device Object (ObjectID:3) is registered as urn:oma:lwm2m:oma:3 ).

## The context of a given oneM2M <mgmtObj> Resource is represented by the objectId attribute which contains the reference to OMA LWM2M [6] Object identifier expressed as OMNA-registered URN.

## Editor Notes if objectID multiplicity is agreed by ARC group the follwing sentence will replace the previous one.The context of a given oneM2M <mgmtObj> Resource is represented by the objectId attribute which can contain from 1 to n references to OMA LWM2M [6] Object identifiers expressed as OMNA registered URN.

6.2.3 Object Instance Identifier

OMA LWM2M [6] permits objects to have multiple object instances where each object instance is contained in the objectPath attribute of the <mgmtObj> Resource within the context of the Resource’s objectId as described in previous section.

Editor Notes if objectPath multiplicity is agreed by ARC group the following sentence will be added.The objectPath attribute in <mgmtObj> Resource contains one (or several) URI(s) representing the local path(s) where the Object Instance(s) are located.

## 6.3	Mapping of resources

This section describes how to map the  <mgmtObj> Resources specified in the Annex D of [1] to the relevant Objects specified  in OMA LWM2M [6].

### 6.3.1	General Mapping Assumptions

OMA LWM2M[6] implements the functionalities of the device management and M2M service enablement as  Objects.  An Object is a collection of resources which are related to a specific management functionality. For example the Firmware Update Object contains all the resources used for firmware update purpose. Before to be able of  fulfilling its role, an Object shall be firstly instantiated into an Object Instance.

Since <mgmtObj> Resources are for providing specific management functionalities, the attributes of a given <mgmtObj> Resource shall be mapped to the resources of one or several LWM2M Object Instances within the context of the Resource’s objectId as defined in sub-section 6.2.2..

The objectPath is a local context which has to be combined with a given <mgmtObj> Resource’s attribute for realizing the final mapping to the targeted OMA LWM2M [6] resource.

Editor Notes if objectPath multiplicity is agreed by ARC group the following sentence will be added. In case the objectPath is multiple (several Object Instances  are referenced in that Resource), a specified couple composed of one element of the objectId list and one element of objectPath list will be associated to a given Resource attribute for realizing the final mapping to the targeted OMA LWM2M [6] resource.

### 6.3.2	Resource [memory]

The Resource [memory] provides memory related information. For OMA LWM2M, this Resource shall be mapped to the unique Instance of LWM2M Device Object (LWM2M ObjectID: 3) .

The context of this Resource is the following:

| Context | Mapping |
| --- | --- |
| objectId | urn:oma:lwm2m:oma:3 |
| objectPath | /3/0 (instance 0 of Object 3) |

The attributes of this Resource shall be mapped to specific resources of the LWM2M Device Object Instance as follows:

| Attribute Name of [memory] | Mapping to resources in LWM2M Device Object Instance |
| --- | --- |
| memAvailable | 10 : estimated current available amount of memory in KB |
| memTotal | 21 : total amount of storage space in KB in the LWM2M Device |

### 6.3.3	Resource [battery]

The Resource [battery] provides battery related information. For  OMA LWM2M, this Resource shall be mapped to the unique Instance of LWM2M Device Object (LWM2M ObjectID: 3).

The context of this Resource is the following

| Context | Mapping |
| --- | --- |
| objectId | urn:oma:lwm2m:oma:3 |
| objectPath | /3/0 |

The attributes of this  Resource shall be mapped to specific resources of the LWM2M Device Object Instance  as follows:

| Attribute Name of [battery] | Mapping to resources in LWM2M Device Object Instance |
| --- | --- |
| batteryLevel | 9 : current battery level as percentage |
| batteryStatus | 20 : contains the battery status |

### 6.3.4	Resource [deviceInfo]

The Resource [deviceInfo] provides device related information. For OMA LWM2M, this Resource shall be mapped to the unique Instance of LWM2M Device Object (LWM2M ObjectID: 3).

The context of this Resource is the following

| Context | Mapping |
| --- | --- |
| objectId | urn:oma:lwm2m:oma:3 |
| objectPath | /3/0 |

The attributes of this Resource shall be mapped to specific resources of the LWM2M Device Object Instance  as follows:

| Attribute Name of [deviceInfo] | Mapping to resources in LWM2M Device Object Instance |
| --- | --- |
| deviceLabel | 2 : Serial Number |
| Manufacturer | 0 : Manufacturer name |
| Model | 1 : Model Number |
| deviceType | 17 : the class of the device |
| fwVersion | 3 : Firmware Version |
| swVersion | 19 : Software Version of the device |
| hwVersion | 18 : Hardware version of the device |

### 6.3.5	Resource [reboot]

The Resource [reboot] is used for rebooting the device. For  OMA LWM2M, this Resource shall be mapped to the unique Instance of LWM2M Device Object (LWM2M ObjectID: 3).

The context of this Resource is the following

| Context | Mapping |
| --- | --- |
| objectId | urn:oma:lwm2m:oma:3 |
| objectPath | /3/0 |

The attributes of this Resource shall be mapped to  LWM2M Device Object Instance  as follows:

| Attribute Name of [reboot] | Mapping to resources in LWM2M Object Instance |
| --- | --- |
| reboot | 4 : reboot the LWM2M Device to restore the Device from unexpected firmware failure |
| factoryReset | 5 : Perform Factory Reset : the LWM2M device return to the same configuration as at the initial deployment. |

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?