| CHANGE REQUEST |
| --- |
| Group Name:* | MAS#11 |
| Source:* | Seungkyu Park, LG Electronics, seungk.park@lge.com |
| Format:* | Plenary / Teleconference |
| Date:* | 2014-6-12 |
| Contact:* | Seungkyu Park, LG Electronics, seungk.park@lge.com |
| Reason for Change/s:* | to provide the procedure mapping for the LWM2M |
| CR against: Release* | Release -1 |
| CR against: TS/TR* | TS-0005 |
| Clauses/Sub Clauses* | 6.4 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution is to provide the procedure mapping for the LWM2M.

### -----------------------Start of change 1-------------------------------------------

## 6.4	Mapping of procedures for management

### 6.4.1. Mapping for <mgmtObj> Resource Primitives

In this section, the oneM2M Primitives are mapped to the LWM2M operations. The mapped LWM2M operations may be executed either by the Piggy-backed response or Separate response as specified by LWM2M. Which response is used is implementation issue, and is independent on whether the Update Primitive is requested as blocking or non-blocking.

#### 6.4.1.1 Create Primitive for <mgmtObj> Resource

The Create Request primitive for the <mgmtObj> Resource, as described in [ref to PRO TS], shall be mapped to LWM2M Create operations that create the corresponding LWM2M Objects. Depending on the mgmtDefinition attribute of the <mgmtObj> Resource (i.e., [memory], [battery], [deviceInfo], etc.), the associated LWM2M Object as specified in the clause 6.3 should be created.

Receiving Create Request primitive does not imply that the LWM2M Create operations shall be always performed since, on receiving the Create Request primitive, the corresponding LWM2M Objects may already exist in the device. For instance, after discovering the LWM2M Objects, the MN or ASN creates <mgmtObj> Resource in the IN-CSE, and in this case the IN-CSE does not need to create the LWM2M Objects.

In case that the LWM2M Objects are successfully created after receiving the Create Request primitive, then the objectID and objectPath attribute should be properly set based on the LWM2M Objects.

The result of creating the LWM2M Object should be mapped to the Create Response primitive for the <mgmtObj> Resource as indicated by the status code mapping in the clause x.y.

#### 5.4.1.2 Retrieve Primitive for <mgmtObj> Resource

The Retrieve Request primitive for the <mgmtObj> Resource, as described in [ref to PRO TS], shall be mapped to LWM2M Read Operations that retrieve the corresponding LWM2M Objects. Depending on the mgmtDefinition attribute of the <mgmtObj> Resource (i.e., [memory], [battery], [deviceInfo], etc.), the associated LWM2M Object as specified in the clause 6.3 shall be retrieved.

The result of retrieving the LWM2M Object should be mapped to the Retrieve Response primitive for the <mgmtObj> Resource as indicated by the status code mapping in the clause x.y.

#### 5.4.1.3 Update Primitive for <mgmtObj> Resource

The Update Request Primitive for <mgmtObj> Resource can be used to modify the LWM2M Objects or to execute the actions related to LWM2M Objects. The mapping in either cases shall be different.

##### 5.4.1.3.1 Update Primitive for Replacing Data in the Management Object

This is the case that the Update Primitive targets the attribute that is mapped to the LWM2M resource that supports Write operation as specified in the clause 6.3. The Update Request primitive for the <mgmtObj> Resource shall be mapped to the LWM2M Write operation that write to the corresponding LWM2M resource. Depending on the mgmtDefinition attribute of the <mgmtObj> Resource (i.e., [memory], [battery], [deviceInfo], etc.), the associated LWM2M Object as specified in the clause 6.3 shall be updated.

The result of updating LWM2M resource should be mapped to the Update Response primitive for the <mgmtObj> Resource as indicated by the status code mapping in the clause x.y.

##### 5.4.1.3.2 Update Primitive for Executing Management Commands

This is the case that the Update Primitive targets the attribute that is mapped to the LWM2M resource that supports the Execute operation. The Update Request primitive for the <mgmtObj> Resource, as described in [ref to PRO TS], shall be mapped to LWM2M Execute operation that execute actions in LWM2M. Depending on the mgmtDefinition attribute of the <mgmtObj> Resource (i.e., [memory], [battery], [deviceInfo], etc.), the associated LWM2M resource as specified in the clause 6.3 shall be executed.

The result of executing the LWM2M resource should be mapped to the Update Response primitive for the <mgmtObj> Resource as indicated by the status code mapping in the clause x.y.

#### 5.4.1.4 Delete Primitive for <mgmtObj> Resource

The Delete Request primitive for the <mgmtObj> Resource, as described in [ref to PRO TS], shall be mapped to LWM2M Delete operations that delete the corresponding LWM2M Objects. Depending on the mgmtDefinition attribute of the <mgmtObj> Resource (i.e., [memory], [battery], [deviceInfo], etc.), the associated LWM2M Object as specified in the clause 6.3 should be deleted.

Receiving Delete Request primitive does not imply that the corresponding LWM2M Objects shall be always deleted. They may not be deleted if the LWM2M Objects are used by other entities such as the LWM2M Server.

The result of deleting the LWM2M Object should be mapped to the Delete Response primitive for the <mgmtObj> Resource as indicated by the status code mapping in the clause x.y.

### 5.4.2 oneM2M Resource Specific Procedure Mapping

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?