| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG#5 |
| Title:* | Mapping of cmdhPolicy resources for TS-0005 |
| Source:* | Qualcomm Inc. (TIA) |
| Contact: | Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com |
| Date:* | 2014-07-21 |
| Abstract:* | This contribution provides text for clauses 5 an 6 of TS-0005 on mapping between cmdhPolicy resources and both OMA-DM and OMA-LWM2M objects. R01: Cleanup of text after first discussion at MAS#11.2 Addition of Annex A.x.1 Note this revision is not complete. R02 will be uploaded shortly. R02: completion of the revision of clause 5.3 (revision of clause 6.3 is still pending) |
| Agenda Item:* | MAS#12 |
| Work item(s): | MAS Management Enablement (OMA) TS |
| Document(s) Impacted* | TS-0005 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Add proposed text to clauses 5 and 6 and of TS-0005v0.2.0 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

Introduction

Following text is proposed to be added to clauses 5.3 and 6.3 of TS-0005v0.2.0 (Management Enablement OMA).

For OMA-DM it is proposed to specify a new OMA DM Management Object, denoted  “M2M cmdhPolicies MO (MCMDHMO)” compliant with the best practices described in OMA-WP-Management_Object_Design_Guidelines-20130129-A.  This is not in the scope of this contribution.  However, the structure of this MCMDHMO assumed here is essentially the same as assumed in TS-0006.

For OMA LWM2M also a respective root object  needs to be defined. The text proposed here for clause 6.3 is very preliminary

R03:

- Root node of MCMDHMO changed from cmdhPolicies to placeholder node <x>

- Some editorial corrections of text in clause 5.3, correction of some attribute names

- Removal of all proposed text for clause 6.3 (mapping to OMA LWM2M)

- Text proposed in the previous revision to be included into Annex A has been moved to clause 5.6

- Completion of the incomplete text in clause 5.6, correction of some attribute names

  - data types marked yellow need to be mapped from m2m-specific types which may require reconsideration

- Additions to table in clause 5.1 (Mapping of basic data types)

## R03:

## Updated tables for list data type

## Updating figure for list data type, optional nodes <x>?, dashed leaf nodes

## ----------------------- start of text addition 1 ---------------

## 5.3.x	Resource cmdhPolicy]

The Resource Type [cmdhPolicy] represents a set of rules associated with a specific CSE that govern the behaviour of that CSE regarding rejecting, buffering and sending request or response messages via the Mcc reference point. See clause D.12 of TS-0001 [1] for a detailed high-level description of the overall structure of the [cmdhPolicy] resource.

Regardless of OMA DM 1.3 and OMA DM 2.0, this resource shall be mapped to M2M cmdhPolicies MO (MCMDHMO) (urn:oma:mo:ext-onem2m-mcmdhmo:1.0).  The root node of the MCMDHMO is denoted in the following by the leftmost placeholder node <x>

The Resource Type [cmdhPolicy] is a multi-instance Resource where each instance of the Resource shall map to an instance of a <x>/cmdhPolicy/<x> node.

The attributes of an instance of [cmdhPolicy] shall be mapped to nodes of the MCMDHMO as follows.

Table 5.3.x-1: Resource [cmdhPolicy]

| Attribute Name of [cmdhPolicy] | Mapping to Nodes in Management Object |
| --- | --- |
| Name | <x>/cmdhPolicy/<x>/name |
| cmdhDefaults | <x>/cmdhPolicy/<x>/defaultRule |
| cmdhLimits | <x>/cmdhPolicy/<x>/limitRules |
| cmdhNetworkAccessRules | <x>/cmdhPolicy/<x>/networkAccessECRules |
| cmdhBuffer | <x>/cmdhPolicy/<x>/bufferRules |

### 5.3.x.1	Resource [activeCmdhPolicy]

The Resource [activeCmdhPolicy] provides a link to the currently active set of CMDH policies, see clause D.12.1 of TS-0001 [1].

The Resource [activeCmdhPolicy]  includes an attribute enable which points to the currently active instance of a <x>/cmdhPolicy  node.

Table 5.3.x.1-1: Resource [activeCmdhPolicy]

| Attribute Name of [activeCmdhPolicy] | Mapping to Nodes in Management Object |
| --- | --- |
| cmdhPolicy | <x>/activeCmdhPolicy/<x>/enable At most one <cmdhPolicy> instance shall be enabled at a time. Hence, there can only be a single instance of the activeCmdhPolicy whose enable parameter points to the active CMDH policy. |

### 5.3.x.2	Resource [cmdhDefaults]

The Resource [cmdhDefaults] defines default CMDH policy values, see clause D.12.2 of TS-0001 [1].

Regardless of OMA DM 1.3 and OMA DM 2.0, this resource shall be mapped to M2M cmdhPolicies MO (MCMDHMO) (urn:oma:mo:ext-onem2m-mcmdhmo:1.0).

The Resource [cmdhDefaults] is a multi-instance Resource where each instance of the Resource shall map to an instance of the <x>/cmdhDefaults/<x> node.

The attributes of an instance of [cmdhDefaults] shall be mapped to nodes of the MCMDHMO as follows.

Table 5.3.x.2-1: Resource [cmdhDefaults]

| Attribute Name of [cmdhDefaults] | Mapping to Nodes in Management Object |
| --- | --- |
| cmdhDefEcValue | <x>/cmdhDefaults/<x>/defaultECRules |
| cmdhEcDefParamValues | <x>/cmdhDefaults/<x>/defaultECParamRules |

### 5.3.x.3	Resource  [cmdhDefEcValues]

The Resource  [cmdhDefEcValues] represents a default value for the ec (event category) parameter of an incoming request, see clause D.12.3 of TS-0001 [1].

Regardless of OMA DM 1.3 and OMA DM 2.0, this resource shall be mapped to M2M cmdhPolicies MO (MCMDHMO) (urn:oma:mo:ext-onem2m-mcmdhmo:1.0).

The Resource  [cmdhDefEcValues] is a multi-instance Resource where each instance of the Resource shall map to an instance of the <x>/cmdhDefEcValues/<x> node.

The attributes of an instance of [cmdhDefEcValues] shall be mapped to nodes of the MCMDHMO as follows.

Table 5.3.x.3-1: Resource  [cmdhDefEcValues]

| Attribute Name of [cmdhDefEcValues] | Mapping to Nodes in Management Object |
| --- | --- |
| Order | <x>/cmdhDefEcValue/<x>/order |
| defEcValue | <x>/cmdhDefEcValue/<x>/defEcValue |
| requestOrigin | <x>/cmdhDefEcValue/<x>/requestOrigin |
| requestContext | <x>/cmdhDefEcValue]/<x>/requestContext |
| requestContextNotification | <x>/cmdhDefEcValue]/<x>/requestContextNotification |
| requestCharacteristics | <x>/cmdhDefEcValue/<x>/requestCharacteristics |

### 5.3.x.4	Resource  [cmdhEcDefParamValues]

The Resource  [cmdhEcDefParamValues] represents a specific set of default values for the CMDH related parameters rqet (request expiration timestamp), rset (result expiration timestamp), oet (operational execution time), rp (response persistence) and da (delivery aggregation) that are applicable for a given ec (event category) if these parameters are not specified in the request, see clause D.12.4 of TS-0001 [1].

Regardless of OMA DM 1.3 and OMA DM 2.0, this resource shall be mapped to M2M cmdhPolicies MO (MCMDHMO) (urn:oma:mo:ext-onem2m-mcmdhmo:1.0).

The Resource  [cmdhEcDefParamValues] is a multi-instance Resource where each instance of the Resource shall map to an instance of the <x>/cmdhEcDefParamValues/<x> node.

The attributes of an instance of [cmdhEcDefParamValues] shall be mapped to nodes of the MCMDHMO as follows.

Table 5.3.x.4-1: Resource  [cmdhEcDefParamValues]

| Attribute Name of [cmdhEcDefParamValues] | Mapping to Nodes in Management Object |
| --- | --- |
| applicableEventCategory | <x>/cmdhEcDefParamValues/<x>/applicableEventCategory |
| defaultRequestExpTime | <x>/cmdhEcDefParamValues/<x>/defaultRequestExpTime |
| defaultResultExpTime | <x>/cmdhEcDefParamValues/<x>/defaultResultExpTime |
| defaultOpExecTime | <x>/cmdhEcDefParamValues/<x>/defaultOpExecTime |
| defaultRespPersistence | <x>/cmdhEcDefParamValues/<x>/defaultRespPersistence |
| defaultDelAggregation | <x>/cmdhEcDefParamValues/<x>/defaultDelAggregation |

### 5.3.x.5	Resource [cmdhLimits]

The Resource [cmdhLimits] represents limits for CMDH related parameter values, see clause D.12.5 of TS-0001 [1].

Regardless of OMA DM 1.3 and OMA DM 2.0, this resource shall be mapped to M2M cmdhPolicies MO (MCMDHMO) (urn:oma:mo:ext-onem2m-mcmdhmo:1.0).

The Resource [cmdhLimits] is a multi-instance Resource where each instance of the Resource shall map to an instance of the <x>/cmdhLimits/<x> node.

The attributes of an instance of [cmdhLimits] shall be mapped to nodes of the MCMDHMO as follows.

Table 5.3.x.5-1: Resource [cmdhLimits]

| Attribute Name of [cmdhLimits] | Mapping to Nodes in Management Object |
| --- | --- |
| Order | <x>/cmdhLimits/<x>/order |
| requestOrigin | <x>/cmdhLimits/<x>/requestOrigin |
| requestContext | <x>/cmdhLimits/<x>/requestContext |
| requestContextNotification | <x>/cmdhLimits/<x>/requestContextNotification |
| requestCharacteristics | <x>/cmdhLimits/<x>/requestCharacteristics |
| limitsEventCategory | <x>/cmdhLimits/<x>/limitsEventCategory |
| limitsRequestExpTime | <x>/cmdhLimits/<x>/limitsRequestExpTime |
| limitsResultExpTime | <x>/cmdhLimits/<x>/limitsResultExpTime |
| limitsOpExecTime | <x>/cmdhLimits/<x>/limitsOpExecTime |
| limitsRespPersistence | <x>/cmdhLimits/<x>/limitsRespPersistence |
| limitsDelAggregation | <x>/cmdhLimits/<x>/limitsDelAggregation |

### 5.3.x.6	Resource [cmdhNetworkAccessRules]

The Resource [cmdhNetworkAccessRules] defines the usage of underlying networks for forwarding information to other CSEs during processing of CMDH-related requests in a CSE, see clause D.12.6 of TS-0001 [1].

Regardless of OMA DM 1.3 and OMA DM 2.0, this resource shall be mapped to M2M cmdhPolicies MO (MCMDHMO) (urn:oma:mo:ext-onem2m-mcmdhmo:1.0).

The Resource [cmdhNetworkAccessRules] is a multi-instance Resource where each instance of the Resource shall map to an instance of the <x>/cmdhNetworkAccessRules/<x> node.

The attributes of an instance of [cmdhNetworkAccessRules] shall be mapped to nodes of the MCMDHMO as follows.

Table 5.3.x.6-1: Resource [cmdhNetworkAccessRules]

| Attribute Name of [cmdhNetworkAccessRules] | Mapping to Nodes in Management Object |
| --- | --- |
| applicableEventCategories | <x>/cmdhLimits/<x>/applicableEventCategories |
| cmdhNwAccessRule | <x>/cmdhLimits/<x>/NetworkAccessRule |

### 5.3.x.7	Resource [cmdhNwAccessRule]

The Resource [cmdhNwAccessRule] define limits in usage of specific underlying networks for forwarding information to other CSEs during processing of CMDH-related requests, see clause D.12.7 of TS-0001 [1].

Regardless of OMA DM 1.3 and OMA DM 2.0, this resource shall be mapped to M2M cmdhPolicies MO (MCMDHMO) (urn:oma:mo:ext-onem2m-mcmdhmo:1.0).

The Resource [cmdhNwAccessRule] is a multi-instance Resource where each instance of the Resource shall map to an instance of the <x>/cmdhNwAccessRule/<x> node.

The attributes of an instance of [cmdhNwAccessRule] shall be mapped to nodes of the MCMDHMO as follows.

Table 5.3.x.7-1: Resource [cmdhNwAccessRule]

| Attribute Name of [cmdhNwAccessRule] | Mapping to Nodes in Management Object |
| --- | --- |
| targetNetwork | <x>/cmdhNwAccessRule]/<x>/targetNetwork |
| minReqVolume | <x>/cmdhNwAccessRule/<x>/minReqVolume |
| backOffParameters | <x>/cmdhNwAccessRule/<x>/backOffParameters |
| otherConditions | <x>/cmdhNwAccessRule/<x>/otherConditions |
| allowedSchedule | <x>/cmdhNwAccessRule/<x>/allowedSchedule |

### 5.3.x.8	Resource [cmdhBuffer]

The Resource [cmdhBuffer] represents limits in usage of buffers for temporarily storing information that needs to be forwarded to other CSEs during processing of CMDH-related requests in a CSE, see clause D.12.8 of TS-0001 [1].

Regardless of OMA DM 1.3 and OMA DM 2.0, this resource shall be mapped to M2M cmdhPolicies MO (MCMDHMO) (urn:oma:mo:ext-onem2m-mcmdhmo:1.0).

The Resource [cmdhBuffer] is a multi-instance Resource where each instance of the Resource shall map to an instance of the <x>/cmdhBuffer/<x>/ node.

The attributes of an instance of [cmdhBuffer] shall be mapped to nodes of the MCMDHMO as follows.

Table 5.3.x.7-1: Resource [cmdhBuffer]

| Attribute Name of [cmdhBuffer] | Mapping to Nodes in Management Object |
| --- | --- |
| applicableEventCategory | <x>/cmdhNwAccessRule/<x>/applicableEventCategory |
| maxBufferSize | <x>/cmdhNwAccessRule/<x>/maxBufferSize |
| storagePriority | <x>/cmdhNwAccessRule/<x>/storagePriority |

## ------------------------ end of text addition 1 ----------------

## ------------------------ start of text addition 2 ----------------

## 5.6	New Management Objects

Editor’s Note: The section specifies the definition of new data models if needed based on the requirements of oneM2M. The definition of new data models in this section need to be liaised to OMA to create corresponding MOs in OMA DM.

5.6.1		M2M CMDH Policies MO (MCMDHMO)

The M2M CMDH Policies MO (MCMDHMO) resides in the Management Tree of any ASN or MN which support Device Management via OMA DM 1.3 and OMA DM 2.0. This MO corresponds to instances of the cmdhPolicy resource and its child resources which all represent subtypes of the mgmtObj resource type, as specified in Annex D.12 of the oneM2M functional architecture TS-0001 [x].

This MO maintains information regarding the remote provisioning and management of CMDH policies.

Figure 5.6.1-1 gives the pictorial description of the MCMDHMO.

The various nodes within this MO are described as follows.

| <x> |
| --- |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | node | Get |  |
|  | This placeholder node is the root node for the MCMDHMO which includes all MOs related to CMDH Policy management. The parent node of this node defines the location of this MO in the Management Tree. The Management Object Identifier for the MCMDHMO shall be: "urn:oma:mo:ext-onem2m-mcmdhmo:1.0". |
| <x>/cmdhPolicy |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | node | Get |  |
|  | This interior node is the parent node of instances of cmdhPolicy MOs. |
| <x>/cmdhPolicy/<x> |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | OneOrMore | node | Get |  |
|  | This placeholder interior node represents the specific instances of cmdhPolicy MOs. |
| <x>/cmdhPolicy/<x>/name |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | chr | Get |  |
|  | This leaf node contains the name attribute of a cmdhPolicy resource instance. |  |

| <x>/cmdhPolicy/<x>/defaultRule |
| --- |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | chr | Get |  |
|  | This leaf node includes a reference (mgmntLink) to an instance of a cmdhDefaults node. |

| <x>/cmdhPolicy/<x>/limitRules |
| --- |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | OneOrMore | chr | Get |  |
|  | This leaf node includes a reference (mgmtLink) to an instance of a cmdhLimits node. |

| <x>/cmdhPolicy/<x>/NetworkAccessECRules |
| --- |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | OneOrMore | chr | Get |  |
|  | This leaf node includes a reference (mgmtLink) to an instance of a cmdhNetworkAccess node. |

| <x>/cmdhPolicy/<x>/bufferRules |
| --- |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | OneOrMore | chr | Get |  |
|  | This leaf node includes a reference (mgmntLink) to an instance of a cmdhBuffer node. |

Figure 5.6.1-1: Structure of OMA-DM compatible M2M CMDH Policies MO (MCMDHMO)

| <x>/activeCmdhPolicy |
| --- |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | node | Get |  |
|  | This interior node is the parent node of an activeCmdhPolicy MO instance. |
| <x>/activeCmdhPolicy/<x> |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | node | Get |  |
|  | This placeholder node represents an instance of a activeCmdhPolicy MO. |
| <x>/activeCmdhPolicy/<x>/enable |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | chr | Get |  |
|  | This leaf node includes a reference (mgmtLink) to the currently active instance of the cmdhPolicy MO. |
| <x>/cmdhDefaults |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | node | Get |  |
|  | This interior node is the parent node of instances of cmdhPolicy MOs. |
| <x>/cmdhDefaults/<x> |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | OneOrMore | node | Get |  |
|  | This placeholder node represents the instances of cmdhDefaults MOs. |
| <x>/cmdhDefaults/<x>/defaultECRules |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | OneOrMore | chr | Get |  |
|  | This leaf node includes a reference (mgmtLink) to an instance of the cmdhDefEcValue MO. |
| <x>/cmdhDefaults/<x>/defaultECParamRules |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | OneOrMore | chr | Get |  |
|  | This leaf node includes a reference (mgmtLink) to an instance of the cmdhEcDefParamValue MO. |  |
| <x>/cmdhDefEcValue |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | OneOrMore | node | Get |  |
|  | This interior node is the parent node of cmdhDefEcValue MOs. |
| <x>/cmdhDefEcValue/<x> |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | OneOrMore | node | Get |  |
|  | This placeholder interior node represents the instances of the cmdhDefEcValue MOs. |
| <x>/cmdhDefEcValue/<x>/order |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | int | Get |  |
|  | This leaf node contains the order attribute of the cmdhDefEcValue resource instance. |
| <x>/cmdhDefEcValue/<x>/defEcValue |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | chr | Get |  |
|  | This leaf node contains the defEcValue attribute of the cmdhDefEcValue resource instance. |
| <x>/cmdhDefEcValue/<x>/requestOrigin |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | node | Get |  |
|  | This interior node contains the requestOrigin attribute of the cmdhDefEcValue resource instance. |
| <x>/cmdhDefEcValue/<x>/requestOrigin/<x> |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | node | Get |  |
|  | This placeholder node represents the root of the list of requestOrigin values. |
| <x>/cmdhDefEcValue/<x>/requestOrigin/<x>/m2mid |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | OneOrMore | chr | Get |  |
|  | This leaf node contains one list element of the requestOrigin attribute. |
| <x>/cmdhDefEcValue/<x>/requestContext |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Optional | ZeroOrOne | chr | Get |  |
|  | This leaf node contains the requestContext attribute of the cmdhDefEcValue resource instance. |
| <x>/cmdhDefEcValue/<x>/requestContextNotification |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Optional | ZeroOrOne | bool | Get |  |
|  | This leaf node contains the requestContextNotification attribute of the cmdhDefEcValue resource instance. |  |
| <x>/cmdhDefEcValue/<x>/requestCharacteristics |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Optional | ZeroOrOne | chr | Get |  |
|  | This leaf node contains the requestCharacteristics attribute of the cmdhDefEcValue resource instance. |
| <x>/cmdhEcDefParamValues/ |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | node | Get |  |
|  | This interior node is the parent node of the cmdhEcDefParamValues MO. |
| <x>/cmdhEcDefParamValues/<x> |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | chr | Get |  |
|  | This interior placeholder node represents the instances of the cmdhEcDefParamValues MOs. |
| <x>/cmdhEcDefParamValues/<x>/applicableEventCategory |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | node | Get |  |
|  | This interior node contains the applicableEventCategory attribute of the cmdhEcDefParamValues resource instance. |
| <x>/cmdhEcDefParamValues/<x>/applicableEventCategory/<x> |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | node | Get |  |
|  | This placeholder node represents the root of the list of eventCat values. |
| <x>/cmdhEcDefParamValues/<x>/applicableEventCategory/<x>/eventCat |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | OneOrMore | chr | Get |  |
|  | This leaf node contains one eventCat list element of the applicableEventCategory attribute. |
| <x>/cmdhEcDefParamValues/<x>/defaultResultExpTime |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | int | Get |  |
|  | This leaf node contains the defaultResultExpTime attribute of the cmdhEcDefParamValues resource instance. |
| <x>/cmdhEcDefParamValues/<x>/defaultOpExpTime |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | int | Get |  |
|  | This leaf node contains the defaultOpExpTime attribute of the cmdhEcDefParamValues resource instance. |  |
| <x>/cmdhEcDefParamValues/<x>/defaultRespPersistence |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | int | Get |  |
|  | This leaf node contains the defaultRespPersistence attribute of the cmdhEcDefParamValues resource instance. |
| <x>/cmdhLimits |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | node | Get |  |
|  | This interior node is the parent node of the cmdhLimits MO. |
| <x>/cmdhLimits/<x> |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | int | Get |  |
|  | This interior placeholder node represents the instances of the cmdhLimits MO. |
| <x>/cmdhLimits/<x>order |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | int | Get |  |
|  | This leaf node contains the order attribute of the cmdhLimits resource instance. |
| <x>/cmdhLimits/<x>/requestOrigin |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | node | Get |  |
|  | This interior node contains the RequestOrigin attribute of the cmdhLimits resource instance. |
| <x>/cmdhLimits/<x>/requestOrigin/<x> |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | node | Get |  |
|  | This placeholder node represents the root of the list of requestOrigin values. |
| <x>/cmdhLimits/<x>/requestOrigin/<x>/m2mid |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | OneOrMore | chr | Get |  |
|  | This leaf node contains one list element of the requestOrigin attribute. |
| <x>/cmdhLimits/<x>/RequestContext |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Optional | ZeroOrMore | chr | Get |  |
|  | This leaf node contains the RequestContext attribute of the cmdhLimits resource instance. |
| <x>/cmdhLimits/<x>/RequestContextNotification |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Optional | ZeroOrOne | bool | Get |  |
|  | This leaf node contains the RequestContextNotification attribute of the cmdhLimits resource instance. |  |
| <x>/cmdhLimits/<x>/RequestCharacteristics |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Optional | ZeroOrOne | node | Get |  |
|  | This leaf node contains the RequestCharacteristics attribute of the cmdhLimits resource instance. |
| <x>/cmdhLimits/<x>/limitsEventCategory |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | node | Get |  |
|  | This interior node contains the limitsEventCategory attribute of the cmdhLimits resource instance. |
| <x>/cmdhLimits/<x>/limitsEventCategory/<x> |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | Node | Get |  |
|  | This placeholder node represents the root of the list of eventCat values. |
| <x>/cmdhLimits/<x>/limitsEventCategory/<x>/eventCat |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | OneOrMore | Chr | Get |  |
|  | This leaf node contains one eventCat list element of the limitsEventCategory attribute. |
| <x>/cmdhLimits/<x>/limitsRequestExpTime |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | node | Get |  |
|  | This interior node contains the limitsRequestExpTime attribute of the cmdhLimits resource instance. |
| <x>/cmdhLimits/<x>/limitsRequestExpTime/<x> |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | Node | Get |  |
|  | This placeholder node represents the root of the list of minimal and maximal Request Expiration Time values. |
| <x>/cmdhLimits/<x>/limitsRequestExpTime/<x>/minTime |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | Int | Get |  |
|  | This leaf node contains the minimal Request Expiration Time in units of milliseconds. |
| <x>/cmdhLimits/<x>/limitsRequestExpTime/<x>/maxTime |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | Int | Get |  |
|  | This leaf node contains the maximal Request Expiration Time in units of milliseconds.. |
| <x>/cmdhLimits/<x>/limitsResultExpTime |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | node | Get |  |
|  | This interior node contains the limitsResultExpTime attribute of the cmdhLimits resource instance. |
| <x>/cmdhLimits/<x>/limitsResultExpTime/<x> |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | Node | Get |  |
|  | This placeholder node represents the root of the list of minimal and maximal Result Expiration Time values. |
| <x>/cmdhLimits/<x>/limitsResultExpTime/<x>/minTime |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | int | Get |  |
|  | This leaf node contains the minimal Result Expiration Time in units of milliseconds. |
| <x>/cmdhLimits/<x>/ limitsResultExpTime/<x>/maxTime |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | int | Get |  |
|  | This leaf node contains the maximal Result Expiration Time in units of milliseconds.. |
| <x>/cmdhLimits/<x>/limitsOpExecTime |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | node | Get |  |
|  | This interior node contains the limitsOpExecTime attribute of the cmdhLimits resource instance. |
| <x>/cmdhLimits/<x>/limitsOpExecTime/<x> |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | node | Get |  |
|  | This placeholder node represents the root of the list of minimal and maximal Operation Execution Time values. |
| <x>/cmdhLimits/<x>/limitsOpExecTime/<x>/minTime |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | int | Get |  |
|  | This leaf node contains the minimal Operation Execution Time in units of milliseconds. |
| <x>/cmdhLimits/<x>/limitsOpExecTime/<x>/maxTime |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | int | Get |  |
|  | This leaf node contains the maximal Operation Execution Time in units of milliseconds.. |
| <x>/cmdhLimits/<x>/limitsRespPersistence |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | node | Get |  |
|  | This interior node contains the limitsRespPersistence attribute of the cmdhLimits resource instance. |
| <x>/cmdhLimits/<x>/limitsRespPersistence/<x> |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | node | Get |  |
|  | This placeholder node represents the root of the list of minimal and maximal Response Persistence Time values. |
| <x>/cmdhLimits/<x>/limitsRespPersistence/<x>/minTime |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | int | Get |  |
|  | This leaf node contains the minimal Response Persistence Time in units of milliseconds. |
| <x>/cmdhLimits/<x>/limitsRespPersistence/<x>/maxTime |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | int | Get |  |
|  | This leaf node contains the maximal Operation Execution Time in units of milliseconds.. |
| <x>/cmdhLimits/<x>/limitsDelAggregation |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | node | Get |  |
|  | This interior node contains the limitsDelAggregation attribute of the cmdhLimits resource instance. |  |
| <x>/cmdhLimits/<x>/limitsDelAggregation/<x> |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | node | Get |  |
|  | This placeholder node represents the root of the list of Delivery Aggregation settings. |
| <x>/cmdhLimits/<x>/limitsDelAggregation/<x>/boolian |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | OneOrMore | bool | Get |  |
|  | This leaf node contains the permitted boolean value(s) of the limitsDelAggregation attribute. This list has one or two elements, representing the allowed values of the boolean value space domain. |
| <x>/cmdhNetworkAccessRules |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | OneOrMore | node | Get |  |
|  | This interior node is the parent node of cmdhNetworkAccessRules MOs. |
| <x>/cmdhNetworkAccessRules/<x> |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | OneOrMore | node | Get |  |
|  | This interior placeholder node represents the instances of the cmdhDefEcValue MO. |
| <x>/cmdhNetworkAccessRules/<x>/applicableEventCategories |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | node | Get |  |
|  | This interior node contains the applicableEventCategories attribute of the cmdhNetworkAccessRules resource instance. |
| <x>/cmdhNetworkAccessRules/<x>/applicableEventCategories/<x> |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | node | Get |  |
|  | This placeholder node represents the root of the list of eventCat values. |
| <x>/cmdhNetworkAccessRules/<x>/applicableEventCategories/<x>/eventCat |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | OneOrMore | chr | Get |  |
|  | This leaf node contains one eventCat list element of the applicableEventCategories attribute. |
| <x>/cmdhDefEcValue/<x>/cmdhNwAccessRule |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Optional | ZeroOrMore | chr | Get |  |
|  | This leaf node includes a reference (mgmtLink) to an instance of the cmdhNwAccessRule MO. |
| <x>/cmdhNwAccessRule |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | OneOrMore | node | Get |  |
|  | This interior node is the parent node of cmdhNwAccessRule MOs. |
| <x>/cmdhNwAccessRule/<x> |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Optional | ZeroOrOne | node | Get |  |
|  | This interior placeholder node represents instances of the cmdhNwAccessRule MO. |
| <x>/cmdhNwAccessRule/<x>targetNetwork |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | chr | Get |  |
|  | This leaf node contains the targetNetwork attribute of the cmdhNwAccessRule resource instance. |  |
| <x>/cmdhNwAccessRule/<x>minReqVolume |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | int | Get |  |
|  | This leaf node contains the minReqVolume attribute of the cmdhNwAccessRule resource instance in units of byte. |
| <x>/cmdhNwAccessRule/<x>/backOffParameters |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | node | Get |  |
|  | This interior node contains the backOffParameters attribute of the cmdhNwAccessRule resource instance. |
| <x>/cmdhNwAccessRule/<x>/backOffParameters/<x> |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | node | Get |  |
|  | This placeholder node represents the root of list backOffParameters list of time values. |
| <x>/cmdhNwAccessRule/<x>/backOffParameters/<x>/backOffTime |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | int | Get |  |
|  | This leaf node contains the backOffTime in units of milliseconds. |
| <x>/cmdhNwAccessRule/<x>backOffParameters/<x>/backOffTimeIncrement |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | int | Get |  |
|  | This leaf node contains the backOffTimeIncrement in units of milliseconds. |
| <x>/cmdhNwAccessRule/<x>backOffParameters/<x>/maximumBackoffTime |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | int | Get |  |
|  | This leaf node contains the maximumBackoffTime in units of milliseconds. |
| <x>/cmdhNwAccessRule/<x>/otherConditions |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | chr | Get |  |
|  | This leaf node contains the otherConditions attribute of the cmdhNwAccessRule resource instance. |
| <x>/cmdhNwAccessRule/<x>/allowedSchedule |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | node | Get |  |
|  | This interior node represents the root of the allowedSchedule attribute of the cmdhNwAccessRule resource instance. |
| <x>/cmdhNwAccessRule/<x>/allowedSchedule/<x> |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | node | Get |  |
|  | This placeholder node represents the root of the time schedule. |
| <x>/cmdhNwAccessRule/<x>/allowedSchedule/<x>/schedule |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | OneOrMore | Chr | Get |  |
|  | This leaf node contains the time schedule in form of extended crontab syntax. |
| <x>/cmdhBuffer |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | OneOrMore | node | Get |  |
|  | This interior node is the parent node of the cmdhBuffer MO. |
| <x>/cmdhBuffer/<x> |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | OneOrMore | node | Get |  |
|  | This interior placeholder represents the instances of the cmdhBuffer MO. |
| <x>/cmdhBuffer/<x>/applicableEventCategory |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | node | Get |  |
|  | This interior node contains the applicableEventCategory attribute of the cmdhBuffer resource instance. |
| <x>/cmdhBuffer/<x>/applicableEventCategory/<x> |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | node | Get |  |
|  | This placeholder node represents the root of the list of eventCat values. |
| <x>/cmdhBuffer/<x>/applicableEventCategory/<x>/eventCat |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | OneOrMore | Chr | Get |  |
|  | This leaf node contains one eventCat list element of the applicableEventCategory attribute. |
| <x><x>/cmdhBuffer/<x>/maxBufferSize |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | Int | Get |  |
|  | This leaf node contains the maxBufferSize attribute of the cmdhBuffer resource instance. |
| <x>/cmdhBuffer/<x>/storagePriority |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | Int | Get |  |
|  | This leaf node contains the storagePriority attribute of the cmdhBuffer resource instance. |

## ------------------------ end of text addition 2 ----------------

## ------------------------ start of text addition 3 ----------------

## 5.1	Mapping of basic data types

oneM2M has defined the data types that describe the format of the value stored at the attribute. Those oneM2M data types are listed in the below table, and mapped to the data types specified by OMA DM Protocol [4], [5]. Note that OMA DM 1.3 [4] and OMA DM 2.0 [5] uses the same data types.

| oneM2M Data Types | Mapping to data types in OMA DM | Description |
| --- | --- | --- |
| TBD | null | OMA DM Nodes with null data type shall not store any value. |
| xs:base64Binary | b64 | Data type for Base64-encoded binary data |
| xs:base64Binary | bin | Data type for binary data. |
| xs:boolean | bool | Data type for Boolean. Detailed Mapping can be given here. |
| xs:string | Chr | Data type for text. The length limitation should be considered for the mapping. |
| xs:integer | Int | Data type for 32-bit signed integer |
| TBD | xml | Data type for XML data |
| xs:date | date | Data type for date in ISO 8601 format with the century being included in the year |
| xs:time | time | Data type for Specifies that the Node value is a time in ISO 8601 format |
| xs:float | float | Data type for a single precision 32-bit floating point type as defined in XML Schema 1.0 as the float primitive type |
| xs:nonNegativeInteger | int | Data type for numbers equal or larger than 0, mapped from 64-bit to 32-bit representation |
| xs:positiveInteger | int | Data type for numbers equal or larger than 1, mapped from 64-bit to 32-bit representation |
| xs:long | int | Data type for signed integer numbers, mapped from 64-bit to 32-bit representation. |
| The mgmtLink attribute in the <mgmtObj> Resource |  | The OMA DM 'node' data type describes the format of the Interior Node that can have child Nodes. The mgmtLink attribute in the <mgmtObj> Resource supports the hierarchy of <mgmtObj> Resource. Note that this is not data type mapping. |

Editor's Note: The oneM2M data types that is related to <mgmtObj> needs to be listed in the above table.

## ------------------------ end of text addition 3 ----------------

# Comments

to be defined as external MO compliant with OMA-WP-AC-MO-20090127-A