| CHANGE REQUEST |
| --- |
| Group Name:* | WG5 (MAS) |
| Source:* | Ericsson |
| Format:* | MAS #12 Face-to-Face Meeting |
| Date:* | 2014-07-29 |
| Contact:* | Shelby Kiewel (skiewel@iconectiv.com) |
| Reason for Change/s:* | Editorial updates to correct grammar and proper wording |
| CR against: Release* | 1.0 |
| CR against: TS/TR* | oneM2M-TS 0005 Management Enablement v 2.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution provides editorial changes to the TS-0005 document.  Various adjustments in English and grammar have been noted for review and approval of the committee.

# 1	Scope

The present document specifies the protocol translation and mappings between the oneM2M Service layer and the management technologies specified by OMA such as OMA DM 1.3, OMA DM 2.0 and OMA LightweightM2M. Note that OMA DM 1.3 and OMA DM 2.0 are collectively referenced as OMA DM in this document.

# 2	References

References are either specific (identified by date of publication and/or edition number or version number) or non-specific. For specific references,only the cited version applies. For non-specific references, the latest version of the referenced document (including any amendments) applies.

## 2.1	Normative references

The following referenced documents are necessary for the application of the present document.

[1]	oneM2M TS-0001: “oneM2M Functional Architecture”

[2]	oneM2M TS-0004: “oneM2M Protocol Specification”

[3]	oneM2M TR-0004: “Definitions and Acronyms”

[4]	“OMA Device Management Protocol”, Version 1.3, Open Mobile Alliance™, http://www.openmobilealliance.org/

[5]	“OMA Device Management Protocol”, Version 2.0, Open Mobile Alliance™, http://www.openmobilealliance.org/

[6]	"OMA LightweightM2M”, Version 1.0, Open Mobile Alliance™, http://www.openmobilealliance.org/

## 2.2	Informative references

The following referenced documents are not necessary for the application of the present document, but they assist the user with regard to a particular subject area.

[i.1]	oneM2M Drafting Rules  (http://member.onem2m.org/Static_pages/Others/Rules_Pages/oneM2M-Drafting-Rules-V1_0.doc)

# 3	Definitions, symbols, abbreviations and acronyms

For the purposes of the present document, the terms and definitions given in TR-0004 [3] apply. In addition, the terms and definitions defined in this section apply.

## 3.1	Definitions

Definition format

<defined term>: <definition>

<defined term>[N]: <definition>

example 1: text used to clarify abstract rules by applying them literally

NOTE:	This may contain additional information.

## 3.2	Symbols

Symbol format

<symbol>	<Explanation>

<2nd symbol>	<2nd Explanation>

<3rd symbol>	<3rd Explanation>

## 3.3	Abbreviations

Abbreviation format

<ABREVIATION1>	<Explanation>

<ABREVIATION2>	<Explanation>

<ABREVIATION3>	<Explanation>

## 3.4	Acronyms

Acronym format

<ACRONYM1>	<Explanation>

<ACRONYM2>	<Explanation>

<ACRONYM3>	<Explanation>

# 4	Conventions

The key words “Shall”, ”Shall not”, “May”, ”Need not”, “Should”, ”Should not” in this document are to be interpreted as described in the oneM2M Drafting Rules [i.1]

# 5.	OMA DM 1.3 and OMA DM 2.0

## 5.1	Mapping of basic data types

oneM2M has defined the data types that describe the format of the value stored with the attribute. Those oneM2M data types are listed in the below table, and mapped to the data types specified by OMA DM Protocol [4], [5]. Note that OMA DM 1.3 [4] and OMA DM 2.0 [5] uses the same data types.

| oneM2M Data Types | Mapping to data types in OMA DM | Description |
| --- | --- | --- |
| TBD | null | OMA DM Nodes with null data type shall not store any value. |
| xs:base64Binary | b64 | Data type for Base64-encoded binary data |
| xs:base64Binary | bin | Data type for binary data. |
| xs:boolean | bool | Data type for Boolean. Detailed Mapping can be given here. |
| xs:string | chr | Data type for text. The length limitation should be considered for the mapping. |
| xs:integer | int | Data type for 32-bit signed integer |
| TBD | xml | Data type for XML data |
| xs:date | date | Data type for date in ISO 8601 format with the century being included in the year |
| xs:time | time | Data type specifying that the Node value is a time in ISO 8601 format |
| xs:float | float | Data type for a single precision 32-bit floating point type as defined in XML Schema 1.0 as the float primitive type |
| The mgmtLink attribute in the <mgmtObj> Resource |  | The OMA DM 'node' data type describes the format of the Interior Node that can have child Nodes. The mgmtLink attribute in the <mgmtObj> Resource supports the hierarchy of <mgmtObj> Resource. Note that this is not data type mapping. |

Editor's Note: The oneM2M data types that are related to <mgmtObj> need to be listed in the above table.

## 5.2	Mapping of Identifiers

OMA DM 1.3 and OMA DM 2.0 specifies many identifiers including device identifier, server identifier, client version identifier, manufacturer identifier, etc. To enable the device management using OMA DM Protocol, oneM2M identifiers need to be mapped to identifiers specified by OMA DM Protocol. The below table shows the oneM2M identifiers that need to be mapped to OMA DM Protocol.

| oneM2M | Mapping to OMA DM Identifiers | Description |
| --- | --- | --- |
| M2M-Node-ID. | Device Identifier (i.e., DevId node in DevInfo MO) | In OMA DM, the device identifier is a unique identifier for the device. This value is globally unique and MUST be formatted as a URN. OMA DM Gateways and OMA DM enabled devices are assigned with the device identifiers, and each can be mapped to the M2M-Node-ID. Note: In case the notion of the device identifier is not supported by the device, the DM Gateway can assign the local identifier for the device, and the M2M-Node-ID should be mapped to this local identifier. |
| The objectID attribute in <mgmtObj> resource. | MOID | A unique identifier of the management object. Each MO is characterized by a unique MOID, which is generally a URN. |
| The objectPath attribute in <mgmtObj> resource | URI for the local path in the device where the relevant Management Object is located | Management Objects in the device are uniquely addressed by a URI that is stored in the objectPath attribute. Note that DM 1.3 and DM 2.0 uses different Addressing scheme, but they are transparent to the oneM2M service layer. |

## 5.3	Mapping of resources

This section describes how to map <mgmtObj> resources specified in Annex D of [1] to the relevant management objects as defined by OMA DM ([4], [5]). Since OMA DM 1.3 and OMA DM 2.0 use the same management objects except standard management objects, the resource mappings can be considered regardless of the specific version of the OMA DM Protocol.

### 5.3.1	General Mapping Assumptions

OMA DM Protocol implements the management functionalities by using the Management Objects. Management Object is a collection of Nodes which are related for providing certain management functionalities. For example, SCOMO is for the software management, and FUMO is for the firmware update, and so on. The individual management operations such as firmware update, software management can be achieved by manipulating the corresponding Management Object. Since oneM2M <mgmtObj> Resources are for providing specific management functionalities, oneM2M <mgmtObj> Resources shall be mapped to Management Objects specified by OMA DM [4], [5].

### 5.3.2	Resource [firmware]

The resource [firmware] is for firmware management in the service layer. Regardless of OMA DM 1.3 and OMA DM 2.0,, the resource shall be mapped to FUMO (urn:oma:mo:omafumo:1.0). The attributes of the resource shall be mapped to nodes of the MO as follows.

| Attribute Name of [firmware] | Mapping to Nodes in Management Object |
| --- | --- |
| Version | <x>/PkgVersion |
| Name | <x>/PkgName |
| URL | <x>/DownloadAndUpdate/PkgURL |
| Update | <x>/DownloadAndUpdate |
| updateStatus | <x>/State |

### 5.3.3	Resource [software]

The resource [software] is for software management in the service layer. Regardless of OMA DM 1.3 and OMA DM 2.0,, the resource shall be mapped to SCOMO (urn:oma:mo:omascomo:1.0). The attributes of the resource shall be mapped to nodes of the MO as the follows.

| Attribute Name of [software] | Mapping to Nodes in Management Object |
| --- | --- |
| Version | <x>/Inventory/Deployed/<x>/Version |
| Name | <x>/Download/<x>/Name (when the software package is not ready for install) <x>/Inventory/Delivered/<x>/Name (when the software package is ready for install) <x>/Deployed/<x>/Name (when the software package is already installed) |
| URL | <x>/Download/<x>/PkgURL |
| Install | <x>/Download/<x>/Operations/DownloadInstall (when the software package is not yet available) <x>/Inventory/Delivered/<x>/Operations/Install (when the software package has already been downloaded) |
| installStatus | <x>/Download/<x>/Status (started install when the software package is not yet available) <x>/Inventory/Delivered/<x>/Status (started install when the software package has already been downloaded) |
| Activate | <x>/Inventory/Deployed/<x>/Operations/Activate |
| deactivate | <x>/Inventory/Deployed/<x>/Operations/Deactivate |
| activeStatus | <x>/Inventory/Deployed/<x>/Status |

### 5.3.4	Resource [memory]

The resource [memory] is for acquire information about the total memory or available memory of the device. Regardless of OMA DM 1.3 and OMA DM 2.0,, the resource shall be mapped to memory information of DiagMO (urn:oma:mo:omadiag:memory:1.0). The attributes of the resource shall be mapped to nodes of the MO as follows.

| Attribute Name of [memory] | Mapping to Nodes in Management Object |
| --- | --- |
| memAvailable | <x>/DiagMonData/RAMAvail |
| memTotal | <x>/DiagMonData/RAMTotal |

### 5.3.5	Resource [areaNwkInfo]

The resource [areaNwkInfo] is for managing the area network. Regardless of OMA DM 1.3 and OMA DM 2.0, the resource shall be mapped to MANMO (urn:oma:mo:ext-etsi-manmo:1.0). The attributes of the resource shall be mapped to nodes of the MO as follows.

| Attribute Name of [areaNwkInfo] | Mapping to Nodes in Management Object |
| --- | --- |
| areaNwkType | M2MAreaNwkInfo/AreaNwks/<x>/AreaNwkType |
| listOfDevices | M2MAreaNwkInfo/AreaNwks/<x>/ListOfDevices |

### 5.3.6	Resource [areaNwkDeviceInfo]

The resource [areaNwkDeviceInfo] is for managing the device of the area network as well as acquiring information about devices in the area network. Regardless of OMA DM 1.3 and OMA DM 2.0, the resource shall be mapped to MANDMO (urn:oma:mo:ext-etsi-mandmo:1.0). The attributes of the resource shall be mapped to nodes of the MO as follows.

| Attribute Name of [areaNwkDeviceInfo] | Mapping to Nodes in Management Object |
| --- | --- |
| devId | DevInfo/DevId |
| devType | DevDetail/DevType |
| areaNwkId | <x>/AreaNwks/<x>/AreaNwkID |
| sleepInterval | <x>/AreaNwks/<x>/SleepInterval |
| sleepDuration | <x>/AreaNwks/<x>/SleepDuration |
| Status | <x>/AreaNwks/<x>/Status |
| listOfNeighbors | <x>/AreaNwks/<x>/Groups/ListOfDeviceNeighbors |

Editor’s Note: The description of which procedures are used to maintain the resource is FFS.

### 5.3.7	Resource [battery]

The Resource [battery] is to provide battery related information. Regardless of OMA DM 1.3 and OMA DM 2.0, this Resource shall be mapped to Battery Info Management Object (MOID: "urn:oma:mo:oma-diag:batteryinfo:1.0"). The attributes of this Resource shall be mapped to Nodes in the Management Object as follows:

| Attribute Name of [battery] | Mapping to Nodes in Management Object |
| --- | --- |
| batteryLevel | "<x>/DiagMonData/<x>/BatteryLevel" Node |
| batteryStatus | "<x>/DiagMonData/<x>/BatteryStatus" Node |

### 5.3.8	Resource [deviceInfo]

The Resource [deviceInfo] is to provide device related information. For OMA DM 1.3, this Resource shall be mapped to DevInfo MO (MOID: "urn:oma:mo:oma-dm-devinfo:1.1") and DevDetail MO (MOID: "urn:oma:mo:oma-dm-devdetail:1.1"). The attributes of this Resource shall be mapped to Nodes in two Management Objects as follows:

| Attribute Name of [deviceInfo] | Mapping to Nodes in Management Object |
| --- | --- |
| deviceLabel | "DevInfo/DevId" Node in DevInfo MO |
| Manufacturer | "DevInfo/Man" Node in DevInfo MO |
| Model | "DevInfo/Mod" Node in DevInfo MO |
| deviceType | "DevDetail/DevType" Node in DevDetail MO |
| fwVersion | "DevDetail/FwV" Node in DevDetail MO |
| swVersion | "DevDetail/SwV" Node in DevDetail MO |
| hwVersion | "DevDetail/HwV" Node in DevDetail MO |

For OMA DM 2.0, this Resource shall be mapped to DevInfo MO (MOID: "urn:oma:mo:oma-dm-devinfo:1.2"). The attributes of this Resource shall be mapped to Nodes in the Management Object as follows:

| Attribute Name of [deviceInfo] | Mapping to Nodes in Management Object |
| --- | --- |
| deviceLabel | "<x>/DevID" Node |
| Manufacturer | "<x>/Man" Node in DevInfo MO |
| Model | "<x>/Mod" Node in DevInfo MO |
| deviceType | "<x>/DevType" Node in DevInfo MO |
| fwVersion | "<x>/FwV" Node in DevInfo MO |
| swVersion | "<x>/SwV" Node in DevInfo MO |
| hwVersion | "<x>/HwV" Node in DevInfo MO |

### 5.3.9	Resource [deviceCapability]

The Resource [deviceCapability] is to manage the device capabilities such USB, camera, etc. Regardless of OMA DM 1.3 and OMA DM 2.0, this Resource shall be mapped to Device Capability Management Object (MOID: "urn:oma:mo:oma-dcmo:1.0"). The attributes of this Resource shall be mapped to Nodes in the Management Object as follows:

| Attribute Name of [deviceCapability] | Mapping to Nodes in Management Object |
| --- | --- |
| capabilityName | "<x>/Property" Node in DCMO |
| Attached | "<x>/Attached" Node in DCMO |
| capabilityActionStatus | "<x>/Enabled" Node in DCMO |
| Enable | "<x>/Operations/Enable" Node in DCMO |
| Disable | "<x>/Operations/Disable" Node in DCMO |

### 5.3.10	Resource [reboot]

The Resource [reboot] is to reboot the device. Regardless of OMA DM 1.3 and OMA DM 2.0, this Resource shall be mapped to Restart Management Object (MOID: "urn:oma:mo:oma-diag:restart:1.0") that is specified in Diag Mon [ref] and Lock and Wipe Management Object (MOID: "urn:oma:mo:oma-lawmo:1.0"). The attributes of this Resource shall be mapped to Nodes in the Management Objects as follows:

| Attribute Name of [reboot] | Mapping to Nodes in Management Object |
| --- | --- |
| Reboot | "<x>/Operations/Start" Node in Restart MO. The restarting level described at the "<x>/DiagMonConfig/ConfigParms/RestartLevel" Node is up to the implementation. |
| factoryReset | "<x>/Operations/FactoryReset" Node in LAWMO |

Editor’s Note: The access right mapping needs to be resolved in a general manner in TS-0005.

### 5.3.11	Resource [eventLog]

The Resource [eventLog] is to record the event log for the device. Regardless of OMA DM 1.3 and OMA DM 2.0, this Resource shall be mapped to several Management Objects according to the logTypeId attribute of this Resource as follows:

- Trap Event Logging Function Management Object (MOID: "urn:oma:mo:oma-diag:trapeventlogging:1.1") if the logTypeId attribute is set to "TBD"

- Trace Logs Management Object (MOID: "urn:oma:mo:oma-diag:tracelog:1.0") if the logTypeId attribute is set to "TBD"

- Panic Logs Management Object (MOID: "urn:oma:mo:oma-diag:paniclog:1.1") if the logTypeId attribute is set to "TBD"

The attributes of this Resource shall be mapped to Nodes in above Management Objects as follows:

| Attribute Name of [eventLog] | Mapping to Nodes in Management Object |
| --- | --- |
| logTypeId | This attribute is not mapped to Nodes in Management Object. Instead, this attribute specifies the log type, and based on the log type, the actual Management Object mapped to this Resource is decided. |
| logData | "<x>/DiagMonData/log" Node for Trap Event Logging Function MO and Trace Logs MO. "<x>/DiagMonData/PanicLog" Node for Panic Logs MO |
| logActionStatus | "<x>/Status" Node for Trap Event Logging Function MO, Trace Logs MO and Panic Logs MO |
| logStart | "<x>/Operations/Start" Node for Trap Event Logging Function MO, Trace Logs MO and Panic Logs MO |
| logStop | "<x>/Operations/Stop" Node for Trap Event Logging Function MO, Trace Logs MO and Panic Logs MO |

## 5.4	Mapping of procedures for management

### 5.4.1. 	Mapping for <mgmtObj> Resource Primitives

#### 5.4.1.1 	Create Primitive for <mgmtObj> Resource

The Create Request primitive for the <mgmtObj> Resource, as described in [2], shall be mapped to external management operations that create the corresponding OMA DM Management Objects. Depending on the type of the <mgmtObj> Resource (i.e., [memory], [battery], [deviceInfo], etc.), the associated OMA DM Management Object as specified in the clause 6.3 should be created. Creating OMA DM Management Object can be performed by the Protocol Command Add in OMA DM 1.3 and HGET in OMA DM 2.0.

Receiving Create Request primitive does not imply that the mapped external management operations shall always be performed since, on receiving the Create Request primitive, the corresponding external management objects may already exist in the device. For instance, after discovering the external management objects, the DMG in MN or ASN creates <mgmtObj> Resource in the IN-CSE; and in this case, the IN-CSE does not need to create the external management objects.

In the case where the external management objects are successfully created after receiving the Create Request primitive, then the objectID and objectPath attribute should be properly set based on the created external management objects.

The result of creating the external management object should be mapped to the Create Response primitive for the <mgmtObj> Resource as indicated by the status code mapping in the clause x.y.

#### 5.4.1.2	Retrieve Primitive for <mgmtObj> Resource

The Retrieve Request primitive for the <mgmtObj> Resource, as described in [2], shall be mapped to external management operations that retrieve the corresponding OMA DM Management Objects. Depending on the type of the <mgmtObj> Resource (i.e., [memory], [battery], [deviceInfo], etc.), the associated OMA DM Management Object as specified in the clause 6.3 shall be retrieved. Retrieving OMA DM Management Object can be performed by the Protocol Command Get in OMA DM 1.3 and HPUT/HPOST/GET in OMA DM 2.0.

The result of retrieving the external management object should be mapped to the Retrieve Response primitive for the <mgmtObj> Resource as indicated by the status code mapping in the clause x.y.

In case of OMA DM 2.0, note that the mapped external management operations may be implemented either by using HPUT, HPOST or GET. If the GET command is used, the requested data is carried within the OMA DM Session; otherwise the requested data is directly embedded within the HTTP message.

#### 5.4.1.3	Update Primitive for <mgmtObj> Resource

The Update Request Primitive for <mgmtObj> Resource can be used to modify the external management objects or to execute the management commands. The mapping in either case shall be different as the following sections specify.

##### 5.4.1.3.1	Update Primitive for Replacing Data in the Management Object

This is the case that the Update Primitive targets the attribute that is mapped to the non-executable Node in external management object as specified in clause 6.3. The Update Request primitive for the <mgmtObj> Resource, as described in [2], shall be mapped to external management operations that replace the data in the corresponding OMA DM Management Objects. Depending on the type of the <mgmtObj> Resource (i.e., [memory], [battery], [deviceInfo], etc.), the associated OMA DM Management Object as specified in the clause 6.3 shall be updated. Replacing data in OMA DM Management Object can be performed by the Protocol Command Replace in OMA DM 1.3 and HGET in OMA DM 2.0.

The result of replacing data in the external management object should be mapped to the Update Response primitive for the <mgmtObj> Resource as indicated by the status code mapping in the clause x.y.

##### 5.4.1.3.2	Update Primitive for Executing Management Commands

This is the case that the Update Primitive targets the attribute that is mapped to the executable Node in external management object as specified in the clause 6.3. The Update Request primitive for the <mgmtObj> Resource, as described in [2], shall be mapped to external management operations that execute the Node in the external management object. Depending on the type of the <mgmtObj> Resource (i.e., [memory], [battery], [deviceInfo], etc.), the Node in the associated OMA DM Management Object as specified in the clause 6.3 shall be executed. Executing the Node in OMA DM Management Object can be performed by the Protocol Command Exec in OMA DM 1.3 and EXEC in OMA DM 2.0.

The mapped external management operations may be executed either by the synchronous or asynchronous reporting as specified by OMA DM 1.3 and OMA DM 2.0. Selecting the synchronous or asynchronous reporting is implementation issue, and is independent on whether the Update Primitive is requested as blocking or non-blocking.

The result of executing the Nodein the external management object should be mapped to the Update Response primitive for the <mgmtObj> Resource as indicated by the status code mapping in the clause x.y.

#### 5.4.1.4	Delete Primitive for <mgmtObj> Resource

The Delete Request primitive for the <mgmtObj> Resource, as described in [2], shall be mapped to external management operations that delete the corresponding OMA DM Management Objects. Depending on the type of the <mgmtObj> Resource (i.e., [memory], [battery], [deviceInfo], etc.), the associated OMA DM Management Object as specified in the clause 6.3 should be deleted. Deleting OMA DM Management Object can be performed by the Protocol Command Delete in OMA DM 1.3 and DELETE in OMA DM 2.0.

Receiving Delete Request primitive does not imply that the corresponding external management objects shall be always deleted. They may not be deleted if the external management objects are used by entities such as the Device Management Server.

The result of deleting the external management object should be mapped to the Delete Response primitive for the <mgmtObj> Resource as indicated by the status code mapping in clause x.y.

### 5.4.2 oneM2M Resource Specific Procedure Mapping

## 5.5	DM Server Interactions

Editor’s Note: This section specifies the action taken for the DMG CSE to communicate with the Management Server by using the ms interface. The server interaction can be different depending on the device management technology. The server interaction might include the establishment, maintainance, usage and termination of communication to the Management Server defined in OMA DM.

### 5.5.1	DM Server interaction management

Editor’s Note: This section describes the management of communication between the oneM2M service layer and the DM Server. The management includes the establishment and termination of a session(s) when needed. The management also includes necessary procedure to utilize the existing sessions.

### 5.5.2	Authorization

Editor’s Note: This section specifies the mapping of authorization rules defined in oneM2M and OMA standards.

## 5.6	New Management Objects

Editor’s Note: This section specifies the definition of new data models if needed based on the requirements of oneM2M. The definition of new data models in this section need to be liaised to OMA to create corresponding MOs in OMA DM.

# 6.	OMA Lightweight M2M 1.0

## 6.1	Mapping of basic data types

oneM2M has defined the data types that describe the format of the value stored at the attribute. Those oneM2M data types are listed in the below table, and mapped to the data types specified by OMA Lightweight M2M 1.0 [6] (shortened in OMA LWM2M)

| oneM2M Data Types | Mapping to data types in OMA LWM2M | Description |
| --- | --- | --- |
| xs:string | String | UTF-8 string |
| xs:integer | Integer | ASCII signed integer 1, 2,4, or 8 bytes |
| xs:boolean | Boolean | Data type for BooleanASCII value 0 or 1 |
| xs:float | Float | A 32 or 64-bit floating point value. The valid range of the value for a Resource SHOULD be defined. |
| xs:base64Binary | Opaque | A sequence of binary octets, the minimum and/or maximum length of the octets MAY be defined. |
| xs:dateTime | Time | Unix Time. A signed integer representing the number of seconds since Jan 1st, 1970 in the UTC time zone. |

Editor's Note: the description column should provide more information on how the mapping can occur (e.g., how to map between Time and xs:dateTime which have different format) and not repeat the existing explanations.

Editor's Note: The mapping contained in the table above only contains items that are necessary and is not all inclusive.

## 6.2	Mapping of Identifiers

OMA LWM2M [6] defines specific identifiers for entities (e.g. End Point Client Name or Device Identifier, Server identifier, Objects identifiers ..) To enable the device management using OMA LWM2M [6], oneM2M identifiers needs to be mapped to identifiers specified by OMA LWM2M [6].

### 6.2.1	Device identifier

A unique identifier is assigned to the Device and referenced as Endpoint Client Name in OMA LWM2M [6].This value is globally unique and is formatted as a URN.

Several URN formats are recommended in OMA LWM2M [6] as UUID URN defined in [RFC4122], OPS URN defined in [TR-069], IMEI URN defined in [3GPP-TS_23.003].

These Device identifiers shall map onto the oneM2M Node Identifier (M2M-Node-ID)

### 6.2.2	Object identifier

In OMA LWM2M [6], each object is characterized by a unique identifier represented by an integer. This identifier is provided  by OMNA (OMA Naming Authority) and is registered as a unique URN :

urn:oma:lwm2m:{oma,ext,x}:objectID (e.g. the LWM2M 1.0  Device Object (ObjectID:3) is registered as urn:oma:lwm2m:oma:3 ).

The context of a given oneM2M <mgmtObj> Resource is represented by the objectId attribute which can contain several references to OMA LWM2M [6] Object identifiers expressed as OMNA registered URN.

### 6.2.3	Object Instance Identifier

OMA LWM2M [6] permits objects to have multiple object instances where each object instance is contained in the objectPath attribute of the <mgmtObj> Resource within the context of the Resource’s objectId as described in previous section.

The objectPath attribute in <mgmtObj> Resource contains one (or several) element(s) representing the local path(s) where the Object Instance(s) are located.

## 6.3	Mapping of resources

This section describes how to map the <mgmtObj> Resources specified in the Annex D of [1] to the relevant Objects specified  in OMA LWM2M [6].

### 6.3.1	General Mapping Assumptions

OMA LWM2M[6] implements the functionalities of the device management and M2M service enablement as  Objects.  An Object is a collection of resources which are related to a specific management functionality. For example the Firmware Update Object contains all the resources used for firmware update purpose. Before to be capable of  fulfilling its role, an Object shall be first instantiated into an Object Instance.

Since <mgmtObj> Resources are for providing specific management functionalities, the attributes of a given <mgmtObj> Resource shall be mapped to the resources of one or several LWM2M Object Instances within the context of the Resource’s objectId as defined in sub-section 6.2.2..

The objectPath is a local context which has to be combined with a given <mgmtObj> Resource’s attribute for realizing the final mapping to the targeted OMA LWM2M [6] resource.

In case the objectPath is multiple (several Object Instances  are referenced in that Resource), a specified couple composed of one element of the objectId list and one element of the objectPath list will be associated to a given Resource attribute for realizing the final mapping to the targeted OMA LWM2M [6] resource.

### 6.3.2	Resource [memory]

The Resource [memory] provides memory related information. For OMA LWM2M, this Resource shall be mapped to the unique Instance of LWM2M Device Object (LWM2M ObjectID: 3) .

The context of this Resource is as follows:

| Context | Mapping |
| --- | --- |
| objectId | urn:oma:lwm2m:oma:3 |
| objectPath | /3/0 (instance 0 of Object 3) |

The attributes of this Resource shall be mapped to specific resources of the LWM2M Device Object Instance as follows:

| Attribute Name of [memory] | Mapping to resources in LWM2M Device Object Instance |
| --- | --- |
| memAvailable | 10 : estimated current available amount of memory in KB |
| memTotal | 21 : total amount of storage space in KB in the LWM2M Device |

### 6.3.3	Resource [battery]

The Resource [battery] provides battery related information. For  OMA LWM2M, this Resource shall be mapped to the unique Instance of LWM2M Device Object (LWM2M ObjectID: 3).

The context of this Resource is as follows:

| Context | Mapping |
| --- | --- |
| objectId | urn:oma:lwm2m:oma:3 |
| objectPath | /3/0 |

The attributes of this  Resource shall be mapped to specific resources of the LWM2M Device Object Instance  as follows:

| Attribute Name of [battery] | Mapping to resources in LWM2M Device Object Instance |
| --- | --- |
| batteryLevel | 9 : current battery level as percentage |
| batteryStatus | 20 : contains the battery status |

### 6.3.4	Resource [deviceInfo]

The Resource [deviceInfo] provides device related information. For OMA LWM2M, this Resource shall be mapped to the unique Instance of LWM2M Device Object (LWM2M ObjectID: 3).

The context of this Resource is the following

| Context | Mapping |
| --- | --- |
| objectId | urn:oma:lwm2m:oma:3 |
| objectPath | /3/0 |

The attributes of this Resource shall be mapped to specific resources of the LWM2M Device Object Instance  as follows:

| Attribute Name of [deviceInfo] | Mapping to resources in LWM2M Device Object Instance |
| --- | --- |
| deviceLabel | 2 : Serial Number |
| Manufacturer | 0 : Manufacturer name |
| Model | 1 : Model Number |
| deviceType | 17 : the class of the device |
| fwVersion | 3 : Firmware Version |
| swVersion | 19 : Software Version of the device |
| hwVersion | 18 : Hardware version of the device |

### 6.3.5	Resource [reboot]

The Resource [reboot] is used for rebooting the device. For  OMA LWM2M, this Resource shall be mapped to the unique Instance of LWM2M Device Object (LWM2M ObjectID: 3).

The context of this Resource is as follows:

| Context | Mapping |
| --- | --- |
| objectId | urn:oma:lwm2m:oma:3 |
| objectPath | /3/0 |

The attributes of this Resource shall be mapped to  LWM2M Device Object Instance  as follows:

| Attribute Name of [reboot] | Mapping to resources in LWM2M Object Instance |
| --- | --- |
| reboot | 4 : reboot the LWM2M Device to restore the Device from unexpected firmware failure |
| factoryReset | 5 : Perform Factory Reset : the LWM2M device return to the same configuration as at the initial deployment. |

## 6.4	Mapping of procedures for management

In this section, the oneM2M Primitives (i.e, Create, Retrieve, Update and Delete) are mapped to logical operations defined in OMA LWM2M.The LWM2M operations involved in that mapping  (i.e. Create, Read, Write, Execute and Delete operations ) are mapped on CoAP methods [7] . which are all carried as  Confirmable CoAP message . In LWM2M the responses to  these operations  are  carried directly in the Acknowledgement message that acknowledges the request

### 6.4.1	Create primitive for <mgmtObj> Resource

Depending on the mgmtDefinition attribute of the <mgmtObj> Resource (i.e. [memory], [battery], [deviceInfo], etc.), an instance of  the associated LWM2M Object as specified in the clause 6.3 should be created.

Receiving Create Request primitive does not imply that the LWM2M Create operations shall be always performed since, on receiving the Create Request primitive, the corresponding LWM2M Object Instance  may already exist in the device.

In case that the LWM2M Object Instance is  successfully created after receiving the Create Request primitive, then the objectID and objectPath attributes should be properly set based on the LWM2M Object.

The  Create primitive shall map to the OMA LWM2M Create operation and shall return one of the codes described in the following Table.

Table 6.4.1-1 Create Returned Codes Mapping

| Primitive Codes | Description | Returned Codes |
| --- | --- | --- |
|  | “Create” operation is completed successfully | 2.01 Created |
|  | Target (i.e., Object) already exists Mandatory Resources are not specified | 4.00 Bad Request |
|  | Access Right Permission Denied | 4.01 Unauthorized |
|  | URI of “Create” operation is not found | 4.04 Not Found, |
|  | Target is not allowed for “Create” operation | 4.05 Method Not Allowed |

### 6.4.2	Retrieve primitive for <mgmtObj> Resource

Depending on the mgmtDefinition attribute of the <mgmtObj> Resource (i.e., [memory], [battery], [deviceInfo], etc.), the associated LWM2M Object resources  as specified in the clause 6.3 shall be retrieved.

The  Retrieve primitive shall map to the LWM2M Read operation and shall return one of the codes described in the following Table.

Table 6.4.2-1 : Retrieve Returned Codes Mapping

| Primitive Codes | Description | Returned Codes |
| --- | --- | --- |
|  | “Retrieve” operation is completed successfully | 2.05 Content |
|  | Access Right Permission Denied | 4.01 Unauthorized, |
|  | Target of “Retrieve” operation is not found | 4.04 Not Found, |
|  | Target is not allowed for “Retrieve” operation | 4.05 Method Not Allowed |

### 6.4.3	Update primitive for <mgmtObj> Resource

The Update Request Primitive for <mgmtObj> Resource can be used to modify the resources of a LWM2M Object instance  or to execute the action related to a resource of a LWM2M Object instance.

The mapping in either case shall be different.

### 6.4.3.1	Update primitive for replacing data

Depending on the mgmtDefinition attribute of the <mgmtObj> Resource (i.e., [memory], [battery], [deviceInfo], etc.), the associated  resource(s) of  the LWM2M Object instance as specified in the clause 6.3 shall be updated.

The  Update  primitive shall map to the LWM2M Write operation and shall return one of the codes described in the following table.

Table 6.4.3.1-1 : Update Returned Codes Mapping

| Primitive Codes | Description | Returned Codes |
| --- | --- | --- |
|  | “Update” operation is completed successfully | 2.04 Changed |
|  | The format of data to be updated is different | 4.00 Bad Request, |
|  | Access Right Permission Denied | 4.01 Unauthorized |
|  | Target of ”Update“ operation is not found | 4.04 Not Found, |
|  | Target is not allowed for “Update” operation | 4.05 Method Not Allowed |

### 6.4.3.2	Update primitive for execution operation

This is the case that the Update Primitive targets the attribute that is mapped to a  LWM2M resource that supports the Execute operation.

The  Update  primitive shall map to the LWM2M Execute operation and shall return one of the codes described in the following table.

Table 6.4.3.2-1 : Execute Returned Codes Mapping

| Primitive Codes | Description | Returned Codes |
| --- | --- | --- |
|  | “Update” (“Execute”) operation is completed successfully | 2.04 Changed |
|  | Some issue with the “Update” argument | 4.00 Bad Request, |
|  | Access Right Permission Denied | 4.01 Unauthorized |
|  | Target of “Update” (“Execute”) operation is not found | 4.04 Not Found, |
|  | Target is not allowed for “Update” (“Execute”) operation | 4.05 Method Not Allowed |

### 6.4.4	Delete  primitive for <mgmtObj> Resource

Depending on the mgmtDefinition attribute of the <mgmtObj> Resource (i.e., [memory], [battery], [deviceInfo], etc.), the associated LWM2M Object instance as specified in the clause 6.3 should be deleted.

Receiving Delete Request primitive does not imply that the corresponding LWM2M Object Instance  shall always be deleted.

The  Delete  primitive shall map to the LWM2M Delete operation and shall return one  of the codes described in the following table.

Table 6.4.4-1 : Delete Returned Codes Mapping

| Primitive Codes | Description | Returned Codes |
| --- | --- | --- |
|  | “Delete” operation is completed successfully | 2.02 Deleted |
|  | Target (i.e., Object Instance) is not allowed for “Delete” operation | 4.00 Bad Request, |
|  | Access Right Permission Denied | 4.01 Unauthorized, |
|  | Target of “Delete” operation is not found | 4.04 Not Found, |
|  | Target is not allowed for “Delete” operation | 4.05 Method Not Allowed |

## 6.5	LWM2M Server Interactions

Editor’s Note: This section specifies the action taken for the DMG CSE to communicate with the Management Server by using the ms interface. The server interaction can be different depending on the device management technology. The server interaction might include the establishment, maintainance, usage and termination of communication to the Management Server defined in OMA LWM2M.

### 6.5.1	LWM2M Server interaction management

Editor’s Note: This section describes the management of communication between oneM2M service layer and LWM2M Server. The management includes the establishment and termination of session when needed. The management also includes necessary procedure to utilize the existing sessions.

### 6.5.2	Authorization

Editor’s Note: This section specifies the mapping of authorization rules defined in oneM2M and OMA standards.

## 6.6	New LWM2M Objects

Editor’s Note: This section specifies the definition of new data models if needed based on the requirements of oneM2M. The definition of new data models in this section need to be liaised to OMA to create corresponding Objects in OMA LWM2M.

----------------------- End of change 1 -----------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?