| CHANGE REQUEST |
| --- |
| Group Name:* | MAS#12 |
| Source:* | Seungkyu Park, LG Electronics, seungk.park@lge.com |
| Format:* | Plenary / Teleconference |
| Date:* | 2014-7-16 |
| Contact:* | Seungkyu Park, LG Electronics, seungk.park@lge.com |
| Reason for Change/s:* | This contribution provides the Management Resource specific procedure mapping. |
| CR against: Release* | Release-1 |
| CR against: TS/TR* | TS-0005, ver 0.2.0 |
| Clauses/Sub Clauses* | 5.4.2 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution provides the Management Resource specific mappings.

### -----------------------Start of change 1-------------------------------------------

### 5.4.2	Management Resource Specific Procedure Mapping

In this clause, mappings specific to the Management Resource are described.

### 5.4.2.1		Resource [firmware]

The generic <mgmtObj> mappings described in the clause 5.4.1 shall apply, and no specific mapping is necessary.

In addition to the status code mapping for the <mgmtObj> CRUD Operations, OMA DM specifies the status codes that are exclusive for FUMO. Those status codes will be used only for the execute command, and shall be used only for the oneM2M UPDATE Request. The status code mappings specific to the [firmware] Resource shall be as follows:

Note that the status codes defined in FUMO are common to the OMA DM 1.3 and OMA DM 2.0.

Table 5.4.2.1-1: Firmware MO Status Code Mapping

| oneM2M Primitive Status Code | OMA FUMO Status Code | Description |
| --- | --- | --- |
| TBD | 200 | Successful |
| TBD | 250-299 | Successful – Vendor Specified |
| TBD | 400 | Management Client Error |
| TBD | 401 | User Cancelled |
| TBD | 402 | Corrupted Firmware Update Package |
| TBD | 403 | Firmware Update Package – Device Mismatch |
| TBD | 404 | Failed Firmware Update Package Validation |
| TBD | 405 | Firmware Update Package Not Acceptable |
| TBD | 406 | Alternate Download Authentication Failure |
| TBD | 407 | Alternate Download Request Time-Out |
| TBD | 408 | Not Implemented |
| TBD | 409 | Undefined Error |
| TBD | 410 | Firmware Update Failed |
| TBD | 411 | Malformed or Bad URL |
| TBD | 412 | Alternate Download Server Unavailable |
| TBD | 450-499 | Client Error – Vendor Specified |
| TBD | 500 | Alternate Download Server Error |
| TBD | 501 | Download fails due to device is out of memory |
| TBD | 502 | Firmware update fails due to device out of memory |
| TBD | 503 | Download fails due to network issues |
| TBD | 550-599 | Alternate Download Server Error – Vendor Specified |

### 5.4.2.2		Resource [software]

The generic <mgmtObj> mappings described in the clause 5.4.1 shall apply, and no specific mapping is necessary.

In addition to the status code mapping for the <mgmtObj> CRUD Operations, OMA DM specifies the status codes that are exclusive for SCOMO. Those status codes will be used only for the execute command, and shall be used only for the oneM2M UPDATE Request. The status code mappings specific to the [software] Resource shall be as follows:

Note that the status codes defined in SCOMO are common to the OMA DM 1.3 and OMA DM 2.0.

Table 5.4.2.2-1: SCOMO Status Code Mapping

| oneM2M Primitive Status Code | OMA SCOMO Status Code | Description |
| --- | --- | --- |
| TBD | 1200 | Successful |
| TBD | 1250-1299 | Successful – Vendor Specified |
| TBD | 1400 | Client Error |
| TBD | 1401 | User cancelled |
| TBD | 1402 | Download Failed |
| TBD | 1403 | Alternate Download Authentication Failure |
| TBD | 1404 | Download failed due to Device is out of memory |
| TBD | 1405 | Install Failed |
| TBD | 1406 | Install failed due to Device out of memory |
| TBD | 1407 | Failed package validation |
| TBD | 1408 | Remove failed |
| TBD | 1409 | Activate failed |
| TBD | 1410 | Deactivate failed |
| TBD | 1411 | Not Implemented |
| TBD | 1412 | Undefined Error |
| TBD | 1413 | Operation rejected – unsupported environment |
| TBD | 1450-1499 | Client Error – Vendor Specified |
| TBD | 1500 | Alternate Download Server Error |
| TBD | 1501 | Alternate Download Server Unavailable |
| TBD | 1550-1599 | Alternate Download Server Error – Vendor Specified |

### 5.4.2.3		Resource [memory]

The generic <mgmtObj> mappings described in the clause 5.4.1 shall apply, and no specific mapping is necessary.

In addition to the status code mapping for the <mgmtObj> CRUD Operations, no [memory] specific status codes are defined in OMA DM.

### 5.4.2.4		Resource [areaNwkInfo]

The generic <mgmtObj> mappings described in the clause 5.4.1 shall apply, and no specific mapping is necessary.

In addition to the status code mapping for the <mgmtObj> CRUD Operations, no [areaNwkDeviceInfo] specific status codes are defined in ETSI M2M.

### 5.4.2.5		Resource [areaNwkDeviceInfo]

The generic <mgmtObj> mappings described in the clause 5.4.1 shall apply, and no specific mapping is necessary.

In addition to the status code mapping for the <mgmtObj> CRUD Operations, no [areaNwkDeviceInfo] specific status codes are defined in ETSI M2M.

### 5.4.2.6		Resource [battery]

The generic <mgmtObj> mappings described in the clause 5.4.1 shall apply, and no specific mapping is necessary.

In addition to the status code mapping for the <mgmtObj> CRUD Operations, no [battery] specific status codes are defined in OMA DM.

### 5.4.2.7		Resource [deviceInfo]

The generic <mgmtObj> mappings described in the clause 5.4.1 shall apply, and no  specific mapping is necessary.

In addition to the status code mapping for the <mgmtObj> CRUD Operations, no [deviceInfo] specific status codes are defined in OMA DM 1.3 and OMA DM 2.0.

### 5.4.2.8		Resource [deviceCapability]

The generic <mgmtObj> mappings described in the clause 5.4.1 shall apply, and no specific mapping is necessary.

In addition to the status code mapping for the <mgmtObj> CRUD Operations, OMA DM specifies the status codes that are exclusive for DCMO. Those status codes will be used only for the execute command, and shall be used only for the oneM2M UPDATE Request. The status code mappings specific to the [deviceCapability] Resource shall be as follows:

Note that the status codes defined in DCMO are common to the OMA DM 1.3 and OMA DM 2.0.

Table 5.4.2.3-1: DCMO Status Code Mapping

| oneM2M Primitive Status Code | OMA DCMO Status Code | Description |
| --- | --- | --- |
| TBD | 1200 | Operation Succeeds |
| TBD | 1201 | Device Capability is enabled and attached |
| TBD | 1202 | Device Capability is enabled and detached |
| TBD | 1203 | Device Capability is disabled and User is not allowed to re-enable it |
| TBD | 1204 | Device Capability is disabled and User is allowed to re-enable it |
| TBD | 1400 | Client Error |
| TBD | 1401 | User cancelled |
| TBD | 1402 | Operation Failed |
| TBD | 1450-1499 | Client Error – Vendor Specific |

### 5.4.2.9		Resource [reboot]

The generic <mgmtObj> mappings described in the clause 5.4.1 shall apply, and no specific mapping is necessary.

The status code mappings specific for executing the reboot attribute in the [reboot] Resource does not require additional mapping other than the status code mapping for the <mgmtObj> CRUD Operations.

In addition to the status code mapping for the <mgmtObj> CRUD Operations, the status code mappings specific for executing the factoryReset attribute in the [reboot] shall be as follows:

Note that the status codes defined in LAWMO are common to the OMA DM 1.3 and OMA DM 2.0.

Table 5.4.2.9-1: LAWMO Status Code Mapping

| oneM2M Primitive Status Code | OMA LAWMO Status Code | Description |
| --- | --- | --- |
| TBD | 1200 | Operation Succeeded |
| TBD | 1250-1299 | Successful – Vendor Specified |
| TBD | 1400 | Client Error |
| TBD | 1401 | User cancelled |
| TBD | 1450-1499 | Client Error – Vendor Specified |

### 5.4.2.10	Resource [eventLog]

The generic <mgmtObj> mappings described in the clause 5.4.1 shall apply, and no specific mapping is necessary.

In addition to the status code mapping for the <mgmtObj> CRUD Operations, no [eventLog] specific status codes are defined in OMA DM.

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?