| CHANGE REQUEST |
| --- |
| Group Name:* | MAS#12 |
| Source:* | Seungkyu Park, LG Electronics, seungk.park@lge.com |
| Format:* | Plenary / Teleconference |
| Date:* | 2014-7-19 |
| Contact:* | Seungkyu Park, LG Electronics, seungk.park@lge.com |
| Reason for Change/s:* | This contribution is to provide the status code mapping for the OMA DM. |
| CR against: Release* | Release-1 |
| CR against: TS/TR* | TS-0005, ver 0.2.0 |
| Clauses/Sub Clauses* | 5.4.1 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution provides the OMA DM status code mappings.

### -----------------------Start of New Text 1-------------------------------------------

### 5.4.1. 	Mapping for <mgmtObj> Resource Primitives

#### 5.4.1.1 	Create Primitive for <mgmtObj> Resource

The Create Request primitive for the <mgmtObj> Resource, as described in [2], shall be mapped to external management operations that create the corresponding OMA DM Management Objects. Depending on the type of the <mgmtObj> Resource (i.e., [memory], [battery], [deviceInfo], etc.), the associated OMA DM Management Object as specified in the clause 6.3 should be created. Creating OMA DM Management Object can be performed by the Protocol Command Add in OMA DM 1.3 and HGET in OMA DM 2.0.

Receiving Create Request primitive does not imply that the mapped external management operations shall be always performed since, on receiving the Create Request primitive, the corresponding external management objects may already exist in the device. For instance, after discovering the external management objects, the DMG in MN or ASN creates <mgmtObj> Resource in the IN-CSE, and in this case the IN-CSE does not need to create the external management objects.

In case that the external management objects are successfully created after receiving the Create Request primitive, then the objectID and objectPath attribute should be properly set based on the created external management objects.

#### 5.4.1.1 	Create Response Status Code Mapping

The result of creating the external management object should be mapped to the Create Response primitive for the <mgmtObj> Resource as indicated by the status code mapping in the clause.

Table 5.4.1.1-1: OMA DM 1.3 Status Code Mapping

| oneM2M Primitive Stauts Code | OMA DM 1.3 Status Code | Description |
| --- | --- | --- |
| TBD | (200) OK | The command accessed leaf node and it completed successfully. |
| TBD | (213) Chunked item accepted | Chunked item accepted and buffered |
| TBD | (215) Not executed | Command was not executed, as a result of User interaction as user chose to abort or cancel, The parent Atomic command failed, causing this command to fail. |
| TBD | (216) Atomic roll back OK | Command was inside Atomic element and Atomic failed. This command was rolled back successfully. |
| TBD | (401) Unauthorized | The originator's authentication credentials specify a principal with insufficient rights to complete the command. |
| TBD | (404) Not Found | The specified data item doesn't exist on the recipient. This may also imply that the stated URI for the location of the new management object cannot be resolved |
| TBD | (405) Command not allowed | Command not allowed. The requested command is not allowed on the target. |
| TBD | (407) Authentication required | No authentication credentials were specified. A suitable challenge can also be returned. |
| TBD | (413) Request entity too large | The data item to be transferred is too large (e.g., there are restrictions on the size of data items transferred to the recipient). |
| TBD | (414) URI too long | URI in command is too long. Either string presenting URI or segment in URI is too long or URI has too many segments. |
| TBD | (415) Unsupported media type or format | The media type or format for the data item is not supported by the recipient. |
| TBD | (418) Already exists | The requested Add command failed because the target already exists. |
| TBD | (420) Device full | The recipient device storage is full. |
| TBD | (424) Size mismatch | The chunked object was received, but the size of the received object did not match the size declared within the first chunk. |
| TBD | (425) Permission denied | The server does not have the proper ACL permissions. |
| TBD | (500) Command failed | Non-specific errors created by the recipient while attempting to complete the command. |
| TBD | (516) Atomic roll back failed | Command was inside Atomic element and Atomic failed. This command was not rolled back successfully. Server should take action to try to recover client back into original state. |

Table 5.4.1.1-2: OMA DM 2.0 Status Code Mapping

| oneM2M Primitive Stauts Code | OMA DM 2.0 Status Code | Description |
| --- | --- | --- |
| TBD | (200) OK | The DM command completed successfully |
| TBD | (400) Bad Request | The requested command could not be performed because of malformed syntax in the command. |
| TBD | (403) Forbidden | The requested command failed because the sender does not have adequate access rights on the recipient. |
| TBD | (404) Not Found | The requested target was not found |
| TBD | (405) Command Not Allowed | The requested command is not allowed on the node since the node is not executable for the EXEC command and the node is mandatory for the DELETE command |
| TBD | (415) Unsupported Media Type | The request is refused because the request uses a format not supported by the requested resource for the requested method |
| TBD | (419) ServerURI Error | The ServerURI provided causes errors |
| TBD | (500) Internal Error | The recipient encountered an unexpected condition which prevented it from fulfilling the request |
| TBD | (501) Not Implemented | The recipient does not support the features to fulfil the request. This is the appropriate response when the recipient does not recognize the requested command and is not capable of supporting it for any resource. |
| TBD | (503) Service Unavailable | The recipient is currently unable to handle the request due to a temporary overloading or maintenance of the recipient. The implication is that this is a temporary condition; which will be alleviated after some delay. |
| TBD | (506) Device Full | The response indicates that the recipient has not enough storage space for the data. |
| TBD | (507) User Rejected | The request is not executed since the user rejected the request. |

#### 5.4.1.2	Retrieve Primitive for <mgmtObj> Resource

The Retrieve Request primitive for the <mgmtObj> Resource, as described in [2], shall be mapped to external management operations that retrieve the corresponding OMA DM Management Objects. Depending on the type of the <mgmtObj> Resource (i.e., [memory], [battery], [deviceInfo], etc.), the associated OMA DM Management Object as specified in the clause 6.3 shall be retrieved. Retrieving OMA DM Management Object can be performed by the Protocol Command Get in OMA DM 1.3 and HPUT/HPOST/GET in OMA DM 2.0.

In case of OMA DM 2.0, note that the mapped external management operations may be implemented either by using HPUT, HPOST or GET. If the GET command is used, the requested data is carried within the OMA DM Session; otherwise the requested data is directly embedded within the HTTP message.

#### 5.4.1.2 	Retrieve Response Status Code Mapping

The result of retrieving the external management object should be mapped to the Retrieve Response primitive for the <mgmtObj> Resource as indicated by the status code mapping in the clause.

Table 5.4.1.2-1: OMA DM 1.3 Status Code Mapping

| oneM2M Primitive Stauts Code | OMA DM 1.3 Status Code | Description |
| --- | --- | --- |
| TBD | (200) OK | The command completed successfully. |
| TBD | (215) Not executed | Command was not executed, as a result of: User interaction as user chose to abort or cancel, The parent Atomic command failed, causing this command to fail. |
| TBD | (217) OK with inherited ACL | The command completed successfully with inherited ACL returned. The Get command was performed to get ACL on a node which has Empty ACL |
| TBD | (401) Unauthorized | The originator's authentication credentials specify a principal with insufficient rights to complete the command. |
| TBD | (404) Not found | The specified data item doesn't exist on the recipient. |
| TBD | (405) Command not allowed | The requested command is not allowed on the target. |
| TBD | (406) Optional feature not supported | The recipient did not recognize the feature specified after the “?” at the end of the URI. |
| TBD | (407) Authentication required | No authentication credentials were specified. A suitable challenge can also be returned. |
| TBD | (413) Request entity too large | The requested data item is too large to be transferred at this time. |
| TBD | (414) URI too long | URI in command is too long. Either string presenting URI or segment in URI is too long or URI has too many segments. |
| TBD | (415) Unsupported media type or format | The media type or format for the data item is not supported by the recipient. |
| TBD | (425) Permission denied | The server does not have the proper ACL permissions. |
| TBD | (500) Command failed | Non-specific errors created by the recipient while attempting to complete the command. |

Table 5.4.1.1-2: OMA DM 2.0 Status Code Mapping

| oneM2M Primitive Stauts Code | OMA DM 2.0 Status Code | Description |
| --- | --- | --- |
| TBD | (200) OK | The DM command completed successfully |
| TBD | (204) No Content | The request was successfully completed but no data is being returned. |
| TBD | (304) Not Modified | The data requested is not modified. |
| TBD | (400) Bad Request | The requested command could not be performed because of malformed syntax in the command. |
| TBD | (403) Forbidden | The requested command failed because the sender does not have adequate access rights on the recipient. |
| TBD | (404) Not Found | The requested target was not found |
| TBD | (406) Not Acceptable | The resource identified by the request is only capable of generating response entities which have content characteristics not acceptable according to the accept headers sent in the request |
| TBD | (500) Internal Error | The recipient encountered an unexpected condition which prevented it from fulfilling the request |
| TBD | (501) Not Implemented | The recipient does not support the features to fulfil the request. This is the appropriate response when the recipient does not recognize the requested command and is not capable of supporting it for any resource. |
| TBD | (503) Service Unavailable | The recipient is currently unable to handle the request due to a temporary overloading or maintenance of the recipient. The implication is that this is a temporary condition; which will be alleviated after some delay. |
| TBD | (507) User Rejected | The request is not executed since the user rejected the request. |

#### 5.4.1.3	Update Primitive for <mgmtObj> Resource

The Update Request Primitive for <mgmtObj> Resource can be used to modify the externam management objects or to execute the management commands. The mapping in either cases shall be different as the following sections.

##### 5.4.1.3.1	Update Primitive for Replacing Data in the Management Object

This is the case that the Update Primitive targets the attribute that is mapped to the non-executable Node in external management object as specified in the clause 6.3. The Update Request primitive for the <mgmtObj> Resource, as described in [2], shall be mapped to external management operations that replace the data in the corresponding OMA DM Management Objects. Depending on the type of the <mgmtObj> Resource (i.e., [memory], [battery], [deviceInfo], etc.), the associated OMA DM Management Object as specified in the clause 6.3 shall be updated. Replacing data in OMA DM Management Object can be performed by the Protocol Command Replace in OMA DM 1.3 and HGET in OMA DM 2.0.

#### 5.4.1.3.1.1 	Update Response Status Code Mapping

The result of replacing data in the external management object should be mapped to the Update Response primitive for the <mgmtObj> Resource as indicated by the status code mapping in the clause.

Table 5.4.1.3.1-1: OMA DM 1.3 Status Code Mapping

| oneM2M Primitive Stauts Code | OMA DM 1.3 Status Code | Description |
| --- | --- | --- |
| TBD | (200) OK | The command accessed an existing leaf node and it completed successfully. |
| TBD | (213) Chunked item accepted | Chunked item accepted and buffered. |
| TBD | (215) Not executed | Command was not executed, as a result of: User interaction as user chose to abort or cancel, The parent Atomic command failed, causing this command to fail. |
| TBD | (216) Atomic roll back OK | Command was inside Atomic element and Atomic failed. This command was rolled back successfully. |
| TBD | (401) Unauthorized | The originator's authentication credentials specify a principal with insufficient rights to complete the command. |
| TBD | (403) Forbidden | The target of a Replace command is a node that cannot be modified for reasons other than access control (for example, if the node is in use). |
| TBD | (404) Not Found | The specified data item doesn't exist on the recipient. |
| TBD | (405) Command not allowed | Command not allowed. The requested command is not allowed on the target. Any attempt to add a child node to a leaf node results in a (405) Command not allowed Status. Additionally, Format, Name and Type properties of permanent nodes cannot be changed, if such an attempt is made, (405) Command not allowed status code is sent back. |
| TBD | (407) Authentication required | No authentication credentials were specified. A suitable challenge can also be returned. |
| TBD | (413) Request entity too large | The data item to be transferred is too large (e.g., there are restrictions on the size of data items transferred to the recipient). |
| TBD | (414) URI too long | URI in command is too long. Either string presenting URI or segment in URI is too long or URI has too many segments. |
| TBD | (415) Unsupported media type or format | The media type or format for the data item is not supported by the recipient. |
| TBD | (418) Already Exists | The requested Replace command failed because the target already exists. |
| TBD | (420) Device full | The recipient device storage is full. |
| TBD | (424) Size mismatch | The chunked object was received, but the size of the received object did not match the size declared within the first chunk. |
| TBD | (425) Permission denied | The server does not have the proper ACL permissions. |
| TBD | (500) Command failed | Non-specific errors created by the recipient while attempting to complete the command. |
| TBD | (516) Atomic roll back failed | Command was inside Atomic element and Atomic failed. This command was not rolled back successfully. Server should take action to try to recover client back into original state. |

Table 5.4.1.3.1-2: OMA DM 2.0 Status Code Mapping

| oneM2M Primitive Stauts Code | OMA DM 2.0 Status Code | Description |
| --- | --- | --- |
| TBD | (200) OK | The DM command completed successfully |
| TBD | (400) Bad Request | The requested command could not be performed because of malformed syntax in the command. |
| TBD | (403) Forbidden | The requested command failed because the sender does not have adequate access rights on the recipient. |
| TBD | (404) Not Found | The requested target was not found |
| TBD | (415) Unsupported Media Type | The request is refused because the request uses a format not supported by the requested resource for the requested method |
| TBD | (419) ServerURI Error | The ServerURI provided causes errors |
| TBD | (500) Internal Error | The recipient encountered an unexpected condition which prevented it from fulfilling the request |
| TBD | (501) Not Implemented | The recipient does not support the features to fulfil the request. This is the appropriate response when the recipient does not recognize the requested command and is not capable of supporting it for any resource. |
| TBD | (503) Service Unavailable | The recipient is currently unable to handle the request due to a temporary overloading or maintenance of the recipient. The implication is that this is a temporary condition; which will be alleviated after some delay. |
| TBD | (506) Device Full | The response indicates that the recipient has not enough storage space for the data. |
| TBD | (507) User Rejected | The request is not executed since the user rejected the request. |

##### 5.4.1.3.2	Update Primitive for Executing Management Commands

This is the case that the Update Primitive targets the attribute that is mapped to the executable Node in external management object as specified in the clause 6.3. The Update Request primitive for the <mgmtObj> Resource, as described in [2], shall be mapped to external management operations that execute the Node in the external management object. Depending on the type of the <mgmtObj> Resource (i.e., [memory], [battery], [deviceInfo], etc.), the Node in the associated OMA DM Management Object as specified in the clause 6.3 shall be executed. Executing the Node in OMA DM Management Object can be performed by the Protocol Command Exec in OMA DM 1.3 and EXEC in OMA DM 2.0.

The mapped external management operations may be executed either by the synchronous or asynchronous reporting as specified by OMA DM 1.3 and OMA DM 2.0. Selecting the synchronous or asynchronous reporting is implementation issue, and is independent on whether the Update Primitive is requested as blocking or non-blocking.

#### 5.4.1.3.2 	Update Response Status Code Mapping

The result of executing the node in the external management object should be mapped to the Update Response primitive for the <mgmtObj> Resource as indicated by the status code mapping in the clause.

Table 5.4.1.3.2-1: OMA DM 1.3 Status Code Mapping

| oneM2M Primitive Stauts Code | OMA DM 1.3 Status Code | Description |
| --- | --- | --- |
| TBD | (200) OK | The command and the associated Alert action are completed successfully. |
| TBD | (202) Accepted for processing | The request to either run a remote execution of an application or to alert a user or application was successfully received. |
| TBD | (215) Not executed | Command was not executed, as a result of: User interaction as user chose to abort or cancel, The parent Atomic command failed, causing this command to fail. |
| TBD | (401) Unauthorized | The originator's authentication credentials specify a principal with insufficient rights to complete the command. |
| TBD | (403) Forbidden | Forbidden. The command could not be executed for reasons other than access control rights. |
| TBD | (405) Command not allowed | The requested command is not allowed on the target. |
| TBD | (406) Optional Feature Not Supported | The specified Exec command is not supported by the recipient. |
| TBD | (407) Authentication required | No authentication credentials were specified. A suitable challenge can also be returned. |
| TBD | (414) URI too long | URI in command is too long. Either string presenting URI or segment in URI is too long or URI has too many segments. |
| TBD | (420) Device full | There is insufficient space in the recipient management tree for the data item. |
| TBD | (425) Permission denied | The server does not have the proper ACL permissions. |
| TBD | (500) Command failed | Non-specific errors created by the recipient while attempting to complete the command. |
| TBD | (510) Data store failure | Error occurs while the recipient copying the data item within the recipient's management tree. |

Table 5.4.1.1-2: OMA DM 2.0 Status Code Mapping

| oneM2M Primitive Stauts Code | OMA DM 2.0 Status Code | Description |
| --- | --- | --- |
| TBD | (200) OK | The DM command completed successfully |
| TBD | (202) Accepted | Accepted for processing. The asynchronous reporting mechanism is used to report the actual results. |
| TBD | (400) Bad Request | The requested command could not be performed because of malformed syntax in the command. |
| TBD | (403) Forbidden | The requested command failed because the sender does not have adequate access rights on the recipient. |
| TBD | (404) Not Found | The requested target was not found |
| TBD | (405) Command Not Allowed | The requested command is not allowed on the node since the node is not executable for the EXEC command and the node is mandatory for the DELETE command |
| TBD | (419) ServerURI Error | The ServerURI provided causes errors |
| TBD | (500) Internal Error | The recipient encountered an unexpected condition which prevented it from fulfilling the request |
| TBD | (501) Not Implemented | The recipient does not support the features to fulfil the request. This is the appropriate response when the recipient does not recognize the requested command and is not capable of supporting it for any resource. |
| TBD | (503) Service Unavailable | The recipient is currently unable to handle the request due to a temporary overloading or maintenance of the recipient. The implication is that this is a temporary condition; which will be alleviated after some delay. |
| TBD | (507) User Rejected | The request is not executed since the user rejected the request. |

#### 5.4.1.4	Delete Primitive for <mgmtObj> Resource

The Delete Request primitive for the <mgmtObj> Resource, as described in [2], shall be mapped to external management operations that delete the corresponding OMA DM Management Objects. Depending on the type of the <mgmtObj> Resource (i.e., [memory], [battery], [deviceInfo], etc.), the associated OMA DM Management Object as specified in the clause 6.3 should be deleted. Deleting OMA DM Management Object can be performed by the Protocol Command Delete in OMA DM 1.3 and DELETE in OMA DM 2.0.

Receiving Delete Request primitive does not imply that the corresponding external management objects shall be always deleted. They may not be deleted if the external management objects are used by entities such as the Device Management Server.

#### 5.4.1.4 	Delete Response Status Code Mapping

The result of deleting the external management object should be mapped to the Delete Response primitive for the <mgmtObj> Resource as indicated by the status code mapping in the clause.

Table 5.4.1.1-1: OMA DM 1.3 Status Code Mapping

| oneM2M Primitive Stauts Code | OMA DM 1.3 Status Code | Description |
| --- | --- | --- |
| TBD | (200) OK | The command and the associated individual commands were completed successfully. |
| TBD | (215) Not executed | Command was not executed, as a result of: User interaction as user chose to abort or cancel, The parent Atomic command failed, causing this command to fail. |
| TBD | (216) Atomic roll back OK | Command was inside Atomic element and Atomic failed. This command was rolled back successfully. |
| TBD | (401) Unauthorized | The originator's authentication credentials specify a principal with insufficient rights to complete the command. |
| TBD | (403) Forbidden | The target of a Delete command is a node that cannot be deleted for reasons other than access control (for example, if the node is in use). |
| TBD | (404) Not found | The recipient determined that the data item doesn't exist on the recipient's management tree. |
| TBD | (405) Command not allowed | The requested command is not allowed on the target. |
| TBD | (407) Authentication required | No authentication credentials were specified. A suitable challenge can also be returned. |
| TBD | (414) URI too long | URI in command is too long. Either string presenting URI or segment in URI is too long or URI has too many segments. |
| TBD | (425) Permission denied | The server does not have the proper ACL permissions. |
| TBD | (500) Command failed | Non-specific error(s) occurred on the recipient while attempting to complete the command. |
| TBD | (516) Atomic roll back failed | Command was inside Atomic element and Atomic failed. This command was not rolled back successfully. Server should take action to try to recover client back into original state. |

Table 5.4.1.1-2: OMA DM 2.0 Status Code Mapping

| oneM2M Primitive Stauts Code | OMA DM 2.0 Status Code | Description |
| --- | --- | --- |
| TBD | (200) OK | The DM command completed successfully |
| TBD | (400) Bad Request | The requested command could not be performed because of malformed syntax in the command. |
| TBD | (403) Forbidden | The requested command failed because the sender does not have adequate access rights on the recipient. |
| TBD | (404) Not Found | The requested target was not found |
| TBD | (405) Command Not Allowed | The requested command is not allowed on the node since the node is not executable for the EXEC command and the node is mandatory for the DELETE command |
| TBD | (500) Internal Error | The recipient encountered an unexpected condition which prevented it from fulfilling the request |
| TBD | (501) Not Implemented | The recipient does not support the features to fulfil the request. This is the appropriate response when the recipient does not recognize the requested command and is not capable of supporting it for any resource. |
| TBD | (503) Service Unavailable | The recipient is currently unable to handle the request due to a temporary overloading or maintenance of the recipient. The implication is that this is a temporary condition; which will be alleviated after some delay. |
| TBD | (507) User Rejected | The request is not executed since the user rejected the request. |

### -----------------------End of New Text 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?